## Slide 1: The functional form of nuclei decay in a point-approximation reactor within the particles' birth and death model
M. Kravchenko, Ed. Rudak, T. Korbut, A. Kuzmin, A. Piatrouski.
m.kravch@sosny.bas-net.by
State Scientific Institution “THE JOINT INSTITUTE FOR POWER AND NUCLEAR RESEARCH – SOSNY” National Academy of Science of Belarus

## Slide 2: Point-approximation reactor aspect
Basic physics processes is rationally to study on a point-approximation reactor.
Properties of that kind of reactor:
Low power release (“Cold reactor”). → No reactivity effects!
Homogeneous medium. → All characteristics of reactor in it’s any part are the same on the whole.
Basic physics in such point reactor can be scaled to a real full-size reactor.

## Slide 3: Some birth and death model’s aspects
For estimation of random variables mean values the formalism of discrete random processes for nuclei transformation in thermal reactor was chosen.
This formalism is based on Kolmogorov equations for transformation probabilities
Notes: P – probability of state
,  – instant intensities
In reactor physics the definition of average number of particles in a system is used. The solution of this differential equation is well known and can be easily written down.

## Slide 4: The function form under the integral
It’s easy to see that full number of neutrons in system inverse proportionality depends on neutron generation lifetime
Generation life time
Notes: It’s easy to see that full number of neutrons in system inverse proportionality depends on neutron generation lifetime. So defining the function form will be easy enough.
And defining the function form of generation life time also can go from certain conclusions

## Slide 5: Fundamental curve
At the beginning neutron will be absorbed with a significant probability and will make an ensemble of delayed neutron emitters.
With the passage of time this delayed neutron emitters will decay with a certain probability.
Notes: So why are we studying only one neutron? If the mathematical equations work well for one example, the math can be scaled to a bigger system. So this is actually a fundamatial study, that will be a foundation of something bigger and more closer to a real world.

## Slide 6: The problem of Poisson and Binomial distributions
Notes: All previous conclusions were made on the assumption that delayed neutron emitters decay according to Poisson distribution. But thinking physics that is not correct, because Poisson distribution goes all the way to the infinity making number of delayed neutron emitters also infinite. On the other hand Binomial distribution make a better sense, but can’t be so easily described mathematically.

## Slide 7: New functional form of neutron generation number
Previous function
Current function
Notes: So choosing the right mathematical form to describe this process is something, that we must do for achieving correct and delicate mathematical apparatus.

## Slide 8: Generation time & generation lifetime
Generation time
Generation lifetime
Expected value

## Slide 9: Generation lifetime & emerge probability

## Slide 10: Conclusions
Particles' birth & death model is proven to be well working apparatus for describing the physics of thermal reactor.
To create a adequate mathematical description several attempts were made before it was done.
At the current stage of model development description of one neutron interaction with breeding medium was completed.
Further development is up to describe an ensemble of neutrons in reactor within the particles’ birth & death model.

## Slide 11: Thank You for attention!

## Slide 12: Some references
1. Т.Н. Корбут, А.В. Кузьмин, Э.А. Рудак Тепловой реактор как аналог ADS-систем с внутренним источником нейтронов. Известия РАН. Серия физическая, 2015, т. 79, №4, с.503-511.
2. T.N. Korbut, A.V. Kuz’min, E.A. Rudak A Thermal Nuclear Reactor as an Analog of ADS Systems with Internal Sources of Ntutrons. Bulletin of the Russian Academy of Sciences. Physics, 2015, v. 79, №4, pp. 461-469. © Allerton Press, Inc., 2015.
3. D.G. Kendall On the Generalized Birth-and-Death Process. Ann. Math. Statist., vol. 19, pp. 1 – 15, 1948.
4. А.Т. Баручча-Рид, Элементы теории марковских процессов и их приложения, М.: Наука, 1969. – 512 с.