## Slide 1
Current status of
the compact 2.45 GHz ECR Ion Source at FLNR JINR
Riyaz Fatkullin (ITEP, JINR)
Sergey Bogomolov (FLNR JINR)
Andrey Efremov (FLNR JINR)
Vladimir Loginov (FLNR JINR)
Yuri Kostukhov (FLNR JINR)
Andrey Bondarchenko (FLNR JINR)
AYSS 2018, 23-27 April 2018

## Slide 2
ECR Ion Source
Basic principles
In ECR ion sources the plasma heating is based on the energy transfer from microwaves to electrons via electron cyclotron resonance in external magnetic field. The electron cyclotron frequency is matched with the microwave frequency – heating is mainly transverse
ECR – Electron Cyclotron Resonance

## Slide 3
Concept
Compact ion source
Radially magnetized permanent magnet ring
Coaxial resonator
Compact ECR ion source
Size: 120 x 70 x 60 mm
Generation of 1+ ions
Low operation power and production cost
Outline

## Slide 4
Timeline
Compact 2.45 GHz ECR Ion Source
January
2018
July
2017
June
2017
Summer 2016
Computer design with CST Studio Suite
(July-August)
Design
Ion source was produced and fully assembled
Production
Measurement of ion current and ignition power
First test
New test stand: ion spectra, higher current
Second test

## Slide 5
Test stand 2017
Outline
Pressure torr
Voltage at the puller electrode U = - 300V
Generator’s frequency MHz
Injected power W
Gases: Ar, He, Ne

## Slide 6
Aim of experiment
Determination of lower limit of injected power for discharge ignition for different discharge conditions (discharge gap, frequency, gas flow)
1
Measurement of extracted current (current of puller electrode) at different discharge parameters (injected power, frequency and gas flow)
2
Measurement of puller electrode current for different discharge gaps
3

## Slide 7
Results 2017
Max current I = 177 µA (He)
1
Min pressure P = 4.2x10 -6 torr
2
Min ignition power P = 0.5 W
3
2.45 GHz easy to discharge, 2.5 GHz max current
4

## Slide 8
Test stand 2018
Outline
Pressure: 10-6 ÷ 10-5 torr
Uex = 9 ÷ 15 kV
Generator’s frequency: 2400÷2500 MHz
Injected power: 0 ÷ 100 W
Gases: He, H2

## Slide 9
Aim of experiment
To obtain spectra of hydrogen and helium
1
To find solutions to increase output current
2

## Slide 10
Results
Test 2018
Extracted current as function of frequency for different coupling loop length (9, 13 and 15 mm, 50 W).
New coupling loop (L = 9, 13, 15 mm)

## Slide 11
Results
Test 2018
Spectra of hydrogen ions. Dext = 2 mm.
f = 2452 MHz, W = 60 W, 8.9 kV, 3.2 *10-6 torr.
Spectra of He . Dext = 2 mm, f = 2450 MHz, W = 60 W, 8.9 kV, 2.1 *10-6 torr.

## Slide 12
Results
Test 2018
Spectra of helium ions. Dext = 3 mm, f = 2454 MHz, W = 100 W, 8.9 kV, 1.6*10-5 torr.

## Slide 13
Results 2018
1
2
3
Max current density of He+ ions consists of 7.5 mA/ cm2 (255 mkA for Ø 2 mm, and 534 mkA for Ø 3 mm)
Spectra of hydrogen contains 3.2% (10 µA) of protons, 82.5% (255 µA) of diatomic molecular ions and 14.3% (44 µA) of triatomic molecular ions
Spectra of helium contains 1 spectral line of He+ ions

## Slide 14
Second compact ECR
ITEP, Moscow

## Slide 15
Conclusions
- Beam from the compact ECR source was examined at ECR sources test stand at FLNR
Spectra of hydrogen contains large amount of H2+ molecular ions
Current can be further increased with new remote coupler control device
Future plans:
- Make new adjustment platform for precise positioning of source;
- Control the coupling device remotely;
- Optimize the optical extraction system;
- Try to use well-known and widely used ECR techniques to increase output current (BIAS electrode);
MASHA (Mass-Analyzer of Supper Heavy Atoms):
- Testing source with heavy gases (Ar, Kr, Xe)
- Measurements of the gas efficiency and time response of ion source;

## Slide 16
Thank you
for your attention