Data processing status of the TOF400 detector
Analysis and Detector Meeting of the BM@N Experiment
13.03.2024

---
TOF400 system.
Two arms of 10 mRPC detectors each.
Active area 2*1,1*1,3 m2
960 Readout strips.
1920 channel of FEE.
mRPC detector with active area 30*60 cm2.
48 readout strips of 1*30 cm2 in one mRPC.
90%C2H2F4 + 5% SF6 + 5% i-C4H10
11,5 kV working point

---
Data processing flow for TOF400.
*.data
raw.root
digi.root
DB
INL for TDC
Mapping
BmnDataToRoot.C
RawToRoot
DataToDigi
run_reco_bmn.C
/input
LR corr
Slewing
TimeShift
DB
geometry
dst.root

---
Calibration of cable length (LR correction).
tL
Y = {T_L - T_R} over {2} * V
TDC
TDC
Y=0
tR
TL
TR

---
Geometry alignment of the TOF400.
dz
σx(track-hit) = 5,2 mm
σy(track-hit) = 6 mm

---
Geometry alignment of the TOF400.
Z + 6,5cm - > Y (Plane) - > Z (Plane) - > X (Plane) - > Z (Plane) - > XY (Plane).
π-
p
π+

---
Slewing correction of the TOF400.
 Presented by Mikhail Mamaev at 10th BM@N collaboration meeting.
Step 1:
Correction for T0 by line
Step 2:
Correction for RPC

---
Slewing correction of the TOF400 by π+(-) particles.
Step 1:
Correction for T0 by line
Step 2:
Correction for RPC

---
Time shift correction of the TOF400.
ToF for π+ band with Slewing
ToF for π+ band w/o Slewing
ToFideal — ToFmes for π+ band
After all corrections

---
PID possibility.

---
PID possibility.
0,02+0,015 GeV2/c4
0,912+0,05 GeV2/c4
0,25+0,016 GeV2/c4
m2(π) = 0,018 GeV2/c4
m2(k) = 0,243 GeV2/c4
m2(p) = 0,880 GeV2/c4
Spector of m2 in 1-1,1 GeV/c momentum range.

---
ToF performance.
What should we choose for time calibration, π or p?

---
ToF performance.
Time resolution during the data taking.
π
proton

---
Conclusion.
The main work on calibrating the TOF 400 system has been completed.
After proton peak correction, all calibrations will be pushed to git.
The problem of mismatching particles of different charges has not been solved.
Еhe problem of choosing the type of particle for time calibration has not been solved.
Thank you for your attention!