## Slide 1
Straw-Barrel status report

## Slide 2
• Productivity- 1m/min • Produced ~20km straw
• Length- 5.5m • Installed ~8000 straw
• Diameter-from 10 mm • After 10 years of operation non- working- 3 straw
• Film thickness-36 microns • Film is available in Russia •Number of employees-10FTE • Number of employees-10FTE
• Coating thickness 50-100nm
• Coating is carried out in the RF
STRAW production line

## Slide 3
New Straw production line and assembling place
Area ~200 sq.m., clean room~100 sq.m, machine shop and assembling hall~50 sq.m and 8,5 m high
Double Production line length~12m
The deadline is the beginning of the 3rd quarter of 2024
Commissioning works-the beginning of the 4th quarter of 2024
Necessary materials and equipment have been purchased
Planned volume ~60km straw
This is what we want to get

## Slide 4
Measurements of the straw performance and choice of the readout electronics parameters
- Spatial resolution (SPS)
– influence of the readout parameters
- electronics noise, threshold
- influence of the wire displacement
- different operation conditions (gas gain, pressure dependence)
- measurements in the magnetic field (H4)
- Charge measurements (PS, low momentum pi, mu, e)
- charge distribution for different particle momenta
- multiple scattering probability
- electronics dynamic range for PID (protons are required, under discussion)
- measurements at PNPI under discussion

## Slide 5
Beam Test activity

## Slide 6
Test beam periods 2024 at SPS and PS
Three different tasks:
- setup development, readout electronics test and debugging :
SPS H8 beam dump (low intensity muons)
- spatial resolution: SPS H4
- charge measurements for low momentum particles: PS T09

## Slide 7
The SPS setup

## Slide 8
Validation with NA62 data
- good agreement between two independent analysis methods
- results similar to the resolution obtained with straw prototype and VMM3/TIGER
- see A.Chukanov’s talk
Notes: 8

## Slide 9
The PS setup
hadron beam
+ electron beam ( reference )
see S.Bulanova talk

## Slide 10
The PS setup
Feedback from PS:
- will investigate possibility for low momenta protons
- for October TB it is possible to increase intensity

## Slide 11
Prototyping
- Small prototype production (lab and test beam straw and readout performance studies) - development and prototyping of the construction elements (gas supply, sealing) - development and optimization of the electrical connections (noise and x-talk reduction

## Slide 12
Electronic R&D
VMM3a PCB with microcontroller.

## Slide 13
FEE на noname ASIC from De Geronimo

## Slide 14
Contributions

## Slide 15
Gas System: design requirement

## Slide 16
Publications for 2023
Testbeam Measurements and Realistic Simulation for the SPD Straw Drift Tubes
November 2023
Physics of Atomic Nuclei 86(5):832-837
Straw signal modeling using Garfield++ interface to LTSPICE
November 2023
Journal of Physics Conference Series 2642(1):012005
Online Gas Gain Monitoring System
October 2023
Physics of Particles and Nuclei Letters 20(5):1240-1242
VMM3 ASIC as a potential front end electronics solution for future Straw Trackers, NIM,Volume 1047,2023,

## Slide 17
Plans
- straw tracker prototyping
- new assembling and production lab spaces - recovery of the miniSPD setup - readout electronics prototyping - test beam measurements at SPS and PS, the corresponding data analysis and feedback to FEE developers - evaluating possibilities for the testbeam measurements at PNPI (Gatchina), INP (Almaty) and AANL(ErPhI,Erevan)
- concept development of the gas supply system - longevity study for straw and supporting element material

## Slide 18: Backup

## Slide 19
Reference tracking -- residuals
Time resolution -- T0
Reference tracking and timing
Better than 500ps
Work ongoing:
- accounting for the reference system uncertainty in the TB analysis
- improvement of the reference tracking resolution

## Slide 20: 10mm Straw Resolution
The weighted mean of Coordinate resolution distribution better than 200 μm
The best time ‘resolution’ is about 4-5 ns
Analysis ongoing
PRELIMINARY