## Slide 1: Status of Forward Hadron Calorimeter (FHCal)
A.Ivashkin
Institute for Nuclear Research RAS, Moscow
on behalf of the FHCal group
13th MPD collaboration meeting, Apr., 2024.
FHCal overview;
Progress in integration;
FHCal readout;
FHCal in trigger;
Open questions.

## Slide 2
FHCal
Two arms of hadron calorimeter at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules.
~1x1 m2 each part.
Beam hole 15x15 cm2.
Lead/scintillator sampling calorimeter.
Longitudinal segmentation;
Light readout- WLS-fibers;
7 sections/photodetectors in each module.
FHCal in MPD
FHCal modules

## Slide 3
The centrality of the collision;
The reaction plane orientation;
Minimum bias trigger;
Physics in forward rapidity?
Tasks of FHCal :
X
Centrality:
2D-Fit of energy distributions in FHCal modules

## Slide 4
FHCal modules are at MPD hall now!
Modules in stockroom at INR
Modules at MPD hall
In Nov’23
90 modules were delivered form INR to MPD hall
Transportation

## Slide 5: Step 1: Assembling of FHCal modules in basket
М10 х30
M8
M6
Drawings

## Slide 6: Step 1: Assembling of FHCal modules in basket
Photos from MPD hall
One FHCal arm already assembled in basket !

## Slide 7: Step 2: FHCal installation into support frame (in pole)
Main problem: beam pipe between two FHCal halves
FHCal inserted into pole from inner side
Two FHCal halves pressed together
Drawings

## Slide 8: Step 2: FHCal installation into support frame (at floor)
Photos from MPD hall
FHCal arm already moved into support frame!

## Slide 9: Step 3: Put FHCal parts together
Photo from MPD hall
FHCal parts pressed together!
Drawing
Up to now all manipulations with FHCal were performed at floor successfully!
Many thanks to S. Gerasimov and JINR technical group!
Can we add additional metal in central hole to symmetrize interactions around beam pipe?
Can it help in centrality reconstruction?

## Slide 10
Installation of Front-End-Electronics;
Installation of Detector Control System (DCS);
Installation of readout;
Calibration with cosmic muons;
Development of FHCal trigger.
Next steps in development of FHCal

## Slide 11
Two PCBs in each module with:
7 photodetectors ;
Photodetectors – MPPCs;
two-stage amplifiers;
HV channels;
LED calibration source.
MPPC: S14160-3010PS
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~18%.
FHCal modules are currently equipped with FEE in the MPD hall.
Front-End-Electronics

## Slide 12
Detector Control System (DCS)
DCS Tasks:
Control of HV at photodetectors (MPPC’s);
Temperature control of photodetectors;
Compensation of temperature drift of MPPC gain;
Monitoring of MPPC gain with stabilized light source.
DCS open question:
Cabling for RS485 bus (now flat cables)?
Pick up noises in real environment ?
Place for System Module: near calorimeter or in Control Room?
LAN
FEE
Database
FHCal New Slow Control (proxy)
General Slow Control
System Module
System Module
FEE
FEE
FEE
FEE
FEE
RS485
Connection diagram
Hardware:
System Module (HV sys. Co.)

## Slide 13
ADC signal readout
FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
All 10 ADC boxes are tested and ready for installation.
Open questions for readout:
Would ADC be replaced by new ECAL-type modules? (Fast ADC for FHCal trigger)?
ADC cooling? Pipes for air?
5 ADCs for each arm of FHCal
Two halves of FHCal.

## Slide 14: FHCal readout and control
FEE
FEE
FEE
1
2
44
…
on detector
ADC64 (1)
(9 modules)
ADC64 (2)
(9 modules)
ADC64 (5)
(8 modules)
…
near detector
FHCal arm
HVsys
DCS Control box
power supply
signal cables
General Control System
- Ethernet
DAQ
~20m cables
Both FHCal arms have the same readout scheme.

## Slide 15
Energy calibration with cosmic nuons
Response of FHCal modules to cosmic muons with different track geometries.
Horizontal muons
Energy deposition 5 MeV;
Narrow peak;
But long time for collection;
(one week data acquisition);
Required at least one time.
Vertical muons
Wide peaks;
Short time for collection;
(one day data acquisition);
Energy deposition should be normalized for horizontal muons;
Tests done for FHCal prototype.
Must be done for full FHCal.

## Slide 16
FHCal trigger (analog version)
Threshold 2 MeV/module
Trigger efficiency ~98%
Dependence of trigger efficiency on the configuration of modules (Au-Au 11 GeV).
Scheme of FHCal trigger
12-channels signal adders
Adders of analog signals from individual modules were produces for full FHCal.
The configuration of modules in trigger would depend on FEE and correlation noises. Flexible configuration is to be developed.

## Slide 17: Digital FHCal trigger ? (Data from MPD trigger group)
Total delay time 387 ns
Version ADC64s2 V5.0 prepared for FHCal
New version ADC64ECAL prepared for ECal
Total delay time 237 ns (150 ns shorter)
New ADC modules allow arrangement of FHCal trigger logic with digitized signals instead of analog adders!?

## Slide 18
Summary (open questions)
Timetable for FHCal installation?
One or two FHCal arms at the beginning?
Cabling for ADC and DCS?
Place for DCS System Module?
What ADCs (previous or new Ecal type)?
What FHCal trigger (analog or digital)?
Pipes with cooling air for ADCs?

## Slide 19
Thank you!

## Slide 20: Mechanical support (main elements)
Пластина
Support frame in magnet pole
Basket of FHCal modules
Outer table
Design of all elements was finished!
The production starts now!

## Slide 21: FHCal cabling
Prepared by
M. Rumyantsev
Patch panel is not ready.
Must be constructed in nearest time