## Slide 1: XIII Collaboration Meeting of the MPD Experiment at the NICA Facility The progress of ECal production in China

## Slide 2: CONTENTS
1
  MPD-ECAL introduction
2
  ECal module and PCB production
3
  Batch test of ECal PCBs
4
  Summary

## Slide 3: MPD-ECal production
MPD-ECal requirements:
particle occupancy : < 5%
Time resolution : <1ns
Energy resolution : < 5% @1GeV
Operate in the magnetic FIELD : ~ 0.5T
Adequate space resolution.
MPD-ECal
The Barrel of ECal
ECal 8-Zone
ECal Half-Sector
ECal Tower
ECal Module
The ECal-MPD
1 Barrel
50 Half-sector
300 8-Zone module
2400 Module
38400 Tower

## Slide 4: ECal module and PCB production in China
ECal module:
Construction of 8 sectors. 768 modules in total.
Institutes: Tsinghua University 60%
Shandong University 20%
Fudan University 10%
University of South China 10%
ECal PCB:
Production and 1200 PCBs (without SiPMs).

## Slide 5: Modules production in China
In the first stage, 8 sectors have been produced in China
8 sectors=16 half sectors=768 modules=12288 towers
1
2
3
4
5
6
7
8
Modules produced in each institutes
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | Total | Progress
THU | 19 | 19 |  | 38 | 96 | 96 | 96 | 96 | 460 | Finished
SDU |  |  | 96 | 58 |  |  |  |  | 154 | Finished
FDU |  | 77 |  |  |  |  |  |  | 77 | Finished
USC | 77 |  |  |  |  |  |  |  | 77 | Finished

## Slide 6: Modules production in China
Module production in THU
Module production in SDU
Module production in THU

## Slide 7: Modules production in China
Module production in USC
Module production in USC
Module production in FDU

## Slide 8: Cosmic Test of 217 Modules from China
Cosmic test in JINR

## Slide 9: PCBs production in China
 | T123 | T4 | T5 | T6 | T7 | T8 | Total | Production | Test | Shipment
THU | 450 | 150 | 150 | 150 | 150 | 150 | 1200 | Finished | Finished | Finished

## Slide 10: Batch test of ECal PCBs
Input Signal
POGO PIN
Adaptor
The pads for SiPM
40P Header
10P Header

## Slide 11: Batch test of ECal PCBs

## Slide 12: Batch test of ECal PCBs
Waveform Generator
Power Supply
NIM Crate
VME Crate
Adapter
Power Splitter
Backplane & PCB
PC

## Slide 13: Batch test of ECal PCBs
Waveform Generator
TRG
V1742
VME Bridge
VME Crate
Fan in-Fan out
Logic Unit
NIM Crate
Power Supply
PC
Adapter
Negative Signals
Positive Signals

## Slide 14: Batch test of ECal PCBs
Example of waveforms of 16 channels

## Slide 15: Batch test of ECal PCBs
The response of PCBs is related to the temperature slightly
R
01
02
15
R
16
17
30
R
Less than 30 minutes

## Slide 16: Batch test of ECal PCBs
The response of PCBs is related to the temperature slightly
1200 boards, 19200 channels

## Slide 17: Summary
The China Group has established a complete QA & QC system. QA & QC of Material, Tower and Module have reached the requirements.
768 modules have been shipped to JINR.
The cosmic test results show that the light yield of different tower is very consistent.
1200 PCBs have been produced in China and shipped to JINR.
Each PCB has been tested before the shipment.