## Slide 1: Central DCS / Run Control Concept
Sergey SERGEEV
XIII MPD Collaboration meeting
Apr. 23-25, 2024

## Slide 2: Concepts
Modular, used defined interface (DIM + defined message format).
Extendable
Modules could be replaced/modified
As simple as possible (KISS – Keep It Stupidly Simple) and transparent
For MPD experiment only (not generic)
Based on DB to be used by MPD (PostgreSQL ?)

## Slide 3: Experiment DCS structure
FFD DCS
TPC DCS
DAQ
TOF DCS
ECAL DCS
LV
HV
Laser
…………
Cooling
…………
Shift leader
Predefined set of RUN types
RC/CDCS
Server
HW
Client
Client
Client
Client
Diagnostics tools
Command
State
Config DB
Client
Command –> set run type
State – actual subdetector state
Off, StdBy, NotRdy,
Rdy, Wrng, Error,…
Run type DB

## Slide 4: CDCS interface I
RC/CDCS subscribes to published by subdetectors state InfoItems with names
  MPD_DCS_State/<subdetector name>
Run configuration contains subdetectors list used in a run
RC/CDCS sends run type name (text) to all CommandItems of subdetectors being in a list. CommandItems should have a name like
  MPD_DCS_IniCmd /<Subdetector name>

## Slide 5: CDCS interface II
Each subdetector DCS root node could (should?) have a CommandItem with name
  MPD_DCS_DisplayCmd/<subdetector node name>
  A command received by this CommandItem should start diagnostic tool (see below)
DAQ should have additional Info/Command items to provide vital information to/from the RC/CDCS (to be discussed with DAQ team)

## Slide 6: CDCS interface III
RC/CDCS has a CommandItem MPD_DCS_Messages to receive messages from subsystems/subdetectors
Format of message should be like (to be discussed)
  <subdetector name>_<severity level>_<message text>
    <severity level> defines a way to process the message
      0 -> just to show in a window. Could be scrolled by messages arriving later
      1 -> stays at the screen until confirmed
      2 -> stays at the screen until confirmed + sound alarm if not confirmed during defined time (1 min as an example)
      3 -> stays at the screen until confirmed + instant sound alarm
All messages have a text content

## Slide 7: How it could look like

## Slide 8: States and colors
  State=-1, Item does not have a state, no color to be displayed
  State=0, OFF - any of sub-elements does not respond
  State=1, StdBy – any of sub-elements is in stand-by mode
  State=2, NotRdy – any of element is in transition state (Time-out should be implemented)
  State=3, Ready – all elements are OK
  State=4, Wrng – any of elements is in Warning state
  State=5, Error – any of elements is in Error state
  State=6, Ignrd – node in Partitioned state

## Slide 9: Extended display (to be discussed)
  A subdetector should provide a set of diagnostics tools started by a CommandItem
  MPD_DCS_DisplayCmd/<subdetector name>
This should be an application running at the CDCS PC(?) or a web-page running AJAX script (?). The web server could be provided by a CDCS. Page content should be developed by the subdetector team and could be located at a common disk space
Start parameters are defined in the CommandItem command content

## Slide 10: Subdetector DCS (obligatory)
Run type name
Subdetector State
Subdetector
DCS
Server
Server
FSM
…………
DB
Run type name to
HW configs
HW Config name
Actual state
FSM:
If any subsystem in Off -> Off
If any subsystem in StdBy-> StdBy
If any subsystem in Error-> Error
…………………………………………………
If all subsystems in Rdy -> Rdy
Partitioning:
Remove part of a system from the common tree.
Works at level of a subdetector DCS and at level of a server

## Slide 11: Subdetector DCS (optional)
Extra info to CDCS
Subdetector
DCS
Server
Server
…………
Additional DISPLAY commands

## Slide 12: Extra parameters interface
“MPD_DCS_State/DAQ”, content=“3”
“MPD_DCS_State/DAQ/Subsystem1”,
content=“3_value=XXX”
“MPD_DCS_State/DAQ/Subsystem1/Value1”,
content=“3_XXXXX”
“MPD_DCS_State/FFD/Laser_power”,
content=“-1”
“MPD_DCS_State/FFD/Laser_power/”,
content=“-1_80%”
Extra info to display in the tree, defined by subsystem/subdetector
Obligatory
MPD state is built using 1-st level nodes

## Slide 13: Thank you for attention

## Slide 14
Based on TCP/IP sockets
Developed in 80-s at DELPHI experiment
Main feature – converts hardware address space (IP + port) to logical name address space -> components could migrate on computers
Event-driven (real-time)
Could have multiple name domains
Open source
Works on Windows, VMS, several Unix flavors (Linux, Solaris, HP-UX, Darwin, etc.) and the real time OSs: OS9, LynxOs and VxWorks
Libraries for C, C++, Jawa, Delphi (Lazarus), Python
A lot of debugging tools
See https://dim.web.cern.ch/

## Slide 15: How it works
At startup every Server registers its services at DNS (DIM name server)
Any Client could request a connection to a service, after that the client receives actual IP and port number for requested service (performed inside the DIM library)
DIM establishes a TCP/IP connection Server-Client
Further communication is done directly via TCP/IP sockets (Server-Client only)
Pleasant bonus: If a Service contains a “description” then debugging tools could interpret TCP/IP buffer content to display in a human-readable way

## Slide 16: Source code C++
DimService servint("TEST/INTVAL",ival);
DimService new_servint("new_TEST/INTVAL",boolval);
DimServer::start(newDns, "new_TEST");
if(!boolval) boolval=1; else boolval=0;
ival++;
servint.updateService();
new_servint.updateService();
New data ready
Publish New data
Create 2 Info items
…………………………………………………………………………..
…………………………………………………………………………..