## Slide 1
SPD ECAL Status Report February 2024 Oleg Gavrishuk, Laboratory of High Energy Physics, Dubna, Russia
ECAL position inside of Cryostat – Sizes Fixed
ECAL New Sizes corrected in 2024 – is READY
SPD Barrel design:
  TZ for LHEP & DLNP - under preparation
Matrix Form for new scintillator production (40x40x1.5 mm3) - READY
Stamp Form for Lead – proceed an Agreement preparation
Scintillate production: Vladimir, Uniplast: DLNP take participation
  Technical task and Agreement – in preparation
End Cup part via 256 cells planning produce during 2024
  Technical task, Agreement - in preparation
3/13/2024
1
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 2
SPD ECAL 2024
1. Обсуждение реализации ТЗ по конструкции поддержки ЕС – каркаса
Кто и что может моделировать с целью влияния мертвых зон , которые есть в раме (каркасе)
  Учет каркаса Бареля
  Учет каркаса Торца
Какие работы , кто проведет с тестированием модулей, волокон
  Есть 4 модуля – для Торца
  Вставить волокна – 2 модуля с петлями – Японский+Тверь
  2 модуля с напылением торца – Японский + Тверь
Какие работы , кто проведет с тестированием диодов
  Точки пробоя
  Коэфф. Термостабилизации
  Темновой ток
Производство пластин сцинтилляционных
  Контроль производства во Владимире
Изготовление свинцовых пластин - где - пока не ясно, хотя есть договор с фрмой, которая делала пресс-форму. Дороговато просит.
  Поиск альтернативы производства Штампа ло ясвинца
Возможная технология изготовления модулей Торцевой части ЕС
  Склейка модуля из 4-х ячеек в Протвино
Согласно пункту 0) - подумать, кто может сделать доклад по калориметру (кроме меня) в Казахстане https://www.jinr.ru/posts/spd-collaboration-meeting-200524/
Определить, кто поедет в командировку с 19 по 24 Мая 2024 года
3/13/2024
2
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 3
ECAL with New Sizes in 2024
3/13/2024
3
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 4
ECAL barrel Gap sizes along beam
3/13/2024
4
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 5
ECAL composition with New Sizes in 2024
3/13/2024
5
Oleg Gavrishuk, JINR, Dubna , Russia
ENDCUP:
Cells per One = 5136
2 End Cups Cells = 10272
ADC64 – 160
16ch Amplifiers – 642
Power units – 20
Weight – 2x12.8 = 25.6 ton
NOT take in account
The Cells Wall Thickness (4 mm)

## Slide 6
ECAL End Cup Frame New Sizes in 2024
3/13/2024
6
Oleg Gavrishuk, JINR, Dubna , Russia
ENDCUP Frame design
Load – 12.8 ton
Cells for 16 Modules (64 cells)
Cells - Stainless Steel , d=4 mm
Frame from Left & Right part
Frame has Support (green)
Support stay on RS Iron
This picture NOT take in account
The Cells Wall Thickness (4 mm)

## Slide 7
MPD Support for ECAL 2024
3/13/2024
7
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 8
3/13/2024
8
Oleg Gavrishuk, JINR, Dubna , Russia
MPD 2024

## Slide 9
MPD 2024
3/13/2024
9
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 10
ECAL Barrel MPD option, 24 sectors
3/13/2024
10
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 11: TZ Barrel support. Design look like MPD
MPD documents are ready in LHEP
Scaling for sizes factor ~ 1.4
Take in account ECAL SPD Barrel Weight - facrot ~2
  Preferences in Design:
    Documentation exist in LHEP
    Experience exist during manufacturing
    Production was done
  Preferences in Setup:
    Support for all inner detectors:
      RPC planes
      STRAW tubes
      Independent ECAL Sectors assembling

## Slide 12: Matrix form for new scintillator production (40x40x1.5 mm3)
Matrix firm is special setup for molding by pressure technology
It allow produce scintillator from granulated polystyrene with doppands
4 set form produce 4 scintillator plate per 1 minute

## Slide 13: Matrix form for new scintillator production (40x40x1.5 mm3)
Matrix firm is ready and tested in Uniplast, Vladimir in February 2024

## Slide 14
New Cells 40x40 – 200 layers
produced I Vladimir at February 2024
Scintillator plate:
40x40 mm
t=1.5+0.010
Gap – 0.055
---------------
100 plates – L=104 mm
200 plates – L= 416 mm

## Slide 15
New 2 cells modules – 200 layers
produced in Protvino 2023 – MPD technologu
Total=500 mm without Readout Card & ADC
ECAL =460 mm , Absorber=420 mm

## Slide 16
New 2 cells modules – 200 layers
produced in Protvino 2023 – MPD technology
Body=200 Layesr, L=460-20=440 mm

## Slide 17
New 4 modules:
Single mod=80.2
Total 4 = 320.6
Single mod=80.2
4 cells 40x40

## Slide 18
New 4 modules:
Single mod=80.2
Total 4 = 320.6
Single mod=80.2
4 cells 40x40

## Slide 19: End Cup for SPD with new scintillator to be produced in 2024 via 256 cells of 40x40 mm2
This Figure shows in red 64 modules, consisting of 4 cells each (256 cells). The weight of this assembly is 597 kg. This will require 130 kg of polystyrene, 465 kg of lead, as well as additives: 1.95 kg of P-terphenyl and 65 g. POPOP, and 2000 meters WLS fiber type Y-11.
It is 1/20 part of End Cup and
taken time of 36 Days to prepared 51200 Stint. plates.
To read this setup, we need four ADC64 - 64-channel amplitude encoders, as well as 16 boards of 16-channel amplifiers and bias voltage regulators.

## Slide 20: End Cup for SPD in Frame. Cells for 16=4x4 modules Border thick=4 mm Stainless steel

## Slide 21: End Cup for SPD with new scintillator to be produced in 2024 via 256 cells of 40x40 mm2
Проверить влияние мертвых зон - перегородок на End Cup ? на энергетическое разрешение - константный член ? Расстояние от центра - 2010 мм от точки взаимодействия - до начала калориметра Перегородки - стенки коробов сталь 4 мм - образуют короба размером примерно 320х320 - рисунок в отдельном письме Энергии - 50 МэВ - 8 ГэВ Модуль - 4 ячейки - 80.2х80.2 мм (обернутый в 2 слоя бумаге). в короб вставляется 4 модуля - 16 ячеек 9каналов) Короб стальной - 4 мм стенка - нерж. сталь.

## Slide 22: End Cup in frame/ Box 4x4 modules – 64 ch
Высота Короба из 4-х модулей 326 мм
Это – 8 границ , ширина которыз равнв 6/8 = 0.75 mm
Стенка короба – 4 мм , нерж.ст.

## Slide 23: WLS installation – loop type in New modules

## Slide 24
Conclusions
New ECAL geometry - corrected in 2024
Technical task for LHEP – preparation in progress
SiPm EQR 20-60 (20 mk pich) were studied soon
WLS Russian production 200 m has be studied soon
New ECAL setup with cell size 4x4 cm2 assembled – 16 cells (4 modules)
ECAL test in cosmic rays was done with SiPm EQR15
Matrix form for new scintillator production should was ready in February 2924
New scintillator production for End Cup part - start soon: March 2024
Lead plates production – start in 2024 July
256 ECAL cells for End Cup (1/20 part) – should assembled in end of 2024
3/13/2024
Oleg Gavrishuk, JINR, Dubna , Russia
24