## Slide 1: technical part of ALICE subsystems
By Culicov Alexandru

## Slide 2: The tree of ALICE SUBSYSTEMS
ALICE EXPERIMENT
DAQ
DCS
Trigger system
HLT
ECS
Online-offline(O2)
Read-out system
event building
Data storage
Hardware monitoring
Env. monitoring
safety systems
CTP
FIT
LTU
Data filtering
Real-time data processing
Data reduction
Run control
Subsystem control
Interlock systems
Time destribution
Continuos readout
RT data-processing
Offline analysis

## Slide 3: What we want?
ALICE subsystem | What it is? | Our expectations of it
DAQ | Manages the collection of raw data from detectors during experiments. | It should be able to accommodate more than 100PB of data and to support sustained data rates of the order of 100GBps.
DCS | Monitors and controls operational parameters of the detectors, ensuring their safe and efficient operation. | It should be able to read more than 300000 values/s
ECS | Coordinates and manages the overall operation of the experiment, including the integration and control of all subsystems. | An operator should can run a detector in standalone mode with a DCAHI having the mastership of a DCA. He/she should can send commands to the DCA, change the rights granted to the DCA, and send commands directly to objects in the DCS, DAQ, and TRG 'online systems'. Without the mastership of the DCA, the DCAHI should can only get information and cannot issue active commands.
Trigger system | Include systems such as the Central Trigger Processor (CTP) and the Fast Interaction Trigger (FIT), which determine when to record events based on specific criteria. | it must comply with certain data transmission and processing protocols.
HLT | It is a sub-system of ALICE, focussing on online event reconstruction and analysis, event selection and data reduction. | The HLT should process and compress data in real time, handling an input stream of up to 25 GB/s. This requires FPGA and GPU technologies that support scalable parallel processing on a powerful computing cluster.
O2 | A new system designed for real-time data processing (online) and detailed subsequent analysis (offline). | The Alice O2 Event Processing Nodes (EPNs) consists of 250 servers, each with 2 AMD Rome 32 core CPUs, 512 GB RAM, 8 AMD MI50 GPUs with 32GB memory each, as well as an Infiniband HDR network interface. The main purpose and the driving design factors of the cluster are the real-time online reconstruction capabilities during Alice Pb-Pb data taking. The EPNs get up to 635 GB/s of zero suppressed detector data as input

## Slide 4: Deeper requirements:
Category of Requirement | Specific Requirements | Additional Details
Bandwidth | Minimum: 50 GBps Maximum: 100 GBps | 
Reliability | Fault tolerance: 99.999% uptime Recovery time: ≤ 5 minutes | Includes protocols for rapid recovery and error handling
DAQ
Category of Requirement | Specific Requirements | Additional Details
Monitoring Accuracy | Measurement accuracy: ±0.1% | Critical for operational efficiency and safety
Control Interfaces | GUI with remote access and configuration capabilities | Facilitates easy and efficient management
Category of Requirement | Specific Requirements | Additional Details
Modularity | Integrate up to 10 new systems | Without full system reboot
Data Management | Support for XML and JSON | Ensures compatibility and seamless data exchange
DCS
ECS
Category of Requirement | Specific Requirements | Additional Details
Reaction Time | Response time: ≤ 10 microseconds | Critical for event accuracy
Data Sampling | Preserve 95% of events meeting criteria | Ensures high-quality data for analysis
Trigger System
Category of Requirement | Specific Requirements | Additional Details
Processing Performance | Time per event: ≤ 1 ms | Necessary for real-time data processing
Resource Usage | Use no more than 2 GB RAM per process | Maximizes efficiency and resource allocation
HLT
Category of Requirement | Specific Requirements | Additional Details
Scalability | Increase power by 50% when data volume increases by 30% | Adjusts to data volume increase automatically
System Integration | Compatible with Hadoop and Spark-based systems | Ensures smooth integration with data analysis platforms
O2 (Online-Offline)

## Slide 5: REFERENCES:
https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=5446521 https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=10274908
https://accelconf.web.cern.ch/ica05/proceedings/pdf/O1_011.pdf
https://arxiv.org/pdf/2106.08353.pdf
https://inspirehep.net/files/dbd6254b24fc39806bcf2ed31a406f67
https://alice-collaboration.web.cern.ch/node/34985