## Slide 1
Status and Prospects of Radiochemical Research
at the Dzhelepov Laboratory of Nuclear Problems of JINR
AYAGOZ Baimukhanova
PhD, research scientist
DLNP Department of Nuclear Spectroscopy and Radiochemistry
59th Meeting of the PAC for Nuclear Physics
June 13, 2024

## Slide 2
Experience in high-precision nuclear spectroscopy using semiconductors, scintillators and other types of detectors;
experience in studying rare processes in different underground environments;
experience in production of radionuclides and in synthesis of radiopharmaceuticals;
experience in nuclear hyperfine interaction spectroscopy.
Section of Radiochemistry
All the personnel: 17 (avg. age 41 yr)
Scientific personnel: 12 (avg. age 41 yr)
PhD: 7 (58%)
Senior researchers
Research
scientists
Junior researchers
Assistant researchers
Engineers, lab assistants
Azerbaijan 1 Bulgaria 2
Jordan 1
Kazakhstan 2
South Africa 1
Uzbekistan 3
Notes: 2

## Slide 3
Radiochemistry and Spectroscopy in Astrophysics and Nuclear Medicine
Scientific directions

## Slide 4
Producing Preparations and Sources of Radionuclides
Applications
II. Nuclear spectroscopy
and neutrino physics
- Obtaining experimental data
- Manufacturing calibration sources
I. Nuclear medicine
- Synthesis of radiopharmaceuticals
- Studying kinetic properties of complexes with metal ions
- Development of radiolabelling based on chelators with "slow" kinetics
III. Radioactive tracers
- Studying sorption in various solution-sorbent systems
- Studying local environment of nuclei via methods of hyperfine interactions
- Development of isolation and separation methods
High specific activity
Radionuclide purity
Radiochemical purity
Chemical purity

## Slide 5
Producing Preparations and Sources of Radionuclides
Production of radionuclides:
1. At JINR facilities
2. By commercial suppliers
3. In cooperation with INP UZ, INP KZ and others
Theoretical calculation of radionuclide yields upon irradiation of a tantalum target (target thickness is 0.184 mol/cm2) with 660-MeV protons, current is 5 μA (Geant4)

## Slide 6
Producing Preparations and Sources of Radionuclides
Radiochemical methods for isolation and separation of radionuclides
Chromatogram of separation of radiolanthanides
with ammonium α–hydroxyisobutyrarate
Typical metal target

## Slide 7
Producing Preparations and Sources of Radionuclides
Radiochemical methods for isolation and separation of radionuclides
Production of radionuclides at accelerators:
177Lu from Yb target
225Ac from Th target
44Sc from Ca target
86Zr from Y target
90Nb from Mo, Zr targets
111In from Ag, Sb targets
Lanthanides from Ta target
Radionuclides from Th target

## Slide 8
Producing Preparations and Sources of Radionuclides
Radionuclide generators
44Ti → 44Sc
68Ge → 68Ga
72Se → 72As
86Zr → 86Y
90Sr → 90Y
111In → 111mCd
172Hf → 172Lu
229Th → 225Ra → 225Ac, etc.
Reverse-tandem scheme of the generator
(1) – syringe for maintaining pressure/underpressure, (2) – reverse storage vessel, (3) – main column , (4) – vial, (5) – solutions with eluents, (6) – tandem column, (7) – waste vial, (8) – vial with radiopreparation
Classic generator scheme

## Slide 9
Studying Sorption Properties of Metal Ions
Using radioactive tracers
(1) Studying the sorption of several elements in unstudied systems regularly
(2) Developing generator schemes
(3) Isolating microquantities of radionuclides
from macroquantities of the target material
(4) Purifying substances for low-background
experiments
(5) Predicting the behavior of superheavy elements

## Slide 10
Synthesis and Analysis of Radiopharmaceuticals
Structure of a modern radiopharmaceutical
Radiopharmaceuticals based on:
211At with DTPA
68Ga with DOTATOC
44Sc with DOTA/DOTATOC
90Nb with rituximab/bevacizumab
Complex requirements:
thermodynamic stability
kinetic insertion
high kinetic of complexation
radiation resistance
Maximal intensity projection (top) and representative slice (bottom) of PET/CT examination of a 77-year-old patient suffering of mCRPC with high tumor load using (A) [44Sc]Sc-PSMA-617 (50 MBq, 60 min p.i.), and (B) [68Ga]Ga-PSMA-11 (120 MBq, 60 min p.i.). (C) On the right hand side the planar scintigraphy is shown (top) and a representative slice of the post therapy SPECT/CT scan, about 24 h after application of 6700 MBq of [177Lu]Lu-PSMA-617.

## Slide 11
Method of Hyperfine Interactions
Using radioactive tracers
111In, 111mCd, 152Eu, 154Eu
with DOTA, DTPA
DTPA
L2 – PAC parameter
111In (EC)
111mCd (IT)
152Eu (EC)
154Eu (β-)

## Slide 12
Recent Results in Nuclear Physics and Research Proposals Presented by DLNP Young Scientists
Production of Trivalent Radionuclides for Nuclear Medicine and Analysis via Nuclear-Spectrometric Methods
Elena Kurakina
Tellurium-Loaded Organic Scintillators for the Search of Neutrinoless Double Beta Decay
Ivan Suslov

## Slide 13
Internal conversion and Auger electron emission from radioactive decay of nucleus
Obtaining experimental data for evaluation of applications of Auger electrons to nuclear medicine
ESA-50 Spectrometer
Electron Spectroscopy
Using radioactive tracers

## Slide 14
High-Purity Materials
Applications
II. Reagents
- Low-background electronics: solder and fluxes
- Media for synthesis of radiopharmaceuticals
I. Low-background materials
- Production of materials with ultralow impurities
- Reduction of radioactive impurities in detector materials, in measured samples and in structural materials of experimental facilities and laboratories
III. Analysis
- ICP-MS, ICP-AES with chemical preparation
- Neutron activation analysis
- Gamma-ray screening, etc.
High specific activity
Radionuclide purity
Radiochemical purity
Chemical purity

## Slide 15
Samples for measurement
48Ca
82Se
96Zr
106Cd
Solders and fluxes
Archaeological Pb+Sn
NH4Cl, CH3COONH4
Detector, protection and construction materials
Etching methods for copper surface
Surface cleaning protocols
Materials and Methods Developed at DLNP

## Slide 16
 | > 30 keV | > 500 keV
Pb (99.9999%), GOST 22861-77 m = 100,8 g | 3161 ± 70 per day | 857 ± 37 per day
Background | 243 ± 6 per day | 112 ± 5 per day
232Th decay chain |  | 238U decay chain | 
Radionuclide | Activity, mBq/kg | Radionuclide | Activity, mBq/kg
208Tl | < 18 | 214Pb | < 17
208Tl | < 27 | 214Bi | < 13
212Bi | < 144 | 210Pb | < 78
212Pb | < 34 | Radionuclide | Activity, mBq/kg
228Ac | < 79 | 40K | < 94
BeO
Preparing Solder Made of Archaeological Pb and Sn. Part 1

## Slide 17
 | > 30 keV | > 500 keV
Arch. Lead m = 114 g | 243 ± 7 per day | 112 ± 5 per day
Background | 243 ± 6 per day | 112 ± 5 per day
 | > 30 keV | > 500 keV
Tin (99.9999%), GOST 860-75 m = 75,1 g | 269 ± 12 per day | 139 ± 9 per day
Background | 243 ± 6 per day | 112 ± 5 per day
Preparing Solder Made of Archaeological Pb and Sn. Part 2

## Slide 18
The original piece of archaeological lead
slag
The molten lead
I.
Tin with chemical purity 99.9999%
II.
Pb, 60%
Sn, 40%
metal cutting and weighing
melting at Т=400 °С
pouring into a Teflon cup
III.
Preparing Solder Made of Archaeological Pb and Sn. Part 3

## Slide 19
 | > 30 keV | > 500 keV
Solder Sn(60%)Pb(40%) m = 154.5 g | 222 ± 8 per day | 105 ± 6 per day
Background | 243 ± 6 per day | 112 ± 5 per day
Solder (60% Sn and 40% archPb)
Preparing Solder Made of Archaeological Pb and Sn. Part 4

## Slide 20
Samples | Purity, % | 238U |  | 232Th |  | 40K | 
 |  | 10-9 g/g | mBq/kg | 10-9 g/g | mBq/kg | 10-9 g/g | mBq/kg
ZnCl2 | 99.999 | 55 ± 15 | 679 ± 185 | < 200 | < 812 | < 64 | < 2.0
NH4Cl | 99.999 | 60 ± 20 | 741 ± 247 | 330 ± 140 | 1340 ± 568 | < 72 | < 2.2
H3PO4 | 99.998 | 27±12 | 333 ± 148 | < 74 | < 300 | < 66 | < 2.1
C9H8O4 | 99.9 | 160 ± 30 | 1970 ± 370 | 170 ± 90 | 690 ± 365 | < 44 | < 1.4
D.S, Akerib, А. D. Silva, D.L. Herli [et al]. Production of solder and flux with low radioactivity / Nucl Instrum Meth -1997. V. 400, I. 1, P. 181-183
High-Purity Ammonium Salts for Fluxes and Radiolabelling. Part 1

## Slide 21
I. Ammonium chloride
II. Ammonium acetate
NH3 + HCl → NH4Cl
Purification of HCl;
synthesis of ammonium chloride solution (transfer of gas phase ammonia to acid);
obtaining NH4Cl in a solid state by vacuum drying at room temperature.
NH3 + CH3COOH → CH3COONH4
Purification of the 16 M CH3COOH acid;
synthesis of ammonium acetate solution (transfer of gas-phase ammonia to acid);
obtaining CH3COONH4 in a solid state by vacuum drying at room temperature.
Synthesis of High-Purity Ammonium Salts. Part 2

## Slide 22
Samples | 232Th, mBq/kg | 238U, mBq/kg | 40K, mBq/kg
NH4Cl | < 0.1 | < 0.1 | < 0.7
CH3COONH4 | < 0.1 | < 0.1 | < 0.7
Radionuclide | Eγ, keV | Activity, mBq/kg
40K | 1461 | < 77
208Tl | 2614 | < 5
210Pb | 46 | < 91
212Pb | 239 | < 2
214Pb | 242 | < 10
214Pb | 352 | < 5
214Bi | 609 | < 10
214Bi | 1765 | < 5
228Ac | 911 | < 5
Measurement results of the synthesized NH4Cl (low-background HPGe)
Impurities of 232Th, 238U and 40K in the synthesized ammonium salts (ICP-MS, ICP-AES)
Analysis of High-Purity Ammonium Salts. Part 3

## Slide 23: ICP-MS and ICP-AES results of analysis of the commercial NH4Cl (GOST 3773-60) and the synthesized one
NH4Cl – Synthesized
NH4Cl – GOST-3773-60
Elements
Element concentration, g/g
Elements
Element concentration, g/g
ICP-MS and ICP-AES results of the commercial CH3COONH4 (OSCh 5-4) and the synthesized one
CH3COONH4 – Synthesized CH3COONH4 – OSCH 5-4
Analysis of High-Purity Ammonium Salts. Part 4

## Slide 24
I. Dissolving
II. Chromatographic purification
III. Reduction to elemental Se with SO2
VI. Vacuum drying
V. Homogenization of selenium (in alcohol)
IV. Centrifugation
(washing with alcohol, water)
Conditioning
At room
temperature
Se+4HNO3 →H2SeO3+4NO2↑+Н2О
SeO2+Н2О ↔ H2SeO3
IV.
V.
VI.
II.
III.
Method for Purification and Conditioning of Selenium. Part 1

## Slide 25
Reverse chromatography scheme of H2SeO3 purification
1 ÷ 6 – solutions; 7, 9, 11, 13 – triple valves; 8, 12 – pumps;
10 – ion-exchange column
Dowex 50W×8, h=500 mm For m=100 g of selenium → d=10 мм
For m>100 g → d=28 мм.
H2SeO3+2SO2+H2O→Se+2H2SO4
1 - SO2; 2 - reducer; 3 – valve; 4 – rotameter;
5 ÷ 8 vessels (10 L); 9 - magnetic stirrer
Scheme of reduction of selenous acid to elemental state
Method for Purification and Conditioning of Selenium. Part 2

## Slide 26
Samples | Specific activities of radionuclide impurities, µBq/kg |  |  | 
 | 40K | 234mPa | 208Tl | 214Bi
82Se | 58700 ± 100 | 17300 ± 100 | 390 ± 10 | 1500 ± 40
* ICP-MS results. Element content converts from g/g to µBq/kg
< - detection limit
Samples | Specific activities of radionuclide impurities, µBq/kg |  |  | 
 | 40K | 238U (234mPa) | 232Th (208Tl) | 226Ra (214Bi)
Purified 82Se | < 9300* | < 2500* | 22 - 150 (8 - 54) | < 600
Improvement factor of purified 82Se | > 6 | > 7 | 7 - 50 | > 2.5
Method for Purification and Conditioning of Selenium. Part 1

## Slide 27
Methods and Techniques for Production and Analysis of
Low-Background Materials
With a low content of radioactive impurities
Development of sample production methods (82Se; 96Zr;
shielding materials – Pb, Cu, Zn; solder; etc.) with impurity content of μBq/kg
Development of sample analysis methods at an ultralow-sensitivity level using Inductively Coupled Plasma Mass Spectrometry (ICP-MS) and other analytical and nuclear spectroscopic methods

## Slide 28
PLANS
To support physical, chemical and radiopharmaceutical studies of radionuclides: to develop methods for production of preparations and sources of radionuclides.
To put into operation two new basic facilities: the LINAC-200/800 Electron Accelerator and a Spectrometric Cluster functioning in tandem.
To complete the reconstruction of radiochemical laboratories at the DLNP Experimental Department of Nuclear Spectroscopy and Radiochemistry.
To expand radiochemical research through new areas: ICP-MS for determining ultra-low concentrations of substances, primarily radioactive Th, U and K; the emission mode of Mössbauer spectroscopy for studying post-effects of the radioactive decay in solids and autoradiolysis of radiopharmaceuticals (119Sb, 161Tb, 57Co, 119mSn, etc.); the improved PAC method for studying the behavior of radiopharmaceuticals (111In, 152Eu, 154Eu, 172Lu, etc.) and solids with isomers (111mCd, 199mHg, 204mPb) in samples irradiated at the LINAC-200/800.
To produce low-background materials for experiments in neutrino physics and astrophysics, and also to analyse these materials at a level of μBq/kg and below.
To manufacture a wide range of radionuclide generators 32Si→32P, 44Ti→44Sc, 68Ge→68Ga, 90Sr→90Y, 194Hg→194Au, 202Pb→202Tl, 227Ac→227Th→223Ra, 229Th→225Ra→225Ac, 237Np→233Pa, 238U→234Th, etc. (up to 40-50)

## Slide 29
Thank you for attention!