## Slide 1
STAR detector upgrade: inner TPC & at forward rapidity
Qian Yang ( 杨 钱 )
Shandong University
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10

## Slide 2
RHIC-STAR experiment
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10

## Slide 3
Physics Programs at RHIC
Beam Energy Scan Phase II program:
RHIC run 2019-2021
QCD phase diagram
Such as CEP, Chiral phase transition …
Cold and hot QCD plans:
RHIC run 2022-2025
Properties of QCD matter
Such as precise imaging of gluons and sea quarks inside protons …
Inner TPC
Forward Tracking System
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10

## Slide 4
The inner TPC upgrade
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
Inner Sectors
        New designed strongback
        New wire frames
-- Replace ageing wires,
MWPC building in Shandong University
        Increases readout pad rows (13 to 40)
-- 20% coverage -> ~100% coverage
New electronics for inner sectors
-- Double # of readout channels per FEE,
use ALICE SAMPA chip
New designed insertion tools
-- Install and replace sectors, STAR operations

## Slide 5
WMPC prototype production at SDU
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
Wire winding
Wire mounting system
Wire tension meas.
Epoxy
Wire tension meas.
Soldering

## Slide 6
Wire pitch and tension for MWPC
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
KPP ：Anode wire tension
Wire tension meas. system
Wire tension control system

## Slide 7
MWPC bench test at SDU
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
MWPC testing system
Gas gain uniformity
Energy resolution uniformity
Amplifier + MCA

## Slide 8
MWPC bench test at BNL
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
Connectivity check
HV tests (N2 and P10 gas)
Material canary check
Radiation source test (55Fe and Sr source)
Connectivity before installation
Documented in traveller

## Slide 9
iTPC operation at STAR
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
iTPC performance in isobar data collisions at 2018
Maximum hits per tracks: 45 → 72
Lower transverse momentum threshold of 60 MeV/c
coverage extended by 0.4 units

## Slide 10
STAR Forward Upgrade
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024

## Slide 11
STAR Forward Upgrade
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024
Real event display

## Slide 12
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
STAR Forward Upgrade: Overview
Installed at STAR successfully in 2021, and started taking data from 2022 (Run 22)
Locate at STAR west side, 2.5 < < 4
Similar coverage as the EIC detector’s hadron endcap
Forward Tracking System:
Forward Silicon Tracker (FST)
Forward small-strip Thin Gap Chamber Tracker (FTT)
Charge separation
~ 20-30% for 0.2 < pT < 2 GeV/c
Forward Calorimeter System:
Forward Electromagnetic Calorimeter (ECal)
Forward Hadronic Calorimeter (HCal)
Good e/h separation
Photon, identification
ECal: for pp and pA, for AA
HCal: for pp and pA

## Slide 13
Forward Tracking System
Forward Silicon Tracker:
  3 disks, at 152, 165, and 179 cm from IP
  Locate inside STAR TPC cone
Forward small-strip Thin Gap Chamber Tracker:
  4 disks, at 307, 325, 343 and 361 cm from IP
  Locate inside STAR magnet pole tip opening
FTT
FST
2.5 < < 4
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10

## Slide 14
Forward Silicon Tracker
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024
Outer silicon sensor
3 Silicon disks:
  152, 165, and 179 cm from IP
  Locate inside STAR TPC cone
  12 modules per disk
  Si from Hamamatsu
Granularity:
  fine in and coarse in R
Front-end chips:
  APV25
Material budget:
  ~1% per disk
Reuse:
  IST DAQ system & IST cooling system

## Slide 15
Forward Silicon Tracker – Prototype Module Performance
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024
T-Board production at SDU
Pre-Installation at BNL
Performance of two fully asembled prototype modules evaluated with cosmis ray
All channels can be read out (KPP:>85%)
Efficiency higher than 90% (KPP:>90%)

## Slide 16
Forward sTGC Tracker
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024
4 sTGC disks:
  307, 325, 343 and 361 cm from IP
  4 pentagon module per disk
  sTGC technique developed by ATLAS
Working gas:
  45% n-pentane + 55% CO2
Position resolution:
  < 200 um
Material budget:
  ~0.5% per layer
Readout:
  VMM chips

## Slide 17
Forward sTGC Tracker
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024
sTGC module since 2018:
  Three versions of module protoypes
Integrations & DQA: BNL
Commissioning & software: BNL, SDU
Detector | Produced | Shipped | Installed
1st prototype | Oct. 2018 | Jan. 2019 | Jun. 2019
2nd prototype | Jan. 2019 | Jul. 2020 | May. 2019
3rd prototype | Oct. 2020 | Jun. 2021 | Sep. 2021

## Slide 18
Forward sTGC Tracker – Prototype Module Performance
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024

## Slide 19
Operation
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024
FST :
HV:
  140V for inner module
  160V for outer module
Hit map:
  Match expectations given known missing APVs and lower bias voltages on a few of the sensors
FTT :
HV:
  2900V for data taking
Hit multiplicity:
  Consisting of predominately minimum bias triggered events

## Slide 20
Charge track multiplicity & Match to FCS
2024/09/10
Qian Yang @ , Sep. 10td - Sep. 13th 2024
Match to FCS:
  Matched(narrow peak) + Random background(wide peak)
  Good alignment between FTS and FCS
  More analysis is ongoing
Charged track multiplicity:
  Reasonable result

## Slide 21
Summary
Qian Yang @ , Sep. 10td - Sep. 13th 2024
2024/09/10
STAR detector has a new inner core
“High-quality, fully tested MWPC modules that met or exceeded the required performance specifications"
Forward detector data taking since 2022