## Slide 1: Status and plans of R&D for Si-detectors on BM@N N. Zamyatin on behalf of Forward Silicon Detector team
13th Collaboration Meeting of BM@N experiment, 8-10 October 2024

## Slide 2: R&D for Si-detectors on BM@N
1. Design of new Si-station #5 for FSD:
two planes with 11pcs of Si-modules;
active area of Si-modules (186×63)mm2;
Number of FEE-channels (strips) of station - 128×10×22=28 160 ch;
Contract # 100-03046 (26.07.2024), ZNTC-JINR for production 50 pcs of DSSD and 60 pcs of PA-640.
2. Design of ASIC-128 ch chip (ASi-BM@N) for FEE station#5 FSD:
- design and simulation of chip (2022-2023 years);
- GDS files for production experimental chips;
- Contract # 100-03185 (06.08.2024), INP BSU (Minsk) - JINR for production 3 wafers/2000 chips – in 2024-2025 years;
3. Design of new beam profilometer for heavy ions Xe(10.8 pC/175 µm-Si), Au (20.9 pC/175 µm-Si), Bi) with high dynamic range of ∆E-signals (240÷500 MeV/175 µm-Si).
4. Experimental measurements of neutrons equivalent fluence (1 MeV) in FSD region (on outer surface beam-pipe and in region FEE-chips)

## Slide 3: 1. Position of the new FSD-station #5 on the BM@N
Текущее положение
станций GEM
Смещенное положение
станций GEM (Z+93 мм)

## Slide 4: X-Z cross section of central tracker
Current position of GEM stations
Position of GEMs after shift (Z+93 мм)
X
Z

## Slide 5
Three type of Si-modules for Forward Si detector
63
93
FEE board
63
93
186
FEE board
63
63
126
FEE board
Detectors size: 63x63x0,3 mm3 (on 4” – FZ-Si-n wafers)
Topology: double sided microstrip (DSSD)
(DC coupling)
Pitch p+ strips: 95 μm;
Pitch n+ strips 103 μm;
Stereo angle between p+/n+ strips: 2.50
Number of strips/DSSD: 640 (p+)×614(n+)
Number of strips/module: 640 (p+)×640(n+)
Detectors size: 63x93x0,3 mm3 (on 6” – FZ-Si-n wafers)
Topology: double sided microstrip (DSSD)
(DC coupling)
Pitch p+ strips: 95 μm;
Pitch n+ strips 107,1 μm;
Stereo angle between p+/n+ strips: 2.50
Number of strips/DSSD: 640 (p+)×603(n+)
Number of strips/module: 640 (p+)×640(n+)
Station 2,3,4
DSSD 63x63mm2
42 modules
Station1
DSSD 63x93mm2
6 modules
New Station 5*
DSSD 63x93mm2
22 modules

## Slide 6: 2. Main parameters and block scheme of ASIC-128 ch/ASi-BM@N
Параметры детектора | 
Тип детектора | Кремниевый, стриповый, двухсторонний
Толщина кремниевого детектора | (200÷500) мкм
Сигнал детектора, m.i.p. | 4 фКл/300 мкм
Напряжение смещения, В | До 100 В
Емкость стрипа, пФ | 20÷100
Параметры ИС | 
Технология | CMOS, 180нм
Количество каналов | 128
Напряжение питания, В | 1.8 (однополярное)
Ток потребления аналоговых блоков, мА | 115
Ток потребления цифровых блоков, мА | 12
Рассеиваемая мощность, мВт | 229
Структура канала | ЗЧУ+Формирователь+СВХ+Мультиплексор
Защита по входам | Контактные площадки с защитными диодами
Компенсация токов утечки | До 5 нА, автоматическая, отключаемая
Тестирование | Нечетных и четных через встроенные конденсаторы ёмкостью 0.05 пФ
Тестовый канал | Контроль формы и амплитуды выходного
Время формирования, нс | 300 и 200
Порядок формирователя | 4
Линейный диапазон входных зарядов, фК | +/-30
Коэффициент преобразования аналогового выхода, мкА/фКл | 20
ENC (r.m.s.), е | 215е+11.6 е/пФ
Мультиплексор | 128:1
Частота чтения данных, МГц | 20
Выход мультиплексора | Токовый, дифференциальный
Цифровые сигналы управления | LVDS

## Slide 7: Beam profilometer is necessary for beam tuning in self trigger mode (alignment of the center beam with the center of the target)
detector: DSSD, (128p+×128n+), strips pitch = 475 μm, thickness (Si) -175 μm, active area (61 × 61) mm2. Strips are combined in pairs on detector board. Total have (64p+×64n+), pitch = 950 μm
mechanical design: the plane of the profilometer is automatically removed from the beam zone to the parking position
FEE based on two VA32HDR11 ASICs. Total number of channels are 64 for X and 64 for Y coordinate. Dynamic range of signals: -35pC ÷ +25pC. Charge of ionization for heavy ions Xe(10.8 pC/175 μm-Si), Au (20.9 pC/175 μm-Si), Bi) corresponded of ∆E-signals (240÷500 MeV/175 μm-Si).
Peaking time 800 ns.
Self trigger mode based on TA32cg2 ASICs
current status:
FEE have been designed, manufactured, work in progress to electronics tests.
Next step is testing FEE with Si detector placed in
flanges with alpha-source (5.5 MeV) and
standalone DAQ subsystem.
3. New beam profilometer for heavy ions (Xe, Au, Bi) with Si-detector (64×64) strips
working position
New readout electronics for beam profilometer
Beam profilometer inside beam vacuum station
Beam profilometer
standalone DAQ

## Slide 8
5mm
5mm
Position of rad_Si-monitors
target
FSD
GEM
Si- pin-detector (rad_monitor) :
- Detectors size: (5×5×0,3) mm3
- Detectors thickness: 300 μm
- Active area: 13 mm2
ΔI=αI×V×Ф
ΔI = Iф − I0, (A):
Iф – dark current after irradiation;
I0 - dark current before irradiation;
αI = (5±0,5)·10−17 (A×cm-1) – radiation damage constant-Si (for neutrons 1MeV at +20°);
V, (cm³) – volume of SCR (spice charge region at Ufd);
Ф, (cm-2) – eq. neutron fluence (1 MeV)
Z
Y
FEE
FEE-chips -VATAG-7
Si-det.
4. Radiation Si-monitors on FSD region for equivalent neutron fluence measurement
DSSD
#1
DSSD
#6
DSSD
#3
DSSD
#2
DSSD
#4
DSSD
#5

## Slide 9: Приложение-1: (девять следующих слайдов)

## Slide 10: FSD: after replacing
Cosmic tests station 1
93643 hit entries
111664 hit entries
Cosmic tests station 2
201548 hit entries
198035 hit entries
All dead zones have been eliminated!
124789 hit entries
138624 hit entries
Cosmic tests station 4
165513 hit entries
319725 hit entries
Cosmic tests station 3
E.V. Martovitsky; D.D. Chemezov
Beam hole

## Slide 11: FSD: before replacing (Run 8305, 30.01.2023)
Summary:
10 dead zones, 3 were discovered before the run and 7 occurred during the run
#14
#9
#19
#17
#12
#5-21
#39
#23
Hits on station 1
6 modules, DSSD 63×93 mm2
Hits on station 2
10 modules, DSSD 63×63 mm2
Hits on station 4
18 modules, DSSD 63×63 mm2
#41
Hits on station 3
14 modules, DSSD 63×63 mm2
#13
Module | Chip
#41 | 5Y
#14 | 5X
#9 | 5X
#39 | 1X
#19 | 5X
#13 | 4X, 5X
#17 | 4X, 5X
#12 | 4X, 5X
#5-21 | 5X
#23 | 4Y
Run | 8305
Beam | Xe
Energy | 3.8 Gev/n
Target | Csl (2%)
D.D. Chemezov

## Slide 12: FEE board replacing
Before replacement
After replacement
To eliminate the dead zones it was necessary to assemble a new FEE board completely, 5 ASICs were spent to eliminate each of defects. The old boards were disconnected from the modules and replaced with a new ones. Total: 9 new black boards (p+ strips) were built, 45 VATAGP 7.2 ASICs were used (30 spare ASICs available).
Bad zone Chip #5
Mod #17
Mod #17
Yu.A. Kopylov; O.G. Tarasov

## Slide 13: Y-Z cross section of central tracker
Current position of GEM stations
Position of GEMs after shift (Z+93 мм)
Y
Z

## Slide 14: Position of double-coordinate Si-detectors relative to the axis of the ion guide
# | X | Y | Z*
#1 | 0.0 | 0.9 | 94.7
#2 | 2.7 | -0.3 | 96.9
#3 (Al) | 0.4 | 0.1 | 94.9
Beam tracker detector center coordinates relative to the ion guide axis (mm)
Beam directions
P+ side of the detector
*Distance between the flange surface and the detector surface.
Detector rotation in the coordinate plane no more than 0.50
Ch #128 (P+)
Ch #1 (P+)
Beam
Ch #1 (n+)
# | X | Y | Z*
#1 (electric) | -1.3±0.1 | 0.7±0.1 | 99.7
#2 (pneumatic) | -2.7±0.5 | 1.4±0.2 | 100.7
Beam profilometer detector center coordinates relative to the ion guide axis (mm)
Strip pitch in the detector: 0.45 mm
Number of strips: 128x128
Thickness: 175 µm
Size: 63 x 63 mm2
Strip pitch in the detector: 1.87 мм
Number of strips : 32х32
Thickness: 175 µm
Size: 60 x 60 mm2
Х
Y
Х
Y
Сh #128 (n+)
Z*

## Slide 15: New beam profilometer (64×64) strips for heavy ions (Xe, Au, Bi) На рис. результаты тестов-2022 с альфа источником Si – профилометра: - такую же картину мы хотели получить при работе с пучком, но не удалось из-за наложений при «медленной» электронике ( ИС-VA163); - оба профилометра были убраны в положение «парковка» и не использовались в сеансе; - наши планы и действия – ведется новая разработка (С.Хабаров+О.Тарасов) конструкции плоскости детектора (128х128) стрипов превращаем в (64х64) стрипа + новая FEE на основе ИС HDR64/VA, чипы есть в наличии, детекторные платы разработаны, изготовлены и готовы к сборке детекторов, FEE-PCB в разработке (С.Хабаров), детекторы есть и тестируются (Е.Стрелецкая+Ю.Копылов), готовность – осень_23.
detector: DSSD, (32p+×32n+), strips pitch = 1.8 mm, thickness (Si) -175 μm, active area (60 × 60) mm2;
mechanical design: the plane of the profilometer is automatically removed from the beam zone to the parking position;
FEE: for light (6C ÷ 18Ar) ions based on VA163 + TA32cg2 (32 ch, dynamic range (DR): -750fC ÷ +750fC) desing in progress;
current status:
- two vacuum stations with flanges and cable connectors are ready, Silicon Detectors assembled on PCBs and tested with alpha-source (5.5 MeV), autonomus (ADC+DAQ) subsystem ready;
- for heavy (Kr ÷ Au) ions will be developed another version of the FEE with DR = ± 20 pC.
working position
parking position

## Slide 16
Токи детекторов BT(1÷3) в начале сеанса и по окончании сеанса:
«подложка» это темновой ток, создаваемый радиационными дефектами ионов Хе;
быстрая импульсная компонента это ток ионизации в течение спилов.
Начало сеанса- 06.12.2022
02.02.2023

## Slide 17
Рис.5. Схема измерений (а) темнового тока двухстороннего стрипового Si-детектора и ВАХ (б) до и после сеанса.
Формула определения эквивалентного 1МэВ флюенса нейтронов по повреждениям кремния
где: αI – токовая константа повреждений кремния равняется 5×10-17 А/см, при +20˚С для нейтронов с энергией 1 МэВ и физически означает приращение тока в кремниевом детекторе объемом 1см3 от прохождения одного нейтрона (1 МэВ),
Ф,см-2 – флюенс нейтронов, V, см3 – объем детектора.
(а)
(б)

## Slide 18
 | Эквивалентный флюенс нейтронов 1 МэВ, см-2 (измерен по радиационным повреждениям Si) | Флюенс 128Xe, см-2 расчет через NIEL, К(128Xe/нейтрон 1МэВ)=276 | Число ядер 128Xe, прошедших за сеанс через Si-детекторы BT(1÷3), Sa=37 см2
BT1 | 5.117e+12 | 1.854e+10 | 6.899e+11
BT2 | 4.945e+12 | 1.792e+10 | 6.667e+11
BT3 | 5.300e+12 | 1.920e+10 | 7.145e+11
Среднее | 5.117e+12 | 1.854e+10 | 6.899e+11
 | Id0, мкА/+20 В/+22.5°C (04.12.2022 начало сеанса) | Id(ф), мкА/+20 В/+26.8°C (2.02.2023 окончание сеанса) | ΔI = Id(ф) – Id0= αI ∙Ф∙V, мкА (приведённое к +20 °C)
BT1 | 0.965 | 12.7 | 4.76
BT2 | 0.692 | 12.5 | 4.6
BT3 | 0.626 | 12.9 | 4.93