## Slide 1: Magnetic field measurement of MPD detector magnet
E. Antokhin, BINP, Novosibirsk.
14-16 October, 2024
Dubna, Russia.
XIV Collaboration Meeting of the MPD Experiment at the NICA Facility

## Slide 2: Magnet MPD
Magnetic field: 0.2 - 0.56 Т
Superconducting coil: (current 1800 А)
Two trim coil: (current 2800 А).
Good field region 1:
Z=±2.6 м, R=2.2 м.
Good field region 2: (ТРС):
Z=±1.7 м, R=1.2 м.
Field uniformity: ± 2×10-4.

## Slide 3: Specification for mapping system
.
Using one 3D Hall sensor (HE444).
Covering all area inside TPC region.
Accuracy 0.3 Gauss.
Measuring positions in X, Y, Z with laser tracker.
Measuring inclination angle of carriage respect to solenoid axis with laser tracker.
Measuring time 1 sec for one point.
Possibility to reconstruct the field inside internal volume of cylinder from data measured at cylindrical surface.

## Slide 4: Magnetic field uniformity
Chart: 

## Slide 5: Magnetic field uniformity change due to SC central coil shift 5 mm
Chart: Difference Bz with and without coil shift
Acceptable shift of coil section is 5 mm

## Slide 6: Free holes of the magnetic yoke at the time of magnetic field measurement

## Slide 7: Very precise vertical flange
Accuracy of manufacturing and assembly of the magnetic yoke about 0.2 mm.
We must take advantage of this!

## Slide 8: Our proposal for MPD magnet
.

## Slide 9: Our proposal for MPD magnet. Measurement procedure.
.
The field map will be built in a Cartesian system, while the measurement results are issued in cylindrical coordinate system.
The direction of the Z axis of the local system obviously coincides with the Z axis of the laboratory system.
The control code uses a procedure that first moves through all the values ​​of the azimuth angle at the same position in Z at the minimum radius, then rotates back 360°, then steps along the radius, with rotation in azimuth at each radius, and reaching the maximum radius.
It is necessary to determine the coordinates of the 3D Hall sensor at each measurement point. To do this, one need to use a laser tracker with a set of reflectors and mirrors.
It is necessary to measure the inclination of the rod with the measuring block of the Hall sensor as a function of the length of the solenoid Z in advance and make correction table. The output file shall be as: N X Y Z Bx By Bz

## Slide 10: Our proposal for MPD magnet. Mapper specification.
.
Parameter | Value
Length of movement for Z | 9 m (2 × 4.5 m)
Length of movement for R | 0.1 – 2.2 m
Rotation of measurement block | 360 deg.
Accuracy of movement for Z | 50 microns
Accuracy of movement for R | 50 microns
Accuracy of rotation | 0.2 deg.
Hall 3D sensor | НЕ444, HE Hoeben Electronix,
Hall 3D sensor accuracy | 0.1 Gs
Hall 3D sensor accuracy total (with accuracy of laser tracker and temperature correction) | 0.3 Gs
Sag of guide line | 4 mm
Weight of mapper | 60 kg
Reading time per one measurement | 1 sec

## Slide 11
9 m
Bearing
□150
Through hole
Bearing
Cross section of guide line
4
Carbon plastic guide line
40 kg.
Carbon plastic carriage
20 kg.
2,1 m
The weight of the carriage is symmetrical about the axis of the guide
Young's modulus for carbon plastic 180 Gpa
The servo drive will be a belt drive. On the servo shaft and on the guide. there will be toothed pulleys.
The carriage is in the furthest position from the servo for calculation of torque
Servo transmission
We have to refuse from carbon plastic and change to Al guide line.

## Slide 12: Mapper design with 9 m carbon plastic guide line had been changed to two 4.5 m Aluminum guide lines.
.

## Slide 13: Design of moved parts with Hall sensor are some changed for using Al and polyamide materials
.
Polyamide
Aluminum

## Slide 14: Status of project
The 3D STEP model and 2D drawings done for carbon plastic design. But had redesigned for Al and polyamide.
Servomotors, driving belts, pulleys had got and tested.
Preparation of test facility for simulating the attachment of the mapper to the MPD magnet and testing the mapper on the Earth's field (at the BINP side).
Control software had developed and under testing.
Control unit electronic blocks had been purchased.
Mechanical parts are in process of manufacturing, the main are fiberglass radial guide line, aluminum moved box and polyamide central bearing.

## Slide 15: Status of project. Examples of measuring block

## Slide 16: Status of project Examples
Servomotor with reducer
Device for winding up wire

## Slide 17: Status of project. Example of control software testing

## Slide 18: Status of project. Radial guide line
High flatness
Sag is less than 3 mm with Hall sensor carriage loading
Time of calm after excitation of oscillations is 0.8 sec.

## Slide 19: Status of project. Assembly issues
Bearing is under
manufacturing
at side company
Base is under manufacturing
at side company
Fiberglass guide line is under
manufacturing
at side company together
with BINP

## Slide 20: Time schedule
Time, month | October | November | December
Aluminum guide line, carriage. and polyamide box |  |  | 
Control code testing |  |  | 
Servomotors and related parts (belts, bearings) | done |  | 
Mechanical parts (bearings and soon) |  |  | 
Assembling of mapper on testing facility at BINP. |  |  | 
Test with Earth field at BINP |  |  | 
Assembling of mapper at JINR |  |  | 
Measurements and correction of magnetic field in JINR. |  |  | 
Works

## Slide 21: Time schedule
Time, weeks Works | 1 (works from 07.10.24) | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Fiberglass guide line |  |  |  |  |  |  |  |  |  |  |  | 
Control software (testing) |  |  |  |  |  |  |  |  |  |  |  | 
Control unit bloks purchasing (nanovoltmeter, commutator) | done |  |  |  |  |  |  |  |  |  |  | 
Hall sensor calibration |  |  |  |  |  |  |  |  |  |  |  | 
Servomotors and their accessories | done |  |  |  |  |  |  |  |  |  |  | 
Mechanics– platform for Hall sensor and fastener parts |  |  |  |  |  |  |  |  |  |  |  | 
Mechanics – aluminum box |  |  |  |  |  |  |  |  |  |  |  | 
Mechanics – central bearing |  |  |  |  |  |  |  |  |  |  |  | 
Mechanics – measurement cub for Hall sensor | ready |  |  |  |  |  |  |  |  |  |  | 
Test of mapper in BINP |  |  |  |  |  |  |  |  |  |  |  | 
Shipmnet to JINR |  |  |  |  |  |  |  |  |  |  |  | 
Assembly of mapper in JINR |  |  |  |  |  |  |  |  |  |  |  | 
Magnetic fired measurement and adjustment |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 22: Thank you for attention