## Slide 1: Status of the gas-filled separator SHANS2
Zaiguo Gan
Institute of Modern Physics, Chinese Academy of Sciences
Lanzhou, China

## Slide 2: Outline
Recent plans
Cold fusion reactions at SHANS2
New isotopes at SHANS2
Gas-filled recoil separators at IMP

## Slide 3: HIRFL +SHANS
RIBLL
Linac
SHANS
Mode: ECR/SECR + SFC
Ions: Ar, Ca, Ne, Mg, Ni, Kr, …
Energy: ~ 5 MeV/u
Typical Intensity: ~500 pnA (36,40Ar)
200~500 pnA (40Ca)
Heavy Ion Research Facility in Lanzhou (HIRFL), China
Spectrometer for Heavy Atoms and Nuclear Structure (SHANS)

## Slide 4: CAFE2+SHANS2
LEBT
RFQ
MEBT
ECR
CW - linac
SHANS2
HEBT
China Accelerator Facility for Superheavy Elements (CAFE2)
中国超重元素研究加速器装置
Designed parameters | Goal
Ions | Ca～Fe
A/Q | 3
Beam energy | 4.5-7 MeV/u
Beam current | 3～5 puA
Running mode | CW

## Slide 5: New gas-filled separator SHANS2
SHANS2

## Slide 6: New gas-filled separator SHANS2
Separator | DGFRS | DGFRS-II | GARIS | GARIS-II | RITU | BGS | TASCA | SHANS | SHANS2
Location | FLNR Dubna Russia | FLNR Dubna Russia | RIKEN Wako Japan | RIKEN Wako Japan | JYFL Jyväskylä Finland | LBNL Berkeley USA | GSI Darmstadt Germany | IMP Lanzhou China | IMP Lanzhou China
Configuration | DQhQv | QvDQhQvD | DQhQvD | QvDQhQvD | QvDQhQv | QvDhD | DQhQv | QvDQvQh | QvDQhQvD
Deflection angle | 23º | 30º+10º | 45º+10º | 30º+7º | 25º | 25°+45º | 30º | 52º | 30º+10º
Bρ (max/T∙m) | 3.1 | 3.2 | 2.04 | 2.46 | 2.2 | 2.5 | 2.4 | 2.88 | 2.5
Length (m) | 4 | 7.1 | 5.76 | 5.06 | 4.8 | 4.6 | 3.5 | 6.5 | 5.85
Dispersion (mm/% Bρ) | 7.5 |  | 9.7 | 19.3 | 10 | 20 | 9 | 7.3 | (22)

## Slide 7: Detection system
 | DSSD (BB17) | SSD (W4) | VETO (MSX25)
Sensitive area | 128×48 mm2 | 65×120 mm2 | 50×50 mm2
Junction side | 48 strips | 8 strips | No strips
Ohmic side | 128 strips | No strips | No strips
Strip width | 1 mm | 15 mm | 
Thickness | 300±20 μm | 500±10 μm | 300 μm
Thickness of dead layer | 100 nm | 100 nm | 100 nm
Depletion bias voltage | 40 V | 30 V | 30 V
Energy resolution (FWHM) | 20~30 keV | ~50 keV | 
Sensitive area | 180×80 mm2
Working gas | Isobutane
Pressure | ~300 Pa
Wire material | Tungsten plated with gold
Diameter of wires | Cathode：20μm Anode：15μm
Distance between wires | Cathode：1 mm Anode：2 mm
Voltage of anode | +500 V
Voltage of cathode | -150 V
Multi-Wire Proportional Counter（MWPC）

## Slide 8: DAQ with digital electronics
Charge sensitive preamplifier directly connected to the digitizer
Provides pulse height, time stamp (10 ns) and waveform
Suited for high resolution spectroscopy (HPGe and Silicon detectors)
Dead time free => beneficial for short-lived isotopes
CAEN S.p.A : http://www.caen.it/csite
Data acquisition system

## Slide 9: Monitor system

## Slide 10: Differential pumping & Rotating target
Differential pumping:
Helium gas filled in separator (P<300 Pa)
High vacuum pressure before differential pumping (P<5×10-6 Pa)
Rotating target:
Target wheel with a diameter of 50 cm for 20 segments
175Lu and 169Tm targets have been used under beams with the intensity up to 3 pμA

## Slide 11: Outline
Recent plans
Cold fusion reactions at SHANS2
New isotopes at SHANS2
Gas-filled recoil separators at IMP

## Slide 12: 209Bi(40Ar, 2n)247Md
 | 1 | 2 | 3 | 4
energy(keV) | 8130~8350 | 8350~8550 | 8550~8700 | 8700~8800
T1/2(s) |  | 1.3(1) |  | 
Nuclide | 247gMd | 247gMd | 247g,mMd | 247mMd
 | 1 | 2 | 3 | 4
energy(keV) | 8130~8350 | 8350~8550 | 8550~8700 | 8700~8800
T1/2(s) |  | 1.3(1) |  | 
Nuclide | 247gMd | 247gMd | 247g,mMd | 247mMd
Bρ(T·m) | Beam (eμA) | time(h) | Time(h)
2.064 | 4.6 | 1.9 | 1.5
1.958 | 6.2 | 0.6 | 0.5
2.000 | 5.9 | 7.8 | 6.0
1.980 | 11.3 | 20.9 | 16.1

## Slide 13: 208Pb(48Ca, 2n)254No
E=219.1MeV, Bρ=1.99Tm

## Slide 14: Simulation and measurement on detection efficiency
209Bi(40Ar, 2n)247Md
208Pb(48Ca, 2n)254No
54% + 33.2% = 87.2%
54% + 31.6% = 85.6%

## Slide 15: Outline
Recent plans
Cold fusion reactions at SHANS2
New isotopes at SHANS2
Gas-filled recoil separators at IMP

## Slide 16: New isotopes 204,205Ac
40Ca +169Tm (Elab=198 MeV)
205
Ac
ER
201
Fr
193
Bi
197
At
1
2
3
7.935 MeV
29.1 ms
7.406 MeV
85.0 ms
6.997 MeV
2.08 s
Phys. Rev. C 89, 014308 (2014)
40Ca +169Tm (Elab=200-214 MeV)
SHANS
SHANS2

## Slide 17: New isotope 203Ac
169Tm(40Ca,6n)203Ac, 225 MeV, Ibeam: ~1.5 pmA, max:3.0 pmA, 217 h, 7.3E18
  The Cross Section: pb
PLB, 850,138503 (2024)
The Sp for 203Ac: -1214 keV.
No evidence for proton decay.

## Slide 18: New isotopes of Np
40Ar+185Re→225Np* @ 200 MeV
Z. Y. Zhang, et al., PRL 122, 192503 (2019).
H. B. Yang, et al., PLB 777, 212 (2018).
L. Ma, et al., PRL 125, 032502 (2020).
M. D. Sun, et al., PLB 771, 303 (2017).
T. H. Huang, et al., PRC 98, 044302 (2018).

## Slide 19: New isotopes of Np
N=126 shell
Z. Y. Zhang, et al., Phys. Rev. Lett. 122, 192503 (2019).
Proton drip line for Np

## Slide 20: New isotope 210Pa
20
175Lu(40Ca, 5n)210Pa ,Elab=212 MeV
α-decay properties of 210Pa and its descendants
Submitted to Nature Communications

## Slide 21: Search for 209Pa
21
Searching for new isotope 209Pa at Elab=228 MeV
No candidates are observed
Measured excitation functions of xn and pxn channels

## Slide 22: Experiments in 2023
54Cr+159Tb→213Ac*
54Cr+165Ho→219Pa*
54Cr+169Tm→223Np*
54Cr+175Lu→229Am*
54Cr+181Ta→235Bk*
54Cr+209Bi→263Bh*
54Cr+197Au→251Lr*
48Ca+243Am→291Mc*
2023.2
40Ar+197Au→237Bk*
40Ar+209Bi→249Md*
2023.4-5
Equilibrium charge state
magnetic rigidity
Cross section
40Ar+232Th→272Hs*
2023.5
54Cr+159Tb→213Ac*
54Cr+165Ho→219Pa*
2023.3
54Cr+232Th→276Fl*
54Cr+238U→292Lv*

## Slide 23: Re-investigation on 288Mc
Experiment：Nov,16,2023-Nov,25,2023
Experiment facility：SHANS2
Reaction channel： 243Am(48Ca,3n) 288Mc
Beam particle：48Ca14+
Beam time：103.7 h
Average beam intensity：~6.8 eA
Beam energy：E = 241 MeV (middle of the target)
243Am Target： Ti foil + AmO2
Target number： 4 arc-shaped targets
Duty ratio： 78%.
Rotating speed：~2900 RPM

## Slide 24: Re-investigation on 288Mc
Five -decay chains, assigned to the decay of 288Mc, were detected.
The measured -decay properties of 288Mc as well as its descendent nuclei are consistent with known data.

## Slide 25: Re-investigation on 288Mc
During the beam-stopped period, the decay of 268Db with an energy of 7.813(23) MeV and a lifetime of 41.2 h were unambiguously identified, which match well with the recent work.

## Slide 26: Re-investigation on 288Mc
Chain No. | Etotal (MeV) | LifeTitme (h) | StripX | StripY | Pran
1 | 7.888(45)ac | 47.2 | 66 | 41 | 0,21
1 | 7.759(23)a | 61.5 | 66 | 41 | 0.34
2 | 7.789(22)a | 1.7 | 51 | 27 | 0.31
3 | 7.771(22)a | 12.4 | 41 | 21 | 0.31
3 | 7.994(34)ac | 13.1 | 41 | 21 | 0.15
5 | 7.831(23)b | 41.2 | 110& 111 | 15 | 0.0019
a particle registered in beam-supplied period.
b particle registered in beam-stopped period.
c Event registered by both DSSD and SSD.
During the beam-supplied period, several -decay candidates of 268Db were detected in Chain 1, Chain 2, and Chain 3.

## Slide 27: α decay of 268Db and SF of 264Lr
SF(264Lr) registration time
α decay of 268Db
55% branching ratio
7.6 – 8.0 MeV
268Db
16 h
264Lr
4.9 h

## Slide 28: Outline
Recent plans
Cold fusion reactions at SHANS2
New isotopes at SHANS2
Gas-filled recoil separators at IMP

## Slide 29: HIAF
HIAF is one of the major national science and technology infrastructure under construction with the support of both central and local governments
The total budget is 3.0 billion CNY
The campus locates in Huizhou City of Guangdong Province
The construction of project started at the end 2018, and the construction period is 7 years
High-Intensity Heavy Ion Accelerator Facility-HIAF

## Slide 30: New gas-filled separator at HIAF

## Slide 31: New gas-filled separator at HIAF
 | Length | Angular acceptance | Transmission (at focal plane) | Focal size | Dispersion (cm/%)
①：D50+Q1+Q2 | 5.4 m | ±6.3°/±2.9° | 18.5% | σx/y=16.7/41.5 mm | Dx=2.5
②：S1+D50+Q1+Q2 | 7.8 m | ±6.3° | 91.2% | σx/y=12.3/38.8 mm | Dx=2.9
③：S1+D50+S2 | 8.2 m | ±7.5° | 98.3% | σx/y=6.9/6.0 mm | Dx/y=-0.2/0.07
S1
D50
S2
D50
Q1+Q2
S1
Superconducting Solenoid
D50
Q1+Q2
③
②
①
①
②
③

## Slide 32: Search for New isotope of Pu,Am
Alpha
40Ar+192Os->232Pu*->227Pu+5n

## Slide 33: N=82 and Z=82?

## Slide 34: Collaboration
Thank you for all your attention!

## Slide 36: 叠加信号
30 μs波形
20 μs波形
4.8 μs
1.85 μs
预触发
<2 μs
小幅的叠加信号可能湮没在高幅的α衰变信号中
>20 μs
寿命更长且幅度低于100 keV阈值的叠加信号未被记录
高能侧几乎没有拖尾
243Es可能有μs量级的同核异能态

## Slide 37
New isotope 227Pu
To probe the robustness of the N=126 shell closure in Pu, it is necessary to continue -decay studies of 221-226Pu.
40Ar+192Os->232Pu*->227Pu+5n
E=8191(28) keV
T1/2=0.78(+0.39/-0.19) s