## Slide 1
SPD ECAL Status Report
IX SPD collaboration meeting
Erevan, May 13 of 2025 Oleg Gavrishuk, Laboratory of High Energy Physics, Dubna

## Slide 2
2
07.05.2025
Oleg Gavrishchuk
The calorimeter placed inside of Cryostat (Red) and shown in layout Green color.
The calorimeter is designed for efficient registration of electrons and gamma quanta in the energy range up to 10 GeV.
The transverse size of the calorimeter cell should be on the order of the effective Moliere radius of the calorimeter medium: ~58 mm.
The cells in the End-Cup part of the calorimeter have a rectangular shape 40x40 mm2.
The cells in the barrel part of the calorimeter have a trapezoidal shape in the azimuthal direction with vertex angle of the trapezoid equals 1.87 and 40 mm in beam direction.
Overview of the SPD ECAL
Notes: 2
2

## Slide 3
3
07.05.2025
Oleg Gavrishchuk
Schematic view of a calorimeter placed inside of cryostat.
Criostat
Barrel
Criostat
End-Cup
Barrel
Notes: 3
3

## Slide 4
End-Cup calorimeter support.
Frame design – option One
Stand for ECAL assembling in the assembly room
ECAL frame mounted inside of Barrel support
Stainless strips for ECAL support
1.5 mm thick.
MPD
Barrel support

## Slide 5
End-Cup calorimeter support.
Frame design – option Two.
ECAL’s modules placed inside of frame
Aluminum frame composed from 4 details made by casting into a mold
ECAL module 80x80
From 2x2 cells 40x40

## Slide 6
6
07.05.2025
Oleg Gavrishchuk
Shashlik type calorimeter has been selected with the sampling structure of 200 layers of 1.5-mm polystyrene scintillator and 0.5-mm lead, the length of the active part 400 mm, which corresponds to ~18X0.
The Cells in the End-Cup part of the calorimeter have a rectangular shape 40x40 mm2.
4 calorimeter cells are assembled into a Module, where four 40x40 mm scintillators cells are joint by a common 80x80 mm lead plate.
200 Polystyrene scintillator plates with 1.5% P-terphenyl and 0.05% POPOP is used.
199 Lead plates 0.5 mm: alloy Cca with 0.5% antimony is used as an absorber.
16 WLS fibers (1 mm diam.) collect light onto the SiPm of 6x6 mm2 with 15 micron pith size. Its corresponded to 160.000 pixels.
SiPm EQR15 11-6060D-S - it is a novel China design of NDL technology. NDL SiPM employs intrinsic epitaxial layer as the quenching resistors
Calorimeters cell composition
Notes: 6
6

## Slide 7
160000 scintillator Cells 40x40x1.5 mm3
produced in Vladimir at February 2024
Scintillator plate:
40x40 mm2 , t=1.5 mm
WLS and PM
Setup for scintillators test
4 scintillators plates after injection molding machine
Spectra from
α-source

## Slide 8
Module assembling – first setup
4-cells module assembling - in beginning stage.
Final stage of module stacking with 200 layers of 1.5+0.5 mm scintillators
And Led plates. The length of Active volume is equal 403 mm , that corresponded to the estimated period 2.02 mm
Led plate 80x80 mm2 to joint 4 Scintillator plates
40x40 mm2.

## Slide 9
Module assembling and stress test setup
Stress test setup
Center part Zoom
4-cells module assembled and tied with a Kevlar rope. It was first example to fix 200 layers stack .
The next stack fixation will be done by 4 stainless rods.

## Slide 10: Assembling Details

## Slide 11: Cluster of 4 Modules (16 cells 40x40) design
Cluster = 4 Modules Setup of 16-ch
Sleeve for 16 fibers
Joint Back Plate
Joint Front Plate

## Slide 12: End Cup and 16-ch Clusters design:
End Cup Quarters consist from 58 Clusters composing from 232 Modules as 2x2 Cells.
Total End Cup consist from 928 Modules or 3712 cells of 40x40 mm2.
16 Ch cluster selected to have associate with Front End card and ADC board.

## Slide 13
End-Cup calorimeter
in support frame
This End-Cup support for 928 Modules (3712 cells 40x40 mm2) – proposed by Valey Shvetcov.
Frame composed from 4 tiles – manufacturing from molded Aluminum.
The frame with ECAL modules should be inserted in Barrel support after their assembling.
Total End-Cup weight is equal ~10 tons.

## Slide 14
Was done up to Now in 2025:
Scintillator tiles production in Vladimir (Uniplast) started since 2024.
Plan: plates 40x40x0.5 mm3 for one End-Cup , ~1000 modules, ~4000 cells:
  Ready for 200 Modules - 160.000 plates – in 2025
  In progress for 500 Modules - 400.000 plates – should be ready in 2026
Lead absorber plates 80x80x0.5 mm3 :
  Ready for 200 Modules - 40.000 plates – 2 tons Lead in 2025
  In progress for 500 100.00 plates – 5 tons Lead – plan for 2025-2026
  Lead plate blanks (85x168 mm2) are produced in JINR and their stamping is done in Vladimir to obtain size 80x80 mm2 with 64 holes for WLS.
Modules assembling:
  200 – JINR VBLHE – 2025 – assembling procedure in progress.
  500 – Vladimir (Uniplast) – assembling will started in 2025 will ready in 2026.
  Modules assembling in Vladimir should be made complete with WLS .
WLS test was done in LNP – Results and report: Baranov V. - Kuraray-OSL8-BC
  MC – Zimin Iliya report – WLS att. length influence on E-resolution.
WLS Fiber preparation – Not solved – polishing – painted – Used Loop option.
ADC and Frontend – status approximately is defined – Anfimov N. , Kreslo I.
5/7/2025
14
Oleg Gavrishuk, JINR, Dubna , Russia

## Slide 15
End of Report
5/7/2025
Oleg Gavrishuk, JINR, Dubna , Russia
15
Thanks for attention to All