## Slide 1
Cryogenic system of SPD
Speaker: Yurii Bespalov
1

## Slide 2
Outline
Elements of the cryogenic system
Placement of cryogenic equipment
3. Cryogenic liquid tanks and related work
4. Steps of creation
5. Conclusions
2

## Slide 3
The model has been developed by Andrey Ponomarev
Cryogenic system
Control cryostat
SPD
Helium and Nitrogen pipelines
Liquefier plant

## Slide 4
He flow for cooling magnet of SPD detector (4.5-6К)
N2 flow for cooling cryogenic plant (~77К)
He line for cooling thermal shields and Cu part of current leads (~50К)
Diagram of cryogenic flows
Cryogenic system
4

## Slide 5
Cryogenic system service position
Service position
Working position
5

## Slide 6
Cryogenic system working position
Service position
Working position
6

## Slide 7
Cryogenic system
Measuring cabinet
Power supply cabinet
Protection system cabinet
Vacuum cabinet
Thermometry system cabinet
7

## Slide 8
 | Operating parameters | Unit
1 | Cooling capacity (for 4.5 K) | 100 - 130 l/h
2 | Cooling capacity (for 50 K) | 150 W
3 | Temperature of outlet flow from the SPD | 4.3 K (1.05 bar)
4 | Temperature of inlet flow from the SPD | 4.5 К (1.15 bar)
5 | Hydraulic resistance of the SC coil | 0.1 bar
6 | Cold weight | 5200 kg
7 | Maximum pressure in coil | 5 MPa
8 | Heat load | 60 – 80 W
9 | Equipment Requirement | Maximum reliability, energy efficiency, compactness, automatic mode
10 | Interval of repair/regulatory work of the plant | Not more than once a year
8
Helium system

## Slide 9
Cryogenic system control
Helium pipeline
Vacuum system
Pneumatic system
Cryogenic plant
Nitrogen system
SC coil system control
Cryogenic system control
9

## Slide 10
1
1
Cryogenic line:
LN2 – 150 m (rigid tube)
Warm line:
Ar – 120 m (rigid tube)
N2 – 120 m (rigid tube)
CO2 – 120 m (rigid tube)
Cryogenic tanks platform
1 – Two storage tanks for LN2;
2 – Storage tank for LAr;
3 – Storage tank for LCO2;
4 – Technical room
Pipelines
2
3
4
10

## Slide 11
Cryogenic tanks platform
11
Cryogenics tanks:
20 000 liters of nitrogen will be spent in 1 month of work;
Refueling of nitrogen tanks can be carried out without stopping the experiment;
10 000 liters of Ar will be spent in 2.6 months of work;
10 000 liters of CO2 will be spent in 4.7 month of work;
Isobutane will be stored in ballons volume of 20 m3(one ballon – 2.5 month of work.

## Slide 12
Steps of creation
Steps of creation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SPD | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 2028 |  |  | 
 | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV
Cryogenic plant |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Helium pipeline |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nitrogen system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Vacuum system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pneumatic system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryogenic system control |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryogenic tests |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13
 |  |  | Technical design |  |  | Technical task |  |  |  |  | Contract execution |  |  |  |  |  | Assembly & Test |  |  |  |  | Commissioning |  |  |  |  | 

## Slide 13
The new location of cryogenic equipment on the technical platform has been approved.
The new location of cryogenic tanks platform has been determined.
A technical project was developed for the construction of a foundation for cryogenic tanks, including a platform for the arrival of a refueling machine.
The development of technical task for the manufacture of cryogenic tanks is in an active phase.
Conclusions:
14

## Slide 14
Thank you for your attention!