## Slide 1
SPD silicon inner tracker
SPIN-Praha-2018 11.07.2018
S.Khabarov, O.Tarasov, N.Zamyatin, E.Zubarev
JINR, Dubna

## Slide 2: Outline
Region of IT on SPD
Main parameters of IT
Specification for Si sensors
Design of Vertex planes for BM@N experiment
Conclusion

## Slide 3
Space region barrel IT
Length = 2360
Diameter = 500

## Slide 4
View of prototype barrel IT, length =1m and three Si layers
(without FEE and cables )

## Slide 5
 | Size of Si detectors, mm2 | Si det., pcs | Area, m2 | Number of FEE, ch (two sensors connected strip to strip)
1 layer | 63x63 | 10x32=320 | 1,3 | (320:2)x640x2=204 800
2 layer | 63x63 | 12x32=384 | 1,6 | (384:2)x640x2=245 760
3 layer | 63x63 | 14x32=448 | 1,8 | (448:2)x640x2=286 720
4 layer | 63x63 | 16x32=512 | 2,1 | (512:2)x640x2=327 680
5 layer | 63x63 | 18x32=576 | 2,3 | (576:2)x640x2=368 640
 |  | Total = 2268 | Total = 9,1 | Total= 1 433 600
Comments: Total numbers of FE chips = 11340 Total power FEE chips~2mW/ch. × 1,44*106 = 3 kW |  |  |  | 
Version #0 (for discussion):
Detectors module consist of two Si-sensors
Topology of Si-sensor are double side strips
640 strips per each side of sensors

## Slide 6
About connection Si-sensors with FEE
FEE
FEE
FEE
(640x2) ch
(640x2) ch
(640x2) ch
OR???
FEE
kaptons cable (640x2) ch
126
63
FEE
FEE
FEE
FEE
(+) No long cables
(-) Power of FEE heat of Si
(-) FEE –”dead” materials take place on IT -space
(+) Power of FEE separates from Si- sensors
(+) Min budget of “dead” materials on IT -space
(-) Big length of the kaptons cables (60-100 cm) (capacitance; noise)

## Slide 7
FEE
FEE
FEE
(640x2) ch
(640x2) ch
(640x2) ch
kaptone cable (640x2) ch
FEE
FEE
FEE
FEE
FEE
N.Zamyatin, MPD and BM@N meeting
12.04.2018 (BM@N design)
Yu. Murin, SPD meeting
03.07.2018 (CBM design)

## Slide 8: Specification for Si sensors version #0 (for discussion):
Size: 63x63mm2 (on 4” – Si wafers)
Topology: double side microstrip (DSSD) (DC or AC coupling)
Pitch: 95mkm – p+ strips and 103mkm – n+ strips
Stereo angle between p+/n+ strips: 2,50÷100
Number of strips: 640x640 (640=128ch × 5 chips)
Si wafers:
  Material: FZ-Si
  Diameter: 4” or 6”
  Surface: DSP (double side polished)
  Thickness: 300mkm
  Resistivity: ρ>5kOm*cm
  Conductivity: n-type (doping by phosphorous)
  Life time carrier: >1ms
Full depletion voltage: ≤60 V
Dark current per sensor: ≤1,5 µA/120 V/+200C
Break down voltage: ≥200 V

## Slide 9
DSSD with DC topology don’t contain integral resistors and capacitors (RC), therefore external R, C are required to supply bias voltage to each strip and to electrically decouple the DC current from the electronic inputs. This role is performed by Pitch Adapter (PA) with a topology of two types for p+ and n+ sides of the detector. In addition, PA has topology of contact pads similar to chips located on the side of electronic chips. PA modules are made on sapphire plates with an epitaxial layer of silicon (SOI). Integrated poly silicon bias resistors have a value of 0.7 – 1.0 MΩ, decoupled capacitors have a value of 140 pF. PA is assembled together with read-out ASICs on the read-out card. Positive polarity signals come from detectors to P+ read-out card (black PCB) while negative signals come to N+ read-out card (red PCB).
The functional scheme of BM@N detectors module and appearance of two electronic boards

## Slide 10
Ultrasonic bonding of the strip to strip
between two DS-Si-sensors on module

## Slide 11
Design and position of Si-planes on the beam-channel BM@N, Session #55 (February-April’18)
Si-Forward plane
Si-Vertex plane-1
Si-Vertex plane-2
beam
target
Si-multiplicity detector
Si-Forward plane consist of two-coordinate Si sensors X-X’(±2.5o) with strip pitch of 95/103 μm, sensitivity area 25 x 25 cm2 , 10240 strips
Vertex plane-1 consist of 4 modules with sensitivity area 12,5×12,5cm2, 5120 strips
Vertex plane-2 consist of 2 modules with sensitivity area 12,5×12,5cm2, 2560 strips

## Slide 12
12
Carbon beam position in Si-planes for SRC-setup
Run 3467:
Beam-C, no target
Beam duration: 2.5 sec. Flux: 25k, MF=107.6 mv, 100K events, Air Empty, BC2-prime 1640 V
beam
target

## Slide 13
Primary Vertex with Si detector vs without Si detector
Carbon run, March 2017
Residuals of Si hits to GEM tracks. Carbon run, March 2017 → accuracy is defined by GEM track resolution
Slide from M. Kapishin

## Slide 14: Position of Si-monitors for measurements of radiation background on beam area BM@N (integral of Ar + Kr is 5×109 ions)
# Si-monitor | Position | Equal neutrons Ф<1MeV>, cm-2
#1 | Center of BC1 | 4,19×1010
#2 | Top BC1 | 2,44×108
#3 | FE-PCB Forward-Si | 3,35×109
#4 | Bottom of BC1 | 4,72×109
#5 | Si-multiplicity trigger (top part) | 1,25×109
1
2
3
5
4
Chart: IV characteristic of Si-monitors (13mm2/260µ)

## Slide 15
Conclusion
Three Si-coordinate planes based on double side Si detectors were developed and manufactured (DUBNA Si-group) for the BM@N experiment (this design can be acceptable for End Cup part of SPD IT)
You need to create a international community for R&D and final design IT SPD