## Slide 1
R.A. Kuzyakin, V.V. Fimushkin, M.V. Kulikov, L.V. Kutuzova, Yu.V. Prokofichev, A.M. Shumkov, A.V. Averyanov, D.O. Krivenkov
Joint Institute for Nuclear Research, Dubna
Status of New Low Energy Polarimeter at the Nuclotron
Notes: Good afternoon dear colleagues. The report I’m present to you is devoted to polarimetry at JINR acceleration complex. Nowadays it is Nuclotron - the only in Europe and Asia superconducting accelerator of nuclei and heavy ions. And The international mega-science project “NICA (Nuclotron based Ion collider facility) complex” which is aimed in the study of the properties of nuclear matter in the region of the maximum baryonic density.
Conceptual design of a new universal low energy polarimeter at Nuclotron is presented. It is proposed to install the new polarimeter behind linear accelerator LU-20 instead of old low energy polarimeter (LEP). The 3He target of this setup allows to measure both the vector polarization of protons and the vector and tensor polarization of deuterons. It is assumed that new design of polarimeter will make it possible to measure vector and tensor polarization of deuterons at the same time. The dipole magnet will be used to remove H2+ component in deuteron beam. Fabrication of the basic parts of the modern polarimeter is in progress now.

## Slide 2: General view of the NICA facility
Physics with polarized light ion beams is considered as an important part of the NICA program.

## Slide 3: NICA operation in Polarized Mode
Polarized dd – collisions:
SPI→ LU-20 → Nuclotron → Collider
Polarized pp – collisions:
SPI→ LU-20 → Nuclotron → Collider

## Slide 4
Source of Polarized Ions (SPI) for the JINR accelerator complex (Nuclotron, NICA)
Low Energy Beam
Transfer (LEBT)
SPI
Radio Frequency
Quadrupole (RFQ)
SPI will be used for the NICA-project scientific program implementation
Notes: Development of the new Source of Polarized Ions (SPI) and the acceleration of polarized beam at JINR accelerator complex made it necessary to measure the polarization of the beam in order to configure and optimize the source systems. Further the SPI will be used for the NICA-project scientific program implementation.

## Slide 5: Implementation of polarization program
F3-polarimeter
Polarimeter at Nuclotron ring
LEP at LU-20

## Slide 6
Bending Magnet and Old LEP
Bending
Magnet
Old LEP
Beam Transfer
to the Nuclotron
From
LU-20
Notes: After it The bending magnet rotates the beam to the Nuclotron. If the magnet is turned off, the beam goes to the Low Energy Polarimeter (LEP) which is located here.

## Slide 7
Old Low Energy Polarimeter (LEP) Details
Electronics and DAQ
Polarimeter Vacuum chamber
Vector part
Tensor part
Two independent parts of polarimeter
Notes: So, let’s consider the low energy polarimeter which is consist of two independent parts. The first is using for the vector polarization measurements. The second one is for tensor mode. Unfortunately the parts can not work together in the same time. But they can replace each other. Here you can see polarimeter vacuum chamber and electronics and daq system.

## Slide 8
LEP for the vector polarization measurements (left – outline, right – photo).1 – ion transfer; 2 – bellows; 3, 4 – Mylar windows; 5 – vacuum chamber; 6 – movable hermetic volume with collimators A,B,C,D; 7 – silicon detectors (Thickness - 55 μm).
Sizes of collimators: А, В – 1,3 × 7,4 [mm]; С – 1,3 × 12,5 [mm]; D – 2,5 × 12,7 [mm].
Scheme of the Old LEP for the Vector
Polarization Mode
Notes: Photo of opened LEP for the vector polarization measurements is here. Also there are ion transfer, bellows, Maylar windows, vacuum chamber, movable hermetic volume with the collimators A,B,C,D and silicon detectors.

## Slide 9
Old LEP Details
The reaction using for the vector polarization measurements is
Analyzing power of the reaction at the deuterons scattering angle θcms = 150⁰
Ed ~ 6.7 MeV
Ay = 0.28
Primary beam energy ~ 10 MeV
Energy after Mylar windows ~ 6.9 MeV
Energy of scattered (15°) deuterons ~ 6.7 MeV
Energy of recoil (15°) α-particles ~ 5.7 MeV
Deuteron energy on the detectors ~ 6.5 MeV
α-particle energy on the detectors ~ 4.5 MeV
Notes: The reaction using for the vector polarization measurements is here. Analyzing power of this reaction at the deuterons scattering angle θcms = 150⁰ is quite big and weakly depends on the energy Ed = 2 to 14 MeV. There are also several energy values of deuterons and α-particles at different stages of the reaction. The asymmetry in the number of deuterons on the left and right detectors gives us the polarization value.

## Slide 10: Old LEP for Tensor Polarization Mode
LEP for tensor polarization mode (left – photo , right – outline).
Ep = 20 MeV
Beam
Notes: LEP for Tensor Mode Polarization is shown here and based on this reaction. T20 component energy dependence of the analyzing power matrix for this reaction is here. T20 component at the registered deuterons energy 6 Mev is about -1.3. The cross-section of the reaction depends of the tensor polarization value. To get this value the numbers of samples in the Si detector, normalized to the intensity of the beam, are compared in two cases: when the beam has tensor polarization and without polarization.

## Slide 11: Old LEP for Tensor Polarization Mode
Ed ≈ 6 MeV
T20 ≈ -1.3
T20 component energy dependence of the analyzing power matrix.
Ep = 20 MeV
Tensor polarization measurements are based on the following reaction:
Notes: LEP for Tensor Mode Polarization is shown here and based on this reaction. T20 component energy dependence of the analyzing power matrix for this reaction is here. T20 component at the registered deuterons energy 6 Mev is about -1.3. The cross-section of the reaction depends of the tensor polarization value. To get this value the numbers of samples in the Si detector, normalized to the intensity of the beam, are compared in two cases: when the beam has tensor polarization and without polarization.

## Slide 12
Motivation for New LEP
Improvements
Make detectors faster
Remove component by dipole magnet
Make the protection of data flow (digital interface ~40 meters)
Measure vector polarization of protons
Measure vector and tensor polarization of deuterons with one setup at the same time (It is necessary because new source can produce beams polarized in different tensor and vector modes at the same time)
Old LEP disadvantages
Detectors are too slow (~3h per 1 point with 5% accuracy)
Old LEP was made for “Polaris”, new SPI has component in the deuteron beam
Old LEP is sensitive to electromagnetic noise from LINAC
Old LEP does not able to measure vector and tensor polarization of deuterons at the same time
Notes: Обдирочная мишень – strip target

## Slide 13
15°
112°
Vector Mode
Proposed Scheme of New Low Energy Polarimeter
3He
D2
D1
θcms = 150o
Ay = 0.3
deuteron 10 MeV
Recoil 3He
Notes: Система отсчета – reference system

## Slide 14
Notes: Система отсчета – reference system

## Slide 15
15°
112°
Tensor Mode
3He
D2
D1
T
Vector Mode
θ = 0o
Т20 = -1.2
θcms = 150o
Ay = 0.3
deuteron 10 MeV
Recoil 3He
daughter proton 20 MeV
Proposed Scheme of New Low Energy Polarimeter
Notes: Система отсчета – reference system
estimate – оценивать
steel plate – стальная пластина
copper plate – медная пластина

## Slide 16
Notes: Система отсчета – reference system

## Slide 17
15°
50°
63°
112°
deuteron 10 MeV
Recoil 3He
proton 5 MeV
daughter proton 20 MeV
Vector Mode
Tensor Mode
3He
P1
P2
T
θcms = 80o
Ay = 0.3
θ = 0o
Т20 = -1.2
θcms = 150o
Ay = 0.3
15°
112°
D2
D1
Proposed Scheme of New Low Energy Polarimeter
Notes: Система отсчета – reference system

## Slide 18
Notes: Система отсчета – reference system

## Slide 19
15°
50°
63°
112°
3He
D2
D1
P1
P2
T
deuteron 10 MeV
Recoil 3He
proton 5 MeV
daughter proton 20 MeV
Proposed Scheme of New Low Energy Polarimeter
Notes: Система отсчета – reference system

## Slide 20
Bending
Magnet
Transfer to Booster
Transfer to Nuclotron
From
LU-20
New Low Energy Polarimeter Location
Dipole
Magnet
Notes: After it The bending magnet rotates the beam to the Nuclotron. If the magnet is turned off, the beam goes to the Low Energy Polarimeter (LEP) which is located here.
stairs – лестница, fastening – крепление, plane – плоскость

## Slide 21
View of New Low Energy Polarimeter
, beam
Dipole Magnet
VC Fastening
Vacuum Chamber
Faraday cup
Cross
Vacuum Gate
DM Fastening
TM Pump
TM Pump
Notes: stairs – лестница
fastening – крепление
plane – плоскость

## Slide 22
View of New Low Energy Polarimeter
17°
From LU-20
To Vacuum Chamber
To Booster
34°
Notes: stairs – лестница turn – поворот
fastening – крепление
plane – плоскость

## Slide 23
View of Dipole Magnet
22°
34°
56 mm
 346 mm
Dipole Magnet
Vacuum Chamber
of Dipole Magnet
Coils
Notes: set – набор
yoke - ярмо

## Slide 24
View of Dipole Magnet
Energy per nucleon E, MeV/nucleon | Particle | Magnetic field (theory) Bт, G | Magnetic field (modeling/ experiment) Bм, G | Coils current Iм, А | Turn radius (theory) Rт, mm
5 | p | 2905 | 2800 / 2830 | 124 | 1112
5 | d | 5808 | 5615 / 5700 | 249 | 1112
7 | p | 3437 | 3319 / 3350 | 147 | 1112
7 | d | 6872 | 6648 / | 296 | 1112
13 | p | 4684 | 4538 / 4600 | 201 | 1112
Magnetic field for different particle energies
Notes: set - набор

## Slide 25
View of Polarimeter Target
Spherical mylar vessel
Cylindrical mylar vessel
3He
3He
3He
Radius – 50 mm
Radius – 50 mm, Height – 70 mm
Notes: glue – клеить
join (connect, unite) – соединять

## Slide 26
View of New Low Energy Polarimeter
Detectors
Detector
Detector
3He
Target
Collimator
Collimators
Plate
Notes: estimate – оценивать, event – событие
steel plate – стальная пластина
copper plate – медная пластина

## Slide 27
Current Status
Old low energy polarimeter was removed
Fabrication and ordering of basic parts of new polarimeter is in progress
Test runs are possible since next year (it’s not necessary to run Nuclotron cryogenic system to get beam on the LINAC output)
It is suggested to use usual silicon and pixel detectors
The use of solid target – deuterated titanium – is also considered

## Slide 28
Thanks for your attention!