## Slide 1
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
PROJECT NICA
Nuclotron based Ion Collider fAcility facility at JINR:
physics goals and status of the construction
Notes: ЛФВЭ является базовой лабораторией для проведения этих исследований

## Slide 2
The first SC
Accelerator
of heavy
ions
1957
Synchrophasotron
1993
Nuclotron
10 GeV proton
synchrotron –
leader in energy
The beginning
of high
energy physics
V.I. Veksler
A.M. Baldin
Investigation of nuclear matter at extreme densities
SC collider of
heavy ions
2008 ->
NICA
High energy physics at jinr
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
Notes: традиции: 1я базовая установка – лидер
2я – взгляд в будущее
3я – возвращение лидир.позиций

## Slide 3
NICA is an international project and brings the efforts of
18 JINR member state and 6 JINR associated state countries.
In 2009 the NICA project was officially approved by the JINR Scientific
Council and the JINR Committee of Plenipotentiaries and included
in the “JINR 7-year Plan for the Development of JINR 2009-2016”.
In 2016 between Russian Federation and JINR was signed an
Agreement on the NICA complex construction and operation.
In 2017 the project NICA was included into ESFRI road map.
General information
Project web-site: http://nica.jinr.ru/
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 4
Agreement
between
RF Government
and JINR
(May 2016)
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 5
Main Research Infrastructure in Particle and Nuclear Physics
NICA – Complementary Project
New issue of the ESFRI Roadmap
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 6
NICA GOALS
In the field of fundamental research
Investigation of hot and dense strongly interacting QCD matter, search
for a mixed phase and critical point in the QCD phase diagram with the
main goal to shed light on the poorly explored region of this diagram and
clarify the basis of QCD in the nonperturbative regime and other theoretical
approaches for the description of strongly interacting matter.
Investigation of the nucleon spin structure and polarized phenomena.
In applied research
development of novel technologies in material science, problem of
nuclear waste utilization, particle beam therapy, ..
In a field of education
The proposed NICA facility offers various educational possibilities, including
Practice at experimental set ups.
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 7
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 8
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 9
NICA/MPD
STAR F.T.
NA-61/SHINE
HADES
CBM
SIS-100 SIS-300
STAR BES II
NICA/BM@N I
NICA/BM@N II
energy region of max.
baryonic density
EXPERIMENTAL STATUS
Interaction rate [Hz]
Collision energy √S [GeV]
NN
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
Complementary to the RHIC/BES, CERN and FAIR programs

## Slide 10
D.Peshekhonov
EMC, J. Ashman et al., PLB 206 (1988) 364
(> 1660 citations)
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 11: Laboratories & Experiments
 | 1970 | 1980 | 1990 | 2000
SLAC |  |  |  | 
CERN |  |  |  | 
DESY |  |  |  | 
JLab |  |  |  | 
RHIC |  |  |  | 
A worldwide effort since decades
E80
EMC
SMC
COMPASS
E130
E142/3 E154/5
HERMES
CLAS/HALL-A
Phenix/Star
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 12: NUCLEON SPIN
Dark spin
Quark spin
?
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 13
- Accelerators providing beams for fixed target and collider experiments
- Experimental facilities (BM@N, MPD, SPD)
- Line for assembling and cryogenic testing of SC-magnets
- Workshops for construction of the detector elements
- NICA innovation center
- Required infrastructure objects (cryogenics, power, IT, ..)
NICA complex
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 14
NICA accelerators
Main accelerator of the NICA complex is the Nuclotron –
superconducting ion synchrotron at magnetic rigidity of about 42 T·m
equipped with two injection chains: for heavy and for light ions.
Injection chain for heavy ions consists of:
the ion source (KRION-6N), heavy ion linear accelerator (HILac),
superconducting synchrotron (Booster) and required beam transport lines.
Injection chain for light ions includes:
Laser ion source (LIS), Source of polarized ions (SPI), Duoplasmatron,
RFQ accelerator as a foreinjector, Drift tube linac of Alvarec type (LU-20)
and required beam transport lines.
The collider experiments will be provided at two storage rings
with two interaction points (IP).
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 15
SPI
LU-20
Nuclotron
ESIS
Booster
Transfer to collider rings
or fixed targets
LIS
RFQ
RFQ
IH1
IH2
HILAc
Structure of the injector complex
Au31+ 3.2 MeV/u
p↑, d↑, ions z/A>0.3 5 MeV/u
DP
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 16
KRION 6T – heavy ion source
was used during Nuclotron RUN №55 for SRC & BM@N experiments
Cryogenic heavy ion source KRION - Electron String Ion Source (ESIS), provides up to 2.5·109 Au31+ particles per cycle at repetition frequency up to 10 Hz
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 17: Acceleration of 124Xe42+ beam RUN № 41 (February 2010)
78Kr+26 beam acceleration (3,2 GeV/u) RUN № 55
Nuclotron: ion acceleration
Signals from ionization beam profile monitor
Main field
Acceleration
Slow extraction
Photo of the 124Xe42+ extracted
beam (Е = 0,57 GeV/u)

## Slide 18
RFQ
IH-1
IH-2
MEBT
Heavy Ion Linear Accelerator HILAc
overall commissioning: Oct. 16
the first Linac with transistor RF amplifier
Design and fabrication by “BEVATECH OHG” Germany, Offenbach/Mainz
3.2 MeV/u, Au31+, 10 mA
Notes: A new heavy ion linac fabricated by BEVATEC was fully commissioned and put in operation last year.

## Slide 19
The Booster will accelerate ions up to 600 MeV/u (for ions with Z/A = 1/6).
The magnetic ring of 211 m long is placed inside the window of the Synchrophasotron yoke.
Injection chain for heavy ions
Fabrication of the magnetic system
is completed.
Start of assembly – September 2018.
First (technological) run – end of 2018.
End of 2018
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 20
Injection chain for light ions
SPI
LU20
RFQ
LIS
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 21
Cooling, 7.3%
Tuning, 8.7%
Repairs, 4%
Unexpected losses, 2.5%
77.6%
Run № 53, 1450 h,
Polarized, unpolarized deuterons,
maximum energy of extracted beam
4.6 GeV/u
Run № 54, 1150 h
Polarized program at Nuclotron with SPI beams
longest run

## Slide 22
Routine operation of SPI and new fore-injector
Polarized deuteron acceleration: Intensity 25*108 per cycle
Deuteron Spin Structure experiment, internal target of the Nuclotron
8 10
Nuclotron: polarized deuterons
Acceleration
Internal target
Injection
Main magnetic field
Beam intensity
8
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
.

## Slide 23
Beam intensity, particles
Time, ms
Magnetic field, G
1.8 E8
Polarized protons
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
New RFQ fore-injector provides output energy of 156 keV for all ions:
the protons can be accelerated in LU-20 at the second harmonics only
the output proton energy after LU-20 is 5 MeV
the Nuclotron magnetic field at injection has to be about 150 G
(instead of 294 G for other ions with Z/A=1/2)

## Slide 24
New Light Ion Linac “LILAc”
Injector for the Nuclotron ring.
LU-20 Hall
Meddle energy section
SC section
First LINac 7 MeV/u section
HILAc
MAC’2017: «The improvement of the acceleration efficiency of polarized proton beam is urgently required.»

## Slide 25
LU-20 Hall
Meddle energy section
SC section
First LINac 7 MeV/u section
HILAc
Contract with BEVATECH signed in Dec. 2017 for 3.5 years.
July 2018: TDR
Summer 2021: commissioning at the test bench with beam.
New linac – 3 sections:
1st sect. from BEVATECH
7MeV/u for ions Z/A>1/3
2nd sect. warm resonators
for p+ up to 13 MeV
3rd for SC res. testing & applied research up to 20MeV
New Light Ion Linac “LILAc”
Injector for the Nuclotron ring.

## Slide 26
First part of the LILAc for z/А=1÷0,5 up tp 7 MeV/u:
RFQ (600 keV/u) – MEBT+ ReBuncher – IH1 (4.2 MeV/u) – IH2 (7 MeV/u)
New Light Ion Linac “LILAc”
Injector for the Nuclotron ring.
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 27
Nuclotron
Circumference 251,52m, Br<43 Tm
The project approved
in 1986 year
Commissioning &
fist beam
March 1993 year
The last RUN № 55
Feb. - April 2018
Slow extraction
2000 year
Accelerated:
Ions from p to Xe (C, Mg, Fe, Ar, Kr)
Polarized p & d beams
Proton energy max 12 GeV
Light ions max 6 GeV/u
Heavy ions max 4.5 GeV/u
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 28
Nuclotron-N
Intensity >10^7 ppc
(with KRION-2)
Energy 6 Gev/n
(for Z/A = 1/2)
Field ~ 2T,
B’< 0,8 T/s
Heavy ions
Stable, safe,
long operation
Development of the
KRION ESIS
Vacuum improvement
Injector modernization
+
Energy evacuation system
Quench protection system
Slow extraction at HE
Control, diagnostics, RF
Power supply system modernization
Cryogenics modernization
Radiation safety
Nuclotron-N
preparation of the ring for NICA project
Nuclotron – superconducting synchrotron
Slide from 2010 year

## Slide 29
Run № 47 02-03.2013 (860 h 70% beam time)
Last shift - acceleration and slow extraction d 4.5 GeV/u (~ 1.8 T)
Run № 48 11-12.2013 (1050 h 73% beam time)
Carbon ions were accelerated and extracted at energy 5.8 GeV/u, 1.5*1010
Run № 49 02-03.2014 (710 h, 66% beam time)
good beam spill at low intensity (STRELA), double user mode.
Run № 50 05-06.2014 (650 h, 61% beam time) Krion
Experiments “40Ar” 1.2 GeV/u, “7Li” 3 Gev/u,
Run № 51 01-03.2015 (1150 h, 70% beam time)
Test of BM@N systems with deuteron and C+6 beams
Run № 52 30-06.2016 (670 h, 57% beam time)
Technical run with SPI and laser source.
Run № 53 25-12.2016 (1450 h, 78% beam time) * Longest Nuclotron run
Polarized deuterons 4,6 GeV/u, DSS, Alpom, Hyper NIS
Run № 54 24-03.2017 (1150 h, 64% beam time)
Polarized protons & deuterons 4,6 GeV/u, DSS, Alpom, BM@N
Run № 55 05-04.2018 (1020 h, 60% beam time) Krion6T
Physical run at BM@N, SRC with 12C, 40Ar, 78Kr beams
Statistics of operation
During 5 last years 9 Runs of the Nuclotron was provided.
operation time ~8710 hour, beam time for experiments ~65%
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 30
Status of the Nuclotron 2018
Parameter | Project | Status (June 2018)
Max. magn. field, T | 2 | 2 (1.7 T routine)
B-field ramp, T/s | 1 | 0.8 (0.7 routine)
Accelerated particles | p–U, d | p, d, p – Xe
Max. energy, GeV/u | 12 (p), 5.8 (d) 4.5( 197Au79+) | 5.6 (d, 12C), 3.6 (40Ar16+)
Intensity, ions/cycle | 1E11(p,d), 2E9 (A > 100) | d 4*1010 (2*1010 routine), 7Li3+ 3*109 12C6+ 2*109 40Ar16+ 1*106 78Kr26+ 2*105 124Xe42+ 1*104
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 31
The Collider ring 503.04 m long has a racetrack shape and is based on double-aperture (top-to-bottom)
superconducting magnets at maximum dipole field 1.8 T;
The major parameters of the NICA Collider are the following:
- magnetic rigidity = 45 T·m;
ion kinetic energy range from 1 GeV/u to 4.5 GeV/u for Au79+;
energy of polarized deuterons is 6 GeV/u, protons – 12 GeV,
- vacuum in a beam chamber: 10−11 Torr;
- zero beam crossing angle at IP;
- 9 m space for detector allocations at IP’s;
Average luminosity 1027 cm−2·s−1 for gold ion collisions at √sNN = 9 GeV.
The luminosity in the polarized mode is up to 1032 cm−2·s−1.
Collider
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 32
Stochastic cooling system
Successfully tested at the Nuclotron in 2013
Collider
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 33
Cooperation with BINP
The Booster acceleration system
(Tested at JINR – October 2014)
The Booster electron cooling system
(commissioned at JINR - December 2017)
Beam transfer line
from the Booster to Nuclotron
RF system of the collider
Electron cooling system of the collider
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 34
Official start up of the construction 25 March 2016
Collider construction
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 35
http://nucloweb.jinr.ru/nucloserv/205corp.htm
Collider construction
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 36: New helium liquefier (1000 l/h)
Largest in Russia commissioned in May 2016
Cryogenic facility
Finally the cooling power
should be doubled
from 4 kW to 8 kW @ 4.5K
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
Notes: He liquefier …..

## Slide 37
Main production areas:
Incoming inspection zone
SC cable production hall
SC coils production hall
Area for assembling the magnets
Area for the magnetic measurements under the room temperature
Leakage test area
Area for mounting the SC-magnets inside cryostats
Cryogenic tests bench
Request: 450 magnets for NICA and FAIR projects
Line for assembling and cryogenic testing of SC-magnets
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 38
2016
2017
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 39
The Nuclotron internal target station equipped with six different targets:
wire, strip and film with material from hydrogen to tungsten dedicated
for particle physics, spin physics, relativistic atomic physics experiments.
Main experimental facilities
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 40
Main experimental facilities
BM@N
Bld.205
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 41
Baryonic Matter at Nuclotron (BM@N) – fixed target experiment
at the Nuclotron extracted beams which main goals are investigations of strange / multi-strange hyperon, hypernuclei production and short range correlations.
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 42
BM@N experiment
GEM’s installed in magnet gap
chamber size | < ’16 | ‘17 | ‘18 | ‘19
66 x 41 cm2 | 5 |  |  | 
163 x 45 cm2 | 2 | 6 | 6 | 
200 x 45 cm2 |  |  |  | 6
silicon tracker stations
Notes: Several milestones are foreseen to put in operation the fully equipped detector. There major tracker is based on the GEM chambers installed inside the gap of dipole magnet. Fully equipped set-up contains as well TOF system, Ecal, zero degree calorimeter and silicon tracker, which will be installed just downstream the target.

## Slide 43
Present status and next plans
M.Kapishin BM@N experiment
BM@N technical runs performed with deuteron and carbon beams at energies T0 = 3.5 - 4.6 AGeV and recently with Ar beam of 3.2 AGeV and Kr beam of 2.4 AGeV
Measurement of Short Range Correlations performed with inverse kinematics: C beam + H2 target
Major sub-systems are operational, but are still in limited configurations
Аlgorithms for event reconstruction and analysis are being developed, signals of Λ hyperon decays are reconstructed
First meeting of BM@N / MPD experiments held in April to form Collaborations
Major BM@N plans for Au+Au to start in 2020:
Collaborate with CBM to produce and install large aperture STS silicon detectors in front of GEM setup
Extend GEM central tracker and CSC outer tracker to full configuration
Implement vacuum / helium beam pipe through BM@N setup

## Slide 44
MPD detector for Heavy-Ion Collisions @ NICA
Tracking: up to |h|<1.8 (TPC)
PID: hadrons, e, g (TOF, TPC, ECAL)
Event characterization:
centrality & event plane (ZDC)
Stage 1: TPC, TOF, ECAL, ZDC, FD
Stage 2: IT + Endcaps (tracker, TOF, ECAL)
trim coil
cryostat
control dewar
SC coil
weight
~ 900 t
B0=0.66 T
General contractor (Dec. 2015):
ASG Superconductors, Genova, Italy
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
Notes: The MPD will be put in operation at two stages. At the first one the barrel part will be equipped with major tracking detector TPC, TOF end ECAL. FHC and FD will be operational as well.
At the second stage the detector will be supplemented with IT and end cap subdetectors.

## Slide 45
45
Yoke production
VITKOVICE Heavy Machinery
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
test assembly

## Slide 46: JINR apeals for the transfer of Know-How to build 6-layer ALICE type ITS
# layer | R0 mm | Rminmm | Rmax mm | Active l, mm | N of chips / staves | N of staves | N of chips / layer | thickness % X0 | active area, cm2 | number of pixel cells
1 | 24,4 | 22,4 | 26,7 | 542,4 | 18 | 12 | 216 | 0,3 | 889,9 | 113 246 208
2 | 42,0 | 40,7 | 45,9 | 542,4 | 18 | 22 | 264 | 0,3 | 1 087,7 | 138 412 032
3 | 60,0 | 59,8 | 65,1 | 542,4 | 18 | 32 | 384 | 0,3 | 1 582,1 | 201 326 592
4 | 107, | 95,1 | 98,9 | 1477,5 | 98 | 12 | 1176 | 1,0 | 4 845,1 | 616 562 688
5 | 156,5 | 144,5 | 147,9 | 1477,5 | 98 | 18 | 1764 | 1,0 | 7 267,7 | 924 844 032
6 | 206,5 | 194,5 | 197,6 | 1477,5 | 98 | 24 | 2352 | 1,0 | 9 690,2 | 1 233 125 376
Total: |  |  |  |  |  |  | 6156 | 3,9 | 25 362,7 | 3 227 516 928
MAPS based Inner
Tracking System of
ALICE ITS Upgrade type
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 47
MPD STATUS
Magnet – fabrication stage
TOF, ECAL, ZDC – TDR are ready
FFD – fabrication stage
TPC
  assembly area in preparations
  fabrication of basic elements
  readout chambers – production + R&D (alternative)
  FEE (ALTRO-based FE card prototype)
MPD first stage program (central rapidity range):
- search for phase transitions (observables – particle yields and spectra) including partial restoration of chiral symmetry (observables – yields of di- leptons);
- search for the critical end-point (observables – event by event fluctuations, particle correlations)
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 48
Spin Physics Detector (SPD) aiming to study of spin physics with colliding beams
of polarized deuterons and protons at the energies up to 27 GeV (for protons).
Leader: Prof. Rumen Tsenov
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 49: Reinforced concrete works at SPD plase
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 50
- cluster of JINR computer center dedicated to collect and process
the data from NICA detectors,
500 offices for scientists,
laboratory rooms for preparation of experimental equipment
and fast analysis of results,
conference halls
NICA innovation center
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
General contractor “Arena”

## Slide 51
NICA COLLABORATION
ARE
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 52
Thank you
NICA
FAIR
LHC

## Slide 54
~ 106 3ΛH are expected
in 10 weeks
P = 1 GeV/c
d
3He
p
p-
3ΛH → 3He + π –
PID
3ΛH → p + d + π -
Hypernuclei @ MPD
Hypertritons (central Au+Au @ 5A GeV (DCM-QGSM)
Hypernuclei production
enhanced at high
baryon densities (NICA)

## Slide 55
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 56
Baryonic Matter at Nuclotron (BM@N):
Three technological runs (2016 – 2017)
5.02 – 4.04.2018 experiments with C, Ar, Kr beams
(Short range correlations, strange production)
Intensity of extracted Kr beam. Spill duration 2.5 sec.
Up to 5105 ions per cycle
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 57
Addition to the BM@N physics program:
"Probing Short-Range Correlations"
Leader: E. Piasetzky, Tel Aviv University, Israel
BM@N collaboration +
Israel: Tel Aviv University
Germany: TUD and GSI
USA: FIU, MIT, ODU, PSU
France: CEA

## Slide 59
Drell-Yan process
No fragmentation functions !
PHYSICS OBJECTIVES AT NICA
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 60
Hard processes:
q g→q γ 85%
q qbar→g γ 15%
single transverse spin asymmetry provides
access to the Sivers function of gluons
double longitudinal spin asymmetry gives
access to gluon polarization
PHYSICS OBJECTIVES AT NICA
DIRECT PHOTONS
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov

## Slide 61
Time Projection Chamber (TPC)
FEC64S плата
length | 340 cм
external R | 140 cм
internal R | 27cм
gas | 90% Ar+10% меth.
Drift velocity | 5.45 см / мкc;
Drift time | < 30 мкc;
N of chambers | 12 + 12
N channels | 95232
rate | < 7 кГц ( L= 1027 )

## Slide 62
Time of Flight (TOF) system
R= 170 cm
28 modules
280 MPRC’s
13 440 channels
FEE
module box housing 10 MPRC’s
MRPC construction
efficiency and t – resolution
NINO & HPTDC-
purchased
triple-stack MRPC
Notes: GEANT simulation was carried out for the construction described above. Mainly used QGSM generator.
clic
Indeed, it can be seen from the histograms, the occupancy does not exceed 15% and the geometric efficiency of the TOF detectors in this arrangement is ~ 94%.

## Slide 63
Pb+Sc “Shashlyk”
read-out: WLS fibers + MAPD
L ~35 cm (~ 14 X0)
Segmentation (4x4 cm2),
s(E) better than 5% @ 1 GeV;
time resolution ~500 ps
Module prototype
Barrel ECAL ~ 43 000 modules
Projective
geometry
Electromagnetic calorimeter: ECAL
Notes: One of the unique high-tech projects within the framework of the MPD experiment is the large scale electromagnetic calorimeter of the shashlik type with projection geometry. This is a joint project with Tsinghua University (Beijing). It is required to produce more than 40 thousand modules and assemble them into a single cylindrical system, calibrate and put into operation.

## Slide 64
LHe Liquefier OG-1000
(the final stage of commissioning):
(2010-2016)
Construction of the new compressor station:
(2015-2017)of 8 kWat 4.5 K
Helium satellite refrigerator of Booster and Collider:
5% completed
(2016-2017)
Two He screw
compressors
(delivered):
95% completed
(2011-2016)
LN2 Re-condensation
(liquefier + 2 compressors)
50% completed
(2012-2018)
LHe 40m3 reservoir:
20% completed
(2016-2017)
Gaseous He purification system:
25% completed
(2016-2017)
He satellite refrigerators for Collider & MPD magnet:
5% completed
(2014-2018)
Development of the NICA Cryogenics
The cooling power
should be doubled
from 4 kW to 8 kW @ 4.5K
SPIN-PRAGUE-2018 9 Jule 2018 D. Peshekhonov
Notes: This complex is permanently developing to reach the cooling power 8 kW at 4.5 K. The decision was taken to construct a new building for the compressor station.
The tender for design is completed.