## Slide 1: Silicon Tracking Systems for BM@N and MPD experiments at NICA
D.Dementev, Yu. Murin
for JINR STS team
JINR LHEP
SPIN-Praha-2018
Charles University, Faculty of Mathematics and Physics

## Slide 2: BM@N (Baryonic Matter at Nuclotron)
Beam parameters and setup at different stages of the experiment
BM@N advantage: large aperture magnet
(~1 m gap between poles)
→ fill aperture with coordinate detectors
which sustain high multiplicities of particles
→ divide detectors for particle
identification to “near to magnet” and “far
from magnet” to measure particles with low
as well as high momentum (p > 1-2 GeV/c)
→ fill distance between magnet and “far”
detectors with coordinate detectors

## Slide 3: BM@N 2020: stage 1
Major BM@N plans for Au+Au to start in 2020:
Upgrade of the BM@N beam line: implement beam pipe instead of air gaps existing, implement instruments to limit beam size and spread at the target
Implement vacuum / helium beam pipe through BM@N setup
Collaborate with CBM to produce and install large aperture STS silicon detectors in front of GEM setup
Extend GEM central tracker and CSC outer tracker to full configuration
Install MPD / CBM type of hadron ZDC calorimeter
One single Au ion at 5A GeV, no beam pipe, BMNroot + GEANT3
Talk by M. Kapishin, BM@N DAC meeting, Jun. 2018:
Status of BM@N project
Talk by P. Zenger, The third Mini-Work Meeting "Making-up a Work Plan for building hybrid DSSD-GEM Tracking System for the BM@N-2" Jul. 2018:
BM@N upgrade for high intensity Au beams

## Slide 4: Hybrid DSSD-GEM Tracking System
STS
GEM
dipole magnet
Mutual interest by CBM groups from Germany and Russia to install, commission and use 4 CBM-like Silicon Tracking Stations in BM@N in 2020.
Δp/p ≈ 1%
25 µm single-hit spatial resolution
material budget per station ~1% X0
40 Ladders
344 Modules
~700 k Channels

## Slide 5: Preliminary layout of BM@N STS
Talk by V.Elsha, The third Mini-Work Meeting "Making-up a Work Plan for building hybrid DSSD-GEM Tracking System for the BM@N-2" Jul. 2018: Tentative Layout of the DSSD Stations with Number of Requested Components
Total:
40 ladders
344 modules
~700 k channels

## Slide 6: Double sided microstrip silicon sensors
6.2 x 2.2 cm2
6.2 x 4.2 cm2
6.2 x 6.2 cm2
CiS
Hamamatsu
Quality assurance of the sensors
Final product inspection at the vendors: detailed data
Quality inspection at JINR has been advanced:
  full inspection during prototyping, sample tests during series production
  sophisticated optical and electrical methods established
  charge collection tests before/after irradiation, S/N determination
Thickness: 300 μm
Pitch: 58 μm
Stereo angle: 7.5°
400 sensors are already ordered and arrived at JINR

## Slide 7: STS/MUCHXYTER ASIC
128 channels+ 2 test channels
Self triggered architecture
Maximum data rate: 250 kHz/channel
5-bit amplitude measurement
  - shaperslow+ ADC
  10 bit DAC for effective slow path threshold setting (~200 e resolution)
  time stamp measurement
  - shaperfast + discriminator
  Dynamic range: 16 fQ at STS mode
  Noise performance for slow shaper: 1000 enc at 30 pF input
  Time stamp resolution: 1 ns
produced in 9/2016
Test bench for characterization
of the ASIC
Test socket for the ASIC-tab-bonds
CBM STS-XYTER 2.1 and SPADIC 2.2 Submission Review (15.03.2018)

## Slide 8: Front-end Boards with 8 STSXYTERS (FEB-8)
Size very much determined through available space: 101.5mm x 30.6mm
Digital signal coupling, crossing ~500V DC sensor bias
Powering: low drop skimming regulators (dedicated development SCL Chandigarh)
ZIF-digital signal connector – for 5, 2 and 1 uplink per chip
10-layer board allows routing of 2 uplinks per chip
5 uplinks per chip may be feasible with 14 layers
Production at AGH-Krakow
Development activities at AGH-Krakow (Lukas Mik) and GSI

## Slide 9: Module assembly site at JINR LHEP
The main room (90m2 ) is class 7 ISO (less than 10 000 p/ft3 < 0.5 mkm)
4 technicians are currently involved in module assembling
jigs for the module assembling

## Slide 10: Modules
distance between traces varies from 74 to 82 µm
Measurement: C_line = 0.38pF/cm
Microcables from Al-polyimide
Mockups of the STS modules
About 420 components are in assembly process at different stages
TabBonder Planar EM-437
Wirebonder F&K Delvotec G5

## Slide 11: Ladder assembly
Material: CF prepreg M55J/ 334EU
Modulus of composite 32800Gpa
Total weight: 10,4 g/m
Mockup of the ladder
Si sensors
FEB box
FEB box
Design by S. Igolkin (CERN)
40 CF frames were already produced (this is already enough for BM@N,
production for the CBM@FAIR is under discussion)
Ladder assembly device
The precision of the sensor orientation:
X coordinate ±50 mkm
Y coordinate ±15 mkm on 1200 mm base
±12 mkm on 180 mm base
Z coordinate ±50 mkm

## Slide 12: Ladder assembly site

## Slide 13: Detector readout chain
STS modules 8 STS-XYTER v2.0 on FEB-8
Common GBTx Readout Board
based on radiation hard GBT and Versatile Link components developed at CERN  all components purchased
fully featured prototype currently being tested and commissioned (CROB - larger than final board)
FLES IN node with FLIBs
on detector
Copper
link
Optical link
GBTx ASIC military graded by IBM!
Banned for export to Russia
off detector
Xilinx Artix 7 FPGA board
Longer cables (~5 m)
80 Mbit/s per link instead of 320 Mbit/s

## Slide 14: HighRose Digital Signal Cable FH41
Signal transmission tested (GSI-Team)
20 differential pairs, shielded 0.5mm pitch HighRose cable
ZIF-connector – 80cm differential pair – ZIF-connector
Beautiful Eye-Pattern at 800 MHz suggest : 1600 Mbit/s feasible  targeted 80 Mbit/s no problem!
Line to line pickup investigated: no visible crosstalk
1.25ns

## Slide 15: Integration to the BM@N DAQ
GPS CLOCK Antenna
Time receiver
WR switch
WR switch
slaves
slaves
Timing system of BM@N experiment is based on White Rabbit network. Supported frequencies are 125 MHz and 125/3 MHz. There is no 40 MHz clock, which is used in CBM. Two different options for STS were suggested:
To run at 125 MHz and link speed of 5 Gb/s instead of 4.8 Gb/s (still problems with PPS)
To install additional time receiver and create a time base with 40 MHz
Current bandwidth of the BM@N DAQ is 1-5 GB/s. SSD storage network has much higher bandwidth, but capacity is limited.
Probability of using a ring buffer for the data storage before receiving of a trigger decision is suggested. Alternative solution is to use embedded computers for that.

## Slide 16: In-beam tests: COSY 2018
Silicon sensor online monitor
Achieved noise level: 1.2 ke

## Slide 17: In-beam tests: mCBM
Activities towards prototype station assembly, construction of mSTS for mCBM@SIS18 (GSI, 2018)
Small scale pilot version of the detector involving pre-final components – before BM@N and CBM.
Very important project requiring joint effort of all groups involved.
JINR team will provide 2 detector layers with ladders from JINR production, for runs in 2019.
mSTS system mechanical design, fully detailed

## Slide 18: In-beam test: Linac-200 JINR FLNP
Checking of the mapping with Ra-226 alpha source
Test station with “baby” sensor
Model of the test station with half-module
STS 0
STS 1
STS 2
S 0
S 1
beam
uTCA crate
with DPB
boards
2 m
STS 0: Test station with baby sensor
STS 1: Test station with baby sensor
STS 2: Test station with STS module
S 0, S 1: Scintillator counters

## Slide 19: ITS for MPD experiment
Stage 2: 2022-2023
Installation of ITS and thin wall Be beam pipe
JINR appeals for the Know-How transfer to build 5-layer ITS of the ALICE ITS Upgrade type with increased length of ladders to fit the NICA/MPD Interaction diamond parameters
MoU was signed
Radiation length for the IB ~ 0.3% X0
for the OB~0.8% X0

## Slide 20: ALPIDE – Monolithic Active Pixel Sensor
One machine is already installed
in a clean room
130,000 pixels / cm2 O(30x30x30 mm3)
Max particle rate: 100 MHz / cm2
fake-hit rate: < 10-10 pixel / event

## Slide 21: ITS for MPD experiment
MPD ITS based on ALICE type staves
Reconstructed Λ-hyperon invariant mass spectrum (pt<0.6 Gev)
A. Zinchenko et al
.
Pointing resolution
Simulations by Valery Kondratiev, SpBSU, SpB
5 Layers of ITS with a beam pipe diameter less than 40 mm
will allow identification of open charm particles

## Slide 22: ITS in a nutshall
IB stave
OB stave

## Slide 23: Work plan
To transfer Know-How on MAPS ITS from CERN to NICA
To design the ITS out of new ALICE ITS components with minimum changes and need for additional R&D
To build the outer layer(s) with all mainframe and installation mechanics completed by the time of the MPD commissioning (2022)
To complete MPD ITS by 2025-26 and install it during NICA LS1 together with Be-pipe of reduced diameter

## Slide 24: Plans for 2018
To sign the Protocol on Agreement CERN -JINR
To send 3 key assembly persons to CERN
To write & sign Addendum for CERN delivery of ALPIDE,SAMPA, etc. and transfer the money to CERN to be able to start assembling of HICs OB at LHEP in 2019
To write the Technical Proposal for MPD/ITS : (1) mechanical sketch design including jigs for ITS installation; (2) ITS optimization through computer simulations
To procure/install the basic equipment for assembly of HIC (ALICIA-8)

## Slide 25: Thank you for your attention!

## Slide 26: Motivation for study of charm production at NICA
  Heavy charm quarks are produced at the very initial stage of the collision of the heavy ions to witness the CBM(NICA,FAIR) or QGP (RHIC,CERN) . C-quarks re-scattering by CBM is the right way to study CBM at NICA
  C-quarks interaction with cold nuclear matter has an exciting perspective at NICA since the estimated yields for the production of the hypothetical light supernuclei cHе3 and cHе4 indicated feasibility of the experimental search at NICA and not anywhere else at the moment
      From the experimental point of view production of open-charm particles in the energy range of NICA is a complete terra incognita

## Slide 27: Physics motivation for a study of charm in cold nuclear matter
J. Steinheimer, A. Botvina, M. Bleicher arXiv:1605.03439v1
Dubna model and coalescense by late K.Gudima

## Slide 28
Expected yields of the C-probes
At the highest energies NICA luminosity will reach values of L=1027 cm2s-1 and the gold-gold collision rate of 5 kHz with the estimates for the number of registered open-charm particles in a two-week run of NICA/MPD as follows
D+
K-
π+
π+
Decay | Multiplicity | сτ, μ | BR,% | Eff,% | Number of events
D0->K+π- | 0,1 | 123 | 4 | 2 | 48 103
Dbar0->K-π+ | 0,1 | 123 | 4 | 2 | 48 103
D+->K+ π-π+ | 0,1 | 312 | 7 | 1,5 | 63,5 103
D-->K- π-π+ | 0,1 | 312 | 7 | 1,5 | 63,5 103
D+s-> K+ K- π+ | 0,1 | 150 | 3 | 1,5 | 27,2 103
Λ+c-> pK+ π- | 10-3 | 60 | 6 | 0,1 | 363
Λbar+c-> pbarK- π+ | 10-3 | 60 | 6 | 0,1 | 363
cHе3-> d+pK+ π- | 10-4 | 60? | ? | ? | 3,6 (?)
cHе4-> t+pK+ π- | 10-5 | 60? | ? | ? | 0,36 (?)

## Slide 29
ALICE Monolithic Pixel Detector
CMOS Pixel Sensor using 0.18mm CMOS Imaging Process
NA ~ 1018
NA ~ 1016
NA ~ 1013
High-resistivity (> 1kW cm) p-type epitaxial layer (25mm) on p-type substrate
Small n-well diode (2 mm diameter), ~100 times smaller than pixel => low capacitance (~fF)
Reverse bias voltage (-6V < VBB < 0V) to substrate (contact from the top) to increase depletion zone around NWELL collection diode
Deep PWELL shields NWELL of PMOS transistors
NA ~ 1018
NA ~ 1013
SEM picture of ALPIDE cross section
 full CMOS circuitry within active area

## Slide 30
zero suppression
zero suppression
zero suppression
zero suppression
Bias, Data Buffering, Interface
THR
COMP
AMP
1024 pixel columns
continuous
or
external trigger
512 rows
ALPIDE – ALice PIxel DEtector
Spatial Resolution & Cluster Size
130,000 pixels / cm2 O(30x30x30 mm3)
spatial resolution: ~ 5 mm (3-D)
Max particle rate: 100 MHz / cm2
fake-hit rate: < 10-10 pixel / event
Power : ~ 300 nW /pixel
pads over matrix
50mm thick

## Slide 31: The status of the MPD-ITS
J. Steinheimer, A. Botvina, M. Bleicher arXiv:1605.03439v1

## Slide 32
To sign the Protocol on Agreement CERN -JINR
Work Plan for 2018
To send 3 key assembly persons to CERN
To write the Technical Proposal for MPD/ITS : (1) mechanical sketch design including jigs for ITS installation; (2) ITS optimization through computer simulations
To procure/install the basic equipment for assembly of HIC (ALICIA-8)
To write & sign Addendum for CERN delivery of ALPIDE,SAMPA, etc. and transfer the money to CERN
to be able to start assembling of HICs OB at LHEP in 2019
To send 3 key assembly persons to CERN

## Slide 33
Towards Technical Proposal
Pre-design!

## Slide 34: Strange hyperons identification ( Λ0)
J. Steinheimer, A. Botvina, M. Bleicher arXiv:1605.03439v1
Towards Technical Proposal: Simulations

## Slide 35: Cascades hyperons identification (Ξ-)
J. Steinheimer, A. Botvina, M. Bleicher arXiv:1605.03439v1
Towards Technical Proposal: Simulations

## Slide 36: Strange hyperons identification Λ+c
J. Steinheimer, A. Botvina, M. Bleicher arXiv:1605.03439v1
Towards Technical Proposal: Simulations

## Slide 37
Towards Technical Proposal: General Mechanical Layout
Key task: To design of the
mainframe and jigs for its
integration with TPC and BP within a year and tune the flow of components for assembly OB at JINR
Sketch design by S.N.Igolkin will start September 2018

## Slide 38
Towards Technical Proposal: Interfaces
Proposed for MPD
In TPC
?
As done in ALICE

## Slide 39
Absense of 3 “leutenants” in the fields pointed by Musa
Critical issues of the MPD/ITS project and ways for remedy
Decision of JINR Director to overcome the standard flow of procurement and transfer the money without delay to CERN
Finding a Deputy for me of a rank of “a captain” to carry on the project after my retirement
Getting an export license on ALPIDE (SAMPA?)

## Slide 40
Italy, China, Germany, Poland, UK
Hiring foreign postdocs with salary from CREMLIN+ (starting 2019)
Perspectives for Internationalization

## Slide 41
MPD/ITS physics case is well justified and has a potential of discovery of super nuclei
After signing the Protocol with CERN the project got a ground for a start
Strategic plan is worked and agreed with CERN
However, the general status to the moment is “just started”
THANK YOU FOR YOUR ATTENTION!