## Slide 1
HIAF-iLinac and key technology R&D
Hongwei Zhao
Institute of Modern Physics (IMP), Chinese Academy of Science,
Lanzhou, 730000, China
NICA-HIAF Accelerator Workshop, Dubna, July 2-3, 2018

## Slide 2: Outline
Brief overview of HIAF
HIAF iLinac design
Key technology R&D
Summary

## Slide 3
iLinac: Superconducting linac
Length:100 m
Energy: 17-22 MeV/u(U35+-45+)
BRing-S: Booster ring
Circumference: 650 m
Rigidity: 86 Tm
Beam stacking
Beam acceleration
MRing: Figure “8” ring
Circumference: 273m
Rigidity: 15 Tm
Ion-ion merging
SRing: Spectrometer ring
Circumference: 273m
Rigidity: 13-15 Tm
Electron/Stochastic cooling
Two TOF detectors
Four operation modes
L: 180m, Bρ: 25 Tm
BRing-N: Fast cycle ring
Circumference: 590 m
Rigidity: 34 Tm
Large acceptance (250/120)
Two planes painting injection
Fast ramping rate（3-5-10Hz, 20Hz）
HIAF Layout Overview
These tunnels will be built in a cut and cover method and will be filled with 5 m overlay of soil. This conforms to the requirements of radiation safety.
Notes: The concept and layout of HIAF facility has evolved from the scientific requirements. This is the whole layout of the HIAF accelerator, it consists of superconducting ECR source, superconducting linac as injector, synchrotron booster, radioactive beam separator, and storage rings for in-ring experiments. ECR source is the next generation ECR source with high operation frequency, the superconducting linac can provide the highest intensity heavy ion beam for low energy research and synchrotron injection. The output energy is the about 17-22MeV, we keep the free space for update to 100MeV/u in the future. The central part of the HIAF facility is a synchrotron complex consisting of two rings. Both rings have near the same circumference and will be installed in the same tunnel.
The maximum rigidity of separator is 25Tm and the length is 180m, with this separator we can produce and separate the secondary beam, these secondary beam will be injected and accepted by storage system. For storage systems, first is SRing,

## Slide 4
Multi-function storage ring
Figure-8 shape ion-ion merging ring
Unprecedented heavy ion beam intensity
HIAF unique features
Notes: The HIAF project addresses a wide scope of scientific issues similar to the FAIR project of GSI, but with focus on different topics.
As I mentioned, HIAF will be a unique machine with unprecedented beam intensity for some new search field. How can HIAF provide unprecedented beam intensity and be a unique machine, now let me introduce the design concept and unique features of HIAF. First is

## Slide 5
SECRALII
24-28 GHz
FECRAL
45 GHz
100 kV HV
100 kV HV
HIAF requires source to deliver:
Pulsed 30 pμA
238U35+
CW 20 pμA
Ion source be able to produce:
Pulsed >50 pμA
238U35+
CW >30 pμA
Challenging !!
High intensity ion sources
Unprecedented heavy ion beam intensity

## Slide 6
Concepts for approaching the highest heavy ion intensity
BRing-N
Novel two planes painting injection scheme - 2.01011 ppp
Fast ramping rate operation mode- 3-5-10 Hz (12T/s dipole)
BRing-S
Innovative timing system of RF synchronization
5 times increase of intensity
1.01012 ppp
Barrier bucket stacking longitudinal
Unprecedented heavy ion beam intensity
BRing-S
BRing-N
Notes: Quite different from the FAIR of Germany, HIAF will use the superconducting Linac as the injector, the basic ideas for high intensity are: firstly a novel two planes painting injection scheme with the fast ramping rate mode in BRing-N, and secondly beam stacking from BRing-N to BRing-S with new barrier bucket technology .

## Slide 7
5 times increase of beam intensity through barrier bucket
Barrier bucket stacking
800MeV/u (238U35+)
2.0×1011
iLinac
5 times
Barrier bucket
BRing-N
BRing-S
2.3GeV/u (238U35+)
1.0×1012
Challenges:
Fast e-cooling for high energy heavy ion
High intensity effect of barrier bucket stacking
Momentum spread
Emittance
Intensity
Unprecedented heavy ion beam intensity
Innovative RF timing system
Notes: Then beam will be stacked longitudinal through from BRing-N to BRing-S, a new timing system of RF synchronization is designed, and

## Slide 8
HIAF First phase
Bring-N:
Circumference: 590 m
Rigidity: 34 Tm
Large acceptance (200/100)
Two planes painting injection
Fast ramping rate（3-5-10Hz）
iLinac: Superconducting linac
Length:80 m
Energy: 17~22 MeV/u(U35+ ~ 46+)
SECRAL and FECR
28-45GHz,
1.0emA(U35+- U46+)
SRing: Spectrometer ring
Circumference: 273m
Rigidity: 13-15 Tm
Electron/Stochastic cooling
Two TOF detectors
Four operation modes
L: 180m, Bρ: 25 Tm
HFRS
External target station
High Energy Density Physics
Nuclear Matter study-CEE
Hypernuclear
High energy irradiation
Low energy nuclear
structure terminal
HIAF: 2018-2024
Budget: 1.5+1.1 B CNY, approved
Bring-N: 0.8 GeV/A, 3×1010ppp

## Slide 9: Outline
Brief overview of HIAF
HIAF iLinac design
Key technology R&D
Summary

## Slide 10
HIAF iLinac Front End
SN：Solenoid
AM：Analyzing Magnet
DC：Diagnostic Chamber
Q：Quad
AT：Acceleration Tube
MM：Merge Magnet
CH：Chopper
BB：Beam Buncher
SL：Slits
100 kV Platform
100 kV Platform
SECRAL II
24-28 GHz
FECR
45GHz

## Slide 11
Ion Source Beam Requirements
Key Parameters from Ion Sources |  | 
 | HIAF | State of the Art and record
Ion | H2+~238U35+ | H2+~238U35+
Extraction Energy (keV/q) | 30~50 | 25~30
Total drain (emA) | 20~30 | ~10
Ion Beam Intensity CW mode (emA) | >1.5 (16O6+) > 1.5 (129Xe27+) > 1.5 (209Bi31+) >1.0 (238U35+) | 6.0 (16O6+) SECRAL ~ 1.0 (129Xe27+) SECRAL ~ 0.7 (209Bi31+) SECRAL ~0.32 (238U35+) VENUS
Transverse ε (π.mm·mrad) | εn, rms ≤ 0.20 & εn, 6rms ≤ 1.2 | εn, rms ≤ 0.20
Pulsed mode | Pulse length: 0.2~2.0 ms Repetition rate: 0.5~5 Hz | --
Energy Spread | Δp/p < ±5.0×10-3 | Δp/p < ±5.0×10-3

## Slide 12
To BRing
Phase I: 17-22 MeV/A
Phase II: 100-200 MeV/A
CW mode
Independent machine
Pulsed mode
BRing injector only
Parallel mode
BRing and experiments
16O6+ 1 emA
129Xe27+ 1 emA
209Bi31+ 1 emA
238U35+ 0.7 emA
16O6+ 2 emA
129Xe27+ 2 emA
209Bi31+ 1.5 emA
238U35+ 1 emA
0.3-5 Hz/0.2-2 ms
The world highest intensity CW HI linac
Challenge
- High intensity operation
- Switching from one to
another setting.
- Long-term reliability
iLinac operation mode

## Slide 13
High energy section
17MeV/u
SECR
LEBT
RFQ
Low energy section
0.5MeV/u
β =0.03
β =0.19
QWR cavity
β = 0.05
f = 81.25MHz
HWR cavity
β = 0.10
f = 162.5MHz
HWR cavity
β = 0.15
f = 162.5MHz
Design option of iLinac
Scheme1:QWR+HWR
Scheme2: Only QWR
High energy section
17MeV/u
SECR
LEBT
RFQ
Low energy section
0.5MeV/u
β =0.03
β =0.19
QWR cavity
β = 0.05
f = 81.25MHz
QWR cavity
β = 0.11
f = 81.25MHz
238U35+
238U35+

## Slide 14
Design Option of iLinac
High energy section
22MeV/u
SECR
LEBT
RFQ
Low energy section
1.0MeV/u
β =0.046
β =0.19
QWR cavity
β = 0.08
f = 81.25MHz
HWR cavity
β = 0.19
f = 162.5MHz
Scheme3: QWR+HWR
238U46+
Scheme4: Only QWR
High energy section
22MeV/u
SECR
LEBT
RFQ
Low energy section
0.5MeV/u
β =0.03
β =0.19
QWR cavity
β = 0.10
f = 81.25MHz
238U46+
NC IH-DTL
E: 1.5 MeV/A
f = 81.25MHz
238U35+
238U35+
SRF cavity option: Pure Nb cavity or Nb coating on Cu-cavity?

## Slide 15
Design ion | 238U35+
Frequency (MHz) | 81.25
Current (emA) | 2
Vane voltage (kV) | 70
Kilpatrick Coefficient | 1.55
Input/Output energy (MeV/u) | 0.014/0.5
Average Aperture (mm) | 5.805
Synchronous Phase | -45°~ -25.5°
Modulation Factor | 1.05~2.04
Length (cm) | 596.352
Transmission efficiency (%) | 97.2 @dW/W<5%
Input Nor. RMS. transverse emit (pi.mm.mrad) | 0.3/0.3
Output Nor. RMS. transverse emit (pi.mm.mrad) | 0.292/0.293
0utput 99.9% transverse emit (pi.mm.mrad) | 1.65/1.66
Output Nor. RMS. Longitudinal emit (pi.mm.mrad) | 0.098
Output 99.9% Longitudinal emit (pi.mm.mrad) | 1.407
Design of RFQ (1)
Notes: The design particle for RFQ is U,the beam current is 2mA. The vane voltage is 70 Kv in order to reduce the power consumption（功率损耗）。 Given the running stability and the RF condition(高频老练), the Kp is 1.55。 The RFQ acceptance study with different m and synchronous phase is done, when the m is 1.05 and the initial synchronous phase is minus 45 degree, the 83% particles going through the 3 harmonic buncher are in the linear acceptance of RFQ. So, we select the m of 1.05 and initial bucket synchronous phase of minus 45 degree. The RFQ length is 5.96m. (The 99.9% longitudinal emittance is 133 deg.kev/u,and the longitudial accetance of superconducting section is 1000 deg.kev/u)
Principle:Kp is inversely proportional to average pore size, and the focusing strength is inversely proportional to the square of the average pore size. So Kilpatrick coefficient less than 1.6
RFQ output longitudinal emittance can be accepted
Average radius is selected compromising KP and radial focusing strength
minimize the length
The input energy of the RFQ is selected compromising the LEBT and RFQ, RFQ need a low energy so that bunching as fast as possible, but the space charge will be very strong at low energy section.

## Slide 16
Parameters of the final model | value
Frequency (MHz) | 81.261
Q factor | 17963
Nearest dipole mode frequency (MHz) | 86.827
Total Power (kW) | 56.76
Power loss per length (kW/m) | 8.945
Max temp rising (deg) | 2
Design of RFQ (2)

## Slide 17
Beam line between RFQ and SC :
  Design with 2 emA @0.5 MeV/u
  6 quadroples and 2 bunchers for transverse and longitudinal matching.
  Enough diagnostics for the re-initialization of beam
Design of MEBT
Point to initial beam
D-Box
Notes: this is the acceptance of rfq，83% percent particles are in the acceptance of RFQ
The normalize rms emittance at different position are listed ：before the buncher，entrance of RFQ and exit of RFQ. The whole transmission efficient is 75 percent and the transmission efficient of rfq is 90 percent. the matching work is optimizing.

## Slide 18
 | Unit | QWR008 | HWR019
f | MHz | 81.25 | 162.5
Vmax | MV | 2.0 | 2.5
Ep | MV/m | 32 | 32
Q0 | E+09 | 8.00 | 5.00
M/C |  | 8/8&4/7&3/7 | 3/7
CM | number | 4 | 5
M:magnet C:cavity CM:croymodule
1.0 MeV/A
RFQ
81.25MHz
81.25MHz
QWR008
7/8 cavity
4 CM
162.5MHz
HWR019
8 cavity
5CM
238U46+
0.014MeV/u
238U46+
22MeV/u
8MeV/u
71.3 m
Design of the iLinac for scheme 3

## Slide 19: Lattice design of iLinac
Cavity Type 1 | 
Cavity type / β | QWR / 0.05
Frequency(MHz) | 81.25
NO of cavity/CM | 29 / 4
NO of solenid | 18
Vacc@Epeak=32MV/m | 1.4
Cavity Type 2 | 
Cavity type / β | QWR / 0.11
Frequency(MHz) | 81.25
NO of cavity / CM | 35/ 5
NO of solenoid | 15
Vacc@Epeak=32MV/m | 2.5
Total length （m） | 71.3
~8.4m
sol
CAV
sol
CAV
sol
CAV
sol
CAV
sol
CAV
sol
CAV
sol
CAV
sol
CAV
QWR008
section
sol
CAV
CAV
sol
CAV
CAV
sol
CAV
CAV
sol
CAV
HWR019
section
sol
CAV
CAV
CAV
CAV
sol
CAV
CAV
sol
CAV
~6.97m
~7.36m
sol
CAV
CAV
CAV
CAV
sol
CAV
CAV
sol
CAV
~7.44m

## Slide 20
Lattice design
TraceWin program is used for beam dynamics
Solenoid is 3D field ,cavity is 1D field
Using Gaussian distribution.
  6d Gaussian with100000macroparticles for the entrance.
  Normalized rms emittance in x/y/z: 0.2π.mm.mrad / 0.2π.mm.mrad / 0.126π.mm.mrad.
QWR008
HWR019

## Slide 21
Lattice design
Epeak per cavity
Synchronous phase of cavities
Energy
Gradient of solenoid

## Slide 22
Lattice design
Beam power
Period phase advance<90deg
Phase advance per meter smooth
RMS envelop smooth

## Slide 23
Multiparticle simulation
Aperture/beam size>2
Max emit growth_X:4.5%
Max emit growth_Y:3.5%
Max emit growth_Z:37.6%
RMS emit growth_X:0%
RMS emit growth_Y:0%
RMS emit growth_Z:2.4%

## Slide 24: Outline
Brief overview of HIAF
HIAF iLinac design
Key technology R&D for iLinac
  Ion source
  RFQ
  SC linac
Summary

## Slide 25
4th G.
O6+
Ar12+
Xe27+
U34+
2nd G.
3rd G.
6.4~18 GHz
24~28 GHz
40~60 GHz
Caprice
ECR4
AECR-U
SERSE
GTS
LECR3
…
VENUS (LBNL)
SECRAL (IMP)
SuSI (MSU)
SCECR (RIKEN)
FRIB ECR (MSU)
…
10 eμA — 100 eμA — 1 emA
45GHz FECR
at IMP only
Highly charged ECR ion source
Past, present and future

## Slide 26
总体设计
理论模拟
400MeV/u@1MW 重离子
RFQ is utilized as a low energy front-end accelerator
for high intensity ion beam
Beam match
Transversal
focusing
Longitudinal
bunching
Acceleration
RFQ accelerator for high intensity ion beam
Integrated into one cavity

## Slide 27
No any CW proton RFQ with current >3 mA in routine operation
No any CW heavy ion ( > Ar) RFQ with current
>10 pµA in routine operation
No any CW proton SC linac with current > 1 mA in routine operation
No any CW heavy ion ( > Ar) SC linac with current > 10 pµA in routine operation
Status of high intensity CW ion RFQ and SC linac
Up to now in the world

## Slide 28
LEAF Layout---HIAF iLinac front-end R&D
45GHz FECR
Power Supplies
HV platform
6m×4m
Irradi-Material
RFQ
L= 6 m
LEBT
MEBT
Atomic Physics
Irradi-Material
Dedicated to
mA heavy ion beams

## Slide 29
Microwave | 45 GHz/20 kW
Magnet conductor | Nb3Sn
Axial fields（T） | 6.5/1.0/3.5
Sextupole field （T） | 3.8@r=75 mm
Maximum field（T） | 11.8 T
Magnet bore（mm） | Ø161~165
Extraction （kV) | 50
Typical beam | 1.0 emA U35+
The world first 45 GHz ECR ion source
45 GHz FECR
H.W. Zhao, et.al. RSI, (2018)

## Slide 30
COIL-PACK
SUBASSEMBLY
COLLARS
SEXTUPOLE
COILS
AXIAL-LOAD
END PLATE
SUBASSEMBLYS
SOLENOID
STRUCTURE
SUBASSEMBLY
SHELL-YOKE
SUBASSEMBLY
(Shell is strain gauged)
MASTER-KEY PLATES
BLADDER
SUBASSEMBLY
LOAD-KEYS
YOKES
YOKE-SHELL
ALIGNMENT PINS
AXIAL RODS
(Strain Gauged)
COIL END
BLOCKS
FECR Nb3Sn magnet mechanical structure
The magnet mechanical structure was designed by
collaboration with ATAP magnet group at LBNL
This Nb3Sn magnet is being built in China

## Slide 31
Key technology R&D for FECR Nb3Sn magnet
Bladder & Keys
Coil prototype
Quench protection
2.2W@4.2K GM
Cryo-cooler test

## Slide 32
FECR Nb3Sn magnet prototyping

## Slide 33
Laser ion source for HCI
CSD for different heavy ions
Ni beam reproducibility < 2%
The world best performance

## Slide 34
LEAF key components
LEAF components: LEBT, HV platform, RFQ
RFQ accelerator, first beam Feb. 9, 2018
45 GHz/20 kW gyrotron system
81.25 MHz/60 kW solid-state amplifier
RFQ: CW 200 µA He1+ , 98% efficiency, E: 0.497 MeV/A

## Slide 35
总体设计
理论模拟
CW RFQ accelerators for high intensity ion beam at IMP
2.1 MeV/162.5 MHz, CW proton 10 mA,
2011-2014, collaborated with LBNL
0.5 MeV/A 81.25 MHz,
CW 238U35+, 1 emA, 2015-2018
ADS CW RFQ
CMIF CW RFQ
1.5MeV/A, 162.5 MHz,
CW 10mA, H2+/D+, 2015-2018
LEAF CW RFQ
0.142MeV/A, 53.667 MHz,
CW 50-200 µA, O-Ar-Bi, 2013-2016
SSC CW RFQ

## Slide 36
ADS RFQ 2.1 MeV/CW proton 10 mA
Total operation time is ~3000 hours
including CW@10mA around 10 hours
The world highest beam intensity for currently operating CW proton RFQ.
CW 10mA@ 2 hours
CW 6mA@5hours

## Slide 37
LEAF RFQ rf power conditioning
75 kW/70 kV
LEAF RFQ 0.5 MeV/A--81.25 MHz

## Slide 38: Beam commissioning of LEAF-RFQ
RFQ CW commissioning @ 200 eμA He1+
Beam current @ 100 eμA at FC
RFQ vacuum
2E10-6 Pa
1.9E10-5 Pa
6 Hr
RFQ Vane temperature
RFQ wall temperature
Transmission efficiency ~ 98.5%
Acceleration efficiency ~ 46.5%
Beam energy 0.497±0.001 MeV/u
@ without MHB
He1+
Notes: Vacuum went bad because of leakage of a pickup.

## Slide 39: Beam commissioning of LEAF-RFQ
TRACK simulation
Measurement
@ slit+slit+FC
Transverse emittance after RFQ
0.08 π.mm.mrad
0.078 π.mm.mrad
0.074 π.mm.mrad
0.062 π.mm.mrad

## Slide 40
162.5 MHz HWR010
3
ECRIS + RFQ + CM1 + CM2
Energy is ~10 MeV
First beam September , 2016
2
ECRIS + RFQ + TCM6
Energy is ~5 MeV
First beam June 6th, 2015
162.5 MHz HWR010
1
ECRIS + RFQ + MEBT + TCM1 (single HWR)
Energy is ~2.5 MeV
First beam October, 2014
162.5 MHz HWR010
SC proton linac development at IMP
2011-2016

## Slide 41: 25 MeV SC proton linac with 4 CM
 | CM1/IMP | CM2/IMP | CM3/IMP | CM4/IHEP
Frequency | 162.5 MHz | 162.5 MHz | 162.5 MHz | 325 MHz
Energy | 6 MeV | 11 MeV | 18.6 MeV | 26.2 MeV
Type | HWR010 | HWR010 | HWR015 | Spoke021
Number | 6 | 6 | 5 | 6
First beam was achieved on May, 2017.
The energy is up to 26.2 MeV
The world’s first 10-25 MeV CW proton superconducting linac
IMP+IHEP
162.5 MHz Taper HWR
162.5 MHz
CW RFQ
2.45 GHz
ECR source

## Slide 42
CW 4 mA/4.6 MeV/40min. Beam Demonstration

## Slide 43: CW Beam Commissioning of 10-25 MeV
140~200uA
CW 25 MeV@0.15 mA, >2 min.
CW 18 MeV@0.2 mA，>80 min. no trip
The most challenging is the long-term reliability without beam trip
CW 10 MeV@1-2 mA, ̴30 min.

## Slide 44: Summary
HIAF will be one of the next-generation world leading heavy ion facility for advances in nuclear physics and related research fields, which requests high intensity highly-charged ion source and heavy
ion linac as an injector.
To reach a better performance-cost effective design, iLinac should be carefully optimized and finalized. Prototyping cavities are being developed.
Baseline design of HIAF ion source and iLinac was defined which can meet HIAF initial operation.
The world first 45GHz FECR is being developed, will meet HIAF requirement for high intensity of those very heavy ion beams.
Four CW proton and heavy ion RFQs were built at IMP in the past years which have demonstrated
high intensity CW ion RFQ performance and technology, also a solid basis for HIAF RFQ.
As baseline design, HIAF iLinac can utilize the HWR cavities developed for ADS linac, which already
demonstrated good performance through 5-25 MeV proton beam commissioning, that is the world
first demonstrations of CW 1-2 mA/10 MeV and CW 25 MeV proton superconducting linac. These
development may guarantee success of HIAF iLinac.
However, very challenging for 45 GHz FECR, reliable and stable operation of HIAF-iLinac with expected high intensity beams.

## Slide 45
Thank you very much for your attention !

## Slide 46
SECRAL Beam Emittance
εn.rms.1 emA~0.2 π.mm.mrad
Emittance control is necessary in LEBT
Higher emittance with higher beam intensity, but ε increasing not so significantly.
Supported by SECRAL tests

## Slide 47
Beam long-term stability at high RF power
O6+ 3.3 mA at 3.5 kW—2 hours
28+18 GHz
SECRAL II
SECRAL
Bi31+ 329 eµA at 3.7 kW—2.5 hours
For accelerator operation, long-term
operation (days) at high microwave
power (> 5kW) for the 3rd G ECRIS need
to be demonstrated.

## Slide 48
FECR key parameters
FECR key parameters and goal
129Xe30+ | >1000 μA
129Xe45+ | > 50 μA
209Bi31+ | >1000 μA
209Bi55+ | > 50 μA
238U35+ | >1000 μA
238U41+ | > 200 μA
238U56+ | > 30 μA
FECR expected beams
and intensities
Microwave | 45 GHz/20 kW
Magnet conductor | Nb3Sn
Axial fields（T） | 6.5/1.0/3.5
Sextupole field （T） | 3.8@r=75 mm
Maximum field（T） | 11.8 T
Magnet bore（mm） | Ø161~165
Extraction （kV) | 50
Typical beam | 1.0 emA U35+

## Slide 49
 | 238U35+ | 238U46+ | 238U55+
Einj（MeV/u） | 1.3 | 1.3 | 1.3
Eout（MeV/u） | 100 | 100 | 100
Design Imax（emA） | 1.0 | 1.0 | 1.0
Cavity Families | HWR009+HWR015+ Spoke021 | HWR009+HWR015+ Spoke021 | HWR009+HWR015+ Spoke021
Cavity Quantity | 44+100+248=392 | 40+92+176=308 | 32+80+152=264
SC-Solenoid | 78 | 65 | 55
CRM Reduced |  | 11 | 16
Total length（m） | 288 | 225 | 197
Budget reduced* |  | >70 M$ | >100 M$
Budget estimate for 100 MeV/u SC-Linac
*not including MP and infrastructure
E～Q2 for Cyclotrons, E～Q for Linac
Ion source determines beam intensity of an accelerator
Why we need high charge state ion beam
Developing intense highly charged ion source is both
performance-effective and cost-effective.

## Slide 50
No any existing ion source is able to fully reach the requirements
proposed by those accelerators in terms of beam intensity and
long-term stability.
Only SECRAL/IMP and VENUS/LBNL can partially reach the beam
intensities, but long-term mA intensities of highly-charged ions
have not yet been demonstrated (days and weeks).
The only solution is to produce higher beam intensity and higher
charge state heavy ion beams by ion source.
Ion source will have to be operated at 50-70% maximum intensity
in order to achieve good long-term reliability.
HCI ion source status and challenge
HIAF requires source to deliver:
Pulsed 30 pμA
238U
CW 20 pμA
Challenging !!