## Slide 1: Web Service for the Trajectory Analysis of Laboratory Animals in the «Morris Water Maze» based on deep learning algorithms
Bezhanyan T.Zh. 1,2, Streltsova O.I.1,2, Stadnik A.V. 4, Shadmehri S.1, Podgaynii D.V. 1, Zuev M.I.1, Bondarev M.Yu. 1,2,
Nechaevski A.V. 1,2, Kolesnikova I.A.2,3, Severiukhin Y.S.2,3
GRID 2025
7-11 July 2025
DUBNA
1 Meshcheryakov Laboratory of Information Technologies JINR, Dubna, Russia
2 Dubna State University, Dubna, Russia
3 Laboratory of Radiation Biology Joint Institute for Nuclear Research, Dubna, Russia
4 NN Sputnik
The research was carried out within the state assignment of Ministry of Science and Higher Education of the Russian Federation
(theme No. 124112200072-2).

## Slide 2
«Morris Water Maze» behavioral test
Mouse/rat | Latency time
Ionizing radiation | Travel distance
Up 2 groups (each group contains up to 10 rodents) | Speed
2 stages (before irradiation and after irradiation on the 30th and 90th days) | Finding the platform
Each stage takes 5 days | trajectory
Every animal being tested 3 times per day | Classification task
~450 Video files
60 seconds
2

## Slide 3
Goal
Developing the Web Service for the Trajectory Analysis of Laboratory Animals in the «Morris Water Maze» based on Deep Learning Algorithms
3

## Slide 4: 01 02 03 04 Object tracking problems
Movable background, changeable lighting
Different conditions for each video/experiment (water reflection, size of lab. animal)
Determination of the beginning of movement of a laboratory animal
Problem with detecting moving (floating) object
4
450
Video data

## Slide 5
Median image construction
Filtering
Hough transformation
Finding external boundary
Finding internal boundary
Finding platform location
Setup field marking
5

## Slide 6: Object tracking
Step 1
Computer vision algorithms
Setup field marking
Finding object contour
Step 2
Local tracking
Detect an object on the first frame
Determine local area centered on the point of the object`s CM
Detect the object in the next frame
Step 3
Construction the trajectory
Superimposed it to a video file and saving as an image
Step 4
Created Data set
For further classification tasks
6

## Slide 7: Prototype of Web service for «Morris Water Maze» behavioral test
0 | Characteristic | Value
1 | Total time traveled (sec) | 60.97
2 | Total distance (cm) | 5400.26
3 | FPS | 30
4 | Speed (cm/s) | 88.58
5 | First frame | 26
6 | Last frame | 1855
7 | Finding platform | No
7

## Slide 8
New ~1500 video data, <2% object is lost, ~97% object tracking (~61% is from the first frame, ~37% must select the starting frame)
~2%
37%
61%
Deep learning algorithms for
MORRISS WATER maze
01
Neural Network architecture Yolo11 for object tracking
02
Classification task – based on Convolutional Neural Network
03
Web service for analyzing video data
8
1500
Video data

## Slide 9
CVAT – for data annotation
01
Deep learning model Yolo11 for object detection
9
mAP50(B) – computed over bounding boxes; evaluates how accurately the model localizes objects with rectangles (reflects the effectiveness of object detection and localization)

## Slide 10: Results for deep learning algorithm YOLO11
01
10

## Slide 11: Classification task CNN Web service for the Trajectory Analysis of Laboratory Animals in the «Morriss Water Maze» behavioral test
8 class
7 class
With an increase the number of epochs, the accuracy drops, due to the fact that the model begins to «remember» the images of the training sample
02
1. Direct path
2. Direct search
3. Indirect search
4. Focal search
Classification for 8 class
5. Chaining
6. Scanning
7. Random search
8. Thigmotaxis
11

## Slide 12: Web Service for the Trajectory Analysis of Laboratory Animals in the «Morris Water Maze» based on deep learning algorithms
03
12

## Slide 13
We are developing Web Service for the Trajectory Analysis of Laboratory Animals in the «Morris Water Maze» based on deep learning algorithms
Developed and tested algorithm for trajectory construction based on computer vision algorithms
Developed prototype of Web service for «Morris Water Maze» behavioral test
Created a dataset for classification task
Developing an algorithm for trajectory construction based on deep learning algorithms
Results

## Slide 14: Thanks for your attention
Authors acknowledge the support of the JINR Multifunctional Information and Computing Complex
for providing computational resources http://hlit.jinr.ru/
11th International Conference "Distributed Computing and Grid Technologies in Science and Education" (GRID’2025) 7–11 July 2025