## Slide 1: Automation of BM@N Run9 data processing on a DIRAC distributed infrastructure
Konstantin Gertsenberger, Igor Pelevanyuk
LHEP
MLIT
AYSS Alushta-2025

## Slide 2: What do we have from BM@N run8
DIRAC distributed infrastructure
RawToDigi
DigiToDst
DIGI
DST
Files: 31306
Size: 436 TB
Jobs: 31306
Size: ~ 25 TB
Jobs: 31306
Size: ~ 66 TB
Input
2. Configure production
Config
3. Form executable
Job.sh
4. Launch jobs
1. Form input file list
Production Manager
Register data
Test software
Launch distributed processing
Detect issues, Analyze performance
Full run8 data production takes around 8 days!
Standard production flow:
1 file: ~14 GB
1 job: ~1 hour
1 file: ~0.8 GB
1 job: ~12 hour
1 file: ~2.2 GB
Total values:
Per file values:

## Slide 3: Why to automate run9 data processing?
Not to save time – data taking happens not so often.
Not to avoid errors – we do not encounter them during jobs submission.
But to reliably deliver data for physics analysis as soon as we can during data taking!

## Slide 4: Transformation system
All components were installed and tested.
Transformation agent
InputData agent
WorkflowTask agent
TransformationDB
Transformation Manager
Detect new files
Submit new jobs
Keep track of transformations
Interface to DB
Transformation is a mechanism in DIRAC to start job when new file appear.
The code of WorkflowTask agent was changed in order to pass input file name as a parameter to the job.

## Slide 5
Runs on DIRAC server
Job.sh
2. Configure production
Transformation task
JOB N
Job.sh
inputN
JOB 2
Job.sh
input2
JOB 1
Job.sh
input1
Config
Config
3. Form executable
Job.sh
4. Setup transformation
1. Form input query
5. Jobs initiation and submission to queue
Production Manager
Automated approach
Special transformations were developed to initiate jobs:
RawToDigi – when RAW file appears this job:
Download RAW file.
Generate DIGI from RAW file.
Upload DIGI to storage system.
Upload DIGI to NICA cluster.
DigiToDST – when DIGI file appears this job:
Download DIGI file.
Generate DST from DIGI file.
Upload DST to storage system.
Upload DST to NICA cluster.
Run only on Tier1.
Govorun and NICA cluster are also possible as a fallback solution.
Run only on Tier2.
Govorun, NICA cluster, Tier1 are possible as fallback solution

## Slide 6: Automation schema
RawToDigi
MLIT EOS
MLIT CTA
DIRAC FileCatalog
New raw file discovery
DIGI
New digi file discovery
DigiToDst
DST
EOS NCX
1
2
3
Detection of a new files rely on the files meta data
RawToDigi query: {type=raw, run_number=9}
DigiToDst query: {type=digi, run_number=9}
For 1 file – 1 job is started

## Slide 7: Corner cases
What if jobs profile change from run8?
Do not activate automation until we check RawToDigi and DigiToDst jobs.
What if RAW file size will be enormous, like 100 GB?
Do not submit jobs automatically for files bigger than 16 GB.
What if one of computing resources is not sustaining the load or unavailable for any reason?
Do not restrict job submission to a computing resource, but rather require
resource to have a special tag: rawtodigi, digitodst.
With that approach it is possible to change destination of waiting jobs manually.

## Slide 8: Simulation of job execution during Run9
Parameters
Simulation system
Results
Written in Python to predict CPU, RAM, network and disk load.
Uses data about performance of resources integrated in DIRAC
It is used to check the behavior of DIRAC jobs in real infrastructure.
Simulation is done every second, but period may be increased for speeding up simulation.
InfluxDB is used for results storage and visualization.
Task
Job
Worknode
Cluster
Storage
Controller
JobQueue
Monitoring
Pelevanyuk, I.S., Campis, D. Simulation of Job Execution in Distributed Heterogeneous Computing Infrastructures. Phys. Part. Nuclei Lett. 20, 1276–1278 (2023). https://doi.org/10.1134/S1547477123050618

## Slide 9: BM@N Run8 data taking
Total raw size ~ 436 TB
Total files: 31306

## Slide 10: Simulation plots
What if previous data taking was automated?
Data rate from Run8 was taken analyzed and used to simulate the same data flow to the system.

## Slide 11: Simulation plots
What if the intensity doubled?
Occasional queues during most intense data taking periods.
Solution: allow Tier1 to process part of DigiToDst jobs

## Slide 12: Conclusion
Meaningful metadata information was introduced.
Automation schema was developed and tested.
Basic simulation was performed.
Now waiting for data taking.
Thank you for attention!