## Slide 1: Calculation of self-shielding correction for Neutron activation experiments at IREN facility using PHITS and MCNP6

## Slide 2: Neutron self-shielding factors?
The Neutron self-shielding Factor is a correction factor that accounts for the effect of neutron absorption within the activation sample itself, which causes the neutron flux inside the sample to be non-uniform compared to the external flux.
The self-shielding effect depends on several factors:
neutron absorption cross-section of the element,
sample’s shape,
elemental composition
is strongly influenced by the spatial and energy distribution of the neutron field
This effect must be calculated separately for thermal and epithermal neutrons due to their distinct energy distributions.

## Slide 3: IREN Converter Structure
Electron beam
Tungsten target to produce Neutron
Fill with water to slow down neutrons
Aluminium

## Slide 4
Fig 2a: The reaction rate calculated for 63Cu at 5cm position
Fig 2b&c: Neutron flux distribution
Neutron flux distribution in IREN

## Slide 5
(1)
)(2)
En is neutron energy
k is the Boltzmann constant
T is average neutron temperature
α is the epi-thermal spectrum shape parameter
Neutron energy spectrum regions
Fig 3: Neutron flux spectrum through surface 1x1cm at 5cm position

## Slide 6
Author, year | Neutron source geometry | Neutron energy spectrum | Specimen geometry | Specimen material | Evaluated G-factor
Salgado et al., 2004 | // beam, iso. field | Epithermal (monoenergetic, 1/E) | Foil | 232Th, 197Au and 56Fe | Gres, Gres*
Goncalves et al., 2002; Goncalves et al., 2001* | // beam, iso. field | Around resonance region (1/E) | Foil, wire | 59Co, 63Cu, 197Au, 115In, 55Mn, 185Re | Gres
Goncalves et al., 2001** | // beam, iso. field | Epithermal, around resonance region (1/E) | Foil, wire | Au, Co, Mn | Gres
Goncalves et al., 2004 | // beam, iso. field | Around resonance region (1/E) | Cylinder | 59Co, 63Cu, 197Au, 115In, 55Mn, 185Re | Gres
Martinho et al., 2003 | iso. field | Around resonance region (1/E) | Foil, wire, sphere | 59Co, 63Cu, 197Au, 115In, 55Mn, 185Re | Gres
Martinho et al., 2004 | iso. field | Thermal (Maxwellian) | Foil, wire, sphere, cylinder | Al, Au, Cd, Co, Cu, Eu, Gd, In, Ir, Mo, Ni, Pb, Pt, Rh, Sc, Sm, Ta | Gth
This work | Spatial and spectral fidelity to the electron-beam-driven neutron source |  | Foil | Au, Cu, W, Zr | Gth, Gepi
Neutron self-shielding factors
Table 1: Comparative reports on calculating G-factors for diverse parametric conditions using MCNP simulations

## Slide 7: Neutron self-shielding factors
The G-factor is defined as the ratio of the reaction rate in the actual sample to that in an infinitely diluted sample (Goncalves et al., 2002):
(3)
ф(E) and ф0(E) are the neutron flux energy distributions in the actual and infinitely diluted sample, respectively;
E1 and E2 define the integration bounds (for Gth: E1 = 10-3 eV and E2 = 0.5 eV; for Gepi: E1 = 0.5 eV and E2 = 0.2 MeV);
σ(E) is the energy-dependent (n, γ) reaction cross-section.
Foil | Density (g/cm3) | Dimension (mm) | Isotopes
Au | 19.32 | 10x10x0.1 | 197Au (100%)
Cu | 8.96 | 10x10x0.5 | 63Cu (69.15%), 65Cu (30.85%)
W | 19.3 | 10x9x0.35 | 180W (0.12%), 182W (26.5%), 183W (14.31%), 184W (30.64%), 186W (28.43%)
Zr | 6.51 | 10x9x0.1 | 90Zr (51.45%), 91Zr (11.22%), 92Zr(17.15%), 94Zr (17.38%), 96Zr (2.8%)
Table 2: Samples used in experiments and simulations

## Slide 8: Transmission function (ф/ ф0(E))
a)Au
c)W
b)Cu
d)Zr

## Slide 9: Results & Discussion
Table 3: Comparison of Neutron self-shielding factor results from 2 simulations
Isotopes | Gth |  |  | Gepi |  | 
 | PHITS | MCNP | Diff_Gth | PHITS | MCNP | Diff_Gepi
197Au | 0.962±0.006 | 0.974±0.004 | 1.2% | 0.337±0.009 | 0.360±0.001 | 6.3%
63Cu | 1.018±0.016 | 1.026±0.014 | 0.8% | 0.979±0.030 | 0.988±0.009 | 1.0%
94Zr | 1.003±0.014 | 1.006±0.007 | 0.2% | 1.004±0.043 | 1.007±0.006 | 0.4%
96Zr | 1.003±0.007 | 1.006±0.005 | 0.2% | 1.001±0.076 | 1.009±0.004 | 0.7%
186W | 0.982±0.007 | 0.989±0.004 | 0.7% | 0.496±0.016 | 0.541±0.002 | 8.4%

## Slide 10
Fig: Comparison of neutron section between ENDF and JENDL
Results & Discussion
a)
c)
b)
d)

## Slide 11
Formula to determine Thermal neutron cross-section σ0 as follows:
(6)
σ0,Au = 98.65 ± 0.09 barn
Rx and Rx,Cd are reaction rates per atom for isotope in bare and Cd-covered
Fcd is cadmium correction factor
gx is Westcott factor correction
Gth is thermal neutron self-shielding factor
Thermal neutron cross-section

## Slide 12: Resonance integral
Formula to determine Resonance integral :
(7)
= 1550 ± 28 barn
Rx and Rx,Cd are reaction rates per atom for isotope in bare and Cd-covered
Fcd is cadmium correction factor
gx is Westcott factor correction
Gth is thermal neutron self-shielding factor
Ge is epi-thermal neutron self-shielding factor

## Slide 13
Results & Discussion
Fig a: Comparison of neutron cross-section σo of 186W(γ,n)187W reaction
This work: σo = 40.659 ± 1.936 (barn)
Fig b: Comparison of resonance integral Io of 186W(γ,n)187W reaction
MCNP: Io = 417.50 ± 36.796 (barn)
PHITS : Io = 406.75 ± 36.796 (barn)
Difference: 2.6%

## Slide 14: Conclusion
PHITS v3.21 uses JENDL-4.0 nuclear data library (Shibata et al., 2011).
MCNP6.1 uses ENDF/B-VII.1 (Kulesza et al., 2022).
The Gth values obtained from the two computational codes show a discrepancy of less than 1.2%, indicating good agreement and reliability of the results.
The observed differences in neutron self-shielding factors in the epithermal region, particularly for 197Au (6.3%) and 186W (8.4%), are primarily caused by significant difference in the neutron cross sections between the nuclear data libraries employed.
Results and calculations are still being updated.

## Slide 15: THANKS FOR YOUR ATTENTION

## Slide 16: Transmission function (ф/ ф0(E))
a)Au
b)Cu
In the /0(E) spectrum of gold  a high neutron absorber (Fig.a), a pronounced dip (/0 = 0.08) occurs at the energy groups of 4.75–5.0 eV, corresponding to the strong resonance absorption of 197Au (27103 barns at 4.9 eV) (Shibata et al., 2011). Depression in the thermal energy region reflects the dominance of absorption cross-section over that of scattering ( > s) herein.
In the /0(E) spectrum of copper (Fig.b), minimal spectral variation is observed except near 1.9–2.1 keV, where /0 peaks at 1.42 (1.9–2.0 keV) before declining to 0.85 (2.0–2.1 keV). As a neutron scatterer (s > ) (Shibata et al., 2011), this behavior arises from resonance self-shielding, whereas neutrons near resonance energies undergo multiple scattering, delaying absorption until energy loss shifts them below resonance thresholds (Goncalves et al., 2002).

## Slide 17: Transmission function (ф/ ф0(E))
c)W
d)Zr
The transmission spectrum /0(E) for tungsten (Fig.c) exhibits complex energy-dependent behavior due to contributions from its isotopic composition (180W, 182W, 183W, 184W, and 186W). Pronounced dips in /0, attributed to resonance absorption, occur at the energy groups of 4.04.25 eV (/0 = 0.33), 1819 eV (/0 = 0.36), 1920 eV (/0 = 0.38), 2021 eV (/0 = 0.59), and 2122 eV (/0 = 0.54). Localized increases in /0, similarly to copper’s behavior, arise from neutron scattering moderation effects prior to absorption below resonance energies.
For zirconium (Fig.d), /0  1 across all energy groups, indicating negligible self-shielding. This neutrality stems from zirconium’s low absorption and scattering cross-sections. A 0.1 mm zirconium foil thus introduces minimal perturbation to the neutron field, validating its use as a reference material in irradiation geometries where self-shielding corrections are unnecessary.

## Slide 18
Neutron self-shielding factor in isotropic neutron field
Table 2: Comparison of Neutron self-shielding factor in isotropic neutron field
Isotopes | Gth |  |  | Gepi |  | 
 | MATSSF Code (Trkov et al. 2009) | MCNP | Diff_Gth | MATSSF Code (Trkov et al. 2009) | MCNP | Diff_Gepi
197Au | 0.8837±0.0084 | 0.8648±0.0242 | 2.1% | 0.2142±0.009 | 0.2777±0.0123 | 22.8%
94Zr | 0.9997±0.0015 | 0.9975±0.0032 | 0.2% | 0.9812±0.0018 | 1.0062±0.0223 | 2.5%
96Zr | 0.9997±0.0015 | 0.9975±0.0032 | 0.2% | 0.9773±0.0018 | 0.9972±0.0715 | 2.0%
186W | 0.9168±0.0017 | 0.9120±0.0192 | 0.5% | 0.2524±0.0023 | 0.3588±0.0215 | 29.7%

## Slide 19
(4)
(5)
Rth,x and Re,x are reaction rates per atom for isotope in the thermal and epi-thermal energy regions of neutrons
Reaction rate