## Slide 1: Quench protection and monitoring systems for pulsed HTS inductive energy storage SMES Ilya Donguzov on behalf of the team

## Slide 2
2
SMES
Purposes:
Decreasing pulsations of superconducting magnets operating current
Reducing inductive load influence to the city’s power grid
Minimizing of energy consumption
Parameter | Value
Inner diameter | 400 mm
Outer diameter | 960 mm
Height | 900 mm
Number of layers | 14
Operating current | 6.7 kA
Inductance | 120 mH
Stored energy | 2.74 MJ
Operating temperature | 30 K
Refrigerant | Neon
SMES (Superconducting Magnetic Energy Storage)

## Slide 3
Purposes:
Testing technologies of production and assembling of such type HTSC solenoids.
Achieving the same proportions of mechanical deformations like at SMES
3
Model SMES
Parameter | Value
Inner diameter | 290 mm
Outer diameter | 459 mm
Height | 500 mm
Number of layers | 4
Operating current | 13 kA
Inductance | 1,79 mH
Stored energy | 163 kJ
Operating temperature | 4.5 – 50 K
Refrigerant | Helium
Model SMES
The assembly consistency of one section of the model solenoid
7

## Slide 4
Cu-Ni tube
Brass tape
HTSC tape (SuperOx)
Kapton tape
Fiberglass tape
HTSC cable SMES
Nuclotron type tubular cable – created in 1979 and first tested in 1980 at JINR
Cu-Ni tube
Strands of the superconductor
Ni-Cr wire
Kapton tape
Fiberglass tape
4
HTSC cable
Winding HTSC tapes on a tube
Cable machine
HTSC cable

## Slide 5
Monitoring and protection systems
5-channel temperature monitoring system
Power sources and ADC for strain gauge system
Quench Protection System for HTS cables
Backup Protection System
5

## Slide 6
Voltage output circuit for the model solenoid
6
Electrical connection of the cable

## Slide 7
cRIO-9057
7
Quench detection system
ADC NI-9202
± 10В
ADC NI-9238
± 0.5В
Current sensor LEM ITZ - 16000
Energy evacuation switch
Current source
MOXA
PC
DAC NI-9263
± 10В
Current value
Energy evacuation signal
Layers
RS-485
Ethernet
Current leads, bridges
Model SMES
Booster
Nuclotron
Booster
Nuclotron

## Slide 8
8
Software
The real-time system enables program execution with guaranteed response time.
The system is implemented using a finite state machine (FSM) pattern - this allows describing the system's behavior through a finite set of states and transition rules between them.
The FPGA provides hardware-level high-speed operation, enabling parallel signal reading and generation with minimal latency

## Slide 9
9
Thermometry system
Measuring range: 4 - 300 K;
Accuracy: ± 0,3 % in the range up to 30 K;
Number of voltage measurement channels: 8;
ADC bit rate: 24 bits;
Built-in current source: 10, 100 мкА;
Supply +24 DC / PoE.
5-channel temperature monitoring system
Current source +
Current source -
Chanel 1 +
Chanel 1 –
Chanel 2 +
Chanel 2 –
Chanel 8 +
Chanel 8 -
Connections of temperature sensors

## Slide 10
At a deformation of 0.1%, a resistance change of 0.735 Ω at room temperature will follow
Operating temperature range - -269 - +250 ⁰С
Rated resistance - 350 Ω
The length of the measuring grid - 1 mm
The width of the measuring grid - 1.6 mm
10
Strain gauge system
Solenoid surface
Hall
Sensor
CFLA
PT-1000
Power supply
R_fixed
R_fixed
R_fixed
Amplifier
ADC
Magnetic field calibration of strain sensors in cryogenic environments
Algorithmic correction of magnetic field artifacts and temperature-induced errors
PC
STRAIN GAUGE
CFLA-1-350-17
Software interface of the strain measurement system

## Slide 11
Conclusion
11
A system to protect the HTS cable from quench has been developed. Currently, it is undergoing debugging and testing. The system will be ready for operation at the autumn of 2025.
A temperature monitoring system has been developed and is ready for operation.
The functional diagram of the strain measurement system has been developed. System testing is scheduled for summer 2025, with deployment expected by autumn of 2025.

## Slide 12: Quench protection and monitoring systems for pulsed HTS inductive energy storage SMES Ilya Donguzov, donguzov@jinr.ru
Thank you for your attention!

## Slide 13
Parameter | Unit | Meaning
Conductive layer |  | ReBCO
The width of the conductor | mm | 4
The Thickness of the conductor | um | 100
Substrate material |  | Hastelloy C276
The thickness of the substrate | um | 100
Crit. current (77 K), | A | 100-150
Layer thickness Ag | um | 1-10
Layer thickness Cu | um | 0-100
ReBCO tape (rare-earth barium copper oxide tape)
5
Superconductor
Buffer layer
HTC
Ag
Cu
Hastelloy
The structure of the HTS tape
Tapes from different manufacturers

## Slide 17
900 mm
500 mm
960 mm
459mm