## Slide 1: Methods of electron cooling friction force measurement suitable for NICA Booster synchrotron
Daniil K. Chumakov
NICA Dispatch Service, LHEP JINR/Диспетчерская служба NICA ЛФВЭ ОИЯИ
National Research Tomsk Polytechnic University
AYSS-2025
Alushta, Russia

## Slide 2: Why do we need cooling
[1] NICA Booster: a new-generation superconducting synchrotron. DOI: 10.3367/UFNe.2021.12.039138
[2] Acceleration in Booster and Nuclotron, V. Lebedev, September, 2023
Intensity of beam is crucial for colliders at each stage;
NICA Booster is the first stage after linac;
Tasks of NICA Booster [1]:
Accumulate ions (up to 10x);
Form required phase volume of beam;
Accelerate intense beam to 578 MeV/nucleon;
Strip accelerated particles to bare nuclei on stripping foil.
Scheme of repeated single-lap injection [2]
Beam fills in available phase space;
No accumulation using only magnetic optics – we need dissipative force;
Cooling exploits such forces, reduces volume of beam in phase space;
Injection → Cooling→Phase space reduced →Repeat;
Circulating beam accumulates until diffusion power exceeds cooling power
1

## Slide 3: Idea of electron cooling
Effective method of particle oscillations damping in proton and antiproton rings // Atomnaya energiya. 1967, 22, pp. 346-348
[3] Beam Cooling. M. Steck. CAS Advanced Acc. Phys., London, 2017
Scheme of ions cooling process with electron beam [3]
Proposed by G.I. Budker in 1966;
Equal mean velocities of ion and electron beams;
Two beams move together;
Beam temperatures: ;
is RMS velocity.
Electron beam by design has lower ;
We move to beam rest frame →
Analogy: particle loses extra energy in foil;
“Foil” is electron beam:
Slow ion in lab frame gains momentum;
Fast ion in lab frame loses momentum;
In both cases – resulting momentum is closer to mean
2

## Slide 4: NICA Booster electron cooling system
[4] Commisioning of electron cooling system of NICA Booster. doi: 10.18429/JACoW-RUPAC2018-TUPSA22
[5] First Experiments on Electron Cooling of Ion Beam in the NICA Booster. doi: 10.1134/S1547477124700122
Top: NICA Booster electron cooler after installation [4]
Down: NICA Booster electron cooler scheme: 1 – electron gun, 2 – electron collector, 3 – electric field plates in electron beam turning section, 4 – longitudinal magnetic field solenoids, 5 – ion beam cooling section [5]
3
Developed by BINP (Novosibirsk, Russia);
Designed to cool ions at injection energy (3.2 MeV/nucleon) and at energies up to 90 MeV/nucleon;
Electron beam diameter 28 mm;
Cooling section length 2.5 m;
Practical parameters at ion energy 3.2 MeV/nucleon:
Electron energy 1.856 keV;
Electron current 25 50 mA;
Magnetic field 0.075 0.1 T;
Temperatures of electron beam (in eV scale):
eV only due to cathode temperature;
eV due to acceleration and beam density;

## Slide 5: NICA Booster beam diagnostics
[5] First Experiments on Electron Cooling of Ion Beam in the NICA Booster. doi: 10.1134/S1547477124700122
[6] Beam diagnositcs at NICA injection complex. E.Gorbachev et al. RuPAC23
Fast current transformer (FCT): (2), (4)
IPM or Ionization profilometer (X,Y, 32 channels per direction): (3), (4)
Schottky spectrometer (2), (3)
E-Cooling system BPMs: (1)
Experimental tasks:
Electron and ion beam alignment;
Longitudinal cooling control (force, time);
Transverse cooling control (force, time);
Beam accumulation and lifetime control.
24 beam position monitors
(BPMs): (1), (3)
Parametric current transformer: (4)
Why measure cooling force/cooling time?
Fokker-Planck equation: evolution of beam particle distribution
Position of electron and ion beams at start and end of cooling section
4
;

## Slide 6: Theoretical models of friction force
Dissipative force dependent on relative velocity ;
Maximum force at from ;
Electrons distribution at source: symmetric Maxwell distribution;
After acceleration: highly anisotropic Maxwell distribution with ;
Magnetic field of solenoid changes electron-ion kinematics [9]
… suppresses degree of freedom for electrons at
At collisions are adiabatic w.r.t. Larmor gyration
Derives from binary Coulomb collisions [7] & collective effects [8] in plasma.
is Coulomb logarithm that limits impact parameters
5
Electron cooling force for 124Xe26+ ions for Booster parameters at 3.2 MeV/nucleon.
Electron beam temperatures are on Slide 3.
[7] Development of ion cooling methods. I.N. Meshkov 10.3367/UFNr.2018.01.038297
[8] Electron cooling. A. Sorensen et al. doi: 10.1016/0167-5087(83)91288-7
[9] The limits of electron cooling. N.S. Dikanskii. et al. Preprint 88-61, BINP

## Slide 7: Longitudinal force measurement methods
Low
High
High
Two regions of : linear (low ) and non-linear (high )
Dynamic methods are for non-linear region
Static methods are for linear region
Longitudinal force measurement
Static
Dynamic
Energy jump
RF phase shift
Stochastic heating
Induction accelerator
Barrier RF
Dynamic methods – evolution of value after single impact
Static methods – continuous impact, comparison of values
6
Low
High

## Slide 8: Longitudinal force: energy jump
Only coasting & pre-cooled beam
Fast change of electrons energy
Electrons shift energy of ions to equilibrium
Energy change ↔ revolution frequency change
Measure with Schottky spectrometer
Works well only for m/s
7
change in energy
420.312 MHz
420.427 MHz
Spectrogram of Schottky noise for coasting beam of 124Xe26+ at 36.7 MeV/nucleon. The signal frequency is shifted with heterodyne.
[10] Experimental studies of the magnetized friction force. DOI: 10.1103/PHYSREVE.73.066503
[11] Electron cooling at CRYRING with an expanded electron beam. DOI: 10.1016/S0168-9002(97)00249-0
[12] Longitudinal electron cooling experiments at HIRFL-CSRe. DOI: 10.1016/j.nima.2015.10.095
[13] Effects of a nonlinear damping force in synchrotrons with electron cooling. DOI: 10.1103/PhysRevE.51.4947
Formulae for cooling force evaluation are from [10-12]
- accelerator circumference, - cooling section length, - chosen revolution frequency harmonic, – phase slip factor, MeV
Let =19993 eV ↔ =36.7 MeV/n
=20004 eV↔ =36.72 MeV/n
=11 eV ↔ m/s
Cooling force for
aligned mean and
shifted w.r.t. [13]

## Slide 9: Longitudinal force: linear region
RF phase shift
Stochastic heating
Bunched beam
RF cavity change → synchrotron oscillations
Synchronous phase is shifted by
measured by FCT or phase discriminator
Before bifurcation point: oscillations damping
After – oscillations amplification
Fokker-Planck equation:
Diffusion power: from fit [14] or [15]
8
[13] Effects of a nonlinear damping force in synchrotrons with electron cooling. DOI: 10.1103/PhysRevE.51.4947
[14] Electron cooling forces for highly charged ions in the ESR. DOI: 10.1016/S0168-9002(97)00027-2
[15] Further results and evaluation of electron cooling experiments at LEAR. DOI: 10.1016/0168-9002(90)91818-V
Cartoon cooling force with blue lines as bifurcation points at [13]
Hopf
bifurcation
Coasting beam, pre-cooled;
RF noise on RF gap at with controlled power;
Cooling switched on – equilibrium reached;
Schottky spectrometer measures equilibrium distribution for each case.
Left: heating fit;
Right: equilibrium distributions for cooled; heated; heated+cooled beam
At equilibrium:

## Slide 10: Longitudinal force: linear region - 2
9
Induction accelerator
Barrier buckets
[16] An induction accelerator for the Heidelberg test storage ring TSR. DOI: 10.1016/0168-9002(92)90230-2
[17] New method to measure the friction force of electron coolers in heavy-ion storage rings. DOI: 10.1016/S0168-9002(02)02142-3
Coasting beam
Constant acceleration to counterbalance cooling force power [16];
Similar to energy jump method, but changes;
Total force shifts stable point ;
is well known; find new stable point.
Measure with Schottky spectrometer.
Force acting on ion without (a)
and with (b), stable point is shifted
RF barrier buckets with slope instead of IndAc [17];
Change slope of or bunching frequency ;
;
;
Control with FCT, BPM (intensity mode), Schottky spectrometer.
Form of barrier buckets potential energy (a) and corresponding force (b) [17]
Beam signal from BPM for:
a) ; b) ; c) [17]

## Slide 11: Transverse force measurement methods
Monitor betatron oscillations damping time with BPM & transverse Schottky spectrometer;
Measure beam size with ionization profilometer.
Right after injection:
high ,
fast decoherence due to chromaticity
Suppress chromaticity to 0
Pre-cool the beam to get small
Excite the oscillations with kicker
Dominant damping due to cooling, not chromaticity!
amplitude of kick
Transverse force measurement
10
Kick the beam
Fokker-Planck solution
Suppress chromaticity
Decrease dp/p (precooling)
Low
High
Betatron oscillations damping
X
V
х
x’
Beam center-of-mass right after kick
… and after some turns due to chromaticity [18]
Cooling shifts to center, not smears
[18] Transverse force measurement. A. Sidorin, NICA operators meeting

## Slide 12: Transverse force measurement methods - 2
11
Stronger kick gives larger from ;
Kicked pencil beam: an oscillator with external force ;
Oscillator energy change: ;
Change the angle of electron beam – change ;
Hopf bifurcation point can be observed:
on IPM: two-sided beam profile (see right pic. on this slide)
on Schottky spectrometer: increase in signal power
Before bifurcation oscillations are damped,
After bifurcation oscillations are amplified,
Measure damping time;
Force can be extracted from or from Fokker-Planck solution
Left - profile of cooled ion beam with aligned electron beam;
Right – with misaligned electron beam after bifurcation point [19]
[19] Studies of electron cooling with a highly expanded electron beam. DOI: 10.1016/S0168-9002(99)01121-3

## Slide 13: Outline
12
Short cooling time is good for accumulation of beam;
BUT: avoid overcooling → growth of instabilities, loss of beam;
NICA Booster Schottky spectrometer is suitable for 30 MeV/n (sensitivity);
For injection energy (3.2 MeV/n) – FCT is the only choice;
For transverse cooling – ionization profilometer monitor (IPM) is OK for all cases;
You need to know Twiss at IPM and in electron cooling section;
The easiest methods for force measurement – RF shift + energy jump;
In principle, Booster RF system allows barrier buckets after additional works [20];
For IndAc-like measurements one need finer amplitude tuning on RF cavity;
Try cooling after chromaticity correction, injection optimization;
Instrumentation allows presented methods
… and tuning of electron cooling system for needs of beam accumulation
[20] Private communication with A.Volodin, LHEP JINR

## Slide 14: Summary on measurement methods
Transverse force measurement
13
Longitudinal force measurement
Static
Dynamic
Energy jump
RF phase shift
Stochastic heating
Induction accelerator
Barrier RF
Low
High
Kick the beam
Betatron oscillations damping
Fokker-Planck solution
Suppress chromaticity
Decrease dp/p
Low
High

## Slide 15: Extra info
14
Cartoon representing ranges of force to be measured with energy jump method
Mechanism of ion bunching in barrier bucket methods for misaligned and well-aligned force [17,21].
BPM signal is fitted with Boltzmann distribution with barrier bucket potential
[21] Laser cooling of fast stored ion beams to extreme phase-space densities. Dissertation of Udo Eisenbarth, 2001