## Slide 1
Status of the BM@N
Slow Control System
I. Osokin, V. Dronik, V. Shutov, R. Nagdasev, D. Egorov
14th Collaboration Meeting of the BM@N Experiment at NICA
14.05.2025

## Slide 2: Preparation for the BM@N beam run
2/12
New additions
New additions
Tested & updated
Waiting for the full assembly
BM@N detectors dashboard
Notes: Most of the BM@N detector systems, such as FSD, Sibeam, GEM, CSC, tof, FhCal and others, are connected to the SC system according to the current BM@N setup and were tested.

## Slide 3: Slow control system
How to connect?
(IP, port, ID, protocol, etc.)
What and how read from server?
Data and command exchange
Monitoring and controls for users
3/12
Tango-based Slow Control System has performed well in previous runs and will be used in the forthcoming run
Notes: For a slow control system, we use TANGO control system, free open source toolkit.
The system did well during the previous BM@N run №8 and will be used in the the forthcoming beam run .

## Slide 4: Forward Si detectors
4/12
.
FSD subsystems were tested and added to the dashboard with mappings
FSD monitoring dashboard in Grafana
Notes: During the preparation of the FSD detector, HV, LV, temperature measurement, and FEE electronics were tested.

## Slide 5: FSD LV autoswitch system
Temperature threshold
Delayed automatic
LV shutdown
5/12
Notes: Among other things, an autoswitch system was created and tested.
Importance of this system is due to reduce the risk of the human factor. In case of, for example, cooling problems with the FSD detector, the electronics boards may overheat, which can have irreversible consequences.
Now, if the electronics are heated to a temp threshold, the LV system will be immediately turned off.

## Slide 6: FSD conditioner monitoring
Historical
DataBase
TCP/IP
WB-MGE Modbus – ethernet converter
MAI6 & WB M1W2 Measurement modules
Modbus RTU
6/12
TANGO device server
Notes: Monitoring of FSD detectors air cooling has also been created
This also increases the reliability of the system and reduces the risks of the working detector in critical conditions.
The WB modules were used as automatization equipment – ADC and interface converter. WB – is Russian based company, produced automatization modules

## Slide 7: Radiation protection doors monitoring
Historical
DataBase
TCP/IP
WB-MGE Modbus – ethernet converter
MAI6 Measurement modules
Modbus RTU
Electrical relay
7/12
TANGO device server
Doors states monitoring in Grafana dashboard
Notes: in addition to detector systems there were some another changes The slow control system for monitoring the condition of the radio protection doors in the BM@N experiment hall have been created and now duplicates the state of information board in BMN control room

## Slide 8: Beam gate & 3SP12 magnets monitoring
Historical
DataBase
TCP/IP
WB-MGE Modbus – ethernet converter
MAI6 ADC
Modbus RTU
Electrical relay
Beam gate
8/12
TANGO device server
Notes: Monitoring of the state of the beam gate and the 3SP12 magnet was created with a similar way, using WB ADCs connected to relay switches

## Slide 9: BM@N Magnets
Historical
DataBase
TCP/IP
NLcon-CED16 Operator’s panel
9/12
TANGO device server
Data is obtained indirectly through the beam pipe line operator's control panel.
Notes: Data about others BM@N magnets, like VKM, SP42 and other, is obtained indirectly through the beam pipe line operator's control panel.

## Slide 10: Target monitoring expend
Historical
DataBase
TCP/IP
WB-MGE Modbus – ethernet converter
MAI6 Measurement modules
Modbus RTU
PT100 temperature sensors
10/12
TANGO device server
Notes: Monitoring of the BM@N target has been expanded. In addition to the existing monitoring of the type of installed target, two temperature sensors were installed to monitor the condition of the target during the beam run

## Slide 11: TOF400 upgrade
11/12
Currently awaiting the completion of the detector's assembly and configuration processes, as well as the finalization of the mappings.
HV, LV, FEE and Gas systems are tested and integrated in the Slow Control System
Notes: Due to the upgrade of the TOF400 detector, the SC system is changing configuration. TOF`s equipments ,like HV, LV and gas system, has been tested, but now we are waiting for the completing the assembly and configuration of the detector and the making of new HV, LV and electronics MAPPINGS.

## Slide 12
Thank You for attention
12/12
Notes: Most of the CSC for BM@N detector systems, such as FSD, Sibeam, GEM, tof, FhCal and others, which are connected to the SC system were tested.