## Slide 1
Ionization of the drift gas volume of the TPC detector by UV nanosecond laser pulses
Minsk, 2025
Speaker: Julia Shafarevich
Supervisor: Alexander Fedotov
Julia Shafarevich, Alexander Fedotov, Sergey Movchan, Julia Fedotova

## Slide 2: Relevance
Laser calibration system TPC design (MPD, NICA)
Comparison of laser pulse characteristics in 3 experiments
Almost all TPC laser calibration systems use an Nd:YAG laser to generate the UV laser beam.
To ensure measurement accuracy calibration of the TPC is necessary. This makes it possible to correct deviations caused by inhomogeneities of the electric and magnetic fields, temperature fluctuations.
Notes: сравнение

## Slide 3: Research objective
Research tasks
Investigate ray propagation and impurity ionization in the working gas volume of TPC
Creation ray tracing model of a laser pulse propagation in TPC calibration system;
Adjustment of the optical elements in the model and determination of the threshold rotation angles of the adjustable mirrors necessary for proper system functioning;
Estimation of the ionization electron concentration in the working gas volume resulting from impurity interactions under laser irradiation.

## Slide 4: System description
Electrons of ionization drift to the pad plane
Schematic representation of a portion of the pad plane segmented by electrodes in the TPC of the NICA experiment
Notes: нет

## Slide 5: Ray tracing method
Gaussian beam
Set of discrete beams
Approximate representation of a Gaussian beam
ω – angular frequency;
t – time;
– wave vector;
– position vector.
The Time-Dependent Solver is applied to ODE. This allows to:
Set the time step;
Stop the calculation under specified conditions (boundary, beam attenuation, etc.);
Use implicit or explicit methods for solving (Runge-Kutta, Euler, BDF);
Notes: BDF (Backward Differentiation Formula, метод обратных дифференцирующих формул)
Применяется, если уравнения становятся жёсткими (например, при резких изменениях n или в анизотропных средах).

## Slide 6: Optical scheme
Optical scheme of the laser calibration system of the TPC of the MPD NICA experiment in AutoCAD
Laser calibration system geometry
A
C1
C2
C3
C4
C1
C2
C3
C4
Notes: Указать элементы

## Slide 7: Optical elements
a) Micromirrors in the bundle;
b) Reflection of laser beams from a band of micro-mirrors into the working gas volume
a)
b)
a)
b)
c)
The trajectories of a laser beam through various optical elements:
a fully reflective mirror,
b) a translucent mirror,
c) a prism

## Slide 8: Simulation
d = 20 mm
λ = 266 nm
I0 = 8,49∙1010 W/m2
A model of beam propagation inside the calibration system of TPC of the MPD NICA experiment in Comsol Multiphysics
https://www.youtube.com/watch?v=qnAeO-Hv7Kk

## Slide 9: Adjusting mirrors
Laser calibration system geometry
Adjusting mirror M1.1
Adjusting mirrors M2.1 - M2.4
M2
M4.1
M4.2
M4.3
M4.4
M3
Notes: Марки моторов
И диапазон вращения

## Slide 10: Angle alignment error
Dependence of the number of beams injected into the working gas volume of the TPC on the angle adjustment error for the mirror M2 a) x-axis, b) z-axis
a)
b)

## Slide 11: Angle alignment error
a)
b)
Dependence of the number of beams injected into the working gas volume of the TPC on the angle adjustment error for the mirror M4.1- M4.4
a) x-axis, b) z-axis

## Slide 12: Ionization model
Dependence of the number of generated ionization electrons on the impurity concentration for 1,2,4 - trimethylbenzene and p - xylene at a pulse duration of 5 ns
a)
b)
Dependence of the number of generated ionization electrons on the impurity concentration for a) 1,2,4 – trimethylbenzene, b) p - xylene at a pulse duration of 5 ns and 7 ns
N0 ⁓ 1020 molecule/m3
Impurity | Ionisation energy, eV | Absolute cross-section of two-photon absorption
1, 2, 3 - trimethylbenzene | 8,27 | 2,8∙10⁻²⁷
p-xylene | 8,44 | 5,8∙10⁻²⁷
Number of ionisation electrons along a single beam:
1, 2, 3 – trimethylbenzene ⁓ 200 - 300
p-xylene ⁓ 400 - 600

## Slide 13
Conclusions
A model of ultraviolet laser pulse propagation (λ = 266 nm, τp = 5-7 ns, d = 20 mm) in the optical chain of the calibration system has been developed based on the ray tracing method;
The permissible deviation from the ideal alignment angles for mirror M2 is Δθₓ ≤ ±0.01° and Δθz ≤ ±0.02°; for mirrors M4.1 – M4.4 – Δθₓ ≤ ±0.01° and Δθz ≤ ±0.02°, respectively.
A model of the two-photon ionization process in the Ar - CH₂ gas mixture with the addition of an organic impurity has been constructed. It was determined that the introduction of trimethibenzene and p-xylene in the amount of 1:10,000 allows for the generation of 105- 106 electrons in the working gas volume, which is sufficient for reconstructing tracks in the detector;

## Slide 14
Thank you for attention!

## Slide 15
Распространение лазерного луча внутри большого бимсплитера

## Slide 16
Изменения профиля луча на выходе из делителя при отклонении зеркала на входе в TPC на 0.1°, 0.2°, 0.3°
Пример влияния нарушения юстировки
Интенсивность сильнее теряют верхние каналы делителя с большим количеством элементов
Нижние каналы теряют интенсивность меньше