## Slide 1: Range (muon) System Status SPD TB, Dubna, 28.05.2025 G.Alexeev, A.Samartsev

## Slide 2: Final 3D engineering version of one (out of 6) “regular” Yoke/Barrel module
After delivery of 3D conceptual model of RS to VBLHEP (Design Bureau №2), we presently concentrate on developing 3D model(s) for all slots of RS (starting from “regular” Yoke/Barrel modules), including: MDT detectors, honeycomb strip board, analog FEE cards, cabling inside/outside, gas pipelines and inter-connections, etc. ---> important information on additional mechanical treatment of steel plates prior to the welding them into the Yoke modules.
Cable channels for inner subsystems
RS cables
MDT protection plates
Outer/biggest detecting plane
Batch of in/out cables

## Slide 3: 3D view of the outer layers (MDT detectors and electronics) in “regular” Yoke/Barrel module
Reading out the signals from detecting layer is based on three 8-channel chips (Ampl-8.53, Ampl-8.11R-G5, Disc-8.17) organized in three boards (High Voltage distributor + Amplifier + Discriminator -> HVAD-8, Preamplifier + Amplifier + Discriminator -> PAD-8, Commutation Board -> CB-64 (8 input cables/8-ch each/ from wires/strips -> 2 output cables /32-ch each/) -> serves 2 inputs of digital FEE module FDM-192 (6 inputs, 32-ch each).
HVAD-8
CB-64
Groove in Fe plate ~ 15 mm x 200 mm to accommodate two CB-64 cards
MDTs
Gas interconnection tubes
Cooling plate

## Slide 5: Barrel module (left: outer 60 mm Fe plate removed, right: 5mm honeycomb removed)
Wire signal cables go to the one edge, strip signals – to another
PAD-8
CB-64
Strip R/O cables
Metallic screen on top of strip honeycomb
MDTs layer (strip cables are left)
Wire R/O side
Strrip R/O side

## Slide 6: Magnified 3D view with removed 60 mm plate:
One PAD-8 board serves 8 strips 3 cm each, thus covering 24 cm of space along Z-axis
RS cables cover
Gas manifold
Special small grooves in Fe plates for fixing CB-64 cards
PAD-8
8 strips x 3 cm = 24 cm
8 –ch flat cable

## Slide 8: Detector Layer Prototype (DLP)
Fully assembled and ready for R&D tests
MDT
Shielding cover
Honeycomb
Strips
DLP recent assembly consists of 60 cm long MDTs, 2 m long strips (3cm width), 5mm thick honeycomb (air gap) with 3mm cells, new type of blades (cylindrical) and 0,3 mm thick iron (zinc plated) shielding cover. (corresponds to new concept of stirp board )

## Slide 9: DLP General R&D Tasks
Shielding cover
HV buss
MDT R/O cables
Strips outputs for signal R/O tests
Strips outputs for parametric tests
DLP is designed to:
study new “air” stripboard parameters and strip signal R/O
study influence of material choice and peculiarities of assembly technological process on strip R/O parameters
study shielding efficiency
develop optimal technological process of full scale detecting layer assembly
study strip registration efficiency
DLP

## Slide 10: DLP: measurement of strip wave impedance and capacity
Results obtained using DLP:
Strip capacity =189pF/m (for max strip length - 491pF)
Strip wave impedance = 21 Ohm
The new concept of the "air" strip board provides a wave impedance of 21 Ohm - the matching resistors will form the corresponding voltage dividers with the input impedances of the amplifiers (5 Ohm Ampl-8.53 or 0.3 Ohm Ampl-8.11R.G-5), improving their high-voltage protection. The measured result is within the calculated range and can be slightly improved by adjusting the assembly technology.
Strip maximum capacity (491pF) fits Ampl-8.53 and Ampl-8.11R.G-5 detector capacity rating of 500pF.

## Slide 11: CONCLUSION
Разработка типовой 3D-модели детекторной плоскости (для максимальной по ширине «щели» на стадии завершения.
Начато моделирование (тиражирование) индивидуально для
всех остальных «щелей» в 6-ти регулярных + Top, Bottom модулей
барреля.
Планируется доработка стенда для отработки сборки и
физического моделирования детекторных плоскостей.