## Slide 1
Measurement of low-energy cosmic muons with multilayer lead-scintillator telescope
AYSS 2025
Lyapin D.D. (INR RAS, NRNU MEPhI)

## Slide 2
Muons under study
The physical sensitivity of low-energy muon research:
Neutrino physics (low-energy muons are the main background)
Dark matter (WIMP can generate neutrino and then low-energy muons)
Primary cosmic rays studies (low-energy mouns depend on models)
Effect of atmospheric variations (low-energy muon flux depends on temperature and density of atmosphere)
Worldwide data of cosmic ray muons
Primary cosmic rays

## Slide 3
Scintillator/lead calorimeter module design
44 modules, 200x200mm2
Beam hole (20 x 20 cm2).
Total weight – 22t.
Status: CANCELLED
CBM Projectile Spectator Detector
(modular sampling Pb/scint hadron calorimeter)
CBM experiment at FAIR
CBM module at INR
Photodetector: SiPM
Hamamatsu S12572-010P
Sensitive area 3 x 3 mm2
Number of pixels 90 000
Nominal gain 1 x 105,
Pixel recovery time - 10 ns
Lead
Scintillator tiles
WLSs to SiPM
readout
Calorimeter module with SiPM readout

## Slide 4
FHCal module (Sc+Pb)
plate with
optic connectors
Module
housing
Veto
detector
Al
Fe
Air
Air
polyethylene
SiPM Hammatsu board adjacent to opto-connectors
Muon telescope with veto detectors in INR
The appearance of the muon telescope

## Slide 5
Muon event selection methodology
Schematic diagram of the experimental module. The effective solid angles for muons stopping in this section are shown on the table. The effective solid angle was obtained from a simulation taking into account scattering.
Signal from the photodiode
Signal amplifier
Summing channel (alternative trigger)
Reading channel
Trigger channel CAEN
CAEN DT5742
(16-channel high-speed digitizer)
Data collection system.
Section number | Effective solid angle (Sr) | Mean kinetic energy of muons stopped in section (MeV)
1 | 0.0401 | 233
2 | 0.0269 | 367
3 | 0.0179 | 504
4 | 0.0120 | 639
5 | 0.0079 | 780
6 | 0.0051 | 924
7 | 0.0032 | 1067
8 | 0.0018 | 1213
9 | 0.0008 | 1358
μ2
μ1
μ3

## Slide 6
Kinetic energy of muons stopped in sections (Simulation)
Module sections:
1 2 3 4
5 6 7 8
9 10
Distribution of energy released by a muon in each section during simulation in the GEANT4 system. Distribution of muon stopping energies in sections in order.
Chart: Section number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 233.9 | 366.4 | 506.7 | 636.5 | 779 | 923.4 | 1072 | 1215 | 1351

## Slide 7
Muon energy release spectrum in the section with a fit. Red is fit parameter.
μ1
Amplitude, mV
Counts
Calibration of signal responses in sections
Counts
MIP
Most probable value (MPV)

## Slide 8
Spectra of stopped muons in the sections
Spectra of muons stopped in the sections up to in section №2-6. Data for 21 days.
Number of stopped muons in sections. Data for 21 days.
Black – 2 section
Blue – 3 section
Green – 4 section
Magenta – 5 section
Orange – 6 section
Chart: Number section
 | 277434 | 80881 | 6958 | 2190 | 649 | 79
MIP
Counts

## Slide 9
A muon telescope based on a hadron calorimeter module to detect muons from cosmic rays on the Earth's surface has been assembled and tested.
The first muon data were obtained.
Planned work
Improving the design of the muon telescope to extend the muon energy range.
To calculate low-energy muon fluxes corrections for the efficiency of scintillation detectors, system veto, event selection efficiency, trigger, and other parameters should be taken into account.
Conclusion
Improving the design of the muon telescope

## Slide 10
References
1. Developmental Programming of Fetal, Growth and Development. S Mishchenko, A Valenti et al. // American Journal of Obstetrics and Gynecology, 2016
2. M. Motoki et al., Precise Measurement of Atmospheric Muon Fluxes at Sea Level Proceedings of ICRC 2001: 927

## Slide 11
Muon energy release spectra in the section
Figure 6. At the top are the spectra of each section with the energy release of muons. At the right is the number of muons stopped in each section.