## Slide 1: Status of DAQ system
Leonid Afanasyev on behalf of DAQ group

## Slide 2: Why triggerless DAQ
Bunch crossing each 76 ns; crossing rate 13.1 MHz,
Collision rate ~3–4 MHz (1st stage about 100kHz)→
Triggerless (or streaming, or free-running) DAQ to avoid any hardware biases
Data flux was estimated for the maximum luminosity L = 1032 cm-2c-1 and maximum energy √s = 27 GeV. Within simplified simulation and some safety margin the data flux is estimated as 20 GBytes/s.

## Slide 3: Why triggerless DAQ
No fast detectors to form a “classic” trigger signal
No 4π detector with 100% efficiency to detect the collisions
The wide SPD physical program eliminates a possibility of rejecting events at a hardware level
SPD is the triggerless detector setup
Bunch crossing time we will get from NICA via White Rabbit protocol (probably). It will be used at event reconstructions to speed up the procedure.
Probably the “Bunch crossing signal” can be used to reject a background/noise signal between the bunch crossing for the fast (SiPM based) detectors as a suppression signal to the Frond-End electronics or as a hardware filter based on the recorded time at the stage of data transfer.
It is the only possible “hardware trigger”, better say “data rejection”

## Slide 4: DAQ structure
L1 concentrator
L2 concentrator
TSS – synchronization system
Computer Read-out and Slice Building system.
SPD Stage | FEE Outputs | L1 (8 ports) | L2 (16 ports) | Read-out PC | Slice Builders
First | ~1292 | >165 | >12 | >6-12 | >5
Second | ~5800 | >730 | >50 | >25-50 | >40

## Slide 5: L1 concentrator (Current prototype)
Cyclone 10GX (105YF780E6G)
8x Links for connect front-end boards (miniSAS connectors) 8 diff pairs per connector
SFP+ 10Gb transceiver for data transmission to L2
SFP+ transceiver for TSS (White Rabbit)
This prototype allowed to test main conceptions for the firmware development and interference with FEE and L2 concentrator.

## Slide 6
Global changes:
Integration WR requirements
  Two external VCXO
  Two 16-bit ADC
  Jitter cleaner
Transition to CDR-mode for FEE-L1 data line.
E-Link line mapping
We’re plan to manufacture it by the end of the year.
L1 next prototype (Hardware) JINR
Link bandwidth per line: 150 Mbps – OK
500 Mbps – OK
750 Mbps – OK
1000 Mbps – OK
1250 Mbps – OK
CDR Mode
MiniSAS
Pin function | Side B Pin | Side A Pin | Pin function
GND | B1 | A1 | GND
Tx0+ | B2 | A2 | Rx0+
Tx0- | B3 | A3 | Rx0-
GND | B4 | A4 | GND
Tx1+ | B5 | A5 | Rx1+
Tx1- | B6 | A6 | Rx1-
GND | B7 | A7 | GND
Unipolar 0 | B8 | A8 | Unipolar 7
Unipolar 1 | B9 | A9 | Unipolar 3
Unipolar 2 | B10 | A10 | Unipolar 4
Unipolar 6 | B11 | A11 | Unipolar 5
GND | B12 | A12 | GND
Tx2+ | B13 | A13 | Rx2+
Tx2- | B14 | A14 | Rx2-
GND | B15 | A15 | GND
Tx3+ | B16 | A16 | Rx3+
Tx3- | B17 | A17 | Rx3-
GND | B18 | A18 | GND

## Slide 7: FEE emulator
FEE Emulator (Need custom PCB)
L2
L1
Plans:
  Study Kintex US (ACKU060 V2.0) chip for FEE emulator
  Create custom PCB for emulator
    8 MiniSAS for test E-Link
    SFP+ for 10G link (For software data generator)
    8 SMA for sync verification
  Firmware
    Eth -> MiniSAS data sender
    TSS command reader
    Slow configuration procedure L1-FEE
    Test Firmware update procedure

## Slide 8
L2 concentrator TSU
Prototype of L2 concentrator card: ZYNQ UltraScale+ FPGA Development Board Z19-P form Alinx. Firmware is being developed.
Instead of the mesonin board with 4 SFPs the board to connect 2 qSFP modules is developed.
8 or 16 L1 connected to L2

## Slide 9
Time Synchronization System – TSS SPbPU
The achieved time synchronization accuracy with the development nodes is better that 10ps!

## Slide 10
Platform:
Alinx AXKU062 V2.0 (Kintex Ultrascale XCKU060)
2 x SFP+ (per line 12.5Gbps)
TSS controller prototype SPbPU
Planed for 2026

## Slide 11
Computer Read-out and Slice Building system
The purpose of slice building systems is to collect data (sub-slices) from all readout computers, build a complete slice and write it to the fast intermediate storage.
Additionally, the system will provide access to raw data (sub-slice) for detector groups in order to monitor the collected data before processing in the online filter.
Components:
Read-out – getting a sub-slice from each detector system
Builder – combining sub-slices and forming a single data structure
Supervisor – arbitration of the slice construction system
Distributor – provides raw data for monitoring
Only industrial standard equipment will be used

## Slide 12
The design of the data acquisition system for SPD experiment
http://arxiv.org/abs/2509.12790
The paper submitted to JINST

## Slide 13
DAQ specification
The current and next versions of the
specification will be published in the
JINR document management system
(docs.jinr.ru).
Available to JINR employees and
collaborators via JINR Single Sign-On
(SSO) → docs.jinr.ru
docs.jinr.ru/spd-experiment/spd-daq/specification

## Slide 14: 2026 plans
Production of the next L1 concentrator prototype
Production of the TSS controller prototype
The firmware development for L1, L2 and TSS
It will include further development of integration with all FEE.
Software development
Test of radiation hardness of FPGA and optical connections need to be foreseen.

## Slide 15
Thank you for your attentions.