## Slide 1: BBC detection and readout system R&D and QA/QC setups for mass production
S. Doronin, F. Dubinin, K. Krivokhin, A. Kuzmin, D. Shafikova, K. Tertyshnaya, P. Teterin, A. Zakharov

## Slide 2: R&D introduction
The goal:
Find optimal configuration of the detector and the front-end electronics
Study detector and electronics performance
Main activities:
Effect of WLS number of loops and outer length on tile detector performance
Measurements with cosmic rays

## Slide 3: Effect of WLS number of loops and outer length on tile detector performance

## Slide 4: Tile for light collection tests
SiPM
WLS extra out hole
Reference LED
Light entre to the tile
LED 410nm
Clear fiber, tale 2mm
Optical connector

## Slide 5: Test setup
Power supply: Keithley 2400
Pulse generator: Rigol DG4102
Pulse analyzer: Lecroy 620Zi
Measured values:
SiPM charge response
Charge RMS
Trigger to SiPM pulse delay RMS
SiPM pulse width
Oscilloscope input impedance: 50 Ohm
Driving pulse for LED:
Amplitude: 5V
Width: 15ns
SiPM – tile distance (WLS tale width): 5cm

## Slide 6: Charge vs number of loops
Chart: Average normalized response
| 1 | 2 | 3 | 4 | 5 | 6
 | 0.71935 | 0.83703 | 0.92379 | 0.95654 | 0.98479 | 1
Chart: Relative charge resolution
| 1 | 2 | 3 | 4 | 5 | 6
 | 0.1444 | 0.092195 | 0.083522 | 0.06891 | 0.063609 | 0.060853

## Slide 7: Time resolution and pulse width
Chart: Delay RMS
| 1 | 2 | 3 | 4 | 5 | 6
 | 383 | 339 | 351 | 342 | 360 | 352
Chart: Pulse with at 5mV level
| 1 | 2 | 3 | 4 | 5 | 6
 | 44.1 | 44.1 | 44.2 | 44.2 | 44.3 | 44.3

## Slide 8: Outlook and plans
Signal charge increase with the number of loops but the dependence is not linear
The width/center ration of charge distribution decrease with the number of loops
Time resolution and pulse width are weekly sensitive to the number of loops
Measurements with long WLS tale are in progress
Measurement of light losses into the tile expect to provide better understanding of light collection by rolled WLS

## Slide 9: Measurements with cosmic rays

## Slide 10: Test setup
10 tiles of 2nd row with similar WLS
WLS: SG BCF-92, 3 loops, ~30cm tail length
Readout by Hamamatsu S13361‐3050AE‐08 matrix coupled to CAEN DT5202
10 SiPMs at 7V overvoltage, the rest 54 SiPMs are at lower voltage
Overall height: 16cm
CAEN DT5202 configuration:
Low gain input, 20 mV/pC amplification
Discriminator: 240 DACu
Trigger: Top and bottom tiles in coincidence by internal logic unit
Pulse height + ToT measurement

## Slide 11: SiPM bias voltage calibration
Calibration performed with LED in pulse mode by obtaining single-photoelectron spectra at different bias voltages
Zero extrapolated distance between neighboring peaks corresponds to the breakdown voltage of the SiPM
Chart: Peaks distance, channel
| 148 | 168 | 122 | 90 | 65
4 | 56.9294 | 57.9294 | 55.9294 | 54.9294 | 53.9294
5 | 56.8471 | 57.8471 | 55.8471 | 54.8471 | 53.8471
6 | 56.9294 | 57.9294 | 55.9294 | 54.9294 | 53.9294
7 | 56.9294 | 57.9294 | 55.9294 | 54.9294 | 53.9294
36 | 57.0447 | 58.0447 | 56.0447 | 55.0447 | 54.0447
37 | 57.5059 | 58.5059 | 56.5059 | 55.5059 | 54.5059
38 | 57.0612 | 58.0612 | 56.0612 | 55.0612 | 54.0612
39 | 56.9294 | 57.9294 | 55.9294 | 54.9294 | 53.9294
12 | 57.0941 | 58.0941 | 55.0941 | 54.0941
45 | 58 | 59 | 56 | 55

## Slide 12: Scale calibration in pulse height mode
Distance between neighboring peaks corresponds to SiPM gain in pulse height value:
MIP pulse height distribution

## Slide 13: Pulse height distribution analysis
The distribution assumes to be approximated by Landau and Gaussian convoluted function:
Channel | MPV
4 | 61
5 | 81
6 | 74
7 | 76
36 | 63
37 | 64
38 | 63
39 | 67
2 times larger compared to previous measurements!
To be cross-checked…
Response variation is within ±15%

## Slide 14: ToT distributions
ToT scale of DT5202 is strongly non-linear → we cannot use Landau-Gaussian convolution function directly
Modification of the function by change of variable according to ToT calibration allows to fit the distribution
Channel | MPV
4 | 72
5 | 78
6 | 75
7 | 76
36 | 77
37 | 78
38 | 76
39 | 74

## Slide 15: ToT scale calibration
ToT scale expect to be able to calibrate in Coulombs (in accordance to the DT5202 datasheet)
ToT could be calibrated in photoelectrons by means of pulse height analysis
CAEN example
Input channel | Channels ToT | Photoelectrons
4 | 72 | 61
5 | 78 | 81
6 | 75 | 74
7 | 76 | 76
36 | 77 | 63
37 | 77 | 64
38 | 76 | 63
39 | 74 | 67

## Slide 16: Outlook and plans
Showed principal capability to calibrate ToT in number of photoelectrons (the units independent to electronics configuration and SiPM gain)
Procedure of ToT calibration in charge values is in progress
Calibration of ToT in photoelectrons is the next step

## Slide 17: Test setups for mass production

## Slide 18: Setup for tests of SiPMs at carrier boards

## Slide 19: Setup overview
Light source: blue LED in pulse mode
External trigger
Adjustable distance to SiPM
Readout system: CAEN DT5202

## Slide 20: LED driver
Pulse source: ATMega 328P
Pulse rate: 1-10kHz
Pulse amplitude: depends on pulse width, 5V max
Pulse width determined by the delay: 10ns, will have coarse adjustment

## Slide 21: Setup for fiber test

## Slide 22: Proposal
Power Supply
Power Supply
SiPM
I/O switches
LED
Ampermeter
…
…
x12 channels
…
…
…
…
Fiber under test
Connector
Connector
…
…
I/O switches
x12 channels

## Slide 23: Hot swapping of test sample
50k + 50k resistors limits current by 25μA per SiPM
12 SiPM → 300μA
Power consumption by open SiPM: W = 25V * 25μA = 625μW
FR4 thermal conductivity: 0,3mW/(mm*K) along thickness
Voltage drop during regular operations: 0,1V @ 1μA
- not negligible but reasonable

## Slide 24: LED circuit
Circuit designed to run LED at very beginning of open part of IV curve
Potentiometer allows to adjust LED brightness to get SiPM response of 1 μA
GNL-0603UBC
λ_max = 470nm
S = 1,6 x 0,8 mm2

## Slide 25: Conclusion
Increase of number of WLS loops embedded to a tile gains light collection and relative energy resolution
Number of WLS loops doesn’t affect significantly on timing performance
Average response of tiles with Saint-Gobain WLS, SKTN glue and Hamamatsu S13361 SiPMs is 71phe with variation over 8 tiles within ±15%
ToT distribution can be fitted with modified Landau-Gauss function
ToT scale can be calibrated in charge value → photoelectrons
Development of setups for test of SiPMs on carrier board and fiber bundles for mass production tests are in progress

## Slide 26: Thank you for your attention!

## Slide 27: КАЛИБРОВКА СИГНАЛОМ С ВНЕШНЕГО ГЕНЕРАТОРА
Калибровочные кривые для одного канала (№60) при различном времени формирования для максимального (63) и минимального (1) коэффициентов усиления.
Chart: LG (коэффициент усиления: 1)
| 1 | 10 | 20 | 30 | 40 | 50 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 0
Sh. time 12.5ns | 123.2 | 165.2 | 260.4 | 344 | 415.8 | 485.5 | 871.5 | 1698.2 | 2680 | 3742.2 | 4843.6 | 5959.6 | 7033.3 | 8009.6 | 0
Sh. time 25ns | 122.9 | 144.9 | 232 | 308.7 | 371.3 | 432 | 766.7 | 1487.3 | 2355 | 3324.6 | 4363.9 | 5464.5 | 6581.1 | 7684.2 | 0
Sh. time 37.5ns | 127.4 | 274 | 380.4 | 658.1 | 1269.3 | 2014.6 | 2859.5 | 3783.2 | 4787 | 5833.2 | 6902.2 | 7947.9 | 0 | 0 | 0
Sh. time 50ns | 119.3 | 218 | 313 | 525.6 | 1019.1 | 1625.8 | 2322.5 | 3092.5 | 3945.8 | 4852.1 | 5796.1 | 6736 | 7638 | 0 | 0
Sh. time 62.5ns | 118 | 191 | 277 | 456 | 884 | 1414 | 2031 | 2718 | 3484 | 4305 | 5169 | 6041 | 6891 | 7700 | 0
Sh. time 75ns | 118 | 168 | 243 | 398 | 767 | 1230 | 1777 | 2388 | 3070 | 3803 | 4582 | 5375 | 6155 | 7568 | 8040
Sh. time 87.5ns | 7981.5 | 7755.4 | 7358.3 | 6930.1 | 5624.8 | 4901.1 | 3803.3 | 2978.2 | 2160.6 | 1879.8 | 1106.6 | 686.6 | 512.4 | 219.4 | 119.7
Chart: LG (коэффициент усиления: 63)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Sh. time 12.5ns | 193.8 | 293.5 | 380.9 | 467.6 | 563.5 | 653.2 | 741.6 | 825.7 | 911.9 | 997.9 | 1809.6 | 2596.4 | 3394.9 | 4193.7 | 4988.3 | 5762.1 | 6510 | 7226.7 | 7863.4
Sh. time 25ns | 123.8 | 270.7 | 360.1 | 447.8 | 542.7 | 630.4 | 715.6 | 800 | 884.4 | 969.3 | 1788.2 | 2606.3 | 3485.8 | 4369.4 | 5249.8 | 6109 | 6944.4 | 7753.3 | 7905
Sh. time 37.5ns | 167 | 505.2 | 907 | 1692.5 | 2496.2 | 3381.8 | 4274.3 | 5163.4 | 6035.4 | 6886.3 | 7717.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sh. time 50ns | 160.6 | 449.3 | 806 | 1515 | 2258 | 3090 | 3931 | 4771 | 5596 | 6402 | 7192 | 7935 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sh. time 62.5ns | 145 | 424 | 759 | 1427 | 2135 | 2942 | 3759 | 4576 | 5380 | 6165 | 6938 | 7668 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sh. time 75ns | 120 | 395 | 706 | 1328 | 1992 | 2764 | 3546 | 4327 | 5095 | 5846 | 6586 | 7287 | 7967 | 0 | 0 | 0 | 0 | 0 | 0
Sh. time 87.5ns | 139.3 | 249.6 | 304.2 | 365.5 | 482.2 | 657.4 | 831.8 | 1008 | 2018.3 | 3341.4 | 4081.2 | 5164.8 | 6222.7 | 7209.8 | 7842.3 | 0 | 0 | 0 | 0
Chart: HG (коэффициент усиления: 1)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80
Sh. Time 12.5ns | 135.9 | 225.3 | 308.4 | 382.2 | 458.3 | 531.4 | 610 | 690 | 771.6 | 853.5 | 1261.1 | 1685.8 | 2136.9 | 2615.3 | 3628.5 | 4689.3 | 5770.5 | 6837.7 | 7855.6
Sh. time 25ns | 129 | 204.7 | 276 | 339 | 403.3 | 464.1 | 530.6 | 597.3 | 665.9 | 736 | 1087.3 | 1458.2 | 1855.8 | 2284.2 | 3211.2 | 4219.7 | 5289.2 | 6394 | 7514.9
Sh. time 37.5ns | 125.2 | 350.8 | 621.6 | 915.7 | 1226.8 | 1565.8 | 1933.3 | 2743 | 3640.2 | 4618.3 | 5655.5 | 6740.4 | 7860.5 | 0 | 0 | 0 | 0 | 0 | 0
Sh. time 50ns | 117.2 | 294 | 502.3 | 734.5 | 982.6 | 1254.8 | 1553.8 | 2222 | 2971 | 3800 | 4702 | 5662.7 | 6673.6 | 7673.3 | 0 | 0 | 0 | 0 | 0
Sh. time 62.5ns | 114 | 264 | 444 | 644 | 858 | 1094 | 1355 | 1943 | 2609 | 3352 | 4168 | 5048 | 5989 | 6933 | 7700 | 0 | 0 | 0 | 0
Sh. time 75ns | 112 | 239 | 400 | 576 | 764 | 972 | 1200 | 1716 | 2304 | 2960 | 3686 | 4480 | 5336 | 6200 | 6914 | 7308 | 7911 | 0 | 0
Sh. time 87.5ns | 108.1 | 218.9 | 306.3 | 429.3 | 527.6 | 628.8 | 734.1 | 808.9 | 926.1 | 1092.8 | 2095.2 | 3353.9 | 4077.5 | 4865.1 | 5664 | 6298.9 | 7114.8 | 7597.5 | 7956.1
Chart: HG (коэффициент усиления: 63)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14 | 15
Sh. time 12.5ns | 656 | 1124.2 | 1650.6 | 2161.5 | 2702.8 | 3202.1 | 3723.2 | 4230.5 | 4747.8 | 5265.1 | 6271 | 7239.5 | 7695
Sh. time 25ns | 704.5 | 1253.6 | 1833.2 | 2398.4 | 2994.2 | 3565 | 4138 | 4716.4 | 5287.1 | 5863.3 | 6992.6 | 7538.2 | 0
Sh. time 37.5ns | 805.1 | 1356.9 | 1934.5 | 2502.9 | 3117.2 | 3697.4 | 4291.8 | 4885.2 | 5473.3 | 6084 | 7216.4 | 7768.1 | 0
Sh. time 50ns | 747 | 1295 | 1869 | 2433 | 3025 | 3595 | 4159 | 4735 | 5305 | 5878 | 7000 | 7553 | 0
Sh. time 62.5ns | 739 | 1280 | 1847 | 2409 | 2992 | 3558 | 4118 | 4689 | 5252 | 5818 | 6930 | 7475 | 0
Sh. time 75ns | 700 | 1219 | 1759 | 2295 | 2863 | 3400 | 3943 | 4490 | 5031 | 5582 | 6648 | 7706 | 0
Sh. time 87.5ns | 682.8 | 905.7 | 1625.1 | 2116 | 3145.9 | 4267.1 | 5183.6 | 6196.8 | 7183.9 | 7858 | 0 | 0 | 0

## Slide 28: Previous measurements with cosmic setup