Technical specification

on the NICA Stochastic Cooling System

This document has been worked out within the JINR Stochastic Cooling working group:

N.Shurkhno

I. Gorelyshev

V. Filimonov

A. Sidorin

The main purpose of the NICA Stochastic Cooling System (SCS) is to reduce the beam phase space growth during the accumulation and bunching and to prevent luminosity losses mainly caused by the process of intrabeam scattering (IBS). SCS has to provide the cooling rates exceeding the IBS rates (see fig.1) or characteristic cooling times has to be faster than times of IBS (table 1) in the beam energy range from 3 to 4.5 GeV/u. Two stages of SCS realization (start-up and project) are ratified according to NICA stages of realization.

Figure 1. Energy dependence of IBS rates for NICA collider.

Table 1. Typical IBS times for different energies in SCS operating region.

| Energy, GeV/u | 3.0 | 3.8 | 4.5 |
| --- | --- | --- | --- |
| IBS time, s | 520 | 1130 | 1900 |

System design

| Figure 2. Channels placement tical | 1’/2’ | Vert. |  | 500 – 618 | 491 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

Longitudinal

| Palmer | 2 |
| --- | --- |

Horiz.

| Configuration | Cooling method | Channel | Pickup | Kicker | ToF, ns | Min. delay, ns |
| --- | --- | --- | --- | --- | --- | --- |
| Start-up | Longitudinal Filter | 1 | Sum | Sum | 600 – 618 | 452 |
| Project | Horizontal | 1 | Horiz. | Combined | 600 – 618 | 405 |
|  | Vertical | 1’/2’ | Vert. |  | 500 – 618 | 491 |
|  | Longitudinal Palmer | 2 | Horiz. | Sum | 500 – 515 | 473 |

Table 3. System Parameters.

| Passband | 2 – 4 GHz |
| --- | --- |
| Pickup Impedance | 288 Ω |
| Pickup output power (peak/average) | 30/2 nW |
| Kicker Impedance | 576 Ω |
| Peak power feeding the kicker | 500 W |
| Gain(without losses) | 110 dB |

General scheme

Figure 4. SCS scheme for the start-up configuration.

Figure 5. SCS scheme for the project configuration

Main system components

| Pickup & signal combination | Diagnostics | Optical Comb filter (if present) | Variable delay & attenuation | Commutation of the kicker & main amplifiers |
| --- | --- | --- | --- | --- |

Pickup and signal combination

Ring-slot couplers produced in FZ Jülich were chosen as pickups and kickers because of their high longitudinal and transverse impedance. One ring contains sensors symmetrically settled in 8 azimuthal directions (fig. 4a). In terms of this document one section is defined as a structure with 16 rings (fig. 4b). Each pickup consists of 2 sections.

| Figure 4a. One ring of the pickup | Figure 4b. Pickup section of 16 rings |
| --- | --- |
| Table 4. Pickup parameters |
| Aperture | 90 mm |
| Section length | 200 mm |
| Number of sections | 2 |
| Pickup length | 500 mm |
| Ring Impedance | 9 Ω |
| Pickup Impedance | 288 Ω |

Figure 5. Pickup commutation scheme

Table 5. Pickup commutation devices

| Low Noise Amplifier 34 dB (NF 0.55) | Miteq JS-2-02000400-05-10P |
| --- | --- |
| Coupler 0̊ | Lynx 111.A0232 |
| Hybrid 180̊ | Anaren 10016-3 |
| Amplifier 50 dB | Miteq AMF-4F02000400-05-10P |

Diagnostics

Table 6. Diagnostic devices

| Spectrum Analyzer | Rohde&Schwarz FSV7 | Schottky noise measurements |
| --- | --- | --- |
| Network Analyzer | Rohde&Schwarz ZNB4 | Beam transfer function measurements |
| Power meter | Rohde&Schwarz NRT + Z43 | Amplifier diagnostics |

Optical Comb Filter

Input RF signal is modulated into optical signal (λ 1550 nm). Modulator is followed by two fine system delays (0-250 ps, 0-330 ps) and filter itself (divider, attenuators etc.). Delay in the long filter line is provided by 800 ns coil, switch delay (0.5-15.5 ns) and fine delay (0-560 ps). Power losses of the filter are compensated by 50 dB amplifier at the output.

Figure 6. Comb filter scheme

Table 7. Comb Filter Components

| Optical platform with integrated laser (10 mW, 1550 nm), splitter and attenuators (0-70 dB) | Viavi MAP-200 |
| --- | --- |
| Modulator (1550 nm, 12 GHz) | Photline Technologies MXAN-LN-10-00 |
| Photodetector (1280-1620 nm, 20 GHz) | Gooch&Housego EM169-03 |
| Filter Total gain | 12 dB |
| Total delay | 47,1 ns |

Variable delay and attenuation

Table 8. Adjustable components

| Variable attenuator 0-55 dB, step 1 dB | Aeroflex Weinschel 3406-55 |
| --- | --- |
| Variable optical delay 0-15,5 ns step 0,5 ns | Agiltron SSTD 525111303 |
| Variable optical delay 0-250/330/560 ns, step 1 ps | General Photonics MDL-002 |
| Coaxial trombone 0-32 ns, step 10 ps | Colby Instruments CDPL-100A-32.0NS |
| Phase shifter 360̊, step 1̊ | Vaunix LPS-402 |

Commutation of the kicker and main amplifiers

Each two azimuthal directions of one kicker section are fed by 30 W amplifiers Rohde&Schwarz BBA-150-D30 (fig. 7a), RF power splitting is provided by Lynx 111.A0232 power dividers. Each kicker consists of 4 sections. Magnetic High order mode suppressors (HOMS) are fastened to the outside of the kicker in the directions of beam propagation (fig. 7b).

| Figure 7a. Feeding scheme of the kicker section | Figure 7b. Kicker section with HOMS |
| --- | --- |
| Table 9. Kicker parameters |
| Aperture | 90 mm |
| Section length | 200 mm |
| Number of sections | 4 |
| Kicker length | 1200 mm |
| Kicker Impedance | 576 Ω |
| Amplifier Peak Power | 30 W |
| Kicker Peak Power | 480 W |

The described system for longitudinal Palmer line provides 2 times faster cooling rates than required (Fig. 8).

Figure 8. Comparison of IBS and cooling rates in the required beam energy range.

# Text boxes

Beam

R&S BBA-150

30W amplifier