## Slide 1: Integration of the Cooling System into the TPC Slow Control and Development of Control and Monitoring Functions for the Cyclone V FPGA Starter Kit
Youmna Ghoneim, Joint Institute for Nuclear Research.

## Slide 2
Project Objectives and Development Environment
Implement and simulate FPGA-based control logic for LED indicators and UART communication.
Utilize the Terasic Cyclone V GX Starter Kit (5CGXFC5C6F27C7) as the experimental platform.
Perform synthesis and waveform verification using Intel Quartus Prime Lite and ModelSim Intel FPGA Starter Edition.
Develop scalable slow-control logic applicable to the TPC readout electronics of the MPD experiment at NICA (JINR).
Prepare integration with MasterSCADA 4D + OPC UA for unified monitoring, data archiving, and fault diagnostics.

## Slide 3: Introduction
The Time Projection Chamber (TPC) is the main tracking detector in the Multi-Purpose Detector (MPD) at the NICA collider.
It tracks charged particles from nucleus-nucleus collisions.
Momentum and energy resolution are defined by the TPC’s design and the applied magnetic field.
The baseline readout system uses a Multi-Wire Proportional Chamber (MWPC) with cathode pad readout.
FPGA Functions:
Synchronizes SAMPA links
Initializes channels
Reformats data to 32-bit

## Slide 4
Cyclone V GX Starter Kit (Board Overview & Architecture)
Key Board Features
FPGA Device : Intel Cyclone V GX (5CGXFC5C6F27C7, C7 package)
Clock Sources : Four 50 MHz oscillators (B5B, B6A, B7A, B8A) and 125 MHz LVDS
I/O Voltage Levels : 3.3 V LVTTL and 2.5 V for user I/O
On-board interfaces : LEDs, switches, keys, UART, I²C, SDRAM, HSMC, audio codec
Power Supply : +12 V DC external input
Board is used as the control and monitoring module within the TPC readout chain.
FPGA firmware written in Verilog implements multi-mode LED logic and UART communication.
Simulation and debugging done with Quartus Prime Lite 20.1.1 + Model Sim-Altera.

## Slide 5
FPGA Pin Mapping and Quartus Functional Interface

## Slide 6
Quartus Prime Project Setup and Compilation

## Slide 7
FPGA Pin Mapping and Functional Interfaces
Component Signal Pin Voltage Description
Clock (50 MHz) CLOCK_50_B5B R20 3.3V Main system clock
Reset CPU_RESET_n AB24 3.3V Active-high global reset
Red LEDs LEDR[9:0] F7…J10 2.5V Visual output indicators
Green LEDs LEDG[7:0] L7…H9 2.5V Visual output indicators
Switches SW[9:0] AC9…AE19 3.3V Mode and speed selection
Push-keys KEY[3:0] P11…Y16 3.3V Manual reset and control
UART TX/RX L9 / M9 2.5 V Serial communication interface

## Slide 8
Integration of HDL Design with Quartus Prime Lite
Inputs (Switches and Key Reset) control visual modes and speed of the LED patterns inside scan_top.v.
SW[9:8] → Mode Select ┐SW[3:0] → Blink Speed ├──► scan_top.v (FPGA Logic)KEY[0] → Reset │ │LEDR[9:0] ←─────────────┘LEDG[7:0]

## Slide 9
Quartus Prime Lite – Compilation and Simulation Flow
The project targeting the Cyclone V GX Starter Kit (5CGXFC5C6F27C7) was compiled in Quartus Prime Lite v20.1.1.Stages of the compilation flow:
Analysis & Elaboration – verifies Verilog syntax and hierarchy.
Fitter – places and routes design logic and assigns I/O pins per .qsf.
Assembler – generates the programming .sof file.
Timing Analyzer – checks all timing constraints from scan_top.sdc
Compilation Results :
✓ HDL compilation completed
✓ 0 errors, 11 warnings✓ Successful pin-assignment verification✓ Peak virtual memory ≈ 4.8 GB✓ Total CPU time ≈ 14 s After successful build, the .sof bit stream is ready for download to the FPGA using USB-Blaster II.

## Slide 10: LED & Switch Logic Overview
SW[9:8] select mode (00–11)
SW[3:0] control blink speed
KEY[0] = reset (active low)
All inputs synchronized to 50 MHz clock
Mode | Pattern Type | Description
00 | Synchronous | All LEDs blink together
01 | Alternating | Red vs Green alternating
10 | Wave | Rotating one-hot pattern
11 | Random | Pseudo-random blink via LFSR
Code Snippet
always @* begin
case (mode_sel)
2'b00: begin LEDR={10{blink}}; LEDG={8{blink}}; end
2'b01: begin LEDR={10{blink}}; LEDG={8{~blink}}; end
2'b10: begin LEDR=wave_r; LEDG=wave_g; end
2'b11: begin LEDR=lfsr16[9:0]; LEDG=lfsr16[15:8]; end
endcase
end

## Slide 11
Mode 0: Synchronous Blink
Selector: SW[9:8]=00
Behavior: All RED and GREEN LEDs toggle in-phase
Speed: SW[3:0] (each +1 ≈ 2× faster)
Use cases: Basic heartbeat/“alive” indicator
From code (scan_top.v):
led_r_raw = {10{blink}};
led_g_raw = { 8{blink}};
Demo script: run_mode0.do

## Slide 12
Mode 1: Alternating Blink
Selector: SW[9:8]=01
Behavior: RED ↔ GREEN toggle in opposite phase (180°)
Speed: SW[3:0]
From code:
led_r_raw = {10{ blink }};
led_g_raw = { 8{~blink }};
Use cases: Quick visual differentiation between two states
Demo script: run_mode1.do

## Slide 13
Mode 2: Wave Mode
Selector: SW[9:8]=10
Behavior: One-hot bit rotates across reds and greens (two rings)
Speed: SW[3:0]
controls shift period (tick)
From code:
wave_r <= {wave_r[8:0],
wave_r[9]};
wave_g <= {wave_g[6:0],
wave_g[7]};
For clearer rotation, use moderate speed (e.g., SW[3:0]=0010)
Demo script: run_mode2.do

## Slide 14
Mode 3: Random
Selector: SW[9:8]=11
Behavior: Pseudo-random LED
patterns per tick LFSR: x^16 + x^14 + x^13 + x^11 + 1, seed 16'hACE1
Mapping: LEDR = LFSR[9:0], LEDG = LFSR[15:8]
Speed: SW[3:0] (faster = more changes)
run_mode3.do

## Slide 15
LED Operation Mode Comparison
Insert Video: Mode 0 – Synchronous Blink
Insert Video: Mode 1 – Alternating Blink
Insert Video: Mode 2 – Wave Rotation
Insert Video: Mode 3 – Random Blink

## Slide 16: Integrated FPGA–SCADA Control Chain
Quartus Prime → Model Sim Intel FPGA Edition → Cyclone V FPGA (Board) → OPC-UA Server → Master SCADA
Tool / System | Primary Role | Description
Quartus Prime Lite | Design & Configuration | Develops HDL logic (Verilog modules), generates bitstream for Cyclone V GX board.
ModelSim | Simulation & Verification | Verifies timing, LED logic, UART behavior using .do testbench automation.
Cyclone V FPGA | Hardware Execution Layer | Runs synthesized design; communicates through UART and GPIO.
OPC-UA Server | Communication Bridge | Exchanges live data between FPGA system and supervisory platform.
MasterSCADA 4D | Visualization & Control | Displays sensor/LED status, allows remote commands, and logs TPC slow-control variables.
Implements real-time slow-control logic for TPC readout electronics at JINR.
The chain supports future expansion to temperature sensors, HV modules, and environmental monitoring.

## Slide 17
Results & Observations
Simulation verified correct LED toggling patterns for all 4 modes.
SW[3:0] adjusts blink frequency. SW3=1 ensured all LEDs active.
UART RX/TX remained idle-high and functional.
Mode | Description | Observable Behavior | Application
0 | Synchronous Blink | All LEDs blink together at adjustable frequency | Clock/reset verification
1 | Alternating Blink | Red and Green LEDs alternate | Logic toggling and diagnostics
2 | Wave Rotation | Sequential LED rotation pattern | Timing & shift-register validation
3 | Random Blink | Pseudo-random LED pattern from LFSR | Noise/immunity and randomness testing
Functional simulations confirmed successful LED control and UART communication across all four operational modes. Each mode displayed distinct blinking or data patterns corresponding to the logic implemented in scan_top.v. The results verified the correctness of mode selection via switches and synchronization of clock-driven signals.

## Slide 18: Cooling System – Time Projection Chamber (TPC)
The system includes ~110 channels, with 76 dedicated to thermal stabilization.
Each channel comprises:
  A water pressure reducer
  An electric heater
  Temperature and pressure sensors
  A flow meter
A network of 250 temperature sensors on the TPC enables multi-zone PLC-based temperature control across all channels.

## Slide 19: PLC Simulator & TIA Portal Integration
PLC-SIM allows virtual testing of PLC programs in TIA Portal, enabling real-time logic simulation, HMI interaction, and system verification—without physical hardware.

## Slide 20: PLC Simulator & TIA Portal Integration “Device &Networks”

## Slide 21: Copper Thermal Stabilization Scheme

## Slide 22: GUI Interface screen using TIA Portal

## Slide 23: GUI Interface screen using TIA Portal

## Slide 24: GUI Interface screen using TIA Portal

## Slide 25: GUI Interface screen using TIA Portal

## Slide 26: Integration of TIA Portal SCADA into Master SCADA
Utilize OPC UA or Modbus TCP for seamless communication.
Configure WinCC (TIA Portal) as an OPC UA Server.
Master SCADA connects as an OPC UA Client to read/write data.
Share and map key process tags (e.g., alarms, setpoints, status).
Implement security settings: authentication, access control, encryption.
Perform real-time testing and validation to ensure proper integration.

## Slide 27: Integration Strategy Overview
Goal: Connect Siemens SCADA (WinCC/PCS 7) to a Master SCADA system
Key Protocols:
- OPC UA / DA: Standard for SCADA integration
- Modbus TCP: Lightweight and widely used
- MQTT / REST: For IoT or cloud-based systems
Use Siemens SCADA as a Data Server
Use MasterSCADA as the OPC UA Client

## Slide 28: GUI-Level Integration Methods
- Remote Desktop / VNC: Directly launch Siemens SCADA interface
- Hyperlink Launcher: Button in MasterSCADA opens Siemens HMI
- Thin Client: Host Siemens SCADA on terminal server for browser access
- Embedded HMI Web Page: Use iframe if web-enabled HMI is available

## Slide 29: Integration Layers Overview
1. Real-Time Control: OPC UA Read/Write
2. Monitoring: OPC UA Read-only / Modbus TCP
3. GUI Integration: RDP, VNC, Thin Clients

## Slide 30
Conclusion
The FPGA logic was implemented and simulated on the Cyclone V GX Starter Kit, demonstrating four LED modes and UART communication via Quartus Prime Lite and ModelSim.
This design establishes a reliable base for slow-control of the MPD TPC readout electronics.
A MasterSCADA 4D and TIA Portal interface enables full monitoring of the leakless cooling system (110 channels, 76 for thermal stabilization) under sub-atmospheric pressure.
Real-time control and diagnostics are achieved through PLCs and OPC UA communication.
Next steps:
• Configure OPC UA server and client
• Validate communication
• Test and document unified FPGA–Master SCADA operation

## Slide 31: Thanks for your Attention
Tel.: +7 (923) 40 80 895
E-mail: youmnasami24@gmail.com, Ghoneim@jinr.ru
23.10.2025
Full Name
Youmna Ghoneim
Telegram Contact