## Slide 1: CNI-поляриметры в ускорительно –коллайдерном комплексе NICA
ОИЯИ, 12 ноября, 2025
А.Н. Зеленский -МФТИ

## Slide 2
STAR
PHENIX
AGS, 24GeV
LINAC
BOOSTER, 2.5 GeV
Pol. H- ion source
Spin Rotators
Siberian Snakes
200 MeV polarimeter
RHIC pC “CNI” polarimeters
RHIC
Absolute H-jet
CNI-polarimeter
L max = 1.6  1032 s-1cm-2 50 < √s < 510 GeV
AGS pC “CNI” polarimeter
Polarization facilities at RHIC
EBIS
LSP
Notes: 2

## Slide 3
Пучки поляризованных протонов/дейтронов в коллайдере NICA
В.В. Фимушкин
p-C CNI
p-C CNI

## Slide 4
V.P.Ladygin, JINR

## Slide 5: Proton-Carbon CNI polarimeters in AGS and RHIC.

## Slide 6: AN for Coulomb -Nuclear Interference.
the left – right scattering asymmetry AN arises from the interference of
the spin non-flip amplitude with the spin flip amplitude (Schwinger)
in absence of hadronic spin – flip contributions
AN is exactly calculable (Kopeliovich & Lapidus):
hadronic spin- flip modifies the QED
“predictions”
interpreted in terms of Pomeron spin – flip
and parametrized as
µ(m-1)p µÖspphad
AN (t)
B.Z. Kopeliovich and L.I. Lapidus, Soviet. J. Nucl. Physics, 19, 114, (1974)
Notes: 6

## Slide 7: CNI –An experiments

## Slide 8: Polarization measurements on the energy ramp in AGS.
Notes: 8

## Slide 10: An experimental plot of dσ/dt vs. −t for pp elastic scattering at √s = 24.3 GeV.
0.003

## Slide 11: CNI = cross-section at 8 TeV LHC

## Slide 12: P-Carbon, 3He-Carbon analyzing power in CNI region

## Slide 13: Deuteron-Carbon analyzing power in CNI region

## Slide 14: p-Carbon Polarimetry at RHIC
Polarized proton
Recoil carbon
90º in Lab frame
Carbon target
Pbeam Required Accuracy ~5%

## Slide 15: AGS –p-Carbon CNI polarimeter
There are three pairs of detectors. The pairs
at ±45◦ measure both horizontal and vertical polarization components. The pair at 90◦ measures vertical component only.
A typical measurement (40M events) takes ~ 40 spills x 3.5 s ~3 min. and provides the statistical accuracy of the measured polarization of about P ~ 2%.
Bunch intensity – 2-3 *10^11 protons/bunch. One bunch in the ring.
810 m/c ~2.6 us. ~0.2*10^6 – target crossings in 600 ms ramp time
Carbon ribbon Target, 50 -150 um wide
3.5 mg/cm2 ~ 1.8*10^17 atoms/cm2
AGS –beam size
~ 1.0 mm -sigma

## Slide 16: Polarization in AGS, 23 GeV
Beam size
Sigma ~1.0 mm

## Slide 17: Детектор поляриметра AGS -это сборка из 12-ти Hamamatsu кремниевых пластин размером-50х5 мм2. Сигналы выводятся из вакуумной камеры наружу, где размещён 12-канальный предусилитель.

## Slide 18: Rate corrections

## Slide 19: Wide target produced by laser ablation technique ~3 times stronger
~ 25-30 nm thickness,
~ 4 micro-gram/ cm2

## Slide 22: Скорость счёта в AGS-один банч
При типичной интенсивности поляризованных протонов в банче -2.5·1011 р/банч и времени измерения на flattop AGS -1 сек, число зарегистрированных событий (ядер углерода в заданном кинематическом диапазоне, Рис.6) во всех параллельно включенных детекторах составляет 1 млн/цикл ускорения AGS. При этом ширина мишени всего -50 мкм, чтобы не превысить порог ограничений на скорость счёта системы сбора данных. При меньшей интенсивности пучка (как это может быть на начальном этапе работы в Нуклотроне), возможно компенсировать уменьшение скорости счёта увеличением ширины мишени в 10-100 раз, причём надёжность работы мишеней только возрастёт. Для измерения с 2%-статистической точностью необходимо набрать 40 млн. событий, что требует 40 циклов AGS ускорителя по 4 сек т.е. примерно 160 сек.
При типичной интенсивности поляризованных протонов в банче -2.5·1011 р/банч и времени измерения на flattop AGS -1 сек, число зарегистрированных событий во всех параллельно включенных детекторах составляет 1 млн/цикл ускорения AGS,
0.6 сек флаттоп.
При этом ширина мишени всего -50 мкм, чтобы не превысить порог ограничений на скорость счёта системы сбора данных. При меньшей интенсивности пучка (как это может быть на начальном этапе работы в Нуклотроне), возможно компенсировать уменьшение скорости счёта увеличением ширины мишени в 10-100 раз, причём надёжность работы мишеней только возрастёт.
Для измерения с 2%-статистической точностью необходимо набрать 40 млн. событий, что требует 40 циклов ускорителя по 5 сек т.е. примерно 200 сек.

## Slide 23: Comparison of the zero -emittance polarization, measured in the RHIC Run13 with the source polarization.

## Slide 24: Polarization measurements on the energy ramp in AGS.
Notes: 24

## Slide 25: The asymmetry measured on the AGS ramp as function real time. The spin flips at every integer of Gγ are due to the presence of two partial Siberian snakes.
2.3 to 23.4 GeV energy ramp.
Polarization losses -80 to 70 %

## Slide 26: Polarization at 23 GeV in AGS, Run-2017

## Slide 28: Схема вакуумной системы, мишенных узлов и детекторов поляриметров RHIC.

## Slide 29: RHIC p-Carbon CNI polarimeter

## Slide 30: New target motion mechanism
Notes: 30

## Slide 31: Detector Setup
Ultra thin Carbon ribbon Target, 20 um wide
3.5 mg/cm2 ~ 1.8*10^17 atoms/cm2
1
3
4
5
6
2
Si strip detectors
(TOF, EC)
18cm
10mm
2mm pitch 12 strips
72 strips in total
Detector port (inner view)
SSD
Bunch intensity – 2-3 *10^11 protons/bunch.
112 bunches in the RHIC ring,
~ 100 ns bunch time spacing. ~10 MHz crossing rate
~ 2*10^18 (0.3A)-number of the beam target crossings

## Slide 33
The target ladder.
Notes: 33
33

## Slide 34: Very thin Carbon strip target-20um x 25 nm L=25 mm

## Slide 35: Carbon strip target deformation due to electrostatic interaction with the beam at 255 GeV.

## Slide 37
Polarization measurements in RHIC at 100 GeV
Polarization at 100 GeV
in RHIC 60-65%.
Notes: 37

## Slide 38: H-jet CNI- polarimeter

## Slide 39: Hydrogen Gas Jet and Carbon Wire Targets.
Gas Jet Target
Carbon Wire Target
Beam Cross Section

FWHM~1.8mm
Average Pave
Peak Ppeak
Notes: 39

## Slide 40
H-jet polarimeter
17 October 2017
PSTP 2017. HJET in RHIC Run17.
40
Notes: 40

## Slide 41: H-Jet polarimeter.
RHIC proton beam
Forward scattered
proton
H-jet target
recoil proton
Ptarget is measured by Breit- Rabi Polarimeter
<5%
Elastic scattering: Interference between electromagnetic and hadronic amplitudes in the Coulumb-Nuclear Interference (CNI) region.
Notes: 41

## Slide 42: Spin filtering technique. Atomic Beam Sources.
Hydrogen atoms with electron polarization: mJ=+1/2 trajectories
RF transition, polarization transfer
from electrons to protons
RHIC beam crossing
Breit-Rabi polarimeter
Ne-Fe-B permanent magnet
sextupole - 1.7 T
gradient 5.7 T/cm
Magnet system design, NIM A256, (2006)
T.Wise, W.Haeberli, H.Kolster et al.
Notes: 42

## Slide 43: Recoil detector can detect H-Jet-target !
Fix RHIC proton beam position (diameter  ~1mm).
Move H-Jet-target system for every 1.5 mm step.
Using RHIC-beam and Recoil detector
Using 2.0 mm diameter compression tube
Find the best collision point !

## Slide 44: H-jet as a luminescence beam intensity profile monitor

## Slide 45
Ch#1
source for energy calibration
241Am(5.486 MeV)
How to identify elastic events ?
proton beam
Forward scattered
proton
proton target
recoil proton
Array of Si detectors measures TR & ToF of recoil particles.
Channel # corresponds to recoil angle R.
2 correlations (TR & ToF ) and (TR & R )  the elastic process
Ch#2
Ch#3
Ch#4
Ch#5
Ch#6
Ch#7
Ch#8
Ch#9
Ch#10
Ch#11,12
Ch#13
Ch#14
Ch#15
Ch#16
Ch#1-16
Ch#  R, R big  TR big  fast protons
R
Ch#1
#16

## Slide 46: P-P Collision chamber

## Slide 47
47
New Si-strips detector assembly. Better energy resolution. Large solid angle and kinematic range.

## Slide 49: Absolute Beam Polarization measurement in Run 2017, 255 GeV
Statistical error summary:
PSTP 2017. HJET in RHIC Run17.
49
A typical result for 8-hrs store: ‹ P › = (~ 56 ± 2.0 stat ± 0.3syst) %
Notes: 49

## Slide 50: H-jet polarimeter at RHIC
The polarized H-jet target thickness is 1.2∙ 1012 atoms/cm2 and with RHIC circulating current ~ 0.3 A (110 bunches 2∙ 1011 bunch intensity, 1.8∙1018 protons/s) the luminosity is 2.2 ∙1030 cm-2s-1
“Point” like target is greatly beneficial for elastic event identification.
The polarimeter Si-strip detectors covers all kinematic range of recoil protons (in CNI region) and about 20% solid angle which gives the statistical accuracy for one 8 hrs store about 2.0%.
The proton polarization is mostly determined by the holding field magnetic field 1.2 kG and is equal to 95.5% (efficiency of the RF transitions are 99.88 % and the polarization dilution by the molecular gas contamination does not exceed 0.5%). At 1.5 kG polarization is 97%.

## Slide 52: H-jet is the absolute high precision polarimeter !
High (~4.5%) analyzing power in a wide energy range (23-255 GeV).
High event rate due to high intensity (~300 mA) circulated beam current in the storage ring and high polarized H-jet thickness in the collision point.
Non-destructive.
No scattering for recoil protons.- windowless.
“Point” like target. Clean elastic scattering event identification.
Straightforward calibration with Breit-Rabi polarimeter.
Most of the false asymmetries are cancelled out in the ratio:
P beam =( 1/A)Beam asym / Target asym
A typical result for 8-hrs store: ‹ P › = (~ 56 ± 2.0 stat ± 0.3syst) %
Notes: 52

## Slide 53: CNI – H-jet polarimeter with the unpolarized hydrogen cluster-jet
The accuracy achieved in determining AN(t) allows one to use a higher density unpolarized hydrogen jet target in a high precision absolute polarimeter.
The unpolarized H-jet thickness of a 1014 -1015 H2/ cm2 can be produced by the cluster-jet technique, which was developed for the PANDA experiment at GSI[29].
Considering a possibility to increase the recoil proton detectors solid angle, one can expect 1000 times higher elastic pp event rate compared to that in the RHIC HJET measurements.
For such a polarimeter, only a 3 min. exposure is needed to determine the beam polarization with a statistical accuracy of stat P~ 1%, while the systematic uncertainty can be kept as low as ΔP /P ~1%.
Therefore, an unpolarized jet can also provide accurate measurement of the polarization decay time and, with additional detectors at different azimuthal angles, the beams spin tilt.

## Slide 54: Back-up slides

## Slide 56
A.Poblaguev, PSTP 2017

## Slide 57
Proton polarization measurements in AGS and RHIC at the beam energies 24-250 GeV) are based on Proton-Carbon and Proton-Proton ( H-jet polarimeter) elastic scattering in the Coulomb Nuclear Interference (CNI) region.
The CNI polarimeters are the essential tools for polarized proton acceleration setup and operation and provide polarization values for RHIC experiments.
Polarimeter operation in the scanning mode also gives polarization profile and beam intensity profile (beam emittance) measurements. Bunch by bunch emittance measurements is a very powerful tool for the machine setup.

## Slide 58: Polarized Proton Polarimetry from the Source to RHIC energies
A polarimeter has to satisfy the following requirements:
Beam polarization monitor for Physics ( < 2% )
Several samples over a reasonable time period, one fill (pol.decay)
Beam polarization diagnostic and Machine tuning tool
Sample on demand and online, fast/within minutes
Low systematic errors.
A large dynamic range & Energy independence
Large analyzing power, large cross section, & low background

## Slide 60
72.7%
Polarization measurement in AGS at 24 GeV.
Polarization out of AGS
60-70%
Notes: 60

## Slide 61: RHIC CNI polarimeter

## Slide 62: RHIC CNI polarimeter

## Slide 63: Polarization measurements in the AGS p-Carbon polarimeter
В этом случае углеродная ленточная мишень с поверхностной плотностью ~3,5 мкг/см2 [Jinnouchi (2004)] содержит 1,75⋅1017 атомов углерода/см2,
что позволяет достигнуть светимости порядка - L = 3,5⋅1034 см–2 с–1.
Считая сечение для установки порядка 9,5 мб, можно
ожидать темп счета порядка 3,3⋅108 событий/с.

## Slide 64
The p-Carbon analyzing power used in data analysis(left). The filled area highlights the kinetic
energy range for the polarization measurements. A typical events distribution in one Si-strip accepted by the DAQ (center).
Polarization measurements in the AGS p-Carbon polarimeter

## Slide 65: Rate corrections

## Slide 66: AN for p-p elastic scattering at −t=0.15(GeV/c)2 as a function of laboratory beam momentum.

## Slide 67: Схема вакуумной системы, мишенных узлов и детекторов поляриметров RHIC.