## Slide 1: Status of Forward Hadron Calorimeter (FHCal) at MPD
A.Ivashkin
on behalf of the FHCal MPD group
Dubna - Moscow

## Slide 2
Tasks: measurement of the geometry of heavy ion collisions:
The centrality of the collision;
b) The reaction plane orientation.
FHCAL
Two arms of hadron calorimeters at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules of ~1.1x1.1 m2 each part.
The forward hadron calorimeter in MPD setup

## Slide 3
Compact ZDC of 20 modules with high granularity.
Extended HCAL of 120 modules with high granularity
Simple, cheap.
Low acceptance,
Poor event plane resolution,
Problem with centrality,
Excessive segmentation.
High acceptance,
Nice event plane resolution.
Very expensive,
Complicated,
Excessive segmentation.
FHCAL of 44 modules:
Optimum segmentation,
High acceptance,
Nice event plane resolution, Centrality measurement,
Reasonably simple and cheap.
transverse sizes 10x10 cm2
transverse sizes 15x15 cm2
Final structure
Interaction length Λi~20 cm defines both longitudinal and transverse sizes of hadron shower.
Evolution of FHCAL geometry.

## Slide 4
Structure of FHCal – two left/right arms.
Each arm:
44 modules;
Beam hole;
Weight – 9 tons.
Modular Lead/Scintillator sandwich compensating calorimeter. Sampling ratio Pb:Scint=4:1.
Light from scintillator tiles is captured by WLS-fibers and transported to SiPM.
Each module:
Transverse size - 15x15cm2 ;
Total length - 106 cm.
Interaction length ~4 λint;
Longitudinal segmentation – 7 sections;
1 section ~ 0.56λint;
7 photodetectors/module;
Photodetectors – silicon photomultipliers (SiPM).

## Slide 5
Permanent quality control of scintillator tiles,
WLS-fibers and gluing is performing with 90Sr β-source.
Stages of FHCal production: scintillators.
Tests of different grooves and reflectors
Scintillator tiles with WLS-fibers.
Scintillator tiles in TYVEC reflector.
FHCal scintillator tiles and modules are assembled in workshop of INR, Moscow.

## Slide 6
Stages of FHCal production: modules.
At present, almost half of FHCal modules are ready for the tests.
All FHCal modules will be ready in 2019.
Tests of modules with cosmic muons are done in parallel with the development of Front-End-Electronics and readout.
Lead absorbers and mechanics.
Lead and scintillators sandwiches in box.
WLS-fibers are aligned.
Optical connectors are polished.

## Slide 7
Tests of FHCal modules with cosmic muons.
A few track geometries are considered:
Horizontal muons (low statistics),
Inclined tracks passed through 2 or 3 sections.
Section #
Section #
Dependence of light yield in modules
Light yield ~40 ph.e. per 5 MeV of deposited energy is rather high for reliable energy calibration with muons.
Higher light yield for shorter WLS-fibers

## Slide 8
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
7 channels:
two-stage amplifiers; HV channels;
LED calibration source.
Photodiodes, FEE and readout electronics.
Front-End-Electronics:
A first samples of FEE with MPPC photodetectors were developed and produced.
MPPC
Integrator
ADC
τ ~ 20ns
Amp
FEE
Dt ~ 50 ns
Hamamatsu MPPC: size – 3x3 mm2;
pixel -10x10 µm2;
PDE~12%.
Photodetectors:
Full readout chain was tested with cosmic muons and at beam!
Dt ~ 200 ns

## Slide 9
Slow control and monitoring system.
HV system and LED-monitoring is based on the developments of HVSYS Co., Dubna
MPPC gain stabilization – by HV correction with temperature.
HV and SC-box
Dependence of MPPC gain on temperature.
T-sensor
All MPPC are placed on Al-plate.

## Slide 10
Test of calorimeter supermodule at CERN T9 line.
Proton momentum range: 3-10 GeV/c
Supermodule consists of 9 (3x3) CBM modules.
The FEE and readout are designed for MPD (BM@N) experiment.
Each module has 10 longitudinal sections with 10 SiPMs at the end.
Full size 60x60x160 cm3.
Weight ~ 4.5 tons.

## Slide 11
Muons energy deposition spectra in 10 sections
of central module.
Sect. 1
Sect. 2
Sect. 3
Sect.4
Sect. 5
Sect. 6
Muons deposit
~5 MeV
in one section
Calibration of longitudinal sections with beam muons, 6 GeV/c
Identification of muons – equal energy deposition in first and last half of modules.
Sect. 8
Sect. 9
Sect. 10
Sect. 7
E2 [MeV]
E2 [MeV]
E1 [MeV]
E1 [MeV]

## Slide 12
Spectra of energy sum in first n sections in central module,
protons 3 and 6 GeV/c.
Some part of protons has only ionizing energy loss without hadron shower in first sections.
p= 3 GeV/c
p= 6 GeV/c
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
MeV
In 7th section the low energy ionizing peak is disappeared. Energy spectrum has Gaussian shape.

## Slide 13
Comparison of amplitude spectra in sections, protons 6 GeV/c.
E [MeV]
----- MC
----- experiment
----- MC
----- experiment
----- MC
----- experiment
----- MC
----- experiment
Section 1
Section 4
Section 3
Section 2
E [MeV]
E [MeV]
E [MeV]
Experimental and simulation spectra are in good agreement.

## Slide 14
Energy resolution for full supermodule.
⨁b ⨁
Linearity of response.
The stochastic term of ~56% practically doesn't depend on the fitting function.
Good agreement with MC results.
The noise term is almost zero.

## Slide 15
Central module
Full supermodule
Dependence of energy resolution on supermodule length.
The energy resolution for central module and for full supermodule is practically constant starting from the 7 longitudinal sections.
Length of 4λI or 7 longitudinal sections is optimum for momentum range 3-6 GeV/c
p= 6 GeV/c
Longitudinal profile of hadron shower in central module.

## Slide 16
Magnet pole alone (left), with FHCal (middle) and endcup detectors (right).
Mechanical platform is under design at JINR now.

## Slide 17
Timetable.

## Slide 18
Technical design of the MPD FHCal is finished.
First half of FHCal modules is produced already.
The basic components are purchased almost for the full calorimeter production.
First samples of Front-End and readout electronics are ready and tested.
Beam tests at NICA energies (T9, CERN) confirmed the expected parameters of FHCal modules.
Tests and the calibration of FHCal modules with cosmic rays are ongoing.
Service systems are in development state.
The production of all 90 FHCAl modules is expected in 2019.
Conclusions.
Notes: That is all. In conclusion I would like to say that:

## Slide 19
Thank you!

## Slide 20
Influence of FHCal acceptance at event pane reconstruction.
Calorimeter with diameter 100-120 cm has an appropriate accuracy in event plane reconstruction in all range of beam energies.

## Slide 21
Event plane and centrality resolution.
Modules 15x15 cm2 are optimum choice and fit the transverse size of hadron showers (interaction length of lead+scint. λI~20 cm).
Energy deposition in FHCal isn’t monotonic due to beam hole and can’t resolve the central and peripheral events.
The event plane resolution of 200-250: two arms of FHCal (maximum spectator multiplicity) and no influence of magnet field.
The ambiguity in centrality determination can be resolved by taking track multiplicity in TPC.
Or by using other observables in FHCal.
=11 GeV

## Slide 22: Other FHCal observable for the centrality measurement.
Let’s construct energy asymmetry:
d 3He
t 4He
π+ π-
π+ π-
π+ π-
Mainly, fragments are produced in peripheral collisions and located near beam hole.
Depending on centrality there must be difference in the energy depositions in inner and outer parts of calorimeter.
while pions are produced
in central collisions.
=5 GeV
=11 GeV

## Slide 23
Calculation of centrality from energy asymmetry – energy correlation.
The resolution of impact parameter for central events is determined by low spectator multiplicity.
Energy and asymmetry bins are used for the calculations.
More advanced analysis can improve the resolution!
Inspite of beam hole FHCal can resolve the central and peripheral events.

## Slide 24
Protons
Neutrons
Fragments
Pions
Protons
Neutrons
Pions
Fragments
Protons
Neutrons
Fragments
Pions
b < 6 fm
b > 6 fm
Occupancy (particles/events/cm2) at front of FW/FHCAL.
Projection at X-axis

## Slide 25
Protons
Neutrons
Fragments
Pions
Protons
Neutrons
Pions
Fragments
Protons
Neutrons
Fragments
Pions
b < 6 fm
b > 6 fm
Occupancy (particles/events/cm2) in front of FW/FHCAL.
Projection at X-axis

## Slide 26
AuAuss11mb AuAuss5mb
Without FWALL acceptance cut
Pseudorapidity distributions in FW/FHCal acceptance
Protons + neutrons
Fragments
Pions
All particles
Acceptance of FW/FHCAL

## Slide 27
only charged spectators (protons and fragments)
All charged particles (+pions)
Angular resolution of event plane for FW at different energies.
The best resolution of event plane is about 300-400 in case of charged spectators only.
For all charged particles the resolution increases to 500-600 for low energies and is drastically worse at highest energy.
Weight wi=1.

## Slide 28
Centrality resolution with FW at different energies.
The FW centrality resolution is significantly worse comparing to FHCal.

## Slide 29
First CBM module is already installed at BM@N.
MeV
Ar-peak in CBM module.
MeV
section#
Shower profile
Notes: That is all. In conclusion I would like to say that: