## Slide 1: DAQ ELECTRONICS at BM@N
AFI Electronics group:
Andrey Terletskiy, Ilya Slepnev, Alexey Shutov, Alexey Baskakov, Andrey Schipunov, Ivan Fillipov, Nikita Tarasov, Vyacheslav Slepnev, Sergey Bazylev

## Slide 2: Interface Modules

## Slide 3: FVME2 & CCB-PCIe
PCI-Express M-Link interface
VME64x Master, System Controller
SFP serial link 2 Gbps
TTC Bus input for spill and trigger
Optional VXS

## Slide 4: FVME2TMWR
Trigger, Timing and Control Module for VMEDAQ system
TTC Bus master. Generate clock, trigger and spill signals
4 software configurable TTL I/O
32 ECL/LVDS trigger inputs
White Rabbit time synchronization support
QSFP connector for clock, trigger synchronization
Optional VXS

## Slide 5: Waveform digitizers

## Slide 6: ADC64s2
Used for digitizing signals from:
ZDC
ECAL
GEM
(ADC64VE)

## Slide 7: ADC64s2
64-channel 12-bit 62.5 MS/s ADC device with signal processing core and Ethernet interface
Capable of time synchronization by White Rabbit network
Optional QSFP connector may be used to provide external clock for very high precision measurements as well as trigger and readout links
Low noise power supply mezzanine board P4S with input range from 5 V to 12 V
2 hardware configurable LEMO TTL/IO

## Slide 8: ADC64VS
64 single ended or differential inputs
TTC (VME mode) or White Rabbit (Standalone mode) synchronization
Ethernet or VME64x data transfer
In Production
14 bit 62.5 Msps ADC
PoE or VME power supply
2 hardware configurable LEMO TTL I/O
Optional VXS

## Slide 9: Time to Digital Converters

## Slide 10: TDC72vhl
is VME64x 72-channel 25 ps multihit timestamping TDC
mRPC (ToF-400)
T0

## Slide 11: TDC72vhl
72 differential 100 Ω LVDS inputs
is VME64x 72-channel 25 ps multihit timestamping TDC
VME mode:
  VME64x for data transfer
  TTC Bus for Clock and Trigger
Standalone mode:
  Ethernet or M-Link data transfer
  Time synchronization by White Rabbit

## Slide 12: TDC32VL
32-channel LVDS 25 ps multihit timestamping TDC
mRPC-2 (ToF-700)

## Slide 13: TDC32VL
32-channel LVDS 25 ps multihit timestamping TDC
32 differential 100 Ω LVDS inputs
VME64x interface
TTC Bus for clocking and triggering
TDC64VHLE under development:
  64-channel 25ps multihit timestamping TDC
  White Rabbit supported
  VME or Standalone mode
  VME64x or Ethernet data transfer
  PoE or VME power supply

## Slide 14: TDC64
VME64x 64-channel 100 ps multihit timestamping TDC
Drift Chambers

## Slide 15: TDC64
VME64x 64-channel 100 ps multihit timestamping TDC
64 differential 100 Ω ECL,PECL or LVDS inputs
VME64x interface
TTC Bus for clocking and triggering

## Slide 16: DRE & Auxiliary modules

## Slide 17: HRB6ASD
96 channels readout module for MWPC
MWPC

## Slide 18: HRB6ASD
96 channels readout module for MWPC
96 differential inputs
Ethernet data transfer
RJ45: clock, trigger, timestamp, spill, busy
PoE power supply
Optional: SFP for white rabbit

## Slide 19: TTB9
Trigger and Timing Distribution Board for HRB6ASD
9 RJ45 for trigger and timing distribution
TTC Bus or White Rabbit synchronization

## Slide 20: U40VE
Universal 40 I/O VME64x board with White Rabbit support
40 sofware configurable I/O
TTC or WR synchronization
PoE, VME or external power supply

## Slide 21: UT24VE
24 software configurable TTL I/O (trigger out/ busy in)
WR or TTC synchronization
PoE, VME or external power supply

## Slide 22: Thank you