## Slide 1: Forward Si tracking detectors Zamyatin Nikolay on behalf of BM@N Collaboration
THE SECOND COLLABORATION MEETING OF THE MPD AND BM@N EXPERIMENTS AT THE NICA FACILITY
October 29-30, 2018, DUBNA, RUSSIA

## Slide 2: Contents
Setup of Si-planes in February-April_2018
Main results
Problems for FE chips without beam zone in Si planes (big amplitudes of ions signal ∆E)
Setup of Si-planes with beam hole for 2020
Conclusion

## Slide 3: Design and position of Si-planes on the beam-channel BM@N, Session #55 (February-April’18)
Si-Forward plane
Si-Vertex plane-1
Si-Vertex plane-2
beam
target
Si-multiplicity detector
Si-Forward plane consist of two-coordinate Si sensors X-X’(±2.5o) with strip pitch of 95/103 μm, sensitivity area 25 × 25 cm2 , 10240 strips
Vertex plane-1 consist of 4 modules with sensitivity area 12,5×12,5cm2, 5120 strips
Vertex plane-2 consist of 2 modules with sensitivity area 12,5×12,5cm2, 2560 strips
Si-planes

## Slide 4
DSSD with DC topology don’t contain integral resistors and capacitors (RC), therefore external R, C are required to supply bias voltage to each strip and to electrically decouple the DC current from the electronic inputs. This role is performed by Pitch Adapter (PA) with a topology of two types for p+ and n+ sides of the detector. In addition, PA has topology of contact pads similar to chips located on the side of electronic chips. PA modules are made on sapphire plates with an epitaxial layer of silicon (SOI). Integrated poly silicon bias resistors have a value of 0.7 – 1.0 MΩ, decoupling capacitors have a value of 140 pF. PA is assembled together with read-out ASICs on the read-out card. Positive polarity signals come from detectors to P+ read-out card (black PCB) while negative signals come to N+ read-out card (red PCB).
The functional scheme of detector module and appearance of two electronic boards

## Slide 5: Three types of Si-modules for Vertex and Forward planes
Vertex plane-1
Forward plane and
Vertex plane-2
Forward plane
of beam region

## Slide 6: Carbon beam position in Si-planes for SRC-setup
Run 3467:
Beam-C, no target
Beam duration: 2.5 sec. Flux: 25k, MF=107.6 mv, 100K events, Air Empty, BC2-prime 1640 V
beam
target

## Slide 7: Reconstruction of the primary vertex Si+GEM track (>=2 track), Ar-beam, Cu-target/1.67 mm (slide from G.Pokatashkin et al.)
Primary Vertex resolution of Z-coordinate Ϭz = 1.8 mm at target thickness = 1.67 mm (without pile-up suppression)

## Slide 8: Track residual of Si-2 (plane) vs Si+GEM track in magnetic field (slide from G.Pokatashkin, Yu.Gornaya, M.Kapishin, I.Rufanov, V.Vasendina, A.Zinchenko)
Si-2 plane residual Ϭ = 67.5 µm vs Si+GEM (>=7 hits/track) track at H = 0 Tl
Si-2 plane residual Ϭ = 89.4 µm vs Si+GEM
track at H=0.6 Tl

## Slide 9
Tracks in forward silicon strip and GEM detectors in Ar run
(slide from G.Pokatashkin et al.)
Si-3 detector X-residual vs GEM+Si track ~ 86 μm
GEM-1 detector X-residual vs GEM+Si track ~ 320 μm
GEM-1 track profile
Si-3 track profile Si-2 track profile Si-1 track profile

## Slide 10: Effect of limitation (DR)dynamics range FE chip (VATAGP7) at big signals from Si-sensors
(a) – test=30fC
(d) – test=500fC
(c) – test=500fC
(b) – test=1pC
Test pulse
Track&Hold
Clock MUX
Output S/A
(a) – input test (ch#0) of 30 fC corresponds to DR =30 fC (~8 m.i.p./300 mkm/Si) and not visible limitation amplitude effect. Output MUX-ch#0 has no signal because S/A pulse not coincidence with T/H.
(b) – input test (ch#0) of 1 pC (~250 m.i.p./300 mkm/Si) much more of DR and amplitude of S/A-pulse is limitation by DR. Output MUX – ch#1 and ch#2 has wrong signal because T/H pulse latches crosstalk reverse polarity on ch#1 and ch#2 inputs.
Pictures (c) and (d) shows two time position of 500 fC input signal (~125 m.i.p./300mkm/Si) in ch#0. On (d)- picture input signal coincidence with T/H pulse and we can see output MUX-ch#0 (big amplitude correspond of DR=max) and MUX-ch#1÷ch3 amplitudes correspond of crosstalk direct polarity.

## Slide 11
Row data: run_1913 (Pb-target), C-beam_ 4.5GeV/n, M8_1 event 325: (session #54, March’17)

## Slide 12: Design and position of Si-planes on the beam-channel BM@N, Session’2020)
Beam pipe

## Slide 13: Three sizes of Si-planes for session-2020
Si-plane #1
Si-plane #3
Si-plane #2

## Slide 14: Conclusion
Three Si-coordinate planes in forward part of GEM-tracker improve Z-accuracy of the primary Vertex up to 1.8 mm at thickness target 1.67 mm (slide #7)
Total number of the strip channels for three Si-planes-2018 equals 17920 pcs and 140 ADC ch
X-coordinate track resolution in Si-planes vs Si+GEM track is 67.5 µm, H=0 Tl (slide#8)
New Si-forward part tracker design have square (60×60)mm2 hot zone for ions beam
Si-forward part tracker-2020 will be increased up to 53760 strips channels and 420 ADC ch. Active area is 0.35 m2 with overlapping of GEM part in X-direction (slide #12)

## Slide 15: Backup slides

## Slide 16
Beam pipe
(diam. 50 mm)

## Slide 18
Primary Vertex with Si detector vs without Si detector
Carbon run, March 2017
Fragments of Kr beam in Si vertex detector, April 2018
Residuals of Si hits to GEM tracks. Carbon run, March 2017 → accuracy is defined by GEM track resolution
(Slide from M. Kapishin)

## Slide 19: Position of Si-monitors for measurements of radiation background on beam area BM@N
# Si-monitor | Position | Equal neutrons Ф<1MeV>, cm-2
#1 | Center of BC1 | 4,19×1010
#2 | Top BC1 | 2,44×108
#3 | FE-PCB Forward-Si | 3,35×109
#4 | Bottom of BC1 | 4,72×109
#5 | Si-multiplicity trigger (top part) | 1,25×109
1
2
3
5
4
Chart: IV characteristic of Si-monitors (13mm2/260µ)

## Slide 20
Row data: run_1898 (CH2 – target), C-beam_4.5GeV/n, M8_1 event 6535; (session #54, March’17)

## Slide 21: Signals from passing through the module of relativistic electrons (106Ru)

## Slide 22: Kr-beam position in Si-Vertex detector, April 2018 (Session #55)
Run 5039:
Kr – 2,6GeV; Beam Triger + BD > 3; Target No; SP41 = 1150,
SP57 = 50, VKM = 125; Cluster Size > 2
Si-Vertex plane-1
Si-Vertex plane-2

## Slide 23: Ar-beam position in Si-Vertex detector, April 2018 (Session #55)
Run 4599:
Ar – 3,2GeV; Beam Trigger + BD > 3; Target No; SP41 = 1250,
SP57 = 0, VKM = 140; Cluster Size > 2
Si-Vertex plane-1
Si-Vertex plane-2

## Slide 24: Fragments of C-beam in Si-Vertex detector, April 2018 (Session #55)
Run 3481:
C – 3,17GeV; Trigger SRC IT; Target Pb 9mm; SP41 = 1400,
SP57 = 0, VKM = 0; Cluster Size > 2
Si-Vertex plane-1
Si-Vertex plane-1

## Slide 25
Region of US-bonding between PADs-chip (VATAGP7) and PADs-pitch adapter (PA-640)
PA-640
VATAGP7

## Slide 26: Visual control in LHEP of the PCBs-640 before encapsulation of VATAG7-chips
Red PCB-640n+ (№007), chip#2, the type of defect: the small piece of the Al-wire Ø18 µ on the surface PCB

## Slide 27: The read-out electronics is designed and based on the non-encapsulated ASICs crystals – VATAGP7.1, manufactured by IDEAS2 (Norway). Each board contains five ASICs, bonding and filled with black compound
The main parameters of the analogy part of this IC:
Number of analog inputs – 128;
The polarity of the input signals – +/-;
Gain – 16,5 μA/fC;
Dynamic range of signals – ±30 fC (~8 m.i.p.);
Integration time (slow SA) – 500 ns;
Integration time (fast SA) – 50 ns;
Intrinsic noise (at Cin = 0 pF) – 70 e;
Dependence of noise on input capacitance – 12 e/pF;
The main parameters of read-out electronics card:
Number of analog inputs – 640;
Five analog multiplexer output with read out clock - 1.25 MHz
Input charges from -30 fC to +30 fC
Slow shaper shaping time - 0.5 µs
Fast shaper shaping time -50 ns
Differential current out – 20 µA/fC
Adjustable threshold, from 0.12 fC min, (at 0 load)
Power supply -2.0 V and +1.5 V
Total power is 280 mW / ASIC
For reminder: the value of the signal 1 m.i.p.(Si=300mkm)=4 fC (~24×103 e)

## Slide 28
Ultrasonic bonding of the strip to strip between two DS-Si-sensors on module

## Slide 29: Progress of Si-coordinate planes after session#54(March’17)
100% working capacity of Forward plane 250×250mm2 (10240 ch);
New design (1/2 beam hole) of Forward plane for SRC-setup;
Two new Vertex-planes (V1=5120ch; V2=2560ch);
Number of ADC channels – 140 (4 modules ADC + 4 modules U40-sequencer) Many thanks for DAQ-group (S. Bazylev)! ;
Design of Si-plane was optimized for SRC-setup (without beam hole in Vertex Si-planes);
Readout time of FE-chips was decreased more than 3 times (up to 34µsec; Fmux=3.905MHz).