## Slide 1: On development of diagnostic systems for Nuclotron extracted beams A.A.Baldin October 30, 2018

## Slide 2
Diagnostic systems of the accelerator complex
MCP-based profilometer
Diagnostic system at the beam output
Diagnostic system in the experimental hall

## Slide 3
Nuclotron
~160 m
BM@N
Building 205
RUN 55 - 2018

## Slide 4: Diagnostics of circulating beam
Детектор монитори-рования пучка
Creation of modern nondestructive control systems of space-time characteristics of the beam during acceleration and extraction is the one of the most important tasks for exploitation of the Nuclotron accelerator complex (JINR LHEP).
The detector was developed for registration of the space-time characteristics of the radial beam component. The system provides measurements in the intensity range of 106 – 108 for singly charged ions which is not covered by existing measuring devices.
Nuclotron
The detector based on
microchannel plates (MCP)
The warm section of Nuclotron

## Slide 5: Diagnostics of circulating beam. Deuteron 2 GeV/n.
Radial beam profile.
The graph of an accelerator cycle with fast beam extraction (50 ms) at an intensity corresponding to the upper limit of the detector operating range (108 single charged ions). At the beginning of the acceleration (the first 0.5 seconds from the time of injection) the detector is overloaded. After transition to the constant magnetic field the beam extraction is produced (3 seconds after injection moment) and than the circulating beam remnants is registered.
Time, s
Beam
Coordinate, mm
The beam extraction area
Beam remnants continue to circulate
Injection
Detector overloading

## Slide 6: 2014.06 – циркулирующий пучок Ar+16.
Динамический профиль циркулирующего пучка Ar+16 500 МэВ/нуклон.
Ar 500 MeV/n

## Slide 7: Диагностика пучка в зоне вывода из Нуклотрона.
Nuclotron ring
Beam extraction
Detectors
Extraction region (top view)
Extraction region (side view)
Beam

## Slide 8: Диагностика пучка в зоне вывода из Нуклотрона.
Nuclear photoemulsions
  Ionization chamber
Thin scintillation counter
Scintillation profilometer
Area of the beam extraction
Nuclotron ring
Beam extraction
Detector stations

## Slide 12: Run 50. Diagnostics of the extracted beam. The beam orbit shifting.
Ar 500 MeV/n
Time, ms
X Coordinate, mm
Horizontal dynamic profile of the extracted beam of Ar+18 500 MeV/n.
Dynamic profile of the circulating beam registered by the MCP detector.

## Slide 13: Run 50. Diagnostics of the extracted beam. Spatial Distribution.
Vertical dynamic profile of the extracted beam of Ar+18 500 MeV/n.
Time, ms
Y Coordinate, mm
Time, ms
X Coordinate, mm
Horizontal dynamic profile of the extracted beam of Ar+18 500 MeV/n.
The spatial distribution of the extracted beam was registered by the scintillation profilometer (hodoscopic PMT Hamamatsu; X, Y – 16 channels; step – 3 mm)

## Slide 14: Diagnostics of circulating beam. Deuteron 4 GeV/n
Radial beam profile (top graph) and magnetic accelerator field (bottom graph).
Time, s
Magnetic
Field, T
Beam
Coordinate, mm
Time, s
Beam
Width, mm
Beam
Coordinate, mm
Radial beam coordinate (top graph) and beam width (bottom graph).
Injection moment
Beam orbit shifting
The beam interacts with the vacuum chamber
Acceleration

## Slide 15: Диагностика пучка в экспериментальном зале фокуса Ф-3.
Focus F3
Detectors
Magnet SP-94
Magnet SP-12
Lenses
Lenses
Экспериментальный зал фокуса Ф-3
Beam

## Slide 16: Kr 2,5 GeV/n
C
Ar
Kr

## Slide 18: Kr 2,5 GeV/n

## Slide 19: ARGON Ar_File 20180328-213035.dat pos1X=185mm, pos2X=-95mm, pos2Y=470, th1=7mV,th2=15mV, HV1=1061V,HT2=1190Vstart from Xp2 The amplitude of the signal in the scintillators

## Slide 20
Z8
Z7
Z6
Z5
Z4
Z3
Z2
Z1
Run 55 Carbon – file 2018/ 03/ 14 - 17/ 45 /51

## Slide 21
Carbon 3.16 AGeV

## Slide 22
Пролетная база = 33,5 м

## Slide 24: Сеанс 51. Диагностика пучка углерода 3,5 ГэВ/нуклон.
Dynamic beam profile of 3.5 GeV/n C

## Slide 25
1 mm

## Slide 26: Сеанс 51. Диагностика пучка углерода 3,5 ГэВ/нуклон.

## Slide 27: Сеанс 51. Диагностика пучка углерода 3,5 ГэВ/нуклон.

## Slide 28: Сеанс 51. Диагностика пучка углерода 3,5 ГэВ/нуклон. Ионизационные потери частиц в сцинтилляторе.
Частица | Энергия, ГэВ/н | dE/dx, MэВ/мм (сцинтиллятор) | 
 | 3,5 | 8,22 | 0,110
 | 2,0 | 8,25 | 0,161
 | 3,5 | 8,2 | 0,120
 | 2,0 | 8,3 | 0,176
 | 3,5 | 8,22 | 0,074
 | 2,0 | 8,25 | 0,108
 | 3,5 | 5,7 | 0,100
 | 2,0 | 5,7 | 0,147
 | 3,5 | 3,6 | 0,088
 | 2,0 | 3,6 | 0,129
 | 3,5 | 2,1 | 0,074
 | 2,0 | 2,1 | 0,108
 | 3,5 | 0,94 | 0,074
 | 2,0 | 0,95 | 0,108

## Slide 29: Dynamic profile and time structure of the beam
Circulating beam
MCP based detector
Vacuum 2×10-6 Pa
Intensity d ≥ 106
Intensity Ar+16 ≥ 104
Intensity Au+65 ≥ 5×103
Extracted beam
MCP based detector
Vacuum 1×10-3 Pa
Intensity d ≥ 108
Intensity Ar+18 ≥ 106
Intensity Au+79 ≥ 3×104
Notes: Детектора предназначен для диагностики пучка многозарядных ионов. Пучки тяжелых ионов на Нуклотроне имеют интенсивность не превышающую 10^8. Так как на Нуклотроне не было детектора способного чувствовать данные интенсивности, возникла потребность в таком детекторе. Была создана система для определения пространственно временных характеристик пучка (профиль; радиальная координата пучка в вакуумной камере, ширину пучка, а также характерные частоты колебаний и качество проводки пучка в моменты инжекции, ускорения и вывода).

## Slide 30: CONCLUSIONS
In order to provide adequate beams at BM&N setup it is required to:
Equip all magnetic elements with Hall sensors;
Vacuum the whole beam line;
Manufacture 4-5 detector stations for
  beam adjustment,
  beam monitoring;
  All information from these detectors (beam position, time structure, channel transportation mode) should be sent to the accelerator control room and be available to users.

## Slide 31: Run 50. Calibration of the thin scintillation counter and the scintillation profilometer
Photo of manifested nuclear emulsion of Ar+18 beam.
Photo of nuclear emulsion. Zoom 200.
Profile of extracted beam registered by nuclear photoemulsion.
Vertical Coordinate, mm
Horizontal Coordinate, mm
Beam shifting
Beam shifting

## Slide 32: Study of the impact of irradiated samples on the monitoring system
A Lead Sample
The place of irradiation samples
To explain the differences of the activation analysis method between the groups we studied the effect of the samples impacting on the beam parameters and on the monitoring system.
To study this effect, we placed lead samples of different thickness between two ionization chambers. Then we observed dependence of the ratio of two chambers from the lead thickness.
The lead samples:
Pb 1 mm;
Pb 2 mm;
Pb 3 mm.
Ionization Chamber 1
Ionization Chamber 2

## Slide 33: Study of the impact of irradiated samples on the monitoring system
This result was obtained at the constant beam intensity
Relative intensity of the extracted beam at the measurement time. Deuteron 2 GeV/n.
Histogram of the dependence of the ratio of two chambers from the lead thickness.