## Slide 1
DYNAMICS SIMULATIONS
OF THREE-COMPONENT ION BEAM
IN HILAC-BOOSTER TRANSPORT CHANNEL
Tuzikov A.

## Slide 2
Beam transfer from HILAC to Booster
Goals
Accumulation of required intensity of ions in Booster by means of several methods of beam injection.
Commissioning: March 2019
Beam parameters
Ions | Au31+
Energy, MeV/u | 3.2
Magnetic rigidity, T m | 1.6
Electric rigidity, MV | 40
Ion number | 2∙109
HILac
Booster

## Slide 3
The beam transport with minimal ion losses.
The beam debunching.
The beam matching.
Separation and adsorption of neighbor charge states of ions.
Providing different schemes of the beam injection into the Booster.
Main goals
HILAC-Booster beam transport channel
Beam transport in the median plane of the Booster.
The debuncher in non-dispersive region of the beam transport channel.
Features

## Slide 4
Composition

## Slide 5
Beam dynamics simulations
Goals
To provide simultaneous tracking of three charge states of ions: Au30+, Au31+, Au32+.
Influence of debunching on transverse dynamics should be taken into account.
Chromatic aberrations should be taken into account.
Ions of Au30+ and Au32+ should be collimated before the second dipole magnet.
Space charge effects should be taken into account.
To define acceptances of the channel.
To study flexibility of the channel tuning for different beam injection schemes.
To study flexibility of the channel tuning for different betatron tunes of the Booster.
To study flexibility of the channel tuning for different initial beam parameters.
To study influence of alignment and field errors of the magnetic elements on the beam dynamics.
To define tolerances on alignment and field errors of the magnetic elements.
To simulate the process of the channel tuning by means of the steerers and the beam diagnostics devices.
Methods/models
2D Twiss simulations (MAD-X).
3D Twiss/r.m.s. simulations:
MAD-X, PTC module (no user-defined elements, no space charge);
TraceWin (two charge states of ions only);
MCIB (2D only);
Own code.

## Slide 6
Lattice functions
Reference tuning of the channel
parameter | channel entry | septum exit
, m | 10 | 7
 | -7,27 | 0,56
, m | 0 | -0,108
 | 0 | 0,009
, m | 2,99 | 6,5
 | -2,44 | -0,55
parameter | channel entry | septum exit
 | 10 | 7
 | -7,27 | 0,56
 | 0 | -0,108
 | 0 | 0,009
 | 2,99 | 6,5
 | -2,44 | -0,55
lens | gradient, T/m
Q1 | 5
Q2 | -6.7
Q3 | 3.6
Q4 | 2.5
Q5 | 8.8
Q6 | -7.8
Q7 | 6.8

## Slide 7
Acceptances
Horizontal and vertical acceptances – 38 π·mm·mrad.

## Slide 8
Separation

## Slide 9
Debunching effects (2D)
Beam model
Energy 3.2 MeV/amu; relativistic = 0.083; magnetic rigidity = 1.64 T·m; electric rigidity = 40.6 MV.
Ion flight time in a gap and a drift tube in units of RF phase .
A bunch is represented by a set of transverse slices with different longitudinal positions and momentum deviations.
Longitudinal distribution of slices at the moment of their entrance into the first gap (in units of RF phase): .
Dependence of average momentum deviation of the slice on its longitudinal position: , где – maximum momentum deviation; , , – minimum, average and maximum RF phases at the moment of the slice entrance into the first gap.
Reference tuning of the channel provide full matching of the central slice (for ) with the Booster lattice functions.
Growth of effective emittance of the slice due to mismatch with the Booster:
,
,

## Slide 10
Debunching effects (2D)
Twiss parameters

## Slide 11
Debunching effects (2D)
Emittance growth

## Slide 12
Chromatic effects (2D)
Emittance growth
Model
Maximum momentum deviation is in the central slice of the beam (with phase ). Momentum spread before the debuncher = ±1·10-3; after the debuncher = ±1·10-3.
Growth of effective horizontal/vertical emittances of the beam
due to chromatic aberrations:
= = +1·10-3 | 6,1% / 1,2%
= = -1·10-3 | 6,2% / 1,3%
 | 6,1% / 1,2%
 | 6,2% / 1,3%

## Slide 13
Beam dynamics simulations (3D)
Goals
To cross-check 2D simulations.
To study debunching effects.
To study chromatic effects.
To study coupling effects in the septum.
To study influence of space charge of three-component beam on:
transverse dynamics
debunching
separation of parasitic charge states
To study non-linear effects.
Methods/models
The beam represents as a set of beamlets which are hyperellipsoids in 6D phase space.
Beamlets are described by phase coordinates of their centers of mass and betatron parameters:
emittances, 3D Twiss parameters и and horizontal dispersions and their derivatives (uncoupled simulations);
6x6 covariance matrix (sigma-matrix) or r.m.s. parameters (coupled simulations).
Criteria of the beam division on beamlets:
charge state of ions (done);
charge state of ions and longitudinal momentum (planning);
charge state of ions, longitudinal position and momentum (planning);
charge state of ions and all 6 phase coordinates (planning).

## Slide 14
Beam dynamics simulations (3D)
Lattice functions and envelopes

## Slide 15
Beam dynamics simulations (3D)
Beam length and momentum spread

## Slide 16
Beam dynamics simulations (3D)
Separation

## Slide 17
Injection scheme | X, mm | X’, mrad | βx, m | αx
1) Single-turn injection. | 49 | -9,98 | 7 | 0,56
2) Multiturn injection with single-plateau pulse. | 48,5 | -1,58 | 7 | 0,56
3) Two-turn injection with double-plateau pulse. | 48,5 | -1,58 | 7 | 0,56
4) Twice injection with single-plateau pulse without dynamic retuning of the channel. | 45,9 | -9,35; -3,59 | 3,9 | 0,32
5) Twice injection with single-plateau pulse with dynamic retuning of the channel. | 49; 44,4 | -9,98; -3,46 | 7; 2,5 | 0,56; 0,2
6) Twice injection with double-plateau pulse without dynamic retuning of the channel. | 49; 48,5 | -9,98; -3,78 | 7 | 0,56
7) Twice injection with double-plateau pulse with dynamic retuning of the channel. | 49; 45,4 | -9,98; -3,54 | 7; 3,4 | 0,56; 0,27
8) Triple injection with double-plateau pulse without dynamic retuning of the channel. | 45,9 | -9,35; -3,59; -3,62 | 3,9 | 0,32
9) Triple injection with double-plateau pulse with dynamic retuning of the channel. | 49; 45,4; 44,9 | -9,98; -3,54; -3,53 | 7; 3,4; 3 | 0,56; 0,27; 0,24
Channel flexibility
Tuning for different injection schemes

## Slide 18
Channel flexibility
Tuning for different injection schemes
Injection scheme | x, mm | x’, mrad | Usep, kV | φcorr, mrad
1) Single-turn injection. | 3,8 | -0,85 | 116,6 | 0
2) Multiturn injection with single-plateau pulse. | -2,3 | -3,41 | 124,7 | -2,56
3) Two-turn injection with double-plateau pulse. | -2,3 | -3,41 | 124,7 | -2,56
4) Twice injection with single-plateau pulse without dynamic retuning of the channel. | 1,2; -2,7 | -1,95; -3,6 | 117,8; 123,3 | -1,1; -2,75
5) Twice injection with single-plateau pulse with dynamic retuning of the channel. | 3,8; -3,9 | -0,85; -4,11 | 116,6; 123,8 | 0; -3,26
6) Twice injection with double-plateau pulse without dynamic retuning of the channel. | 3,8; -0,8 | -0,85; -2,78 | 116,6; 122,6 | 0; -1,93
7) Twice injection with double-plateau pulse with dynamic retuning of the channel. | 3,8; -3,1 | -0,85; -3,77 | 116,6; 123,5 | 0; -2,92
8) Triple injection with double-plateau pulse without dynamic retuning of the channel. | 1,2; -2,7; -2,7 | -1,95; -3,6; -3,59 | 117,8; 123,3; 123,3 | -1,1; -2,75; -2,74
9) Triple injection with double-plateau pulse with dynamic retuning of the channel. | 3,8; -3,1; -3,5 | -0,85; -3,77; -3,93 | 116,6; 123,5; 123,6 | 0; -2,92; -3,08

## Slide 19
Channel flexibility
Tuning for different injection schemes

## Slide 20
Channel flexibility
Tuning for different injection schemes
Variation of and at the entrance of the septum

## Slide 21
Channel flexibility
Tuning for different betatron tunes
Booster tunes and lattice functions at the exit of the septum

## Slide 22
Channel flexibility
Tuning for different betatron tunes
Variation of Booster tunes and

## Slide 23
Channel flexibility
Tuning for different initial beam parameters
Variation of , , and at the exit of the HILAC

## Slide 24
Tolerances
Alignment errors
Magnetic field inhomogeneities on pulse top
Dipoles | ± 5·10-4
Quadrupoles | ± 1·10-3
Steerers | ± 1·10-2
Dipoles | 
Displacement along longitudinal axis, mm | 20
Horizontal displacement, mm | 1
Vertical displacement, mm | 1
Rotation around vertical axis, deg | 0,5
Rotation around horizontal transverse axis, deg | 0,5
Rotation around longitudinal axis, deg | 0,5
Quadrupoles | 
Displacement along longitudinal axis, mm | 5
Transverse displacement, mm | 1
Rotation around vertical axis, deg | 0,5
Rotation around horizontal transverse axis, deg | 0,5
Rotation around longitudinal axis, deg | 0,5

## Slide 25
Alignment and field errors
Statistical analysis of beam trajectory
Let is a transfer matrix between i-th and j-th elements of the channel lattice, is a vector of phase coordinates’ displacement in i-th element due to errors. Then phase coordinates of a beam trajectory (center of mass) at the exit of n-th element equal to:
,
where index 0 corresponds to initial point of the channel. If then .
The expression in the sum is a beam trajectory in presence of errors in i-th element only with :
.
Then:
Vectors are independent random vectors, i.e. .
Covariance matrix of phase coordinates of a beam trajectory can be defined as follows:
.
Taking into account the matrix is expressed:
Determinant of the matrix is an analogue of emittance:

## Slide 26
Dipoles’ field errors
Beam trajectory distribution

## Slide 27
Dipoles’ field errors
Beam emittance growth

## Slide 28
Alignment errors
Beam trajectory distribution

## Slide 29
Alignment errors
Local trajectory correction
Two pick-ups + two steerers on drift section beam trajectory gets zero

## Slide 30
Alignment errors
Beam trajectory distribution with local correction

## Slide 31
Alignment errors
Beam envelopes and clearances

## Slide 32
Alignment errors
Beam trajectory distributions for different charge states

## Slide 33
Tuning simulations (example 1)
Initial state
Beam current | 
FCT1, FC1, FC2 | 100%
FC3 | ~70%
FCT2 | ~50%
FCT3 | ~20%
Sigma of errors | 
Dipole long. shift, mm | 20
Dipole rotation, mrad | 7.5
Quadrupole transverse shift, mm | 1

## Slide 34
Tuning simulations (example 1)
Iteration 1 (Q1-Q3 tuning)
Beam current | 
FCT1, FC1, FC2 | 100%
FC3 | ~100%
FCT2 | ~95%
FCT3 | ~80%

## Slide 35
Tuning simulations (example 1)
Iteration 2 (correction by CM1-CM2)
Beam position (X/Y) , mm |  | 
 | before | after
BPM1 | 0 / 0.5 | 0 / 0.5
BPM2 | -1.5 / 0.5 | 0 / 0.5

## Slide 36
Tuning simulations (example 1)
Iterations 3-4 (collimation, correction by CM3 and Q1-Q3 tuning)
Beam current |  | 
 | before | after
FCT2, BPM4 | ~90% | 100%
BPM5 | ~10% | 100%

## Slide 37
Tuning simulations (example 1)
Iteration 5 (correction by CM5-CM6)
Beam position (X/Y) , mm |  | 
 | before | after
BPM4 | -6 / 2 | -6 / 2
BPM5 | -4 / 6 | 0 / 0

## Slide 38
Beam dynamics simulations
Plans
To develop 3D code with space charge in order:
to study debunching effects;
to study chromatic effects;
to study coupling effects in the septum;
to study influence of space charge of three-component beam on transverse dynamics, debunching, separation of parasitic charge states;
to study non-linear effects.
To study influence of field errors of quadrupoles on the beam dynamics.
To simulate the full process of the channel tuning by means of quadrupoles, steerers and beam diagnostics devices.
To develop methods and tools of the channel tuning.

## Slide 39
THANK YOU FOR ATTENTION

## Slide 40
EXTRA SLIDES

## Slide 41
Parameters of main elements
Channel equipment
Quadrupoles
Effective length, m | 0.29 / 0.21
Max gradient, T/m | 10 / 19
Gap (diameter), mm | 95 / 71
Dipoles
Effective length, m | 0.65
Max field, T | 1
Gap, mm | 45
Steerers
Effective length, m | 0.25
Max field, T | 0.05
Gap, mm | 125 × 110

## Slide 42
Parameters of main elements
Channel equipment
Debuncher
Designed and fabricated by Bevatech team
Inner length, m | 0.49
Frequency, MHz | 100.625
Max effective voltage, kV | 260
Status of channel equipment
Power supplies are being assembled.
Beam diagnostics is purchased partially. Full set of beam diagnostics will not be purchased until the channel commissioning.
First part of vacuum equipment is delivered. Full set of vacuum equipment will be delivered in the nearest future.
Design of stands is near completion.

## Slide 43
Mathematical models
Debuncher
Approximate model
4 gaps of 65 mm;
3 inner drift tubes of 64 mm and 2 entry/exit drift tubes of 74 mm;
RF amplitude = 65 kV;
RF frequency = 100,625 MHz.

## Slide 44
Mathematical models
Debuncher
Paraxial equations of motion inside the i-th gap
Transverse transfer matrix of the i-th gap
,
where , – the average RF phase during the i-th gap transfer.

## Slide 45
Mathematical models
Debuncher
Averaging the i-th gap field over the beam
If then
Longitudinal transfer matrix of the i-th gap
,

## Slide 46
Mathematical models
Debuncher
Paraxial equation of transverse motion on edges of the i-th gap
where j = 1, 2 – index of the gap entry and exit correspondingly; – length of linear RF field ramp on the gap edge; – local longitudinal coordinate.
Transverse transfer matrix of the j-th edge of the i-th gap
,
where , , – RF phases at the moments of the particle entrance and exit of the i-th gap. Positive values of fringe lenses’ strengths mean the beam focusing.

## Slide 47
IP1
ESS
IP2
IP3
Mathematical models
Electrostatic septum ESS
Booster injection system

## Slide 48
Mathematical models
Electrostatic cylindrical deflector
Equations of motion in cylindrical coordinates (over time)
, varies!!!
Accompanying coordinates:
linearized equations of motion

## Slide 49
Mathematical models
Electrostatic cylindrical deflector
6x6 transfer matrix (for as a phase coordinate)
Motion is uncoupled
If then the matrix can be used for uncoupled Twiss simulations.

## Slide 50
Mathematical models
Electrostatic cylindrical deflector
Linearized angular momentum:
6x6 transfer matrix (for as a phase coordinate)
Longitudinal-transverse coupling!!!
The matrix can be used for coupled 3D r.m.s. simulations.

## Slide 51
Tuning simulations (example 2)
Initial state
Beam current | 
FCT1, FC1 | 100%
FC2 | ~95%
FC3 | ~40%
FCT2, FCT3 | <10%
Sigma of errors | 
Dipole long. shift, mm | 20
Dipole rotation, mrad | 7.5
Quadrupole transverse shift, mm | 2

## Slide 52
Tuning simulations (example 2)
Iterations 1-3 (tuning of Q1-Q5, correction by CM1-CM2, collimation)
Beam position (X/Y) , mm |  | 
 | before | after
BPM1 | 9 / 3.5 | 7 / 2
BPM2 | 12 / 8 | 0 / 0

## Slide 53
Tuning simulations (example 2)
Iterations 4-5 (correction by CM3-CM5)
Beam position (X/Y) , mm |  | 
 | before | after
BPM4 | 8 / -1.5 | 0 / 0
BPM5 | 2 / -5 | 0 / 0