## Slide 1: Commission results of the new Rebuncher for the linac LU-20
A. Govorov, V. Monchinskiy, K. Levterov, D. Donetc, B. Golovenskiy, K. Shevchenko
on behalf of NICA team (JINR, Dubna)
In collaboration with ITEPH, MEPHI,
VNIITF (Snezhinsk), EZAN.

## Slide 2
SPI
LU-20
Nuclotron
ESIS
Krion
booster
Transfer to collider rings
LIS
RFQ
RFQ
IH1
IH2
HILAc
Structure of the injector complex
Heavy ions z/A>0.17,
Au31+ 3.2 MeV/u
p↑, d↑, ions z/A>0.3 5 MeV/u
B
Project new LILAc
7 MeV/u
B
RFQ
IH1
IH2
B
?
?
?
13 MeV/u
?
?
SC resonators
2

## Slide 3: Forinjector for Alvarez LU-20
Accelerating tube
HV terminal
until 2016
3
Импульсное напряжение до 800 кВ
Мощность электрооборудования источника ионов до 5 кВт

## Slide 4: Upgraded forinjector for Alvarez LU-20
Assembling LEBT, RFQ, MEBT in march - april 2016
LEBT
RFQ
4
cover
resonator
Импульсное напряжение до 120 кВ
Мощность электрооборудования источника ионов до 35 кВт

## Slide 5: RFQ linac
Z/A | 1.0 | 0.5 |  0.3
Injection energy, [keV] | 31 | 61.8 | 103
Max current, [mА] | 10 | 20 | 10
Output energy [keV/u] | 156 |  | 
Norm emittance (output) [π·cm·mrad] | ≤ 0.5 |  | 
RFQ length, [m] | 2.2 |  | 
Transmission, % | > 85% | > 89% | > 93%
In LU-20 acceptance with buncher | 70 % | 71 % | 80 %
In LU-20 acceptance without buncher | 15 % | 15 % | 20 %
5

## Slide 6
MEBT section
RFQ section
(2.1m for z/A=0.3÷1)
Simulations results for the deuteron beam 20mA
(Q triplet + Rebuncher + Q triplet)
at LU-20 entrance
6

## Slide 7
MEBT
QT + Rebuncher + QT
RFQ
Resonator LU-20 (DTL)
Vacuum chamber LU-20
7

## Slide 8
Parameters Rebuncher
Parameter | Value
Z/A ratio | 0,3-1
RF Frequency, MHz | 145,2
Aperture diameter, mm | 30
Gap length, mm | 10
Length of central drift tube, mm | 46,5
Internal rounding radius of the tube, mm | 5
External rounding radius of the tube, mm | 5
Length along the beam, mm | 89
Height resonator, mm | 450
RF Power, kW | 5
Max voltage on the gap, kV | 75
Q-factor | 5160
Adjustment range of upper plunger, kHz | 1700
Adjustment range of lower plunger, kHz | 160
8

## Slide 9
Resonator test and measurements (april 2017)
tuning plunger
SWR=1,15
9
Notes: КСВ

## Slide 10
Assembling Rebuncher (april 2017)
10

## Slide 11
RF amplifier
Parameter | Value | 
Maximum impulse power, kW | Rebuncher | RFQ
 | 5 | 430
RF Frequency, MHz | 145,2 | 
Generator lamp | GI-39B | GI-27AM
11

## Slide 12
RFQ
Buncher’s
plunger
ЛУ-20
Plungers RFQ
К1
К2
К3
К4
К5
К6
Ampl
LLRF system
Buncher
12

## Slide 13
LLRF system
Software
13

## Slide 14
RF Load and Multipactor
14
RF LU-20
RF RFQ
RF Buncher
Notes: Вторичноэлектронный резонансный разряд, резонансный высокочастотный разряд или мультипакция. Механизм этого разряда может быть представлен следующей схемой. Электроны, вышедшие из электрода, когда он являлся катодом, ускорятся ВЧ-напряжением и, попадая на противоположный электрод, вызовут вторичную электронную эмиссию. Если время пролета первичных электронов близко к полупериоду ВЧ-напряжения, то вторичные электроны, вылетая из второго электрода, который к этому времени стал катодом, также ускорятся и вызовут вторичную эмиссию уже из первого электрода. При коэффициенте вторичной эмиссии >1 такой взаимный обмен приведет к появлению заметного тока между электродами.

## Slide 15
RF Load and Multipactor
15
RF LU-20
RF RFQ
RF Buncher
Notes: Вторичноэлектронный резонансный разряд, резонансный высокочастотный разряд или мультипакция. Механизм этого разряда может быть представлен следующей схемой. Электроны, вышедшие из электрода, когда он являлся катодом, ускорятся ВЧ-напряжением и, попадая на противоположный электрод, вызовут вторичную электронную эмиссию. Если время пролета первичных электронов близко к полупериоду ВЧ-напряжения, то вторичные электроны, вылетая из второго электрода, который к этому времени стал катодом, также ускорятся и вызовут вторичную эмиссию уже из первого электрода. При коэффициенте вторичной эмиссии >1 такой взаимный обмен приведет к появлению заметного тока между электродами.

## Slide 16
Beam (June 2017)
D+
C4+
Without Rebuncher
1,1 mA
1,7 mA
0,1 mA
1,1 mA
With Rebuncher
16

## Slide 17: Results
Parameter | Laser Ion Source (CO2 laser) |  |  | 
 | D+ | Li3+ | C5+ | C4+
I, mA after RFQ | 5 | 3 | 4 | 6
ICF-1, mA without buncher | 1,1 | 0,5 | 0,6 | 0,1
ICF-1, mA Q, nC N ions with buncher | 1,7 mA 13 nC ~ 8,5∙1010 | 1,3 mA 5,2 nC ~ 1,1∙1010 | 1,5 mA 2,25 nC ~ 2,8∙109 | 1,1 mA 4,4 nC ~ 6,8∙109
Buncher ratio | 1,54 | 2,6 | 2,5 | 11
Transmission without / with buncher, % | 22 / 34 | 17 / 43 | 15 / 38 | 1,6 / 18
Achieved parameters of accelerated beam
June 2017
17

## Slide 18: Results
Parameter | KRION |  | 
 | 40Ar16+ | 78Kr26+ | 124Xe41+
I, μA Q, pC after RFQ | 200 μA 800 pC | 150 μA 600 pC | 30 μA 120 pC
ICF-1, μA without buncher | 2,5 μA | 1,5 μA | 0,15 μA
ICF-1, μA Q, pC N ions with buncher | 40 μA 160 pC ~ 6∙107 | 35 μA 140 pC ~ 3∙107 | 3 μA 12 pC ~ 2∙106
Buncher ratio | 16 | 23 | 20
Transmission with buncher, % | 20 | 23 | 10
Achieved parameters of accelerated beam
Nov. – Dec. 2017, Feb. – Apr. 2018
18
RUN 55

## Slide 19: Проблемы
Масло в резонаторе ЛУ-20
Мультипакция в группирователе
Уход собственной частоты при нагреве резонатора от тренировки
19
Запуск ВЧ группирователя раньше ВЧ ЛУ-20
Для борьбы с мультипакцией создана схема непрерывного ввода ВЧ малой мощности
Тренировка банчера 2 раза в сутки по 5-10 мин
Решения

## Slide 20: Итого
20
Смонтирован банчер
Решена проблема мультипакции
Проведены тесты и ускорительные сеансы на инжекционном комплексе и Нуклотроне
Найдены неожиданные режимы работы банчировки/ускорения
Повышены интенсивности пучков

## Slide 21
21

## Slide 22
Thank you for attention!
22
4 сентября 18

## Slide 23: Laser Ion Source

## Slide 24: Source of Polarised Ions (SPIon)
JINR + INR
V. V. Fimushkin,
A. S. Belov
P+, D+, ↑P+, ↑D+, H2+

## Slide 25: ESIS KRION

## Slide 26: Krion-6Т Electron String Ion Source – stand prototype for Krion-N(ica) ion source. Krion-6T project main parameters: magnetic filed up to 6.0 Т, electron energy up to 15 keV. Expected ion beam parameters: 1 ÷ 4 x 109 ppp Au31+ (or, alternatively Au51+); Ion beam extraction time from ESIS: 8 – 30 µs. RMS emittance: 0.6 π mm mrad (extraction time 8 µs); 0.15 π mm mrad (30 µs).

## Slide 27: Krion-6T ESIS
 | Project | At test bench | At Nuclotron run #50 (2014)
Element | Au31+ | Tu50+ | Ar16+
Ion intensity, ppp | 1.4x109 | 3x107 | 4x108
Magnetic field, T | 6 | 5.4 | 4.6
Extraction time from ESIS, μs | 8 - 30 | 8 | 8
Energy of electron string, keV | 25 | 9-10 | 5-6
RMS emittance | 0.6 π mm mrad (for 8 μs extraction time) 0.15 π mm mrad (for 30 μs extraction time) |  | 
Plans:
1) Preparation for Ar16+ and Kr26+ injection in 2017.
2) Improvement of internal Au and Bi injection.
3) Experiments in Au production in magnetic field up to 6Т.