## Slide 1: Test Bench for the NICA Stochastic Cooling Elements
I.Gorelyshev on behalf of the team

## Slide 2: Nuclotron-based Ion Collider fAcility
Tasks:
Beam accumulation
Longitudinal emittance reduction during the bunching
Luminosity preservation (IBS suppression)

## Slide 3: Stochastic cooling
Provides the reduction of the betatron amplitudes () or momentum spread ()
Energy distribution
Broadband RF system with feedback via the beam

## Slide 4: How many equipment units do we need?
6 pickups
4 kickers
80 Amplifiers

## Slide 5: Why do we need a test bench?
Quality control
Measurements(PU/KK, Amplifiers, etc …)
Pickup/Kicker
Impedance dependence on azimuthal and longitudinal position
Electrical center position as a function of frequency
Influence of High-Order Mode suppressors
Influence of ceramic vacuum chamber
Kicker SWR
Amplifiers
Gain vs frequency
Gain vs input power
Gain linearity (frequency & power)
Phase linearity
Group delay
Intermodulation products
Reproducibility (gain, electrical length, …)

## Slide 6
4-channel Vector Network Analyzer
Power meter
Test Bench
Comb Filter

## Slide 7
Pickup and Kicker
Universal for 3 degrees of freedom
Large impedance
Bandwidth | 2-4 GHz
Aperture | 90 mm
Length | 300 mm
Ring Shunt Impedance | 9 Ω
Pickup Shunt Impedance | 144 Ω
Structure of 16 rings
with combiner boards
Structure of one ring
Ring Slot Couplers
Quality control –> loop impedance
128 loops –> electrical center

## Slide 8
Pick-up inside cryostat
Assembling of the kicker
In this design it is hard
to achieve ultra-high vacuum
Stochastic Cooling Experiment at Nuclotron

## Slide 9
Possible Improvement of Pickup/Kicker
Separated structure with ceramic vacuum chamber inside rings

## Slide 10
Prototype to Test

## Slide 11
PU & KK Test Bench

## Slide 12
IN
OUT
Quality control (Impedance)

## Slide 13
IN
OUT
Δ
Electrical center

## Slide 14: Kicker SWR
Back Reflected Power 4,76% ≃ 1.5W
SWR < 1.3

## Slide 15: Amplifiers
Requirements | 
Bandwidth | 2 – 4 GHz
Gain | 43 ± 2 dB
1 dB compression (3 GHz) | Input 0 dBm (1 mW)
Power linearity (intermodulation products) | Notch depth reduction <10 dB
Phase linearity | ± 5 deg
Group delay variation | ±200 ps
Reproducibility | 

## Slide 16: Amplifiers

## Slide 17
Intermodulation products
Δ
Δ < 10 dB

## Slide 18: Summary
Pickup Manufacturing Technology has been tested
Pickup prototype has been produced
Amplifier prototypes have been produced
Test Bench has been created
Measurement methodic has been developed
Measurements has been started

## Slide 19
Thank you for attention

## Slide 20: BTF Measurements from the Run 2018
Intensity (elementary charges): C6+ 3×108 Ar16+ 1,5×107 Kr26+ 2×106
Sensitivity is high enough to obtain response from low intensity beams

## Slide 21: Disadvantages of Actual Pickup/Kicker Structure
Ultra high vacuum (10-11) can not be guaranteed
Some RF characteristics were not measured
Combiner board frequency (3 GHz) does not matched to that of the rings (2 GHz)

## Slide 22: Advantages of new Pickup/Kicker Structures
Ultra high vacuum is achievable
Easy to repair in case of malfunctions
Higher power can be dissipated in the kicker