## Slide 1
Dipole and quadrupole modules of the magnetic system of the NICA Collider
G. Kuznetsov, A. Galimov, H. Khodzhibagiyan.
        Joint Institute for Nuclear Research, Dubna

## Slide 2
Arrangement of the magnetic modules in the Collider NICA
 | In arches | In Stright section
Dipole | 80 | --
Quadrupole | 46 | 32

## Slide 3
Periodic FODO Cell.

## Slide 4
Power supply circuit of the structural magnets of the Collider NICA

## Slide 5
Dipole Module Magnet
Number of magnets | 80
Maximum magnetic field | 1.8 T
Effective magnetic length | 1.94 m
Beam pipe aperture (h/v) | 120 mm/70 mm
Overall weight | 1670 kg
Operating current | 10.4 kA
Inductance | 450µH
Total heat releases | ≤13.0 W
SC cable length | 122 m + 15m

## Slide 6
Installation of the additional bus bars

## Slide 7
Number of magnets (in the arches) | 46
Maximum magnetic field gradient | 23.1 T/m
Effective magnetic length | 0.47 m
Pole radius | 47.5 mm
Overall weight | 550 kg
Operating current | 10.4 kA
Number of turns in the coil | 8
Inductance | 94µH
Total heat releases | ≤5.7 W
SC cable length | 44m + 12m
Quadrupole Module Magnet

## Slide 8
Assembly units of the Quadrupole Magnet

## Slide 9
Installation of the additional bus bars

## Slide 10
Quadrupole module magnet with pumping devices

## Slide 11
Quadrupole module magnet with pumping devices

## Slide 12
Joining of the magnets

## Slide 13
Location of the magnet modules in the tunnel
Outer radius
Inner radius

## Slide 14
Спасибо за внимание !