## Slide 1: Магнитная система детектора ATLAS
Николай Зимин

## Slide 2: LHC
Lake of Geneva
Large Hadron Collider
Airport
CMS
ATLAS
LHCb
ALICE

## Slide 3
Н.Зимин 09/2018
The full LHC accelerator complex
LHC ring is divided
into 8 sectors
> 60 years of CERN history still alive and operational
Linac
Booster
PS
SPS
LHC

## Slide 4
9135 magnets:
1232 main dipole (twins)
392 lattice quadrupole (twins)

## Slide 5
Note: The acceleration is not such a big issue in pp colliders (unlike in e+e- colliders),
because of the ~ 1/m4 behaviour of the synchrotron radiation energy losses
[~ E4beam/Rm4]
LHC at 7 TeV LEP at 100 GeV
Synchrotron radiation loss 6.7 keV/turn 3 GeV/turn
Peak accelerating voltage 16 MV/beam 3600 MV/beam
The particle beams are accelerated by superconducting Radio-Frequency (RF) cavities

## Slide 6
LHC Accelerator Challenge: Dipole Magnets
1232 LHC dipole magnets are cooled with
pressurized superfluid helium
Coldest Ring in the Universe ?
1.9 K (CMBR is about 2.7 K)
Magnetic Field for Dipoles
p (TeV) = 0.3 B(T) R(km)
For p = 7 TeV and R = 4.3 km
B = 8.4 T
Current 12 kA

## Slide 7
Special quadrupole magnets (‘Inner Triplets’) are focussing the
particle beams to reach highest densities (‘luminosity’) at their
interaction point in the centre of the experiments
Relative beam sizes around the collision point

## Slide 8
Main parameters of the machine
crossing angle
'long range’ interactions
two beams, 2808 bunches each, separated by 25 ns
Beam energy 7 TeV
Instantaneous luminosity L 1034 cm-2s-1
Integrated luminosity/year ~ 100 fb-1
Dipole field 8.4 T
Dipole current 11700 A
Circulating current/beam 0.53 A
Number of bunches 2808
Bunch spacing 25 ns
Protons per bunch 1011
R.m.s. beam radius at IP1/5 16 m
R.m.s. bunch length 7.5 cm
Stored beam energy 360 MJ
Crossing angle 300 rad
Number of events per crossing 20
Luminosity lifetime 10 hours
n. of protons
per bunch
n. of bunches
beam size at IP
(x,y = 16 m)
n. of turns
per second
N = L x pp  X)

## Slide 11
  Barrel Toroid + 2 End-Cap Toroids + Central Solenoid
  Project started in 1996
  The largest superconducting magnet in the world !
Superconducting Magnets

## Slide 12
ATLAS toroids
BT Cryoring
10kL dewar valve box pump cryostat
Transfer lines
ECT flexibles
Solenoid control dewar

## Slide 13: Toroids 20.5 kA/16V electrical circuit
Toroids in series - Dump in parallel - Power convertor - 2 switches - Dump resistor and diodes unit - 200m Al bus bars
Bus bars

## Slide 14
Barrel Toroid Cold Mass Integration
Scale
8 coils in separate cryostats
Force transfer ~ 1100t/coil
Cold mass ~ 450t

## Slide 15
Barrel Toroid Cryostat Integration
Challenge
Scale of components and integration accuracy
Tolerances << 1 mm in 26m

## Slide 16
Barrel Toroid Coil Installation

## Slide 17
Completed Barrel Toroid
Н.Зимин 09/2018
Семинар ЛФВЭ
16

## Slide 18
The End-Cap Toroids
2 x 8 coils, 4 x 4.5 m2
20 kA, 4 T
8 keystone boxes
hanging on bore tube

## Slide 20
  Barrel Toroid + 2 End-Cap Toroids + Central Solenoid
  4 magnets provide magnetic field for
  Inner detector (solenoid), 2.4 m diameter x 5.4 m long
  Muon detectors (toroids), 21 m diameter x 25 m long
  8300 m3 volume
  170 t superconductor
  700 t cold mass
  1320 t total weight
  90 km conductor
  20.4 kA at 4.7 K
  1.6 GJ stored energy
  10 years construction 98-07
  The largest trio of toroids ever built!
Superconducting Magnet System

## Slide 21
ATLAS Supplier Award
В.Данилов, Н.Данилов, А.Любимцев, М.Куликов, С.Баков, А.Забалуев, Ф.Лупенко, О. Лыков, И.Титенков, М.Андрианов, Н.Жуков и еще более 100 сотрудников ОП и ОИЯИ

## Slide 22
Трудности
Коллаборация:
ЦЕРН-ОИЯИ(ОП)-Сакле-Оксфорд-Милан
(Ансальдо, Занон, Фелькуера)
Напряженный график, первая система в каверне.
Сварка алюминиевых труб
Сварка переходников алюм. – нерж.сталь.
Рентгеновский контроль
Транспортировка готовых труб (длина более 30 м)
Переделки из-за «человеческого фактора»
(термозащита, тоководы)

## Slide 24
Run condition screenshort

## Slide 25
Field Map

## Slide 26: M&O and Maintaining skills……
After completion of ATLAS installation and commissioning…
Being successful is an incentive for more…
Collaboration with JINR continued for ATLAS Maintenance, Repairs and R&D:
Various works for Technical Coordination
Yearly Magnet Opening and Closing work during winter stops
Maintenance on vacuum and cryogenic systems, electrical circuits, controls, etc.
Exceptional repair works, like:
  ECT-A insulator breakdown (2008)
  ECT-C bellows damage (2016)
Various R&D work, sensor developments etc.
And, to maintain skills of the team, …….work on other magnets thereby serving the community…

## Slide 27
DATA-TAKING: 2018
LHCC 12-Sep-18

## Slide 28
Pile-up challenge
2018 <pile-up> ~ 50 (up to 80 max)
Z->mm with 20 reconstructed vertices
Семинар ЛФВЭ
Н.Зимин 09/2018

## Slide 30
ATLAS Hardware status
>96%

## Slide 32
ATLAS upgrades plan
Phase 0 (2013-2014):
- New beam pipe(Al)+ pixel layer at inner radius (IBL)->reduce BG and improve b tagging)
- New LV power suplies (Tilecal+Lar) ; complete EE m chambers
Phase 1 (2018): (LOI by the end of 2011)
- Fast track trigger
- Muon system
- Improve L1&2 trigger
Phase 2 (~2022): (LOI end of 2012)
New inner Detector
New calorimeter FE electronics
    New forward calorimeter

## Slide 38: ATLAS 2006
Hcp2006, 22 May 2006
Marzio Nessi
CERN-RRB-2004-152
Herman ten Kate - CERN
ATLAS Magnet Project
Construction, Maintenance, Operations & Repair
- - a very successful ATLAS-JINR collaboration -
Content: Magnets in the System
Starting up and organization
Construction, integration, installation
Schedule, Cost, Lesson
Maintaining skills……M&O and Repairs
Spin-off and Outlook
Conclusion
April 25, 2017

## Slide 39
Cпасибо
за
внимание

## Slide 40
«Хорошо изученные процессы»,
нет необходимости регистрировать все события…
Физика LEP - большого электрон-позитронного коллайдера
«Новая Физика»
Это мы хотим выделить и записать для дальнейшего анализа...
Cечения взаимодействия

## Slide 41
Суперсимметрия (SUSY)
Our known world
Maybe a new world?
Establishes a symmetry between fermions (matter)
and bosons (forces):
- Each particle p with spin s has a SUSY partner p
with spin s -1/2
- Examples q (s=1/2)  q (s=0) squark
g (s=1)  g (s=1/2) gluino
Motivation:
- Unification
(fermions-bosons,
matter-forces)
- Solves some deep
problems of the
Standard Model
~
~
~
(Julius Wess and Bruno Zumino, 1974)

## Slide 42
SM/Higgs searches in ATLAS

## Slide 44
First collisions at the LHC end of November 2009
with beams at the injection energy of 450 GeV

## Slide 45
Детектор ATLAS

## Slide 46
Детектор ATLAS

## Slide 47
Calorimeters
Hadron calorimeter:
Trigger; measure jets; ET,miss:
• σ/E ~ 50-60%/√E⊕3% central
• σ/E ~ 90%/√E ⊕ 7% in fwd
• σ(ET,miss) / ΣET ≈ 55 %
• |η|<1.7: Fe/scint. Tiles (Tilecal)
• 3.2 <|η|<1.5: Cu-LAr (HEC)
• 3.1<|η|<4.9: FCAL Cu/W-Lar
• |η|<4.9
• 10λ at |η|=0
• Δη×Δφ : 0.1x0.1 up to |η|<2.5
• 3-4 Longitudinal layers
• 20x103 channels
Lar-Pb EM calorimeter (|η|<3.2):
• e/γ trigger, identification; measurement
• σ/E ~ 10%/√E ⊕ 0.7%
• Granularity: 0.025x0.025 ; 22X0
• 3 long. layers + presampler(0 <|η|<1.8)
• 180x103 channels

## Slide 48
LAr
electromagnetic
LAr forward
Tiles hadronic
LAr endcap
Hadron calorimeter
Trigger;measure jets; Etmiss:
s/E~50-60%/E3% central
s/E~90%/E  7% in fwd
  (ET,miss) / ET  55 %
|h|<1.7: Fe/scint. Tiles (Tilecal)
3.2 <|h|<1.5: Cu-Lar (HEC)
3.1<|h|<4.9: FCAL Cu/W-Lar
|h|<4.9
10l at |h|=0
 : 0.1x0.1 up to |h|<2.5
3-4 Longitudinal layers
20x103 channels
  Lar-Pb EM calorimeter (|η|<3.2):
e/g trigger, identification; measurement
s/E ~ 10%/E  0.7%
Granularity: 0.025x0.025 ; 22X0
3 long. layers + presampler(0 <|h|<1.8)
  180x103 channels
Calorimeters

## Slide 49
End-Cap Toroid Cold Mass Assembly
Coils
KSB

## Slide 50
Commissioning up to Full Current (21 kA)
Cool down 6 weeks (Jul-Aug)
Powering step-by-step to 21 kA (9 Nov’06)
At each step: slow dump, fast dump & re-cool down
Full Current 20.4 kA
Ramp-up / down = 2 h + 2 h
E = 1.1 GJ
Fast dump Tmax = 55 K
Cryo-recovery = 84 h

## Slide 52
The Birth of ATLAS
March 1992
Evian Meeting with EoI presentations
March 1992 – Summer 1992
Merging of EAGLE and ASCOT, two
proto-collaborations
September 1992
Decision on the name
October 1992
ATLAS LoI submitted to the LHCC
Official birth of the ATLAS
Collaboration

## Slide 55
Precise tracking and vertexing, e/π separation; coverage: |η|<2.5
B (solenoid) =2T
<hits> in barrel ~ 3/8/30 in Pixel/SCT/TRT; 0.5X0 at η=0 ; 1.1 X0 at η=1.8
σ/pT = 0.038% pT(GeV) ⊕ 1.5% (3.8% pT= 100GeV ; <2% pT<35GeV)
Impact parameter resolution (0.25<|η|<0.5) (σd0) = 10 μm ⊕140 μm / pT [GeV/c]
Si Pixels: 80M channels ; 3 layers and 3 disks ; σ = 10 μm [rφ]
Si strips (SCT): 6M channels; 4 layers and 9 disks ; σ = 17 μm [rφ]
Transition Radiation Tracker (350k channels ; σ =120 μm/straw)

## Slide 56
Calorimeters
Hadron calorimeter:
Trigger; measure jets; ET,miss:
• σ/E ~ 50-60%/√E⊕3% central
• σ/E ~ 90%/√E ⊕ 7% in fwd
• σ(ET,miss) / ΣET ≈ 55 %
• |η|<1.7: Fe/scint. Tiles (Tilecal)
• 3.2 <|η|<1.5: Cu-LAr (HEC)
• 3.1<|η|<4.9: FCAL Cu/W-Lar
• |η|<4.9
• 10λ at |η|=0
• Δη×Δφ : 0.1x0.1 up to |η|<2.5
• 3-4 Longitudinal layers
• 20x103 channels
Lar-Pb EM calorimeter (|η|<3.2):
• e/γ trigger, identification; measurement
• σ/E ~ 10%/√E ⊕ 0.7%
• Granularity: 0.025x0.025 ; 22X0
• 3 long. layers + presampler(0 <|η|<1.8)
• 180x103 channels
LAr
electromagnetic
LAr forward
Tiles hadronic
LAr endcap
12 m
8m
4000 tons

## Slide 57
Muon Spectrometer
4 chambers types gas based (|η|<2.7)
1.1x106 channels ; 12000 m3
Precision chambers : MDT ; CSC
Trigger chambers (LVL1): RPC; TGC
Muon trigger and measurement
Alignment accuracy: ~ 30μm
MDT resolution = 80μm (|η|<2)
CSC resolution =60μm (2<|η|<2.7)
Momentum resolution (ID+MS) |η|<1.1:
σpT/pT ~10% (pT ~ 1 TeV)
σpT/pT ~2% (pT =50 GeV)
4 Superconducting magnets:
- Solenoid around ID (B=2T; 7.6 kA)
- 3 Air core Toroids (with 8 coils each): 20kA, Btoroid ~0.5-1T