## Slide 1
Spatial positioning of underwater components
for Baikal-GVD
Alexander Avrorin
INR RAS

## Slide 2
OVERVIEW
GVD components are mounted on flexible strings strung between an anchor and subsurface buoys.
Acoustic measurements show that coordinate deviations can reach several meters for depth and 10s of meters for XY plane over the course of the season.
Strings can also twist and rotate OMs up to 360 degrees.
1 m error in positioning OM is equivalent to ~4.4 ns error in time calibration.
We need to know OM coordinates and spatial orientation at any given time. That’s what the spatial positioning system is for.

## Slide 3
SPATIAL ORIENTATION
Each new OM is equipped with an array of sensors.
These sensors include, among others, an accelerometer and a compass.
Their data is used to reconstruct OM direction.
Avg error: 0.33 deg
LAB SAMPLE
LAB SAMPLE
Accelerometer data
Compass data
ALL SECTIONS​
BOTTOM SECTION
CENTER SECTION
TOP SECTION
On-site calibration (2017)

## Slide 4
COORDINATES
Coordinate measurements are performed with the hydro-acoustic positioning system (APS)
4 acoustic modems (AMs) on each string (default).
1 AM (node) is fixed to the anchor, the rest (beacons) are mobile.
Anchor coordinates are measured once, during winter expedition.
Beacons measure acoustic distances to the nodes, regularly send data to the shore.
Beacon coordinates are then trilaterated, online.
OM and calibration light source coordinates are linearly interpolated from beacon positions.
EvoLogics S2C R42/65 acoustic modem

## Slide 5
APS PERFORMANCE

## Slide 6
BEACON BEHAVIOR
Z-coordinate variation is ~several cm (except autumn).
X, Y – 10s of meters.
Coordinate variation decreases with depth.
Z variation gives a good estimate of trilateration error
Strings are near-vertical.

## Slide 7
STRING BEHAVIOR
Beacon coordinates correlate within one string
Beacon coordinates correlate
within one cluster (on the same depth)
Beacon coordinates correlate between clusters
Strings tend to move in sync, and so do clusters

## Slide 8
SEASONAL VARIATION
Active period (September-October)
Regular beacon behavior

## Slide 9
Dynamics

## Slide 10
COORDINATE ERROR ESTIMATION
Coordinate error for each OM depends on its distance to the nearest beacons and beacon speed (varies with time and depth).
We have installed an additional AM at the center of top section, then compared interpolated coordinates with acoustic measurements.
Mean XY error is ~13 cm ( 20 cm for active period)

## Slide 11
Acoustics/OM sensors crosscheck
Both APS and OM sensors can be used to estimate section inclination.
APS and OM sensors are fully independent systems.
Comparing section inclination estimates allows us to crosscheck both systems.
Work done by S. Koligaev
Section azimuth
Section inclination
Difference between estimates
2017, Cluster #2. String #1, Section #3, OM #2
2017, Cluster #2. String #1, Section #2, OM #6

## Slide 12
Summary
Coordinates of GVD components are determined via a hydro-acoustic positioning system. OM positioning error varies, but our baseline estimate is 10 cm.
OM orientation is estimated from inclinometer and compass mounted inside OMs. Average error – 0.33 deg.
Acoustic modem coordinates correlate with each other heavily, both within a string, a cluster or between clusters, providing positioning redundancy.
Top-most (and most spatially volatile) components move at a speed < 3 cm/s.
Crosscheck between acoustic and orientation data shows commendable consistency.
THANK YOU

## Slide 13
String profiles

## Slide 14
String behavior

## Slide 15
Extreme string displacement 2016-2017