## Slide 1
The new CLBv4 for the KM3NeT neutrino telescope
David Calvo, Diego Real
1
VLVNT 2018, Dubna

## Slide 2
KM3NeT
2
Neutrino telescope in Mediterranean sea
12800 Digital Optical Modules (DOM) in the deep sea
Complex optical network to connect the DOMs with the shore station
VLVNT-18 10-2018

## Slide 3
Digital Optical Module (DOM)
3
Upper Hemisphere
12 PMTs
Lower Hemisphere
19 PMTs
Central Logic Board
(CLB)
PMT Base:
High Voltage Supply
Analog Front-End
VLVNT-18 10-2018
31 PMTs.
1 Central Logic Board (CLB)
1 Power Board
2 Octopus

## Slide 4
First version of CLB (CLBv2)
4
VLVNT-18 10-2018
SFP Transceiver
White Rabbit:
Tunable oscillators
References, DACs
Configuration:
SPI Flash
Octopus:
PMT signals
FMC HPC
Instrumentation
Nanobeacon LED
Test and Debug
Kintex 7
FPGA

## Slide 5
5
Successfully tested:
JTAG and FLASH programming
Nanobeacon and instrumentation
Optical and acoustic readout
Currently installed in the lines.
Next implementation:
Maintain performance
Reduce cost
Reduce power consumption
KM3NeT Electronic meeting 02-03-2018
First version of CLB (CLBv2)

## Slide 6
Second version of CLB (CLBv3)
6
VLVNT-18 10-2018
SFP Transceiver
White Rabbit:
Tunable oscilators
References, DACs
Configuration:
SPI Flash
Octopus:
PMT signals
FMC LPC
Nanobeacon LED & acoustic
Test and Debug
Artix
FPGA
Instrumentation

## Slide 7
Spectrum analysis of CLBv3 and CLBv2
7
CLBv3
CLBv2
VLVNT-18 10-2018

## Slide 8
CLB upgrade: CLBv4
8
Power consumption: no big difference
Lower performance.
Lower switching frequency
Difficult to implement optical
front-end (250 MHz)
Noisy clocks
More or less the same price.
Conclusion:
Redesign the CLBv3.
Move back to Kintex7-160T -2
Improve the clocks layout
After CLBv3 tests:
KM3NeT Electronic meeting 02-03-2018

## Slide 9
Third version of CLB (CLBv4)
9
VLVNT-18 10-2018
Glenair Transceiver
White Rabbit:
Tunable oscilators
References, DACs
Configuration:
SPI Flash
Octopus:
PMT signals
FMC HPC
Instrumentation
Nanobeacon LED & acoustic
Test and Debug
Kintex
FPGA

## Slide 10
CLBV4 clock scheme
10
VLVNT-18 10-2018
25 MHz
CDCM
125 MHZ
125 MHz
125 MHz
FPGA
REFERENCE CLOCK
25 MHz
CDCM
124.99 MHZ
124.99 MHz
DMTD CLOCK

## Slide 11
CLBV4 Glenair transceiver
11
VLVNT-18 10-2018
The design of the optical network will change in KM3NeT Phase 2:
Improving the reliability is mandatory
New Glenair BiDi model with better reliability.

## Slide 12
CLBV4 Layout
12
More than 200
new components
w.r.t. to CLBv3
Improved the placement of
the synchronization stuff
Improved teh routing and grounds to avoid noise
The new design has been sent to the company to produce the first prototypes
VLVNT-18 10-2018

## Slide 13
CLB layout
13
VLVNT-18 10-2018
12 Layers:
2 Power planes
4 Ground planes
4 Signal layers
Differential pairs delay:
less than 100 ps between PMT signals
Less than 20 ps between clock signals

## Slide 14
CLB Firmware
14
VLVNT-18 10-2018

## Slide 15
Summary
15
VLVNT-18 10-2018
The CLB manages the full DOM functionalities
The design has been improved over time
  Hardware, firmware and software
Last protoype ready for production:
  Routing improvement
  New clock scheme
  New transceiver

## Slide 16
The new CLBv4 for the KM3NeT neutrino telescope
David Calvo, Diego Real
16
VLVNT 2018, Dubna