## Slide 1: Разработка концептуального и технического проектов для установки SPD на коллайдере NICA
Conceptual and technical design of the Spin Physics Detector (SPD) at the NICA collider
Руководитель проекта: проф. Румен Ценов
ТЕМА: 02-0-1065-2007/2019

## Slide 2
Main targets of the NICA project:
- study of hot and dense baryonic matter
- investigation of nucleon spin structure,
polarization phenomena
NICA (Nuclotron based Ion Colider fAcility)
is the flagship project in high energy physics
of the Joint Institute for Nuclear Research
Ring circumference, m | 503.04
heavy ions | 
energy range for Au79+: √SNN, GeV | 4 - 11
r.m.s. Dp/p, 10-3 | 1.6
Luminosity for Au79+, cm-2 s-1 | 1x1027
polarized particles | 
max. √S for polarized p, Gev | 27
Luminosity for p, cm-2 s-1 | 1x1032

## Slide 3
NUCLOTRON 0.6-4.5 GeV/u
PS & LU-20 (5MeV/u)
hall for fixed target
experiments
BM@N
MPD
The NICA complex
existing facilities
KRION-6T+ HILac (3MeV/u)
Booster
(600 MeV/u)
MPD hall
SPD hall
Collider
to be constructed
SPD

## Slide 4: Polarized beams
Bunch crossing each 80 ns;
crossing rate 12.5 MHz .
Polarized beams
pp at spp = 12 - 27 GeV, Lav ≈ 1032 cm-2s-1
dd at sNN = 4 - 13 GeV
longitudinal and transverse polarization at SPD and MPD

## Slide 5: Start of the SPD project
arXiv: 1408.3959
Letter of Intent presented at the JINR PAC in summer 2014, where:
  the physics program of the experiment was developed;
  requirements to NICA polarized beams were formulated;
  desired detector characteristics and sketch of the facility were given;
A few presentation at international conferences about the physics potential and program of the SPD were given;
Several workshops on spin physics at NICA were organized:
  NICA-SPIN-2013, Дубна, 17-19.03.2013
  SPIN-Praha-2013, 7-13.07.2013
  NICA-SPIN-2014, Praha, 11-16.02.2014
  SPIN-Praha-2015, 26-31.07.2015
  DSPIN2013, DSPIN2015, DSPIN2017
In 2017 a new stage of the project started:
From LoI to CDR (Conceptual Design Report)

## Slide 6
Physics tasks
Nucleon spin structure studies
  Drell-Yan pair production;
  Direct photons;
  Nucleon PDFs by J/ψ production;
Spin-dependent effects in elastic pp, pd and dd scattering;
Spin effects in exclusive hadron production;
Spin effects in production of hadrons with high pT ;
etc….
Notes: 6
6
6
6

## Slide 7: Spin dependent PDFs

## Slide 8: Structure functions

## Slide 9
σtot ~ 9 nb
Drell-Yan pairs
Notes: 10/24/17
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
10/24/17
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
10/24/17
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
10/24/17
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
10/24/17
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
10/24/17
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
10/24/17
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
9
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
9
9

## Slide 10: COMPASS data, pion beam

## Slide 11: Asymmetries in DY pair production
s= 400 GeV2
Sivers
Boer-Mulders
J.C.Collins et al., PRD73
(2006)014021
Q2 = 4 GeV2
Q2 = 15 GeV2

## Slide 12: Prompt photons
The gluon Compton scattering gives access to the gluon content of proton:
NICA
RHIC
Transverse beam polarization: access to the Sivers function for gluons
Longitudinal beam polarization: access to gluon polarization ∆g/g
Longitudinal beam polarization: access to gluon polarization ∆g/g

## Slide 13: Prompt photon production cross section

## Slide 14: Expected asymmetries

## Slide 15: Charmonium production
NRQCD CEM
Quark annihilation
Gluon fusion

## Slide 16: GPD through vector meson exclusive production
Exclusive DY
p+p → p+p+VM

## Slide 17
Asymmetries in high pT hadron production
Diquark properties;
Confinement laws;
Nature of the huge spin effects;
Deuteron spin structure;
Properties of the bare N- and NK-interactions;
Nature and properties of the cold super dense baryonic matter (CsDBM) (pA and AA);
Dilepton production puzzle in np-interaction.
Notes: 17
17

## Slide 19
SPD advantages:
measurements with pp, pd and dd beams,
possibility to perform energy scan with small steps,
measurements via muon
and electron-positron pairs,
operations with
non-polarized,
transverse and
longitudinally
polarized beams
and their combinations,
possibility to extract all
first order PDFs in one
experiment.
HOME INSTITUTE, EXPERIMENT | RHIC, STAR | RHIC, fsPHENIX | NICA, SPD
Beams | pp, pA, pHe3 | pp pA, pHe3 | pp,pd, dd, pHe3, dHe3
Polarisation | 0.6 | 0.6 | 0.6-0.8
Luminosity, cm-1 s-1 | 5∙1032 | (0.8-6)∙1032 | 1032
√s , GeV | 160,200, 500 | 160,200, 500 | 10-26
X1, range | 0.3-1.0 | 0.3-1.0 | 0.1-0.8
Q T, GeV | 1-10 | 1-10 | 0.5-6
Lepton pairs | µ+µ- | µ+µ- | µ+µ-, e+e-
Start of data taking | >2020 | >2021 | 2025
Measurements |  |  | 
Transversity | yes | yes | yes
Boer-Mulders | yes | yes | yes
Sivers | yes | yes | yes
Predzelosity | no | yes | yes
Worm-Gear | yes | no | yes
Flavour separation | yes | yes | yes
Exclusive DY | yes | no | yes
Deuteron quadrupole structure | no | no | yes

## Slide 20: Minimum biased events
PYTHIA 6, √spp = 26 GeV; 4 MHz event rate
Average charged particle multiplicity ≈ 7.8
Average neutral particle multiplicity ≈ 6.5
from A. Guskov
√s

## Slide 21: Local polarimetry

## Slide 22
close to 4π geometrical acceptance;
high-precision (~50 µm) and fast vertex detector;
high-precision (~100 µm) and fast tracker,
good particle ID capabilities;
efficient muon range system,
good electromagnetic calorimeter,
low material budget over the track paths,
trigger and DAQ system able to cope with event rates at luminosity of 1032 (cm.s)-1,
modularity and easy access to the detector elements, that makes possible further reconfiguration and upgrade of the facility.
Requirements for the SPD

## Slide 23: General view

## Slide 24: Dimensions

## Slide 25: Hybrid magnetic system
stainless steel tube
insulation epoxy
layer, 0.3 mm
copper shield
multilayer thermal shield
outer cover,
1mm stailess steel

## Slide 26: Reconfigurable design

## Slide 27: Beam-beam interaction and t0 counters

## Slide 28
Silicon Vertex Detector
Silicon vertex detector around the beam pipe;
Several layers of double ­sided silicon strips and MAPS;
Optimized number of layers w.r.t. material budget;
Goal: few tens of µm resolution for the vertex reconstruction → detection of particles with open charm and rejection of (π) decay muons.
Vertex detector / Inner tracker
From A. Zinchenko, MPD ITS with MAPS → open charm registration
mm
DSSD: 19.5 m2
MAPS: 3.5 m2
Notes: 28

## Slide 29
Minimum material on the particle tracks (X0 ~ 0.1);
Time (~ 100 ns) and spatial resolution (~100 μm);
Expected particle rates (DAQ rates) ~ MHz;
Technology developed also in JINR, production workshops available
Central tracker: straw tubes
Notes: 29
A.P.Nagaytsev, SPIN-2010, October 1, Juelich
29
29

## Slide 30
Photon energy range 0.1 - 10 GeV;
Due to space limitations the total length of the ECAL module should be less than 50 cm;
Required energy resolution <10.0%/√E (GeV) and energy threshold below 100 MeV.
Design ("shashlik") similar of that for KOPIO
calorimeter,
Crystal variant is being considered, too.
Electromagnetic calorimeter
~6500 modules
Notes: 30
30
30

## Slide 31
It should provide good (>95%) muon identification for momenta above 1 GeV.
Combination of responses from the ECal and RS could give additional lever for regecting of pions and protons in a wide energy range.
The RS also provides additional coordinate measurement.
Our design will follow closely the design of the PANDA experiment range system (at FAIR, GSI) being developed now at the DLNP of JINR
Range system
Notes: 31
31
31

## Slide 33: DAQ
The SPD DAQ may be developed a la upgraded DAQ of the COMPASS experiment;
Event rate ~3.0 MHz (at L=1032 cm-2s-1, √s=27 GeV);
Rough preliminary estimation of the total data flux from the detectors (Si tracker + straw tracker + PID + ECal + range system): 10-20 GBytes/s (no detailed simulation results available yet);
Triggered or trigger-less DAQ: to be decided.

## Slide 34: Software and computing

## Slide 35
System for particle ID (multigap glass RPCs, Micromegas, Aerogel Cherenkov?);
"Zero degree" system (fine grained hadron calorimeter?)
Front-end electronics of the different subsystems;
Systems that have not been thought out yet…
Notes: 35

## Slide 36: Beam test facility

## Slide 37
Форма 29
Resources
NN пп | Наименование статей затрат | Полная стоимость | 2019 | 2020 | 2021
1. | Ускоритель, часы | 2100 | - | 700 | 1400
2. | Конструкт. бюро, нормо-часы, | 12250 | 4000 | 4000 | 4250
3. | Опытное пр-во, нормо-часы | 12700 | 4700 | 4000 | 4000
4. | Материалы, тыс. долл. | 850 | 445 | 205 | 200
5. | Оборудование, тыс. долл. | 920 | 465 | 235 | 220
6. | Оплата НИР, тыс. долл. | 280 | 105 | 105 | 70
7. 8. | Команд. расходы, тыс. долл., в т. ч. а) в страны не рублёвой зоны б) в страны рублевой зоны По протоколам о сотрудничестве | 285 225 60 120 | 95 75 20 30 | 95 75 20 40 | 95 75 20 50
 | Итого по прямым расходам, тыс. долл. | 2455 | 1140 | 680 | 635

## Slide 38: JINR participation: 112 authors, 37.7 FTE
Laboratory of High-Energy Physics
  authors: 74
  FTE: 24.4
Laboratory of Nuclear Problems
  authors: 30
  FTE: 11.3
Laboratory of Theoretical Physics
  authors: 6
  FTE: 2
Directorate (1), Laboratory of Information Technologies (1)

## Slide 39: Collaborating institutions
  INFN section of Turin and University of Turin;
  Charles University, Prague;
  Technical University, Prague
  Tomsk State University;
  Tomsk Polytechnic University;
  Institute of Applied Physics of the Belarus Academy of Sciences;
  Gomel State Technical University, Belarus;
  Institute for High Energy Physics, Protvino;
  Institute of Nuclear Physics of the Moscow State University;
  Institute for Nuclear Research of the RAS, Troitsk;
  Lebedev Physics Institute of the RAS, Moscow;
  Institute for Theoretical and Experimental Physics, Moscow;
  St. Petersburg Nuclear Physics Institute, Gatchina;
  St. Petersburg State University;
  St. Petersburg Polytechnic University;
  Instituto Superior de Tecnologías y Ciencias Aplicadas (INsTEC), Havana University
Protocols for joint research within the SPD project signed.
Bilateral agreements on NICA exist.

## Slide 40: Roadmap
JINR project for the SPD design (Jan. 2019);
Setting up of the collaboration, MoU (2019);
Preparation of the Conceptual Design Report (2019);
Preparation of the Technical Design Report, including prototyping (2020-2022).
Construction of the detector would take at least three years (2022-2025) and first measurements could be expected as early as close to the end of 2025…

## Slide 41
SPD/NICA will provide a unique opportunity
not available at other facilities
to study all of the PDFs in one experiment
and obtain comprehensive information
on the nucleon spin structure
at high statistical level
with minimal systematic uncertainties

## Slide 42: Back-ups

## Slide 43
Year 2014

## Slide 44
 | Ускоритель,часы | КБ, часы | ОП, часы | Материалы, k$ | Оборуд., k$ | НИР, k$ | Итого, k$
Калориметр |  | 800 | 800 | 25 | 25 | 20 | 70
Мюонная система |  | 1000 | 1000 | 135 | 135 | 10 | 280
Идентификация частиц |  | 1000 | 1000 | 15 | 15 | 40 | 70
Магнит |  | 2000 | 2000 | 15 | 15 | 100 | 130
Трекер |  | 1000 | 500 | 135 | 135 | 20 | 290
Вершинный детектор |  | 1500 | 1500 | 250 | 250 |  | 500
Система сбора данных |  |  |  |  | 70 |  | 70
Компьютинг |  |  |  |  | 30 |  | 30
Тестовая зона | 1800 | 3500 | 4000 | 250 | 250 |  | 500
Локальная поляриметрия | 300 | 1100 | 1100 | 105 | 105 | 50 | 260
Станция мечения |  | 350 | 800 | 20 | 20 | 40 | 80
2100 ч. 12250ч. 12700ч. 850 k$ 920 k$ 280 k$ 2050 k$
ИТОГО из бюджета лаборатории: 2050 k$ + 285 k$ (МНТС) = 2335 k$
Ресурсы по подсистемам