## Slide 1
BM@N SLOW CONTROL SYSTEM
D. Egorov, V. Shutov, R. Nagdasev, P. Chumakov

## Slide 2
NICA
BM@N

## Slide 3
Baryonic matter at nuclotron

## Slide 4
What is slow control SYSTEM
Monitoring of the experimental hardware
Centralized control of the Slow Control equipment (LV, HV, gas flow etc.)
Archiving Slow Control data
Alarm system
SC Configuration database
Is not Slow Control:
Main data stream (data acquisition)
Event builder (reconstruction)/event display
Data quality
Run control

## Slide 5
Main goals of sc system
Centralized control of diverse hardware
Scalability
Reliability – monitoring of hardware and software operation
Easy incorporation of existing subsystems and new hardware
Storage of Slow Control data in unified format
Common Slow Control configuration database for all subdetectors (HV, thresholds etc. )
Access control
Modern and easily customizable user interface

## Slide 6
OPTIONS FOR BMN SC BACKBONE
 | Tango Controls | EPICS | WinCC (PVSS)
Free | + | + | -
Open-source | + | + | -
Crossplatform | + | + | -
Multiple language and commercial system bindings | + | + | +
Scalability | + | ± | +

## Slide 7
TANGO-BASED SCS SCHEME
PCs
VMs
Tango middleware
PCs
Front-end layer
Service layer - VMs (Linux)
Client layer – PСs (Linux, Windows)
Ethernet – serial bus convertors(RS485, RS232 …)
devices
Central Services:
- Tango DB
- Configuration DB
- Archiving
- ……
storage
Applications
Device servers
devices
devices

## Slide 8
Status monitoring of bmn subsystems
Desktop application, that displays status of all subdetectors’ equipment, which is controlled by SCS. The color of detector show hardware state according to its priority (OFF>ALARM>WARNING>ON).
Also value from hall sensor and information from DAQ system are presented in the application window.

## Slide 9
MWPC and tof400 hv
Both detectors are using Wiener MPOD power supplies. All data from crates can be obtained by SNMP.

## Slide 10
Magnet field monitoring
Hall sensor measurements are read by ADC, implemented in BMN SCS.

## Slide 11
gem, dch and si tracker HIGH Voltage
and low voltage
These detectors are using the same high voltage and low voltage hardware, made by Wiener and CAEN, and software, that is written in Labview.
Tango has bindings for Labview, so existing software were easily implemented into existing Slow Control System.

## Slide 12
TOF400, TOF700, ZDC and ECal HV
Both detectors are using HVSys high voltage modules, with existing software.
Implemented TCP-socket server send information on request about module to Tango JSON Parsing server.

## Slide 13
Tof400 gas control
Gas control application is used to control and monitor gas flow of system based on MKS PAC-100 modules;
Scales made by CAS with RS-232 interface is using for weight measurement of gas containers for TOF detectors;
Oxygen and humidity sensors made by GE Measurement are used to control the quality of gas mixture.

## Slide 14
Tof400 gas control

## Slide 15
Tof400 preamplifier control and monitoring
X 20
This application monitors preamplifiers’ parameters, like power voltage, thresholds, temperature, and can control its’ DAC.

## Slide 16
Network switch monitoring
Poe switch control the client application to control power over Ethernet (PoE) on a switch (particularly HP J9574A).
Monitors power and network status on each port;
Lets user enable, disable and reset power and network connection of selected switch ports;
Supports multiple devices.

## Slide 17
DAQ VME crate control
Crate Control is a desktop application that was developed for monitoring and control of crates made by Wiener and ELMA.
Main functions:
Monitor state and detailed status of crates
Switch on/off one crate, or all at once
Reset
…

## Slide 18
Uninterruptible power supply monitoring
Uninterruptable power supplies application shows information about power sources at BM@N:
Input and output voltage
Load
Battery info and remaining time
Additional info and load by port
…

## Slide 19
STANDS DEVICES: DUST MONITORING
MPD TOF assembling and testing stand requires clean room.
We use Dylos DC1100 Pro Air Quality Monitor to control number of dust
particles.

## Slide 20
STANDS DEVICES: TEMPERATURE AND HUMIDITY
Temperature and humidity are important for proper detector functioning.
PIR-230-E temperature, and humidity sensor modules are used for this task.

## Slide 21
CONCLUSION
The system so far successfully worked during 5 Nuclotron runs;
Almost all subdetectors’ groups are involved in work and their devices are implemented in BMN Slow Control System;
About 1 month of data taking during 55th Nuclotron Run;
Slow Control system archived > 30 Gb of data;
Existing BMN Slow Control System will be base for the future MPD Slow Control System.

## Slide 22: thanks!
Any questions?
?