## Slide 1: Distributed control and monitoring tools at LU-20 and HILAC complexes.
Elkin Vladimir
Joint Institute for Nuclear Research
VBLHEP

## Slide 2: Injection complex
LU 20
HILAC

## Slide 3: Server equipment
Includes:
CPU Intel® Xeon E5-2640v4 2.40GHz,25M,8.00GT/s 10-Cores
Memory modules DDR4-2400MHz 8GB (8pcs)
HDD SAS 3,5" Seagate Enterprise 600GB (8pcs)
2-port controller Ethernet 1GbE
2-port controller Ethernet 10GbE
SuperServer 6028TR-D72R
Two hot-pluggable systems (nodes) in a 2U form factor.

## Slide 4: Control System layout
Archiving
Tango DB
CS services
Storage
Equipment
Service
layer
Client
layer
WebSocket
REST (HTTP)
TANGO
protocol
Web Application
Desktop Application
PXI, VME
PS …
MODBUS, TCP/IP SOCKET … etc

## Slide 5: The TANGO Device Server
A Tango device server is the process where the Tango class(es) are running.
Tango device class A
Tango device class B
Device
id4/mot/3
A Tango device server
Device
sr/v-ip/1
Device
sr/v-ip/2
Device
id4/mot/1
Device
id4/mot/1

## Slide 6: TANGO devices
TANGO Software Bus
Client
Macro device: e.g. Accelerator
sub devices: e.g. powersupplies
sub devices: e.g. ADC, modbus…
Client

## Slide 7: TANGO devices
Each Tango device is a CORBA object
Each Tango device supports the same network interface
What do we have in this interface ?

## Slide 8: Commands & Attributes
On the network a Tango device mainly has
  Command(s): Used to implement “action” on a device (switching ON a power supply)
  Attribute(s): Used for physical values (a motor position, a temperature, a spectrum, an matrix)
Clients ask Tango devices to execute a command or read/write one of its attributes
A Tango device also has a state and a status which are available using command(s) or as attribute(s)

## Slide 9: POGO. Device Server Code Generator

## Slide 10: POGO. Device Server Code Generator

## Slide 11: Control System. Client layer. TANGO apps.
TANGO control system has several software suites for client-level.
Sardana (open source SCADA using python)
Jddd (Java editor for control system panels)
QTango (c++ and python)
Taurus (python)
Labview (client API)

## Slide 12: Control System. Client Layer. Web applications

## Slide 13: Client-Server communication
This TANGO modules are used for communications between TANGO devices and Web applications
RestDS - to provide access to TANGO control system units through http(s) requests (Ajax) (The developer - Sedykh G.)
WebSocketDS - to provide access to TANGO control system units through WebSocket. Its main advantage is the use of full duplex communication. (The developer - Elkin V.)
These modules are cross-platform generic Tango device-servers, developed in C++ with Boost library. It includes built-in web servers. No additional software is needed. The client web pages could be developed in html with any JavaScript framework

## Slide 14: RestDS
RestDS
Host:port
Threads number
Authentication
Security (SSL)
Web-Client
http://host:port/tango/rest/rc4/devices/thermo/shoulder/1/attributes/T56/value
{
“name”: “T56”,
“quality”: “VALID”,
“timestamp”: 1473348563,
“value”: 273.12,
}
JSON response if successful
Or error code in case of failure
400 – Bad Request 403 – Forbidden
401 – Unauthorized 404 – Not Found
HTTP providing half-duplex communication
One connection - One request – One response

## Slide 15: WebSocketDS
WebSocketDS
Host:port
Authentication
Security (SSL)
Web-Client
ws://host:porte
Or error code in case of failure
400 – Bad Request 403 – Forbidden
401 – Unauthorized 404 – Not Found
WS providing full-duplex communication
One connection - Unlimited requests – Data from server without requests
JSON data from events
JSON data from events
Command or other request
Command response
ETC…

## Slide 16: Beam profile measurement module
A client for managing and monitoring injection profiles is a great example of the effectiveness of using WebSocketDS.
(Профилометр автор Д. Понкин)

## Slide 17: Beam profile measurement module HTTP or WebSocket?
CLIENT
SERVER
CLIENT
SERVER
1 request every
100 ms
Do you have
new data?
No,
Sorry
ETC…
ETC…
ETC…
ETC…
Do you have
new data?
Yes. Get it
Hey!
New data for you
HTTP (RESTDS)
WEBSOCKET (WEBSOCKETDS)
5 - 10 seconds or more

## Slide 18: Web application for combining pages
<iframe> An inline frame places another HTML document in a frame.
list of links to other pages
selected page in tag
<iframe>

## Slide 19: Desktop Emulation
Widgets can be moved within the page. Position is saved in local storage. Widgets are set to the last position on the next loading page.

## Slide 20: Desktop Emulation

## Slide 21: Clients for PS Control
table headers. Names and widths
This parameters are set In JSON file:
connection status
List of power supplies with used components (Inputs, outputs, buttons)

## Slide 22: Clients for PS Control
Alias of device
Input with max min and step set
Buttons with commands
Polarity
Output data of chosen attributes
List of power supplies with used components (Inputs, outputs, buttons) is written in JSON file. Each components has JSON object with parameters.

## Slide 23: Clients for PS Control
tabs
<div> with <iframe>

## Slide 24: Web + Desktop applications
Desktop APP
Web Application
Another method is to write a universal application that works as a standard desktop application, and through a browser (web application).

## Slide 25: Web application for visualizing archived and online data
This Web application can work in different modes.
Mode with settings panel. The user sets the type of graph, and also sets the data source and data types (online or archived data) as well as common chart settings

## Slide 26: Web application for visualizing archived and online data
The mode of the saved charts.
All settings for the type of charts and data source are contained in the URL (GET parameters) or are stored in the database
Title
Aliases

## Slide 27: Web application for visualizing archived and online data. URL mode
In this mode, all settings are contained in the URL. This, for example, eliminates the need to write individual clients for different data sources. Charts can be inserted into any webpages using the <iframe> tag
List of displayed attributes
Displayed attribute names
The minimum settings of the general form
svconf=BASE64(JSON)
JSON configuration contains

## Slide 28
Thanks for attention

## Slide 29: Protection. 2-step authentication
This server has several IP:
External (eg 159.93.0.0/16)
Internal (eg 172.16.0.0/12)
A managed application is running on this server
This server has only an internal local IP. (eg 172.16.0.0/12) The application (AuthDS) is located on this server.
“nonce” request with login
1
2
3
Temporary storage
Getting «salt» (nonce)
4
MD5(“nonce” + “password”)
5
6
checking
confirmation
7
8
Removal of "salt"
response
One of the security methods used is 2-step authentication.