## Slide 1: Modern Heavy Ion Accelerator Facilities in JINR and Worldwide Boris Sharkov JINR, Dubna Состояние дел в ведущих ускорительных центрах Борис Шарков
Boris Sharkov JINR Dubna
1

## Slide 3
Full range of ion beam species: p+ - 239U ;
Highest beam intensities & luminosities;
Generation of ‘Precision beams’: sophisticated beam manipulation methods-stochastic and electron cooling of ion beams, also applicable to the secondary radioactive and antiproton beams;
Rings as accelerator structures of choice: capability to store, cool, bunch, and stretch beams ;
Substantial increase in beam energy variation: by a factor of 20 in energy for beams as heavy as Uranium .
Facilities goals : pushing the “intensity” and the “precision frontiers” to the extremes – not “energy frontier”!
Boris Sharkov JINR Dubna
3
1. Low and medium enegy accelerators E < N GeV

## Slide 4: Key Questions in modern Nuclear Physics

## Slide 5: Accelerator Challenges
Accelerator performance – is progressing well
Fast acceleration
High gradient, variable frequency Ferrite & MA loaded cavities
Compact & cost effective accelerators
Fast cycling superconducting magnets dB/dt ~ 4T/s
Precision beams
Electron & stochastic cooling
XHV @ high beam intensities
Extremely high vacuum ~10-12 mbar
Notes: Accelerator components are being manufactured in high-tech industrial plants in partner countries. A big fraction of them are manufactured in Russia (JINR, Budker, Efremov etc….)

## Slide 6
Flerov Laboratory of Nuclear Reactions

## Slide 7
Dubnium
105
]
Db
D.I. Mendeleev's Periodic Table
Notes: Thus, now the seventh period of D.I. Mendeleev’s Table is fully completed. A considerable (dozens of times) increase of the experimental efficiency is required in order to go ahead and start the pioneer experiments on the synthesis of the elements 119 and 120, the first elements of the 8th period, as well as in order to perform a detailed study of the chemical and physical properties of the known elements. To this end, the JINR implements an ambitious project to construct the world's first Factory of superheavy elements. This accelerator complex was included into the NuPECC Long-Range Plan.

## Slide 8: SHE Factory
High-current cyclotron DC-280
New facilities:
New gas-filled separator
Preseparator
SHELS
SHE Factory Building
Flerov Laboratory of Nuclear Reactions JINR
Notes: The project of the SHE factory includes three principal components: i) high current accelerator, ii) new experimental hall and iii) a number of the next generation facilities.

## Slide 9
DC-280 cyclotron – stand-alone SHE factory
DC280 (expected) E=4÷8 MeV/A |  | 
Ion | Ion energy [MeV/A] | Output intensity
7Li | 4 | 1×1014
18O | 8 | 1×1014
40Ar | 5 | 6×1013
48Ca | 5 | 0,6-1,2×1014
54Cr | 5 | 2×1013
58Fe | 5 | 1×1013
124Sn | 5 | 2×1012
136Xe | 5 | 1×1014
238U | 7 | 5×1010
Synthesis and study of properties of superheavy elements.
Search for new reactions for SHE-synthesis.
Chemistry of new elements.

## Slide 10
New cyclotron DC-280
First extracted beam – 17.01.2019

## Slide 11
First experiments at SHE Factory Synthesis of new elements 119 and 120
From 48Ca to 50Ti
Test reactions: 246Cm+48Ca 294Lv* 244Pu+50Ti 294Lv*

## Slide 13
Классика : SHE-factory, GANIL, MSU, DERICA
Rel. HI : NICA, FAIR magnets
HEP & PP : LHC, HL-LHC, FCC , technologies

## Slide 14
SPIRAL2 LINAC
33 MeV p,
40 MeV d (5mA)
14.5 A.MeV HI (1mA)

## Slide 17: Фабрики радиоактивных изотопов: Все больше, и больше, и больше…и дороже !
FAIR, Germany
SPIRAL2 France
FRIB USA
RIBF Japan

## Slide 18: No. Even bigger…
RAON Korea
HIAF China
Horizontal scale of the slide ~1 km

## Slide 19
Спектрометр в точке столкновения
Поиск тематической «экологической ниши»
«Дефицитная» область: физика экзотических ядер в накопительных кольцах
«Пустыня»: изучение экзотических ядер в электрон-РИ коллайдере
Накопительное кольцо для РИ
Электронное накопительное кольцо
Изохронная масс-спектрометрия
Атомная физика с ободранными ионами
Исследования радиоактивности с ободранными ионами
Высокоточные реакции на внутренних газовых мишенях
Комплекс электрон-РИ коллайдера
Etc….
Электронный ускоритель

## Slide 20
Empty “thematic niche”
Storage ring physics with RIBs
Non-explored field: studies of RIBs in electron-RIB collider
RIB storage ring
electron storage ring
Isochronous mass spectromentry
Atomic physics studies with striped ions
Radioactivity studies with striped ions
Precision reaction studies on internal gas jet target
Studies of electromagnetic formfactors of exotic nuclei in e-RIB collider
Etc….

## Slide 21
e-RIB collider
LINAC–100 (EHI: 100 AMeV)
- Gas cell - Ion trap
- Charge breeder
Experimental hall EH-2: RIBs 15–70 AMeV
50 m
Collector Ring CR:
ERIB  300 AMeV
Gas jet target
p,d,3,4He
Stage 0: LoI, CDR, R&D etc. 2018-2019
Stage 1: Buildings, LINAC–100, DFS, EH-1,2 2020-2024 Stage 2: Gas cell etc., LINAC–30, FRR, EH-3 2022-2027 Stage 3: CR, e-RIB collider, ring experiments 2025-2030
Electron
Ring ER
DERICA Fragment Separator DFS
Ion Sources
Fast Ramping Ring Synchrotron FRR: ERIB  300 AMeV
Experimental hall EH-3: reaccelerated RIBs
5 – 300 AMeV
Velocity filter
e-LINAC (Ee: 500 MeV)
Neutron source
≥ 108 n/cm2
Experimental hall EH-1: Application science
Electron cooler
LINAC–30 (ERIB: 30 AMeV)
Concept of DERICA (Dubna Electron – Radioactive Ion Collider fAcility) project
Long-term research program of RIB at JINR

## Slide 22: Strong Field QED & QCD @ FAIR & NICA
Stoecker & Gutbrod Scientific American 1992
Notes: Utilizing the most powerful particle accelerators, physicist now conduct head- on- head collisions between heavy ions, such as gold or lead nuclei, to recreate the conditions that existed at the birth of Universe.
22

## Slide 23
Boris Sharkov JINR Dubna
23
NUCLOTRON 0.6-4.5 GeV/u
PS & LU-20 (5MeV/u)
hall for fixed target
experiments
BM@N
MPD
The NICA Complex - JINR
existing facility
KRION-6T+ HILac (3MeV/u)
Booster
(600 MeV/u)
MPD hall
SPD hall
Collider
under construction
Notes: 23

## Slide 24
International cooperation NICA
Italy
Japan
Kazakhstan
Moldova
Mongolia
Poland
Romania
RSA
Russia
Serbia
Slovakia
Ukraine
USA
Uzbekistan
Vietnam
Armenia
Australia
Azerbaijan
Belarus
Bulgaria
Brazil
CERN
China
Cuba
Czech Rep.
DPRK
France
Georgia
Germany
Greece
India

## Slide 25
25
NICA/MPD
STAR F.T.
NA-61/SHINE
HADES
CBM
SIS-100 SIS-300
STAR BES II
Interaction rate [Hz]
Collision energy √S [GeV]
NN
NICA/BM@N I
NICA/BM@N II
energy region of max.
baryonic density
Present and future HI experiments/machines for super-dense
nuclear matter physics
Boris Sharkov JINR Dubna
Notes: 25

## Slide 26
 105 - 107 Au+Au reactions/sec
 determination of (displaced) vertices (σ  50 m)
 identification of leptons and hadrons
 fast and radiation hard detectors
 free-streaming readout electronics
high speed data acquisition and high performance
computer farm for online event selection
 4-D event reconstruction
Central Au+Au collision at 25 AGeV (UrQMD + GEANT4):
160 p 400 - 400 + 44 K+ 13 K-
HPC technological challenges

## Slide 27
Полная энергия NN соударений √sNN , [GeV]
Сегодня и завтра в физике
«умеренно» высоких энергий
STAR F.T.
HADES
CBM
«Скорость счёта» [Гц]
NICA/BM@N II
NA-61/SHINE
> 2025: SIS-100 FAIR
energy region of max.
baryonic density
NICA/MPD
STAR BES II

## Slide 28
2022
2025
20??
2018
Fixed target:
L-limited by
detectors
Colliders:
scale of L,
in cm-2s-1
SIS-18 (GSI)
Nuclotron-M (JINR)
SPS (NA-49/61, CERN)
AGS (BNL)
RHIC (BNL)
BM&N (JINR)
NICA (JINR)
SIS-100 (FAIR)
SIS-300 (FAIR)
2
4
6
8
20
40
60
80
for Au+Au
1
10
102
√SNN, GeV
Expected region of phase transition at max baryonic density
1027
1025
1023
Existing and future HI accelerators
in operation
28
CBM – NICA co-operation agreement
>
Notes: Compared to other heavy ion facilities CBM driving experimental requirements are in precision and extremely high reaction rates for the most interesting energy range of heavy ion collisions.

## Slide 29
Антипротонное Накопительное кольцо
HESR
СП Синхротроны
SIS100 SIS300
p - Линак
Накопитель
CR
Новое экспериментальное кольцо
NESR
СП фрагмент-сепаратор
Super-FRS
Рециркулятор RESR
Rare Isotope
Production Target
Antiproton
Production Target
300m
ФАИР (FAIR) – новый, крупнейший в мире, строящийся, международный исследовательский центр
в г. Дармштадт, Германия
Россия – стратегический партнер и
собственник установки
Russia

## Slide 30
UNILAC
SIS18
SIS100/300
p-Linac
HESR
CR & RESR
NESR
Cryring
Rare-Isotope
Production Target
Anti-Proton
Production Target
100 m
Primary Beams
1012/s; 1.5 GeV/u; 238U28+
1010/s 238U73+ up to 35 GeV/u
3x1013/s 30 GeV protons
Secondary Beams
Storage and Cooler Rings
radioactive beams
1011 antiprotons 1.5 - 15 GeV/c,
stored and cooled
Technical Challenges
cooled beams, rapid cycling superconducting magnets
range of radioactive beams up to 1.5 - 2 GeV/u; up to factor 10 000 higher in intensity than presently
antiprotons 3 - 30 GeV
new international research laboratory to explore the nature of matter in the Universe
ФАИР (FAIR) – новый, крупнейший в мире, строящийся, международный исследовательский центр в г. Дармштадт, ФРГ
Notes: FAIR accelerator will generate beams of heavy ions, protons and antiprotons of unprecedented intensity, brightness and luminousity.

## Slide 31
Intensity gain: x 100 – 1000
10 x energy (comp. to GSI)
Antimatter: antiproton beams
Precision: System of storage and cooler rings
Unique features:
Flexibility and parallel operation
Intense and high-energy heavy-ion beams
Storage rings and beam cooling: Beam quality
Major accelerator developments
ESFRI Landmark
Top priority for European Nuclear Physics Community
Driver for Innovation in Science and Technology
FAIR: Facility for Antiproton and Ion Research – a World-Wide Unique Accelerator Facility
Russia

## Slide 32
CBM
nuclear matter at high densities
NUSTAR
neutron-rich nuclei
APPA
ions in extreme electro-magnetic fields
PANDA
hadron physics with antiprotons
4 Research Pillars of FAIR

## Slide 33
FAIR Signatory Countries
Германия | 
Россия | 
Финляндия | 
Франция | 
Индия | 
Польша | 
Румыния | 
Словения | 
Швеция | 
Великобритания (a) | 
FAIR – 500 ученых из 20 российских
Институтов участвовало в
разработке Н/Т Обоснования (BTR)
Россия – стратегический партнер и
собственник установки
FAIR – исследовательская
инфраструктура, нацеленная на
международное междисциплинарное
сотрудничество
~3 000 ученых из ~50 стан мира
Международный проект FAIR

## Slide 34
Институты России в мега-проекте ФАИР
34
Структура заявки головных институтов России на участие в ФАИР
Институт | Стоимость в М€ (в ценах 2005) |  | 
 | эксперименты | ускорители | Сумма
ИЯФ СО РАН | 2,9 | 34,5 | 37,4
ИФВЭ | 17,34 |  | 17,34
ОИЯИ | 13,32 | 27,1 | 40,42
ИТЭФ | 5.8 | 0.27 | 6,07
НИИЭФА |  | 17,8 | 17,8
ПИЯФ | 9,29 |  | 9,29
ФТИ РАН |  | 0,83 | 0,83
ИПХФ РАН | 1,77 |  | 1,77
ИЯИ РАН | 0,78 |  | 0,78
НИЦ КИ | 0,48 |  | 0,48
МЭИ | 0,35 |  | 0,35
ФИ РАН | 0,35 |  | 0,35
ИТОГО | 52,38 | 80.5 | 132,88
75% вклада РФ должно возвратиться в виде контрактов в российские институты
Notes: 34
PANDA Collaboration Meeting
March 03, 2008
34

## Slide 35: Heavy ion accelerator chain
SIS18
NuSTAR
Collector Ring
Super-FRS
CBM
CBM
SIS 100
35
Plasma Physics
cave

## Slide 36
Important beam parameters: - all elements (H through U) - intensity ~ 1012 ions/sec. - beam energies up to 1.5 GeV/u - fast and slow (DC-type) extraction
The NuSTAR experimental facilities at FAIR
Four experimental areas:
- superconducting fragment separator
- high-energy branch with reaction setup
- storage-ring complex (CR, RESR, NESR, eA)
- low-energy branch with energy focusing and re-acceleration

## Slide 37: Anti proton accelerator chain
SIS18
p-Linac
p-bar target
Collector Ring
HESR
SIS 100
PANDA
37

## Slide 38: Full Length SIS100 Dipole
Manufactured by BNG (Würzburg)
Dipole and quadrupole under manufacturing at JINR and BNG

## Slide 39
Manufacturing design of first of series module, completed by GSI design department
Design service contract for overall cryomagnetic quadrupole module system signed and progressing
In-kind & R&D contract for production and testing of quadrupole units with JINR signed
Production of FoS unis until end of 2017 in JINR
Cryomagnetic Quadrupole Modules for SIS100 (JINR)
SIS100
Design of QM module including end boxes (link to local cryogenics)
Design of FoS modul and components by GSI Design Office

## Slide 40
SIS100 Quad. Units Collaboration Contract with JINR
Dubna 20.02.2015

## Slide 41: Status of FAIR: Civil Construction rapid progress since official start on 4th of July 2017
Excavation SIS100 tunnel
Upgraded SIS18 completed ready for FAIR and FAIR phase 0
Start of concrete shell works for SIS100
Excavation transfer building & CBM cave
Civil Construction

## Slide 42
BRing
SRing
MRing
iLinac
SECR
iLinac: Superconducting linac
Length:100 m
Energy: 17MeV/u(U34+)
BRing: Booster ring
Circumference: 530 m
Rigidity: 34 Tm
Beam accumulation
Beam cooling
Beam acceleration
MRing: Figure “8” ring
Circumference: 268 m
Rigidity: 13 Tm
Ion-ion merging
SRing: Spectrometer ring
Circumference:290m
Rigidity: 13Tm
Electron/Stochastic cooling
Two TOF detectors
Four operation modes
High-Intensity Heavy Ion Accelerator Facility General description – Main components

## Slide 43
 | Ions | Energy | Intensity
SECR | 238U34+ | 14 keV/u | 0.05 pmA
iLinac | 238U34+ | 17 MeV/u | 0.028 pmA
BRing | 238U34+ | 0.8 GeV/u | ~1.41011 ppp
SRing | RIBs: neutron-rich, proton-rich | 0.84 GeV/u(A/q=3) | ~109-10 ppp
 | Fully stripped heavy ions H-like, He-like heavy ions | 0.8 GeV/u(238U92+) | ~1011-12 ppp
MRing | 238U92+ | 0.8 GeV/u | ~1.01011 ppp
General description – Basic beam parameters

## Slide 44
HIAF site
HIAF site
Artist impression HIAF campus
General description – New campus

## Slide 45
20~ | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Critical Points |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Construction and Installation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commissioning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Budget periods |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Idea design
Conceptual design
Key technologies R&D
Design report preparation,
submission,
approval
Detailed design &
prototype
Civil construction
Equipment construction, Fabrication
Installation
iLinac, BRing, CRing commissioning
Combined commissioning
Start of operation
Plan
Approval
Start
construction
Commissioning
Operation
BP2
BP3
BP4
BP1
General description – Schedule

## Slide 46
Summary
A number of modern international research facilities are under construction;
Generation of intense “precision beams” : sophisticated beam manipulation methods-stochastic and electron cooling of ion beams, also applicable to the secondary radioactive and antiproton beams;
Rings as accelerator structures of choice: capability to store, cool, bunch, and stretch beams ;
Full range of ion beam species: p+ - 239U ;
Highest beam intensities & luminosities;
A number of large scale experiments are in advanced praparatory phase.
Boris Sharkov JINR Dubna
46

## Slide 47
2.

## Slide 48: Future Energy Frontier Colliders
All proposals are focused on :
  (High) Luminosity and Cost (Affordable)
  Usually :
  Scale of civil construction grows with Energy
  Cost of accelerator components grows with Energy
  Requirement site power grows with Energy
So, the total cost grows with ENERGY
  Thankfully, not linearly , more like cost ~ β E κ , κ≈ ½…2/3
    Take ILC as an example: 0.25  0.5  1 TeV 0.69 : 1 : 1.67
  Still, huge challenge for energies E some x10 of LHC
  Choice of technology ( β ) and prior investments are critical

## Slide 50: Accelerator Technologies advanced in PP
Type | Acclerator | Op. Years | Beam Energy (TeV) | B [T] | E [MV/m] | Pioneering/Key Technology
CC hh | Tevatron | 1983-2011 | 2 x 0.5 | 4 T |  | Superconducting Magnet (SCM)
 | HERA | 1990 -2007 |  | 4.68 T |  | SCM, e-p Collider,
 | RHIC | 2000 ~ |  | 3.46 T |  | SCM
 | SPS LHC HL-LHC | 1981-1991 2008 ~ Under constr. | 2 x 0.42 2 x ( 6.5 >> 7) | (NC mag.) 7.8T -->8.4 11~12 |  | P-bar Stochastic cooling SCM (NbTi) at 1.8 K, SRF SCM (Nb3Sn), SRF, e-cooling
CC ee | TRISTAN | 1986-1995 | 2 x 0.03 |  | 5 | SRF (Nb-bulk), SCM-IR-Quad (NbTi)
 | LEP | 1989-2000 | 2 x 0.55 |  | 5 | SRF (Nb-Coating) , SCM-IRQ
 | KEKB Super-KEKB | 1998~2010 2018 ~ | 0.002+0.008 0.004+0.007 |  | 5 5 | Luminosity, SRF Crabbing, SCM-IRQ Luminosity, Nano-beam, SCM-IRQ
LC ee | SLC/PEP-II | 1988/98~2009 | 2 x 0.5 |  |  | Normal conducting RF
 | (Eu-XFEL) | (2018 ~) | (0.0175) |  | (23.6) | SRF (Nb-bulk)

## Slide 51: LHC performance at a glance
7 TeV  8.33 tesla, 86% of the max Ic
WG on quench performance.
E. Todesco, chair
F. Bordry, CERN Director for A&T
Notes: Trovare rampa cpllisioni 30 marzo 2010 2x3.5; in 2012 2x4 T ; in 2015 2x6.5 T

## Slide 52: LHC Performance: Integrated Luminosity
Goal of Run1+Run2 was 150 fb-1!
F. Bordry, CERN Director for A&T
Cryo availbility: 97-99 % !

## Slide 53: Goal of HL-LHC
The main objective of HiLumi LHC Design Study is to determine a hardware configuration and a set of beam parameters that will allow the LHC to reach the following targets:
A peak luminosity of Lpeak = 5×1034 cm-2s-1 with levelling, allowing: An integrated luminosity of 250 fb-1 per year, enabling the goal of Lint = 3000 fb-1 twelve years after the upgrade. This luminosity is more than ten times the luminosity reach of the first 10 years of the LHC lifetime.
From EC-FP7 HiLumi LHC Design Study application of 2010
Ultimate performance established 2015-2016: with same hardware and same beam parameters: use of engineering margins:
Lpeak ult  7.5 1034 cm-2s-1 and Ultimate Integrated Lint ult  4000 fb-1
LHC should not be the limit, would Physics require more…
Experiment are designing for this goal. We need to be compatible with it!

## Slide 54
Half way
7 TeV  8.33 tesla, 86% of the max Ic
Performance: Integrated Luminosity

## Slide 55: HL-LHC parameters
ОИЯИ - Экономичные 6 Тл магниты для реконструкции SPS

## Slide 56: Pile up
5 events
400
events
Pushing at the maximum the parameters of HL-LHC we would start the fill at L = 15x1034 with 400 events/crossing.
Notes: Ask Rogelio how degrade sensitivity wit pile up and ple up density.

## Slide 57
Technology landmarks

## Slide 58
LBH_A (11T)
LBH_B (11T)
By-pass cryostat with collimator
Complete 11.2 T cryo-assembly replacing a 15 m long 8.3 LHC dipole
Operation 7 TeV
7 TeV
Hybrid (long proto): Excellent!, But strong permanent degradation after thermal cycle. Absence of thermal gradient control in the procedure.
L. Bottura & A. Devred
HiLumi WP11- F. Savary et al.
JINR – efficient 6T magnets for SPS upgrade
ОИЯИ - Экономичные 6 Тл магниты для реконструкции SPS

## Slide 59: What will look like this new HE-LHC option? A realistic LHC1.5 @ 21 TeV for 2040…
LHC1.5
12 T Nb3Sn dipoles HiLumi technology in LHC: 21 TeV c.o.m.
7 T Nb-Ti dipole (low cost LHC, 4.2 K):
44 TeV c.o.m. (100 km)
Energy tripler 100km
2040
In LHC, 14 T dipoles give 23.5 TeV
But timeline is NOT the same
HTS

## Slide 60: Circular pp Colliders
Input #133
Key facts: HE-LHC / FCC-hh* / SppC*
Large tunnel – 27 / 100 / 100 km
SC magnets – 16 / 16 / 12 T
High Lumi / pileup O(1035) / O(500)
Site power (MW) – 200 / 500? / ?
Cost (BCHF) – 7.2 / 17.1 / ?
* follow up after e+e- Higgs factories
FCC-hh CDR (2018)
Input #136
HE-LHC CDR (2018)
Input #51
FCC-hh 100 TeV
HE-LHC 27 TeV
SppC 75 TeV

## Slide 63
X. Lou
CEPC-SppC timeline

## Slide 64
Circular hadron colliders: FCC-hh and SppC
circumference 100 km, two high-luminosity experiments up to 3 (1) x 1035 cm-2s-1, two additional experiments possibly combined with injection section, collimation insertions (betatron and momentum cleaning), extraction/dump insertion, RF insertion,
FCC-hh
SppC
new injector chain,
simultaneous operation with e+e- collider
based on existing CERN injector chain,
Luminosity goal ~20 ab-1 per main IP within 25 years
values in brackets refer to CEPC

## Slide 65: Frontier Accelerators based on SC Technology
Courtesy, A. Ballarino
High-energy and High-Intensity frontier accelerators
are relying
on superconductivity
as core technology
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 66
high-field magnet R&D for FCC-hh
FCC baseline: 16 T magnets, Nb3Sn, exploiting experience of LHC and HL-LHC
In parallel, HTS magnets (special magnets, hybrid configurations)
After ~2 years development, prototype Nb3Sn wires from several R&D partners already achieve HL-LHC Jc performance
Worldwide short model magnet R&D  various coil geometries
2018 – 2025
CEA, CIEMAT, INFN, PSI,
US-MDP (FNAL, LBNL), BINP
FCC goal
Worldwide wire R&D towards
Jc (16T, 4.2K) > 1500 A/mm2
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 67: Personal View on Relative Timelines
Timeline | ~ 5 | ~ 10 | ~ 10 |  |  | ~ 15 |  | ~ 20 |  | ~ 25 | ~ 30 | ~ 35 | 
Lepton Colliders |  |  |  |  |  |  |  |  |  |  |  |  | 
SRF-LC/CC | Proto/pre-series | Construction | Construction |  |  |  |  | Operation |  |  | Upgrade |  | 
NRF—LC | Proto/pre-series | Construction | Construction | Construction |  |  |  | Operation |  |  | Upgrade |  | 
Hadron Collier (CC) |  |  |  |  |  |  |  |  |  |  |  |  | 
8~(11)T NbTi /(Nb3Sn) | Proto/pre-series |  | Construction |  |  |  |  | Physics Experiment | Operation |  |  | Upgrade | Upgrade
12~14T Nb3Sn | Short-model R&D |  |  |  | Proto/Pre-series |  |  |  | Construction | Construction to Physics Experiment | Operation |  | 
14~16T Nb3Sn | Short-model R&D |  |  |  |  |  | Prototype/Pre-series |  |  |  | Construction | Construction | 
Note: LHC experience: NbTi (10 T) R&D started in 1980’s --> (8.3 T)
Production started in late 1990’s, in ~ 15 years

## Slide 69
Challenges for hadron colliders
High stored energy in the beam ~8-9 GJ
  Beam handling and dumping
  Collimation cleaning system optimisation
High synchrotron radiation inside magnets several MW
  Beam screen design and cryogenic efficiency
LHC pattern
FCC dump pattern
FCC Secondary Collimator
max power density
115 Wcm-3
Beam screen prototype
R&D on new materials, kickers & generators, vacuum systems, cryogenic system, electron lenses, ….
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 70: Summary: Challenges - SRF and SC Magnet
Superconducting RF:
  Nb-bulk (for > 1 GHz)
    High-Q (> 3E10) and High-G (> 45 MV/m) , w/Low-T treatment w/ or w/o N-infusion.
    Large-Grain SRF cavity for cleaner condition with cost-reduction,
  Thin-Film (for wider applications)
    Thin-film on Nb to improve effective Bsh, resulting higher gradient, and further Potential
    New material such as NB3Sn/MgB2 to drastically improve performance.
Superconducting Magnet:
  Nb3Sn requires much longer steps to reach 16 T, for improvement of SC current density, mechanical property, field quality control, training quenches, magnet protection, and industrialization.
  “Nb3Sn + HTS-insert” be inevitably required, beyond 16 T, and cost effective HTS will be essentially required for practical accelerator applications.

## Slide 71: Personal Prospect (2/2)
Nb3Sn superconducting magnet technology for hadron colliders, still requires step-by-step development to reach 14, 15, and 16 T.
It would require the following time-line (in my personal view):
  Nb3Sn, 12~14 T: 5~10 years for short-model R&D, and the following 5~10 years for prototype/pre-series with industry. It will result in 10 – 20 yrs for the construction to start,
  Nb3Sn, 14~16 T: 10-15 years for short-model R&D, and the following 10 ~ 15 years for protype/pre-series with industry. It will result in 20 – 30 yrs for the construction to start, (consistently to the FCC-integral time line).
  NbTi , 8~9 T: proven by LHC and Nb3Sn, 10 ~ 11 T being demonstrated. It may be feasible for the construction to begin in > ~ 5 years.
Continuing R&D effort for high-field magnet, present to future, should be critically important, to realize highest energy frontier hadron accelerators in future.

## Slide 72: Comparisons
Project | Type | Energy [TeV] | Int. Lumi. [a-1] | Oper. Time [y] | Power [MW] | Cost
ILC | ee | 0.25 | 2 | 11 | 129 (upgr. 150-200) | 4.8-5.3 GILCU + upgrade
 |  | 0.5 | 4 | 10 | 163 (204) | 7.8 GILCU
 |  | 1.0 |  |  | 300 | ?
CLIC | ee | 0.38 | 1 | 8 | 168 | 5.9 GCHF
 |  | 1.5 | 2.5 | 7 | (370) | +5.1 GCHF
 |  | 3 | 5 | 8 | (590) | +7.3 GCHF
CEPC | ee | 0.091+0.16 | 16+2.6 |  | 149 | 5 G$
 |  | 0.24 | 5.6 | 7 | 266 | 
FCC-ee | ee | 0.091+0.16 | 150+10 | 4+1 | 259 | 10.5 GCHF
 |  | 0.24 | 5 | 3 | 282 | 
 |  | 0.365 (+0.35) | 1.5 (+0.2) | 4 (+1) | 340 | +1.1 GCHF
LHeC | ep | 60 / 7000 | 1 | 12 | (+100) | 1.75 GCHF
FCC-hh | pp | 100 | 30 | 25 | 580 (550) | 17 GCHF (+7 GCHF)
HE-LHC | pp | 27 | 20 | 20 |  | 7.2 GCHF

## Slide 74: Conclusion
Success of experiments is granted by two basic factors :

## Slide 75: Back up slides

## Slide 76
Neutron halos
Shape
Coexistance
New magic numbers
Exotic Shapes
Fission dynamics
2p radioactivity
Lattice Effective
Field Theory
Clusters
n-p pairing
Equation of state
Coupling to
continuum
New oppurtunities:
Physics at the Femtometer scale
Limits of existance
Search and understand regular and simple patterns that emerge in the structure of
complex nuclei
Key variables in the dynamics of colliding nuclei

## Slide 77
Cyclotrons vs. LINACs – pro et contra
Injection <50% transmission
Accelerate 1 charge state
Flexible acceleration strategy
Length
“No loss” operation
Plus
Minus
Basic
Cyclotron
LINAC
RFQ ~99% transmission
Accelerate 3 charge states
Factor 6
Upgradable
Cost per AMeV
Superconductivity for CW
Compact
HI Injection/extraction problems
Easy to repair
Superconductivity for U > 50 AMeV
Easy to operate
Could be hard to repair

## Slide 78
Cyclotrons vs. LINACs – pro et contra
Injection <50% transmission
Accelerate 1 charge state
Flexible acceleration strategy
Length
“No loss” operation
Plus
Minus
Basic
Cyclotron
LINAC
RFQ ~99% transmission
Accelerate 3 charge states
Factor 6
Upgradable
Cost per AMeV
Superconductivity for CW
Compact
HI Injection/extraction problems
Easy to repair
Superconductivity for U > 50 AMeV
Easy to operate
Could be hard to repair

## Slide 79: Superconducting?
Superconducting magnets and RF structures are widely used in modern accelerators.
Superconducting CW machines like SNS in the USA or j-Parc in Japan reach high acceleration efficiency in their RF structures (>50% efficiency from wall plug to beam is possible in SC CW linacs including refirigerator.).
Pulsed superconducting RF delivers often no higher energy efficiency compared to NC due to the longer RF pulse required or high complexity and cost for low gain.
Losses, caused for example by ramped synchrotron magnets, must be cooled by liquid helium with a typical efficiency of 1 W cooling power for 250 W of refrigerator/ liquefier.

## Slide 80
Superconducting technologies (Т=4.5 К, Т=77К)
R&D and construction of high-temperature superconducting current leads (HTSC @ 77К), conductors and elements. (20кА х 200 V = 4 МW).
Power saving factor of ~ 20-30
R&D, serial production of compact fast-cycling superconducting (5 Hz, 4-8 T/s) magnets (dipoles, quadrupoles, multipoles). Compactification with factor
of ~2-3 in geometrical sizes in comparison to “warm” magnets.

## Slide 81
FAIR Signatory Countries
Research Projects – a platform
for coordination of international
efforts in order to define
research priorities and
maximise scientific impact.
FAIR and NICA are building
research infrastructures with a
specific focus on international
and interdisciplinary collaboration.
International Research - global dimension
B. Sharkov
81

## Slide 82
Unprecedented beam Intensity( Comparison with HIRFL):
Primary beam intensity increases by x 1000 - x 10000
secondary beam intensity increases by up to x 10000
Wide beam Energy: heavy-ion energy : x 10 - x 15
Precisely-tailored beams
beam cooling (Electron, Stochastic, laser; high quality, very small spot )
Beam compression (Ultra-short bunch length: 50-100ns)
Super long period slow extraction
(Super long, high energy, quasi-continuous beam )
Versatile operation modes:
parallel operation, beam splitting
( increase of target time, high integrated luminosity)
HIAF General description – Basic beam parameters

## Slide 83
Nuclear physics
Nuclear astrophysics
High energy and density physics
Atomic physics
Spontaneous electron–positron pair production
Science motivations
Notes: First is science motivations, the proposed research fields of HIAF are ….

## Slide 84
HIAF建设经费概算
Items | 1st phase (MRMB)
iLinac | 360
BRing | 350
High energy electron cooling | 
Beam transfer line | 50
Experiment setups | 240
Cryogenics | 80
Civil engineering | 190
Tunnel construction | 160
Contingency cost | 100
Total of facility | 1530 (central government)
Land & infrastructure | 1000 (local government)
Total | 2530
General description – Budget

## Slide 85
Future – Path to Very High Energies:
Hadron /e+e-/ Muon Colliders

## Slide 86
US electron-ion colliders
two collider rings (e-, A) at c.o.mass energies from 20 - 100 GeV, upgradable to 140 GeV; high luminosity 10 33-34 cm -2 s -1, highly polarised electron and nucleon beams; possibility of 2 IPs, ion beams from deuteron to the heaviest nuclei (uranium or lead); pre-CDRs completed
Some key ingredients: efficient SRF cavities; crab cavities; high-energy hadron beam cooling (IBS) for high luminosity, high field magnets for the interaction points, etc.
BNL-eRHIC
JLAB-JLEIC
Electron ion colliders combine challenges of circular ee & hh colliders  strong opportunities for collaborations

## Slide 87
FCC-eh & CEPC-SppC
Future hadron colliders will provide possibility for lepton-hadron collisions.
FCC-eh: ~60 GeV e- from Energy Recovery Linac (PERLE test facility proposal Orsay)
SppC: e-beam from co-existing CEPC in same tunnel
PERLE TF
at Orsay
ep Higgs factory based on
FCC-hh & ERL
luminosity
~10 34 cm -2 s -1
luminosity e-p
~5 x10 33 cm -2 s -1
Y. Zhang

## Slide 88: Long term development of SC is critical for HEP Hadron Collider: Open SC Lab Proposal
L. Bottura and F. Bordry
Phase I - Construction and commissioning (3 years)
• Equipment and labour: 10 MCHF
• Surface: 2000 m2
• Personnel: 10 FTEy (1 project engineer + 2 techn.)
Phase II - Facility ramp-up and initial operation (7 years, processed R&D material of the order of 25 kg/week, operation 40 weeks/year)
• Total cost: 20-30 MCHF

## Slide 89: General Summary: Personal Prospect (1/2)
Accelerator Technologies are ready to go forward for lepton colliders (ILC, CLIC, FCC-ee, CEPC), focusing on the Higgs Factory construction to begin in > ~5 years.
SRF accelerating technology is well matured for the realization including cooperation with industry.
Continuing R&D effort for higher performance is very important for future project upgrades.
  Nb-bulk, 40 – 50 MV/m: ~ 5 years for single-cell R&D and the following 5 – 10 years for 9cell cavities statistics to be integrated. Ready for the upgrade, 10 ~ 15 years.